| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRE/2005/9 11 January 2005 Original: ENGLISH ENGLISH AND FRENCH ONLY |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Lighting and Light-Signalling (GRE)

(Fifty-fourth session, 5-8 April 2005,

agenda item 14.1.)

DRAFT PROPOSAL FOR AMENDMENTS TO REGULATION No. 6

(Direction indicators)

Transmitted by the expert from the Working Party "Brussels 1952" (GTB)

Note:	The text reproduced below was prepared by the expert from GTB, in order to insert into Regulation No. 6 additional provisions which would allow testing of direction indicators incorporating multiple light sources with regard to the activation of the operating tell-tale prescribed in Regulation No. 48.  The modifications to the current text of the Regulation are marked in bold characters.

_______

__________________

Note:	This document is distributed to the Experts on Lighting and Light-Signalling only.

A.	PROPOSAL

Insert a new paragraph 2.2.4., to read:

"2.2.4.	For a direction indicator equipped with more than one light source (including those specified in paragraph (i) of footnote 3 to paragraph 6.1. of this Regulation), information regarding the activation criteria for the operating tell-tale (see paragraph 6.5.8. of Regulation No. 48);"

Paragraph 2.2.4. (former), renumber as paragraph 2.2.5.

Paragraph 6.1., footnote 3, delete paragraph (ii) and renumber the former paragraph (iii) as paragraph (ii).

### Annex 2

Item 9., add at the end:

"For direction indicators equipped with more than one light source:

Activation criteria for the operating tell-tale: 	"

*          *           *

B.	JUSTIFICATION

This proposal to amend Regulation No. 6 is a consequence of the proposal to insert into Regulation No. 48 new provisions in order to cover the activation of the operating tell-tale for direction indicators with multiple light sources.  This issue has been addressed by GRE at several instances, and a proposal regarding footnote 3 to paragraph 6.1. was adopted at the forty-sixth session.  However, it was recognized that this solution only covers lamps designed for two light sources and it should be replaced by a general approach which covers lamps with more than one light source.

__________________