| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRE/2005/11 14 January 2005 Original: ENGLISH ENGLISH AND FRENCH ONLY |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Lighting and Light-Signalling (GRE)

(Fifty-fourth session, 5-8 April 2005,

agenda item 6.2.)

PROPOSAL FOR A CORRIGENDUM TO REGULATION No. 99

(Gas-discharge light sources)

Transmitted by the expert from the Working Party "Brussels 1952" (GTB)

Note:	The text reproduced below was prepared by the expert from GTB in order to correct the specifications of D3R and D4R.  It is based upon the text of Revision 1 of Regulation No. 99, including Corrigendum 1 to Supplement 1, and Amendment 1.  The proposed corrections to the current text of the Regulation are marked in bold characters.

________

_______________

Note:	This document is distributed to the Experts on Lighting and Light-Signalling only.

A.	PROPOSAL

Annex 1,

Sheet DxR/6, the existing table:

"

| Dimension in mm | Production light sources | Standard light sources |
| --- | --- | --- |
| r | 0.50 ( 0.25 | 0.50 ( 0.20 |
| s | 1.10 ( 0.25 | 1.10 ( 0.25 |

"

should read:

"

| Dimension in mm | Production light sources | Standard light sources |
| --- | --- | --- |
|  | D1R/D2R | D3R/D4R |  |
| r | 0.50 ( 0.25 | 0.50 ( 0.25 | 0.50 ( 0.20 |
| s | 1.10 ( 0.25 | 1.10 + 0.25/-0.40 | 1.10 ( 0.25 |

"

*          *           *

B.	JUSTIFICATION

The proposed modification of tolerances for dimension "s" for D3R/D4R production light sources takes into account the learning experience of manufacturers regarding light source production, as well as the corresponding values for the S type light sources.  It has been verified that there are no negative consequences for headlamp safety performance.

__________________