#### UNITED

# NATIONS

Distr.

# GENERAL

# TRANS/WP.15/159/Add.3

# 31 July 2000

# ENGLISH

Original: ENGLISH AND FRENCH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport

of Dangerous Goods

REPORT OF THE WORKING PARTY ON ITS SIXTY-SEVENTH SESSION

(8-12 November 1999)

Addendum 3

Chapter 4.1 of the restructured ADR

The secretariat reproduces below the text of Chapter 4.1 of the restructured ADR. Later decisions taken by the RID/ADR/ADN Joint Meeting at its 13-24 March 2000 session have also been taken into account.

GE.00-

CHAPTER 4.1

USE OF PACKAGINGS, INCLUDING INTERMEDIATE

BULK CONTAINERS (IBCs) AND LARGE PACKAGINGS

Introductory notes

NOTE 1: Packing groups

Dangerous substances of all classes other than those of Classes l, 2, 5.2, 6.2 and 7 and than the self-reactive substances of Class 4.1 have for packing purposes been assigned to three packing groups in accordance with the degree of danger they present, i.e.:

Packing group I: 	Substances presenting high danger;

Packing group II: 	Substances presenting medium danger ; and

Packing group III: 	Substances presenting low danger.

The packing group to which a substance is assigned is indicated in Table A of Chapter 3.2.

NOTE 2: Explosives, self-reactive substances and organic peroxides

Unless specific provision to the contrary is made in ADR, the packagings, including IBCs and large packagings, used for goods of Class l, self-reactive substances of Class 4.1 and organic peroxides of Class 5.2 shall comply with the requirements for the medium danger group (Packing group II).

4.1.1	General provisions for the packing of dangerous goods, other than goods of Classes 2, 6.2 or 7, in packagings, including IBCs and large packagings

NOTE: Some of these general provisions may apply to the packing of goods of Class 2, 6.2 and 7. Refer to sections 4.1.6 (Class 2), 4.1.8 (Class 6.2), 4.1.9 (Class 7) and to the applicable packing instruction in section 4.1.4.

4.1.1.1	Dangerous goods shall be packed in good quality packagings, including IBCs and large packagings, which shall be strong enough to withstand the shocks and loadings normally encountered during carriage, including trans-shipment between transport units and/or warehouses as well as any removal from a pallet or overpack for subsequent manual or mechanical handling. Packagings, including IBCs and large packagings, shall be constructed and closed so as to prevent any loss of contents when prepared for transport which might be caused under normal conditions of transport, by vibration, or by changes in temperature, humidity or pressure (resulting from altitude, for example).  No dangerous residue shall adhere to the outside of packages, IBCs and large packagings during carriage. These provisions apply, as appropriate, to new, reused, reconditioned or remanufactured packagings and to new and reused IBCs and large packagings.

4.1.1.2	Parts of packagings, including IBCs and large packagings, which are in direct contact with dangerous goods:

(a)	shall not be affected or significantly weakened by those dangerous goods; and

(b)	shall not cause a dangerous effect e.g. catalysing a reaction or reacting with the dangerous goods.

Where necessary, they shall be provided with a suitable inner coating or treatment.

4.1.1.3	Unless provided elsewhere in ADR, each packaging, including IBCs and large packagings, except inner packagings,  shall conform to a design type successfully tested in accordance with the requirements of 6.1.5, 6.5.4 or 6.6.5, respectively. The packagings for which the test is not required are mentioned under 6.1.1.3.

4.1.1.4	When filling packagings, including IBCs and large packagings, with liquids, sufficient ullage (outage) shall be left to ensure that neither leakage nor permanent distortion of the packaging occurs as a result of an expansion of the liquid caused by temperatures likely to occur during transport.  Unless specific requirements are prescribed, liquids shall not completely fill a packaging at a temperature of 55 °C. However, sufficient ullage shall be left in an IBC to ensure that at the mean bulk temperature of 50 °C it is not filled to more than 98% of its water capacity. For a filling temperature of 15 °C, the degree of filling shall be determined as follows, unless otherwise provided under a particular Class, either:

(a)

| Boiling point (initial boiling point) of the substance in °C | <60 | (60 <100 | (100 <200 | (200 <300 | (300 |
| --- | --- | --- | --- | --- | --- |
| Degree of filling as a percentage of the capacity of the packaging | 90 | 92 | 94 | 96 | 98 |

or

In this formula ( represents the mean coefficient of cubic expansion of the liquid substance between 15 °C and 50 °C; that is to say, for a maximum rise in temperature of 35 °C,

d15 and d50 being the relative densities  of the liquid at 15 °C and 50 °C and tF the mean temperature of the liquid at the time of filling.

4.1.1.4.1	For air transport, packagings intended to contain liquids shall also be capable of withstanding a pressure differential without leakage as specified in the international regulations for air transport.

4.1.1.5	Inner packagings shall be packed in an outer packaging in such a way that, under normal conditions of carriage, they cannot break, be punctured or leak their contents into the outer packaging.  Inner packagings that are liable to break or be punctured easily, such as those made of glass, porcelain or stoneware or of certain plastics materials, etc., shall be secured in outer packagings with suitable cushioning material.  Any leakage of the contents shall not substantially impair the protective properties of the cushioning material or of the outer packaging.

4.1.1.6	Dangerous goods shall not be packed together in the same outer packaging or in large packagings, with dangerous or other goods if they react dangerously with each other and cause:

(a)	combustion and/or evolution of considerable heat;

(b)	evolution of flammable, toxic or asphyxiant gases;

(c)	the formation of corrosive substances; or

(d)	the formation of unstable substances.

NOTE: For mixed packing special provisions, see 4.1.10.

4.1.1.7	The closures of packagings containing wetted or diluted substances shall be such that the percentage of liquid (water, solvent or phlegmatizer) does not fall below the prescribed limits during transport.

4.1.1.7.1	Where two or more closure systems are fitted in series on an IBC, that nearest to the substance being carried shall be closed first.

4.1.1.8	Liquids may only be filled into inner packagings which have an appropriate resistance to internal pressure that may be developed under normal conditions of carriage. Where pressure may develop in a package by the emission of gas from the contents (as a result of temperature increase or other cause), the packaging may be fitted with a vent, provided that the gas emitted will not cause danger on account of its toxicity, its flammability, the quantity released, etc. A venting device shall be fitted if dangerous overpressure may develop due to normal decomposition of substances. The vent shall be so designed that, when the packaging is in the attitude in which it is intended to be carried, leakages of liquid and the penetration of foreign matter are prevented under normal conditions of carriage.

4.1.1.9	New, remanufactured or reused packagings, including IBCs and large packagings, or reconditioned packagings and repaired IBCs shall be capable of passing the tests prescribed in 6.1.5, 6.5.4 or 6.6.5, respectively.  Before being filled and handed over for carriage, every packaging, including IBCs and large packagings, shall be inspected to ensure that it is free from corrosion, contamination or other damage and every IBC shall be inspected with regard to the proper functioning of any service equipment.  Any packaging which shows signs of reduced strength as compared with the approved design type shall no longer be used or shall be so reconditioned,  that it is able to withstand the design type tests. Any IBC which shows signs of reduced strength as compared with the tested design type shall no longer be used or shall be so repaired that it is able to withstand the design type tests.

4.1.1.10	Liquids shall be filled only into packagings, including IBCs, which have an appropriate resistance to the internal pressure that may develop under normal conditions of carriage. Packagings and IBCs marked with the hydraulic test pressure prescribed in 6.1.3.1(d) and 6.5.2.2.1, respectively shall be filled only with a liquid having a vapour pressure:

(a)	such that the total gauge pressure in the packaging or IBC (i.e. the vapour pressure of the filling substance plus the partial pressure of air or other inert gases, less 100 kPa) at 55 °C, determined on the basis of a maximum degree of filling in accordance with 4.1.1.4 and a filling temperature of 15 °C, will not exceed two-thirds of the marked test pressure; or

(b)	at 50 °C less than four-sevenths of the sum of the marked test pressure plus 100 kPa; or

(c)	at 55 °C less than two-thirds of the sum of the marked test pressure plus 100 kPa.

Metal IBCs intended for the carriage of liquids shall not be used to carry liquids having a vapour pressure of more than 110kPa (1.1 bar) at 50 °C or 130kPa (1.3 bar) at 55 °C.

EXAMPLES OF REQUIRED MARKED TEST PRESSURES FOR PACKAGINGS, INCLUDING IBCs, CALCULATED AS IN 4.1.1.10 (c)

| UN No | Name | Class | Packing group | Vp55 (kPa) | Vp55 × 1.5 (kPa) | (Vp55 × 1.5) minus 100 (kPa) | Required minimum test pressure gauge under 6.1.5.5.4.(c) (kPa) | Minimum test pressure (gauge) to be marked on the packaging (kPa) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2056 2247 1593 1155 | Tetrahydrofuran n-Decane Dichloromethane Diethyl ether | 3 3 6.1 3 | II III III I | 70 1.4 164 199 | 105 2.1 246 299 | 5 -97.9 146 199 | 100 100 146 199 | 100 100 150 250 |

NOTE 1: For pure liquids the vapour pressure at 55 °C (Vp55) can often be obtained from scientific tables.

NOTE 2: The table refers to the use of 4.1.1.10 (c) only, which means that the marked test pressure shall exceed 1.5 times the vapour pressure at 55 °C less 100 kPa.  When, for example, the test pressure for n-decane is determined according to 6.1.5.5.4 (a), the minimum marked test pressure may be lower.

NOTE 3:  For diethyl ether the required minimum test pressure under 6.1.5.5.5 is 250 kPa.

4.1.1.11	Empty packagings, including IBCs and large packagings, that have contained a dangerous substance are subject to the same requirements as those for a filled packaging, unless adequate measures have been taken to nullify any hazard.

4.1.1.l2	Every packagings, including IBCs, intended to contain liquids shall successfully undergo a suitable leakproofness test, and be capable of meeting the appropriate test level indicated in 6.1.5.4.3 or 6.5.4.7 for the various types of IBCs:

(a)	before it is first used for carriage;

(b)	after remanufacturing or reconditioning of any packaging, before it is re-used for carriage;

(c)	after the repair of any IBC, before it is re-used for carriage.

For this test the packaging, or IBC, need not have its closures fitted. The inner receptacle of a composite packaging or IBC may be tested without the outer packaging, provided the test results are not affected. This test is not necessary for inner packagings of combination packagings or large packagings.

4.1.1.13	Packagings, including IBCs, used for solids which may become liquid at temperatures likely to be encountered during carriage shall also be capable of containing the substance in the liquid state.

4.1.1.14	Packagings, including IBCs, used for powdery or granular substances shall be sift-proof or shall be provided with a liner.

4.1.1.15	For plastics drums and jerricans, rigid plastics IBCs and composite IBCs with plastics inner receptacles, unless otherwise approved by the competent authority, the period of use permitted for the carriage of dangerous substances shall be five years from the date of manufacture of the receptacles, except where a shorter period of use is prescribed because of the nature of the substance to be carried.

4.1.1.16   	Packages marked in accordance with 6.1.3 but which were approved in a State which is not a Contracting Party to ADR may nevertheless be used for carriage under ADR.

4.1.1.17	Use of salvage packagings

4.1.1.17.1	Damaged, defective or leaking packages, or dangerous goods that have spilled or leaked may be carried in salvage packagings mentioned in 6.1.5.1.11. This does not prevent the use of  bigger size packagings of appropriate type and performance level under the conditions of 4.1.1.17.2.

4.1.1.17.2	Appropriate measures shall be taken to prevent excessive movement of the damaged or leaking packages within a salvage packaging. When the salvage packaging contains liquids, sufficient inert absorbent material shall be added to eliminate the presence of free liquid.

4.1.2	Additional general provisions for the use of IBCs

4.1.2.1	When IBCs are used for the carriage of liquids with a flash-point of 61 °C (closed cup) or lower, or of powders liable to dust explosion, measures shall be taken to prevent a dangerous electrostatic discharge.

4.1.2.2	The periodic testing and inspection requirements for IBCs are provided in Chapter 6.5.  An IBC shall not be filled and offered for carriage after the date of expiry of the last periodic test required by 6.5.4.14.3, or the date of expiry of the last periodic inspection required by 6.5.1.6.4.  However, an IBC filled prior to the date of expiry of the last periodic test or inspection may be carried for a period not to exceed three months beyond the date of expiry of the last periodic test or inspection.  In addition, an IBC may be carried after the date of expiry of the last periodic test or inspection:

(a)	after emptying but before cleaning, for purposes of performing the required test or inspection prior to refilling; and

(b)	unless otherwise approved by the competent authority, for a period not to exceed six months beyond the date of expiry of the last periodic test or inspection in order to allow the return of dangerous goods or residues for proper disposal or recycling.

Note: For the particulars in the transport document, see 5.4.1.1.11.

4.1.2.3	IBCs of type 31HZ2 shall be filled to at least 80% of the volume of the outer casing and always be carried in closed vehicles or containers.

4.1.3	General provisions concerning packing instructions

4.1.3.1	Packing instructions applicable to dangerous goods of Classes 1 to 9 are specified in section 4.1.4. They are subdivided in three sub-sections depending on the type of packagings to which they apply:

Sub-section 4.1.4.1 	for packagings other than IBCs and large packagings; these packing instructions are designated by an alphanumeric code starting with the letter "P" or "R" for packagings specific to RID and ADR;

Sub-section 4.1.4.2 	for IBCs; these are designated by an alphanumeric code starting with the letters  "IBCs";

Sub-section 4.1.4.3	for large packagings; these are designated by an alphanumeric code starting with the letters "LP".

Generally, packing instructions specify that the general provisions of 4.1.1, 4.1.2 or 4.1.3, as appropriate, are applicable. They may also require compliance with the special provisions of sections 4.1.5, 4.1.6, 4.1.7, 4.1.8 or 4.1.9 when appropriate. Special packing provisions may also be specified in the packing instruction for individual substances or articles. They are also designated by an alphanumeric code comprising the letters:

"PP" 	for packagings other than IBCs and large packagings, or "RR" for special provisions specific to RID and ADR;

"B"	for IBCs;

"L"	for large packagings.

Unless otherwise specified, each packaging shall conform to the applicable requirements of Part 6. Generally packing instructions do not provide guidance on compatibility and the user shall not select a packaging without checking that the substance is compatible with the packaging material selected (e.g. glass receptacles are unsuitable for most fluorides). Where glass receptacles are permitted in the packing instructions porcelain, earthenware and stoneware packagings are also allowed.

4.1.3.2	Column (8) of Table A of Chapter 3.2 shows for each article or substance the packing  instruction(s) that shall be used. Columns (9a) and (9b) indicate the special packing provisions and the mixed packing provisions (see 4.1.10) applicable to specific substances or articles.

4.1.3.3	Each packing instruction shows, where applicable, the acceptable single and combination packagings. For combination packagings, the acceptable outer packagings, inner packagings and when applicable the maximum quantity permitted in each inner or outer packaging, are shown.  Maximum net mass and maximum capacity are as defined in 1.2.1.

4.1.3.4	The following packagings shall not be used when the substances being carried are liable to become liquid during carriage:

Packagings

Drums:	1D and 1G

Boxes:	4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H1 and 4H2

Bags:	5L1, 5L2, 5L3, 5H1, 5H2, 5H3, 5H4, 5M1 and 5M2

Composite packagings:	6HC, 6HD2, 6HG1, 6HG2, 6HD1, 6PC, 6PD1, 6PD2, 6PG1, 6PG2 and 6PH1

IBCs

For substances of packing group I: All types of IBC

For substances of packing groups II and III:

Wooden:	11C, 11D and 11F

Fibreboard:	11G

Flexible:	13H1, 13H2, 13H3, 13H4, 13H5, 13L1, 13L2, 13L3, 13L4, 13M1 and 13M2

Composite:	11HZ2, 21HZ2 and 31HZ2

For the purposes of this paragraph, substances and mixtures of substances having a melting point equal to or less than 45 °C shall be treated as solids liable to become liquid during transport.

4.1.3.5	Where the packing instructions in this chapter authorize the use of a particular type of outer packaging in a combination packaging (e.g. 4G), packagings bearing the same packaging identification code followed by the letters “V”, “U” or “W” marked in accordance with the requirements of Part 6 (e.g. 4GV, 4GU or 4GW) may also be used under the same conditions and limitations applicable to the use of that type of outer packaging according to the relevant packing instructions.  For example, a combination packaging marked with the packaging code “4GV” may be used whenever a combination packaging marked “4G” is authorized, provided the requirements in the relevant packing instruction regarding types of inner packagings and quantity limitations are respected.

4.1.3.6	Gas cylinders and gas receptacles approved by the competent authority are authorized for the transport of any liquid or solid substance assigned to packing instruction P001 or P002 unless otherwise indicated in the packing instruction or by a special provision in column (9a) of Table A of Chapter 3.2. The capacity of gas cylinders shall not exceed 450 litres.  The capacity for gas receptacles shall not exceed  1000 litres.

4.1.3.7 	Packagings or IBCs not specifically authorized in the applicable packing instruction shall  not be used for the carriage of a substance or article unless specifically allowed under a temporary derogation agreed between Contracting Parties in accordance with 1.5.1.

4.1.4	List of packing instructions

NOTE: Although the following packing instructions use the same numbering system as used in the IMDG Code and the UN Model Regulations, readers should be aware that some of the details may be different in the case of ADR.

4.1.4.1 	Packing instructions concerning the use of packagings (except IBCs and large packagings)

| P001 PACKING INSTRUCTION (LIQUIDS) P001 |
| --- |
| The following packagings are authorized provided the general provisions of 4.1.1 and 4.1.3 are met: |
| Combination packagings: | Maximum capacity/Net mass (see 4.1.3.3.) |
| Inner packagings | Outer packagings | Packing group I | Packing group II | Packing group III |
| Glass 10 l Plastics 30 l Metal 40 l | Drums |  |  |  |
|  | steel (1A2) | 250 kg | 400 kg | 400 kg |
|  | aluminium (1B2) | 250 kg | 400 kg | 400 kg |
|  | metal other than steel or aluminium (1N2) | 250 kg | 400 kg | 400 kg |
|  | plastics (1H2) | 250 kg | 400 kg | 400 kg |
|  | plywood (1D) | 150 kg | 400 kg | 400 kg |
|  | fibre (1G) | 75 kg | 400 kg | 400 kg |
|  | Boxes |  |  |  |
|  | steel (4A) | 250 kg | 400 kg | 400 kg |
|  | aluminium (4B) | 250 kg | 400 kg | 400 kg |
|  | natural wood (4C1, 4C2) | 150 kg | 400 kg | 400 kg |
|  | plywood (4D) | 150 kg | 400 kg | 400 kg |
|  | reconstituted wood (4F) | 75 kg | 400 kg | 400 kg |
|  | fibreboard (4G) | 75 kg | 400 kg | 400 kg |
|  | expanded plastics (4H1) | 60 kg | 60 kg | 60 kg |
|  | solid plastics (4H2) | 150 kg | 400 kg | 400 kg |
|  | Jerricans |  |  |  |
|  | steel (3A2) | 120 kg | 120 kg | 120 kg |
|  | aluminium (3B2) | 120 kg | 120 kg | 120 kg |
|  | plastics (3H2) | 120 kg | 120 kg | 120 kg |
| Single packagings: |
| Drums |  |  |  |
| steel, non-removable head (1A1) | 250 l | 450 l | 450 l |
| steel, removable head (1A2) | 250 l */ | 450 l | 450 l |
| aluminium, non-removable head (1B1) | 250 l | 450 l | 450 l |
| aluminium, removable head (1B2) | 250 l */ | 450 l | 450 l |
| metal other than steel or aluminium, non-removable head (1N1) | 250 l | 450 l | 450 l |
| metal other than steel or aluminium, removable head (1N2) | 250 l */ | 450 l | 450 l |
| plastics, non-removable head (1H1) | 250 l | 450 l | 450 l |
| plastics, removable head (1H2) | 250 l */ | 450 l | 450 l |
| Jerricans steel, non-removable head (3A1) steel, removable head (3A2) aluminium, non-removable head (3B1) aluminium, removable head (3B2) plastics, non-removable head (3H1) plastics, removable head (3H2) | 60 l 60 l */ 60 l 60 l */ 60 l 60 l */ | 60 l 60 l 60 l 60 l 60 l 60 l | 60 l 60 l 60 l 60 l 60 l 60 l |
| */ Only substances with a viscosity of more than 2 680 mm2/s are authorized. |
| P001 PACKING INSTRUCTION (LIQUIDS) (cont’d) P001 |
| Single packagings (cont’d) | Maximum capacity/Net mass (see 4.1.3.3.) |
| Composite packagings | Packing group I | Packing group II | Packing group III |
| plastics receptacle with outer steel or aluminium drum (6HA1, 6HB1) | 250 l | 250 l | 250 l |
| plastics receptacle with outer fibre, plastics or plywood drum (6HG1, 6HH1, 6HD1) | 120 l | 250 l | 250 l |
| plastics receptacle with outer steel or aluminium crate or box or plastics receptacle with outer wooden, plywood, fibreboard or solid plastics box (6HA2, 6HB2, 6HC, 6HD2, 6HG2 or 6HH2) | 60 l | 60 l | 60 l |
| glass receptacle with outer steel, aluminium, fibreboard, plywood, solid plastics or expanded plastics drum (6PA1, 6PB1, 6PG1, 6PD1, 6PH1 or 6PH2) or with outer steel or aluminium crate or box or with outer wooden or fibreboard box or with outer wickerwork hamper (6PA2, 6PB2, 6PC, 6PG2 or 6PD2) | 60 l | 60 l | 60 l |
| Additional requirement: For substances of Class 3, packing group III, which give off small quantities of carbon dioxide or nitrogen, the packagings shall be vented. |
| Special packing provisions: PP1 For UN Nos. 1133, 1210, 1263 and 1866, substances of packing groups II and III may be carried in quantities of 5 litres or less per packaging in metal or plastics packagings which are not required to meet the performance tests of Chapter 6.1, provided that such packagings are carried: (a) in palletized loads, a pallet box or unit load device, e.g. individual packagings placed or stacked and secured by strapping, shrink or stretch-wrapping or other suitable means to a pallet; or (b) as inner packagings of combination packagings with a maximum net mass of 40 kg. PP2 For UN Nos. 3065 and 1170, wooden barrels (2C1 and 2C2) may be used. PP4 For UN No. 1774, packagings shall meet the packing group II performance level. PP5 For UN No. 1204, packagings shall be so constructed that explosion is not possible by reason of increased internal pressure. Gas cylinders and gas receptacles shall not be used for these substances. PP6 For UN Nos. 1851 and 3248, the maximum net quantity per package shall be 5 l. PP10 For UN No. 1791, packing group II, the packaging shall be vented. PP31 For UN No. 1131, packagings shall be hermetically sealed. PP33 For UN No. 1308, packing groups I and II, only combination packagings with a maximum gross mass of 75 kg allowed. |
| Special packing provisions specific to RID and ADR |
| RR01 For UN No. 1790, packing group II with not more than 60% hydrofluoric acid and UN No. 2031 containing more than 55% pure acid, the permissible period of use for plastics drums and jerricans shall be two years from the date of manufacture. RR02 For UN No. 1261, removable head packagings are not permitted. |

| P002 PACKING INSTRUCTION (SOLIDS) P002 |  |  |  |  |
| --- | --- | --- | --- | --- |
| The following packagings are authorized provided the general provisions of 4.1.1 and 4.1.3 are met: |  |  |  |  |
| Combination packagings: |  | Maximum net mass (see 4.1.3.3) |  |  |
| Inner packagings | Outer packagings | Packing group I | Packing group II | Packing group III |
| Glass 10 kg Plastics 1/ 50 kg Metal 50 kg Paper 1/, 2/, 3/ 50 kg Fibre 1/, 2/, 3/ 50 kg | Drums steel (1A2) aluminium (1B2) metal, other than steel or aluminium (1N2) plastics (1H2) plywood (1D) fibre (1G) | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg |
| 1/ These inner packagings shall be sift-proof. 2/ These inner packagings shall not be used when the substances being carried may become liquid during carriage (see 4.1.3.4). | Boxes steel (4A) aluminium (4B) natural wood (4C1) natural wood with sift proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) expanded plastics (4H1) solid plastics (4H2) | 400 kg 400 kg 250 kg 250 kg 250 kg 125 kg 125 kg 60 kg 250 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 60 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 60 kg 400 kg |
| 3/ These inner packagings shall not be used for substances of packing group I. | Jerricans steel (3A2) aluminium (3B2) plastics (3H2) | 120 kg 120 kg 120 kg | 120 kg 120 kg 120 kg | 120 kg 120 kg 120 kg |
| Single packagings: |  |  |  |  |
| Drums steel (1A1 or 1A2 4/) aluminium (1B1 or 1B2 4/) metal, other than steel or aluminium (1N1 or 1N2 4/) plastics (1H1 or 1H2 4/) fibre (1G) 5/ plywood (1D) 5/ |  | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg |
| Jerricans steel (3A1 or 3A2 4/) aluminium (3B1 or 3B2 4/) plastics (3H1 or 3H2 4/) |  | 120 kg 120 kg 120 kg | 120 kg 120 kg 120 kg | 120 kg 120 kg 120 kg |
| 4/ These packagings shall not be used for substances of packing group I that may become liquid during carriage (see 4.1.3.4). |  |  |  |  |
| 5/ These packagings shall not be used when substances being carried may become liquid during carriage (see 4.1.3.4). |  |  |  |  |
| P002 PACKING INSTRUCTION (SOLIDS) (cont’d) P002 |  |  |  |  |
|  |  | Maximum net mass (see 4.1.3.3.) |  |  |
| Single packagings (cont’d): |  | Packing group I | Packing group II | Packing group III |
| Boxes steel (4A) 5/ aluminium (4B) 5/ natural wood (4C1) 5/ plywood (4D) 5/ reconstituted wood (4F) 5/ natural wood with sift-proof walls (4C2) 5/ fibreboard (4G) 5/ solid plastics (4H2) 5/ Bags bags (5H3, 5H4, 5L3, 5M2) 5/ |  | Not allowed Not allowed Not allowed Not allowed Not allowed Not allowed Not allowed Not allowed Not allowed | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 50 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 50 kg |
| Composite packagings |  |  |  |  |
| plastics receptacle with outer steel, aluminium, plywood, fibre or plastics drum (6HA1, 6HB1, 6HG1 5/, 6HD1 5/, or 6HH1) plastics receptacle with outer steel or aluminium crate or box, wooden box, plywood box, fibreboard box or solid plastics box (6HA2, 6HB2, 6HC, 6HD2 5/, 6HG2 5/ or 6HH2) glass receptacle with outer steel, aluminium plywood or fibre drum (6PA1, 6PB1, 6PD1 5/ or 6PG1 5/) or with outer steel or aluminium crate or box or with outer wooden, or fibreboard box or with outer wickerwork hamper (6PA2, 6PB2, 6PC, 6PD2 5/, or 6PG2 5/) or with outer solid plastics or expanded plastics packaging (6PH2 or 6PH1 5/) |  | 400 kg 75 kg 75 kg | 400 kg 75 kg 75 kg | 400 kg 75 kg 75 kg |
| 5/ These packagings shall not be used when the substances being carried may become liquid during carriage (see 4.1.3.4). |  |  |  |  |
| Special packing provisions: PP6 For UN No. 3249, the maximum net mass per package shall be 5 kg. PP7 For UN No. 2000, celluloid may be transported unpacked on pallets, wrapped in plastic film and secured by appropriate means, such as steel bands as a full load in closed vehicles or containers. Each pallet shall not exceed 1000 kg. PP8 For UN No. 2002, packagings shall be so constructed that explosion is not possible by reason of increased internal pressure. Gas cylinders and gas receptacles shall not be used for these substances. PP9 For UN Nos. 3175, 3243 and 3244, packagings shall conform to a design type that has passed a leakproofness test at the packing group II performance level. PP11 For UN No. 1309, packing group III, and UN No. 1362, 5H1, 5L1 and 5M1 bags are allowed if they are overpacked in plastic bags or are wrapped in shrink or stretch wrap on pallets. PP12 For UN Nos. 1361, 2213 and UN No. 3077, 5H1, 5L1 and 5M1 bags are allowed when carried in closed vehicles or containers. PP13 For articles classified under UN No. 2870, only combination packagings meeting the packing group I performance level are authorized. PP14 For UN Nos. 2211, 2698 and 3314, packagings are not required to meet the performance tests in Chapter 6.1. PP15 For UN Nos. 1324 and 2623, packagings shall meet the packing group III performance level. PP20 For UN No. 2217, any sift-proof, tearproof receptacle may be used. PP30 For UN No. 2471, paper or fibre inner packagings are not permitted. PP34 For UN No. 2969 (as whole beans), 5H1, 5L1 and 5M1 bags are permitted. PP37 For UN Nos. 2590 and 2212, 5M1 bags are permitted. Packages shall be carried in closed vehicles or containers or as stretch or shrink-wrapped unit loads. PP38 For UN No. 1309, packing group II, bags are permitted only in closed vehicles or containers. |
| P003 PACKING INSTRUCTION P003 |
| Dangerous goods shall be placed in suitable outer packagings. The packagings shall meet the provisions of 4.1.1.1, 4.1.1.2, 4.1.1.4, 4.1.1.8 and 4.1.3 and be so designed that they meet the construction requirements of 6.1.4. Outer packagings constructed of suitable material of adequate strength and design in relation to the packaging capacity and its intended use shall be used. Where this packing instruction is used for the transport of articles or inner packagings of combination packagings, the packaging shall be designed and constructed to prevent inadvertent discharge of articles during normal conditions of carriage. |
| Special packing provisions: PP16 For UN No. 2800, batteries shall be protected from short circuits and shall be securely packed in strong outer packagings. NOTE 1: Non-spillable batteries which are an integral part of, and necessary for, the operation of mechanical or electronic equipment shall be securely fastened in the battery holder on the equipment and protected in such a manner as to prevent damage and short circuits. NOTE 2: For used batteries (UN No. 2800), see P801a. PP19 For UN Nos. 1364 and 1365, carriage as bales is authorized. PP20 For UN Nos. 1363, 1386, 1408 and 2793 any sift-proof, tearproof receptacle may be used. PP32 UN Nos. 2857 and 3358 may be carried unpackaged, in crates or in appropriate overpacks. |

P099 PACKING INSTRUCTION P099

Only packagings which are approved by the competent authority may be used.

P101 PACKING INSTRUCTION P101

Only packagings which are approved by the competent authority of the country of origin may be used. If the country of origin is not Contracting Party to the ADR, the packaging shall be approved by the competent authority of the first ADR country reached by the consignment. The State’s distinguishing sign for motor vehicles in international traffic of the country for which the authority acts, shall be marked on the transport documents as follows: “Packaging approved by the competent authority of...” (see 5.4.1.2.1 c))

| P110(a) PACKING INSTRUCTION P110(a) |  |  |
| --- | --- | --- |
| RESERVED NOTE: This packing instruction in the UN Model Regulations is not admitted for carriage under ADR. |  |  |

| P110(b) PACKING INSTRUCTION P110(b) |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Receptacles metal wood rubber, conductive plastics, conductive Bags rubber, conductive plastics, conductive | Intermediate packagings and arrangements Dividing partitions metal wood plastics fibreboard | Outer packagings and arrangements Boxes natural wood, sift-proof wall (4C2) plywood (4D) reconstituted wood (4F) |
| Special packing provision: PP42 For UN Nos. 0074, 0113, 0114, 0129, 0130, 0135 and 0224, the following conditions shall be met: (a) Inner packagings shall not contain more than 50 g of explosive substance (quantity corresponding to dry substance); (b) Compartments between dividing partitions shall not contain more than one inner packaging, firmly fitted; and (c) The outer packaging may be partitioned into up to 25 compartments. |  |  |
| P111 PACKING INSTRUCTION P111 |  |  |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper, waterproofed plastics textile, rubberized Sheets plastics textile, rubberized | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, expanded (4H1) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) plywood (1D) fibreboard (1G) plastics, removable head (1H2) |
| Special packing provision: PP43 For UN No. 0159, inner packagings are not required when metal (1A2 or 1B2) or plastics (1H2) drums are used as outer packagings. |  |  |
| P112(a) PACKING INSTRUCTION P112(a) (Solid wetted, 1.1D) |  |  |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper, multiwall, water resistant plastics textile textile, rubberized woven plastics Receptacles metal plastics | Intermediate packagings and arrangements Bags plastics textile, plastic coated or lined Receptacles metal plastics | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, expanded (4H1) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |
| Additional requirement: Intermediate packagings are not required if leakproof removable head drums are used as the outer packaging. |  |  |
| Special packing provisions: PP26 For UN Nos. 0004, 0076, 0078, 0154, 0219 and 0394, packagings shall be lead free. PP45 For UN Nos. 0072 and 0226, intermediate packagings are not required. |  |  |

| P112(b) PACKING INSTRUCTION P112(b) (Solid dry, other than powder 1.1D) |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper, kraft paper, multiwall, water resistant plastics textile textile, rubberized woven plastics | Intermediate packagings and arrangements Bags (for UN No. 0150 only) plastics textile, plastic coated or lined | Outer packagings and arrangements Bags woven plastics, sift-proof (5H2) woven plastics, water-resistant (5H3) plastics, film (5H4) textile, sift-proof (5L2) textile, water resistant (5L3) paper, multiwall, water resistant (5M2) Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, expanded (4H1) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |
| Special packing provisions: PP26 For UN Nos. 0004, 0076, 0078, 0154, 0216, 0219 and 0386, packagings shall be lead free. PP46 For UN Nos. 0209, bags, sift-proof (5H2) are recommended for flake or prilled TNT in the dry state and a maximum net mass of 30 kg. PP47 For UN Nos. 0222 and 0223, inner packagings are not required when the outer packaging is a bag. |  |  |

| P112(c) PACKING INSTRUCTION P112(c) (Solid dry powder 1.1D) |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper, multiwall, water resistant plastics woven plastics Receptacles fibreboard metal plastics wood | Intermediate packagings and arrangements Bags paper, multiwall, water resistant with inner lining plastics Receptacles metal plastics | Outer packagings and arrangements Boxes steel (4A) natural wood, ordinary (4C1) natural wood, sift-proof (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) |
| Additional requirements: 1. Inner packagings are not required if drums are used as the outer packaging. 2. The packaging shall be sift-proof. |  |  |
| Special packing provisions: PP26 For UN Nos. 0004, 0076, 0078, 0154, 0216, 0219 and 0386, packagings shall be lead free. PP46 For UN No. 0209, bags, sift-proof (5H2) are recommended for flake or prilled TNT in the dry state and a maximum net mass of 30 kg. PP48 For UN No. 0504, metal packagings shall not be used. |  |  |

| P113 PACKING INSTRUCTION P113 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper plastics textile, rubberized Receptacles fibreboard metal plastics wood | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) |
| Additional requirement: The packaging shall be sift-proof. |  |  |
| Special packing provisions: PP49 For UN Nos. 0094 and 0305, no more than 50 g of substance shall be packed in an inner packaging. PP50 For UN No. 0027, inner packagings are not necessary when drums are used as outer packagings. PP51 For UN No. 0028, paper kraft or waxed paper sheets may be used as inner packagings. |  |  |

| P114(a) PACKING INSTRUCTION P114(a) (Solid wetted) |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags plastics textile woven plastics Receptacles metal plastics | Intermediate packagings and arrangements Bags plastics textile, plastic coated or lined Receptacles metal plastics | Outer packagings and arrangements Boxes steel (4A) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) plywood (1D) fibre (1G) plastics, removable head (1H2) |
| Additional requirement: Intermediate packagings are not required if leakproof removable head drums are used as outer packagings. |  |  |
| Special packing provisions: PP26 For UN Nos. 0077, 0132, 0234, 0235 and 0236, packagings shall be lead free. PP43 For UN No. 0342, inner packagings are not required when metal (1A2 or 1B2) or plastics (1H2) drums are used as outer packagings. |  |  |

| P114(b) PACKING INSTRUCTION P114(b) (Solid dry) |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper, kraft plastics textile, sift-proof woven plastics, sift-proof Receptacles fibreboard metal paper plastics woven plastics, sift-proof | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) Drums steel, removable head (1A2) aluminium, removable head (1B2) plywood (1D) fibre (1G) plastics, removable head (1H2) |
| Special packing provisions: PP26 For UN Nos. 0077, 0132, 0234, 0235 and 0236, packagings shall be lead free. PP50 For UN Nos. 0160 and 0161, inner packagings are not required if drums are used as outer packagings. PP52 For UN Nos. 0160 and 0161, when metal drums (1A2 or 1B2) are used as outer packagings, metal packagings shall be so constructed that the risk of explosion, by reason of increased internal pressure from internal or external causes is prevented. |  |  |

| P115 PACKING INSTRUCTION P115 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Receptacles plastics | Intermediate packagings and arrangements Bags plastics in metal receptacles Drums metal | Outer packagings and arrangements Boxes natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) Drums steel, removable head (1A2) aluminium, removable head (1B2) plywood (1D) fibre (1G) |
| Special packing provisions: PP45 For UN No. 0144, intermediate packagings are not required. PP53 For UN Nos. 0075, 0143, 0495 and 0497, when boxes are used as outer packagings, inner packagings shall have taped screw cap closures and be not more than 5 litres capacity each. Inner packagings shall be surrounded with non-combustible absorbent cushioning materials. The amount of absorbent cushioning material shall be sufficient to absorb the liquid contents. Metal receptacles shall be cushioned from each other. Net mass of propellant is limited to 30 kg for each package when outer packagings are boxes. PP54 For UN Nos. 0075, 0143, 0495 and 0497, when drums are used as outer packagings and when intermediate packagings are drums, they shall be surrounded with non-combustible cushioning material in a quantity sufficient to absorb the liquid contents. A composite packaging consisting of a plastics receptacle in a metal drum may be used instead of the inner and intermediate packagings. The net volume of propellant in each package shall not exceed 120 litres. PP55 For UN No. 0144, absorbent cushioning material shall be inserted. PP56 For UN No. 0144, metal receptacles may be used as inner packagings. PP57 For UN Nos. 0075, 0143, 0495 and 0497, bags shall be used as intermediate packagings when boxes are used as outer packagings. PP58 For UN Nos. 0075, 0143, 0495 and 0497, drums shall be used as intermediate packagings when drums are used as outer packagings. PP59 For UN No. 0144, fibreboard boxes (4G) may be used as outer packagings. PP60 For UN No. 0144, aluminium drums, removable head (1B2) shall not be used. |  |  |

| P116 PACKING INSTRUCTION P116 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper, water and oil resistant plastics textile, plastic coated or lined woven plastics, sift-proof Receptacles fibreboard, water resistant metal plastics wood, sift-proof Sheets paper, water resistant paper, waxed plastics | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Bags woven plastics (5H1) paper, multiwall, water resistant (5M2) plastics, film (5H4) textile, sift-proof (5L2) textile, water resistant (5L3) Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) Jerricans steel, removable head (3A2) plastics, removable head (3H2) |
| Special packing provisions: PP61 For UN Nos. 0082, 0241, 0331 and 0332, inner packagings are not required if leakproof removable head drums are used as outer packagings. PP62 For UN Nos. 0082, 0241, 0331 and 0332, inner packagings are not required when the explosive is contained in a material impervious to liquid. PP63 For UN No. 0081, inner packagings are not required when contained in rigid plastic which is impervious to nitric esters. PP64 For UN No. 0331, inner packagings are not required when bags (5H2), (5H3) or (5H4) are used as outer packagings. PP65 For UN Nos. 0082, 0241, 0331 and 0332, bags (5H2 or 5H3) may be used as outer packagings. PP66 For UN No. 0081, bags shall not be used as outer packagings. |  |  |
| P130 PACKING INSTRUCTION P130 |  |  |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Not necessary | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, expanded (4H1) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |
| Special packing provision: PP67 The following applies to UN Nos. 0006, 0009, 0010, 0015, 0016, 0018, 0019, 0034, 0035, 0038, 0039, 0048, 0056, 0137, 0138, 0168, 0169, 0171, 0181, 0182, 0183, 0186, 0221, 0243, 0244, 0245, 0246, 0254, 0280, 0281, 0286, 0287, 0297, 0299, 0300, 0301, 0303, 0321, 0328, 0329, 0344, 0345, 0346, 0347, 0362, 0363, 0370, 0412, 0424, 0425, 0434, 0435, 0436, 0437, 0438, 0451, 0488 and 0502: Large and robust explosives articles, normally intended for military use, without their means of initiation or with their means of initiation containing at least two effective protective features, may be carried unpackaged. When such articles have propelling charges or are self-propelled, their ignition systems shall be protected against stimuli encountered during normal conditions of carriage. A negative result in Test Series 4 on an unpackaged article indicates that the article can be considered for carriage unpackaged. Such unpackaged articles may be fixed to cradles or contained in crates or other suitable handling devices. |  |  |

| P131 PACKING INSTRUCTION P131 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper plastics Receptacles fibreboard metal plastics wood Reels | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |
| Special packing provision: PP68 For UN Nos. 0029, 0267 and 0455, bags and reels shall not be used as inner packagings. |  |  |

| P132(a) PACKING INSTRUCTION P132(a) (Articles consisting of closed metal, plastics or fibreboard casings that contain a detonating explosive, or consisting of plastics-bonded detonating explosives) |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Not necessary | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) wood, natural, ordinary (4C1) wood, natural, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) |

| P132(b) PACKING INSTRUCTION P132(b) (Articles without closed casings) |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Receptacles fibreboard metal plastics Sheets paper plastics | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) |

| P133 PACKING INSTRUCTION P133 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Receptacles fibreboard metal plastics wood Trays, fitted with dividing partitions fibreboard plastics wood | Intermediate packagings and arrangements Receptacles fibreboard metal plastics wood | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) |
| Additional requirement: Receptacles are only required as intermediate packagings when the inner packagings are trays. |  |  |
| Special packing provision: PP69 For UN Nos. 0043, 0212, 0225, 0268 and 0306, trays shall not be used as inner packagings. |  |  |

| P134 PACKING INSTRUCTION P134 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags water resistant Receptacles fibreboard metal plastics wood Sheets fibreboard, corrugated Tubes fibreboard | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, expanded (4H1) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) |

| P135 PACKING INSTRUCTION P135 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper plastics Receptacles fibreboard metal plastics wood Sheets paper plastics | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, expanded (4H1) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |

| P136 PACKING INSTRUCTION P136 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags plastics textile Boxes fibreboard plastics wood Dividing partitions in the outer packagings | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |
| P137 PACKING INSTRUCTION P137 |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |
| Inner packagings and arrangements Bags plastics Boxes fibreboard Tubes fibreboard metal plastics Dividing partitions in the outer packagings | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) Drums steel, removable head (1A2) aluminium, removable head (1B2) plywood (1D) fibre (1G) plastics, removable head (1H2) |
| Special packing provision: PP70 For UN Nos. 0059, 0439, 0440 and 0441, when the shaped charges are packed singly, the conical cavity shall face downwards and the package marked "THIS SIDE UP". When the shaped charges are packed in pairs, the conical cavities shall face inwards to minimize the jetting effect in the event of accidental initiation. |

| P138 PACKING INSTRUCTION P138 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags plastics | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) |
| Additional requirement: If the ends of the articles are sealed, inner packagings are not necessary. |  |  |

| P139 PACKING INSTRUCTION P139 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags plastics Receptacles fibreboard metal plastics wood Reels Sheets paper plastics | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) plywood (1D) fibre (1G) plastics, removable head (1H2) |
| Special packing provisions: PP71 For UN Nos. 0065, 0102, 0104, 0289 and 0290, the ends of the detonating cord shall be sealed, for example, by a plug firmly fixed so that the explosive cannot escape. The ends of flexible detonating cord shall be fastened securely. PP72 For UN Nos. 0065 and 0289, inner packagings are not required when they are in coils. |  |  |

| P140 PACKING INSTRUCTION P140 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags plastics Reels Sheets paper, kraft plastics | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) |
| Special packing provisions: PP73 For UN No. 0105, no inner packagings are required if the ends are sealed. PP74 For UN No. 0101, the packaging shall be sift-proof except when the fuse is covered by a paper tube and both ends of the tube are covered with removable caps. PP75 For UN No. 0101, steel or aluminium boxes or drums shall not be used. |  |  |

| P141 PACKING INSTRUCTION P141 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Receptacles fibreboard metal plastics wood Trays, fitted with dividing partitions plastics wood Dividing partitions in the outer packagings | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |

| P142 PACKING INSTRUCTION P142 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper plastics Receptacles fibreboard metal plastics wood Sheets paper Trays, fitted with dividing partitions plastics | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) fibre (1G) plastics, removable head (1H2) |

| P143 PACKING INSTRUCTION P143 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |  |  |
| Inner packagings and arrangements Bags paper, kraft plastics textile textile, rubberized Receptacles fibreboard metal plastics Trays, fitted with dividing partitions plastics wood | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary (4C1) natural wood, sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) plastics, solid (4H2) Drums steel, removable head (1A2) aluminium, removable head (1B2) plywood (1D) fibre (1G) plastics, removable head (1H2) |
| Additional requirement: Instead of the above inner and outer packagings, composite packagings (6HH2) (plastics receptacle with outer solid plastics box) may be used. |  |  |
| Special packing provision: PP76 For UN Nos. 0271, 0272, 0415 and 0491, when metal packagings are used, metal packagings shall be so constructed that the risk of explosion, by reason of increase in internal pressure from internal or external causes is prevented. |

| P144 PACKING INSTRUCTION P144 |
| --- |
| The following packagings are authorized, provided the general packing provisions of 4.1.1, 4.1.3 and special packing provisions of 4.1.5 are met: |
| Inner packagings and arrangements Receptacles fibreboard metal plastics Dividing partitions in the outer packagings | Intermediate packagings and arrangements Not necessary | Outer packagings and arrangements Boxes steel (4A) aluminium (4B) natural wood, ordinary with metal liner (4C1) plywood (4D) with metal liner reconstituted wood (4F) with metal liner plastics, expanded (4H1) |
| Special packing provision: PP77 For UN Nos. 0248 and 0249, packagings shall be protected against the ingress of water. When water-activated contrivances are transported unpackaged, they shall be provided with at least two independent protective features which prevent the ingress of water. |

| P 200 PACKING INSTRUCTION P200 |
| --- |
| Type of packagings: Cylinder, tubes, pressure drums and bundles of cylinders Cylinder, tubes, pressure drums and bundles of cylinders are authorised provided the special packing provisions of 4.1.6 and the provisions listed below under A, B, C and D are met: A. General (1) Receptacles shall be so closed and leakproof as to prevent escape of the gases; B. Test pressure and filling ratios (2) The minimum test pressure required for is 1 MPa (10 bar); (3) For compressed gases having a critical temperature below -50 °C the internal pressure (test pressure) to be applied in the hydraulic pressure test shall be at least one and one-half times the filling pressure at 15 °C; (4) For compressed gases having a critical temperature of -50 °C or above and for liquefied gases having a critical temperature below 70 °C, the degree of filling shall be such that the internal pressure at 65 °C does not exceed the test pressure of the receptacles; For gases and gas mixtures with insufficient data, the maximum filling degree (FD) shall be determined as follows: FD = 8.5 ( 10-4 ( dg ( Pe where FD = maximum filling degree (in kg.l-1) dg = gas density (at 15 °C, 1 bar)(in kg/m³) Pe = minimum test pressure (in bar) If the density of the gas is unknown, the maximum filling degree shall be determined as follows: where FD = maximum filling degree (in kg.l-1) Pe = minimum test pressure (in bar) MM = molecular mass (in g.mol-1) R = 8,31451 × 10-2 bar ( l ( mol-1 ( K -1 (gas constant) (For gas mixtures the average molecular mass is to be taken, taking into account the concentrations of the various components); (5) For liquefied gases having a critical temperature of 70 °C or above, the maximum mass of contents per litre of capacity (degree of filling) equals 0.95 times the density of the liquid phase at 50 °C (in kg/l); in addition, the vapour phase shall not disappear below 60 °C. The test pressure will be at least equal to the vapour pressure of the liquid at 70 °C, minus 100 kPa (1 bar). For pure gases with insufficient data the maximum filling degree shall be determined as follows: FD = (0.0032 ( BP - 0.24 ( d1 ) where FD = maximum filling degree in kg.l-1 BP = boiling point (in Kelvin) dl = density of the liquid at boiling point (in kg.l-1) |
| P 200 PACKING INSTRUCTION (cont'd) P200 |
| (6) For UN No. 1001 acetylene, dissolved, once equilibrium has been achieved at 15 °C, the filling pressure shall not exceed the value prescribed by the competent authority for the porous mass. The quantity of solvent and the quantity of acetylene shall likewise correspond to the figures specified in the approval; (7) Other test pressure and degree of filling may be used provided they satisfy the general requirements outlined in the previous paragraphs of this section; C. Periodic inspections (8) Refillable receptacles shall be subjected to periodic inspections in accordance with the provisions of 6.2.1.6. (9) If special requirements for certain substances do not appear in the table below, periodic inspections shall be carried out: (a) Every 3 years in the case of receptacles intended for the carriage of gases of classification codes 1TC, 1TFC, 1TOC, 2TC, 2TFC and 2TOC; (b) Every 5 years in the case of receptacles intended for the carriage of gases of classification codes 1T, 1TF, 1TO, 2T, 2TF and 2TO and gases of classification codes 4A, 4F and 4C; (c) Every 10 years in the case of receptacles intended for the carriage of gases of classification codes 1A, 1O, 1F, 2A, 2O and 2F. By derogation from this paragraph, the periodic inspection of receptacles which make use of composite materials (composite receptacles) shall be carried out at intervals determined by the competent authority of the Contracting Party to ADR which has approved the technical code for the design and construction. D. Table (10) The following table: - identifies what types of receptacles are authorised for what gases; - identifies the test pressure, degree of filling and limitation of capacity for the different gases, as well as restrictions concerning toxic gases with a LC50 less than 200 ppm; - refers to additional requirements that are product specific. (11) Keys for the column “ receptacles” (1) Cylinders; (2) Tubes; (3) Pressure drums; (5) Bundles of cylinders. (12) Keys for the column "Special requirements": a: Aluminium alloys not allowed in contact with gas. b: Valves made of copper are not accepted. c: Metal parts in contact with the contents shall not contain more than 70% copper. d: No receptacle may contain more than 5 kg of the substance. e: The valve outlets shall be fitted with plugs or cap-nuts ensuring gas-tightness. f: The necessary steps to prevent dangerous reactions (e.g. polymerisation, decomposition...) during carriage shall be taken. If necessary, stabilisation or addition of an inhibitor is required. g: The use of test pressures other than those indicated are allowed provided the provisions of P200(4) are followed. h: If a monolithic material is used as a porous mass, the interval between inspections may be extended to 10 years. i: Maximum filling according to the figures specified in the approval. j: The test pressure and degree of filling shall be calculated in accordance with the provisions of P200 (3), (4) or (5). k: The interval between tests may be extended to 10 years when receptacles are made of aluminium alloys. l: Each cylinder in a frame (bundle) shall be fitted with an individual valve that shall be closed during carriage. |
| P 200 PACKING INSTRUCTION (cont'd) P200 |
| m: The interval between inspections for steel cylinders may be extended to 15 years: (a) with the agreement of the competent authority (authorities) of the country (countries) where the periodic inspection and the carriage take place; and (b) in accordance with the requirements of a technical code or a standard recognised by the competent authority, or standard EN 1440:1996 “Transportable refillable welded cylinders for liquefied petroleum gas (LPG) - Periodic requalification”. n:(1) allowed for carriage in capsules under the following conditions: (a) The mass of gas shall not exceed 150 g per capsule; (b) The capsules shall be free from faults liable to impair the strength; (c) The leakproofness of the closure shall be ensured by an additional device (cap, crown, seal, binding, etc.) capable of preventing any leakage of the closure during carriage; (d) The capsules shall be placed in an outer packaging of sufficient strength. A package shall not weigh more than 75 kg. (2) not allowed for carriage in capsules: (a) methylsilane or mixtures thereof, assigned to UN No. 3161; (b) dimethylsilane, trimethylsilane or mixtures thereof, assigned to UN No. 3309; (c) mixtures of UN No. 1589 cyanogen chloride, UN No. 2188 arsine, UN No. 2202 hydrogen selenide, UN No. 2189 dichlorosilane. z: In the case of receptacles for the carriage of gases under a N.O.S entry, the following requirements shall be taken into account as applicable: (1) The materials of which the receptacles and their closures are made shall not be liable to attack by the contents or form harmful or dangerous compounds therewith; (2) The special requirements of each component shall be taken into account when selecting and filling the receptacles; (3) The test pressure and degree of filling is to be calculated in accordance with the requirements of P200 (3), (4) or (5); (4) Toxic gases and gas mixtures with a LC50 less than 200 ppm are not allowed for transport in tubes and pressure drums; (5) The valves of receptacles for toxic gases and gas mixtures with a LC50 less than 200 ppm or of pyrophoric gases or flammable mixtures of gases containing more than 1% of pyrophoric compounds shall be fitted with gas tight plugs or cap-nuts. When these receptacles are manifolded in a bundle, each of them shall be fitted with an individual valve that shall be closed during carriage; (6) The necessary steps to prevent dangerous reactions (i.e. polymerisation, decomposition) during carriage shall be taken. If necessary, stabilisation or addition of an inhibitor is required; (7) Other criteria may be used for filling of welded steel cylinders intended for the carriage of substances of UN No. 1965: (a) with the agreement of the competent authorities of the countries where the transport is carried out; and (b) in compliance with the provisions of a national code or standard recognised by the competent authorities or standard EN 1439:1996 "Transportable refillable steel cylinders for liquefied petroleum Gases (LPG) - Procedures for checking before, during and after refilling)". When the criteria for filling are different from those in P200(5), the transport document shall include the statement "Carriage in accordance with packing instruction P200, special requirement z" and the indication of the reference temperature used for the calculation of the filling factor (see also 5.4.1.1.12). |
| P 200 PACKING INSTRUCTION (cont'd) P200 |
| E. Reference to standards (13) The applicable requirements of this packing instruction are considered to have been complied with if the following standards, as relevant, are applied: |
| Applicable requirements | Reference | Title of document |
| P200 (6) | EN1801: 1998 | Transportable gas cylinders - Filling conditions for single acetylene cylinders (including list of permissible porous masses) |
| P200 (6) | EN 12755: 2000 | Transportable gas cylinders - Filling conditions for acetylene bundles |

| P 200 PACKING INSTRUCTION (cont'd) P200 |
| --- |
| UN No. | NAME AND DESCRIPTION | CLASSIFI-CATION CODE | PACKING | TEST | FILLING | SPECIAL REQUIRE-MENTS |
|  |  |  | TYPE OF RECEPTACLE | PRESSURE (T.P.) | PERIOD (years) 1/ | MAX. FILL. DEGREE kg/l or MPa or Vol% |  |
|  |  |  |  | X FILL. PRESS. | MPa |  |  |  |
| 1001 | ACETYLENE, DISSOLVED | 4F | (1),(5) |  | 6.0 | 5 |  | c,h,i |
| 1002 | AIR, COMPRESSED | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1005 | AMMONIA, ANHYDROUS | 2TC | (1),(2),(3),(5) |  | 3.3 | 5 | 0.53 | b,n |
| 1006 | ARGON, COMPRESSED | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1008 | BORON TRIFLUORIDE, COMPRESSED | 1TC | (1),(2),(3),(5) (1),(2),(3),(5) |  | 22.5 30.0 | 3 | 0.715 0.86 | g g |
| 1009 | BROMOTRIFLUOROMETHANE (REFRIGERANT GAS R13B1) | 2A | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 4.2 12.0 25.0 | 10 10 10 | 1.13 1.44 1.60 | g,n g,n g,n |
| 1010 | 1,2-BUTADIENE, INHIBITED, or 1,3-BUTADIENE, INHIBITED, or MIXTURES OF 1,3-BUTADIENE AND HYDROCARBONS, INHIBITED | 2F | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 1.0 1.0 1.0 | 10 10 10 | 0.59 0.55 0.55 | f,n f,n f,n |
| 1011 | BUTANE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.51 | n |
| 1012 1012 1012 1012 | BUTYLENES MIXTURE or 1-BUTYLENE or CIS-2-BUTENE or TRANS-2-BUTYLENE | 2F | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 1.0 1.0 1.0 1.0 | 10 10 10 10 | 0.5 0.53 0.55 0.54 | j,n |
| 1013 | CARBON DIOXIDE | 2A | (1),(2),(3),(5) (1),(2),(3),(5) |  | 19.0 25.0 | 10 10 | 0.66 0.75 | g,n g,n |
| 1014 | CARBON DIOXIDE AND OXYGEN MIXTURE, COMPRESSED | 1O | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1015 | CARBON DIOXIDE AND NITROUS OXIDE MIXTURE | 2A | (1),(3),(5) |  | 25.0 | 10 | 0.75 | g,n |
| 1016 | CARBON MONOXIDE, COMPRESSED | 1TF | (1),(2),(3),(5) | 1.5 |  | 5 | 2/3 T.P. | k |
| 1017 | CHLORINE | 2TC | (1),(2),(3),(5) |  | 2.2 | 5 | 1.25 | a,n |
| 1018 | CHLORODIFLUORO- METHANE (REFRIGERANT GAS R22) | 2A | (1),(2),(3),(5) |  | 2.9 | 10 | 1.03 | n |
| 1020 | 1-CHLORO-1,2,2,2-TETRAFLUOROETHANE (REFRIGERANT GAS R124) | 2A | (1),(2),(3),(5) |  | 1.2 | 10 | 1.2 | n |
| 1022 | CHLOROTRIFLUORO-METHANE (REFRIGERANT GAS R13) | 2A | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 10.0 12.0 19.0 25.0 | 10 10 10 10 | 0.83 0.90 1.04 1.10 | g,n g,n g,n g,n |
| 1023 | COAL GAS, COMPRESED | 1TF | (1),(2),(3),(5) | 1.5 |  | 5 | 2/3 T.P. |  |
| 1026 | CYANOGEN | 2TF | (1),(2),(3),(5) |  | 10.0 | 5 | 0.70 | k,n |
| 1027 | CYCLOPROPANE | 2F | (1),(2),(3),(5) |  | 2.0 | 10 | 0.53 | n |
| 1028 | DICHLORODIFLUORO-METHANE (REFRIGERANT GAS R12) | 2A | (1),(2),(3),(5) |  | 1.8 | 10 | 1.15 | n |
| 1029 | DICHLOROFLUOROMETHANE (REFRIGERANT GAS R21) | 2A | (1),(2),(3),(5) |  | 1.0 | 10 | 1.23 | n |
| 1030 | 1,1-DIFLUOROETHANE (REFRIGERANT GAS R152a) | 2F | (1),(2),(3),(5) |  | 1.8 | 10 | 0.79 | n |
| 1032 | DIMETHYLAMINE, ANHYDROUS | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.59 | b,n |
| 1033 | DIMETHYL ETHER | 2F | (1),(2),(3),(5) |  | 1.8 | 10 | 0.58 | n |
| 1035 | ETHANE | 2F | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 9.5 12 30 | 10 10 10 | 0.25 0.29 0.39 | g,n g,n g,n |
| 1036 | ETHYLAMINE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.61 | b,n |
| 1037 | ETHYL CHLORIDE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.80 | a,n |
| 1039 | ETHYL METHYL ETHER | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.64 | n |
| 1040 | ETHYLENE OXIDE or ETHYLENE OXIDE WITH NITROGEN up to a total pressure of 1MPa (10 bar) at 50C | 2TF | (1),(2),(3),(5) |  | 1.5 | 5 | 0.78 | f,n |
| 1041 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with more than 9% ethylene oxide but not more than 87% | 2F | (1),(2),(3),(5) (1),(2),(3),(5) |  | 19 25 | 10 10 | 0.66 0.75 | g,n g,n |
| 1045 | FLUORINE, COMPRESSED | 1TOC | (1),(5) |  | 20.0 | 5 | 2.8 | a,d,e,l |
| 1046 | HELIUM, COMPRESSED | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1048 | HYDROGEN BROMIDE, ANHYDROUS | 2TC | (1),(2),(3),(5) |  | 6.0 | 3 | 1.54 | a,n |
| 1049 | HYDROGEN, COMPRESSED | 1F | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1050 | HYDROGEN CHLORIDE, ANHYDROUS | 2TC | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 10.0 12.0 15.0 20.0 | 3 3 3 3 | 0.30 0.56 0.67 0.74 | a,g,n a,g,n a,g,n a,g,n |
| 1053 | HYDROGEN SULPHIDE | 2TF | (1),(2),(3),(5) |  | 5.5 | 5 | 0.67 | k,n |
| 1055 | ISOBUTYLENE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.52 | n |
| 1056 | KRYPTON, COMPRESSED | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1058 | LIQUEFIED GASES, non-flammable, charged with nitrogen, carbon dioxide or air | 2A | (1),(2),(3),(5) | 1.5 |  | 10 |  | j,n |
| 1060 | METHYLACETYLENE AND PROPADIENE MIXTURE, STABILIZED Propadiene with 1% to 4% methylacetylene MIXTURE P1 MIXTURE P2 | 2F | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 2.2 3.0 2.4 | 10 10 10 10 | 0.50 0.49 0.47 | c,f,j,n c,f,n c,f,n c,f,n |
| 1061 | METHYLAMINE, ANHYDROUS | 2F | (1),(2),(3),(5) |  | 1.3 | 10 | 0.58 | b,n |
| 1062 | METHYL BROMIDE | 2T | (1),(2)(3),(5) |  | 1.0 | 5 | 1.51 | a |
| 1063 | METHYL CHLORIDE (REFRIGERANT GAS R 40) | 2F | (1),(2)(3),(5) |  | 1.7 | 10 | 0.81 | a,n |
| 1064 | METHYL MERCAPTAN | 2TF | (1),(2)(3),(5) |  | 1.0 | 5 | 0.78 | k,n |
| 1065 | NEON, COMPRESSED | 1A | (1),(2)(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1066 | NITROGEN, COMPRESSED | 1A | (1),(2)(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1067 | DINITROGEN TETROXIDE (NITROGEN DIOXIDE) | 2 TOC | (1),(3),(5) |  | 1.0 | 3 | 1.30 | e,l |
| 1069 | NITROSYL CHLORIDE | 2TC | (1),(5) |  | 1.3 | 3 | 1.10 | e,l,n |
| 1070 | NITROUS OXIDE | 2O | (1),(2)(3),(5) (1),(2)(3),(5) (1),(2)(3),(5) |  | 18.0 22.5 25.0 | 10 10 10 | 0.68 0.74 0.75 | g g g |
| 1071 | OIL GAS, COMPRESSED | 1TF | (1),(2)(3),(5) | 1.5 |  | 5 | 2/3 T.P. |  |
| 1072 | OXYGEN, COMPRESSED | 1O | (1),(2)(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1076 | PHOSGENE | 2TC | (1),(3),(5) |  | 2.0 | 3 | 1.23 | e,l,n |
| 1077 | PROPYLENE | 2F | (1),(2)(3),(5) |  | 3.0 | 10 | 0.43 | n |
| 1078 | REFRIGERANT GASES, N.O.S. MIXTURE F1 MIXTURE F2 MIXTURE F3 | 2A | (1),(2)(3),(5) (1),(2)(3),(5) (1),(2)(3),(5) (1),(2)(3),(5) |  | 1.2 1.8 2.9 | 10 10 10 10 | 1.23 1.15 1.03 | n,z |
| 1079 | SULPHUR DIOXIDE | 2TC | (1),(2)(3),(5) |  | 1.4 | 3 | 1.23 | n |
| 1080 | SULPHUR HEXAFLUORIDE | 2A | (1),(2)(3),(5) (1),(2)(3),(5) (1),(2)(3),(5) |  | 7.0 14.0 16.0 | 10 10 10 | 1.04 1.33 1.37 | g,n g,n g,n |
| 1081 | TETRAFLUOROETHYLENE, INHIBITED | 2F | (1),(2)(3),(5) |  | 20.0 | 10 | 0.5 | f,n |
| 1082 | TRIFLUOROCHLORO-ETHYLENE, INHIBITED | 2TF | (1),(2)(3),(5) |  | 1.9 | 5 | 1.13 | f,k,n |
| 1083 | TRIMETHYLAMINE, ANHYDROUS | 2F | (1),(2)(3),(5) |  | 1.0 | 10 | 0.56 | b,n |
| 1085 | VINYL BROMIDE, INHIBITED | 2F | (1),(2)(3),(5) |  | 1.0 | 10 | 1.37 | a,f,n |
| 1086 | VINYL CHLORIDE, INHIBITED | 2F | (1),(2)(3),(5) |  | 1.2 | 10 | 0.81 | a,f,n |
| 1087 | VINYL METHYL ETHER, INHIBITED | 2F | (1),(2)(3),(5) |  | 1.0 | 10 | 0.67 | f,n |
| 1581 | CHLOROPICRIN AND METHYL BROMIDE MIXTURE | 2T | (1),(2)(3),(5) |  | 1.0 | 5 | 1.51 | a |
| 1582 | CHLOROPICRIN AND METHYL CHLORIDE MIXTURE | 2T | (1),(2)(3),(5) |  | 1.7 | 5 | 0.81 | a |
| 1589 | CYANOGEN CHLORIDE, INHIBITED | 2TC | (1),(5) |  | 2.0 | 3 | 1.03 | e,f,l |
| 1612 | HEXAETHYL TETRAPHOSPHATE AND COMPRESSED GAS MIXTURE | 1T | (1),(2),(3),(5) | 1.5 |  | 5 | 2/3 T.P, |  |
| 1660 | NITRIC OXIDE, COMPRESSED | 1TOC | (1),(5) | 1.5 |  | 3 | 2/3 T.P. | e,l |
| 1741 | BORON TRICHLORIDE | 2TC | (1),(2),(3),(5) |  | 1.0 | 3 | 1.19 | n |
| 1749 | CHLORINE TRIFLUORIDE | 2TOC | (1),(2),(3),(5) |  | 3.0 | 3 | 1.40 | a |
| 1858 | HEXAFLUOROPROPYLENE (REFRIGERANT GAS R1216) | 2A | (1),(2),(3),(5) |  | 2.2 | 10 | 1.11 | n |
| 1859 | SILICON TETRAFLUORIDE, COMPRESSED | 1TC | (1),(2),(3),(5) (1),(2),(3),(5) |  | 20 30 | 3 | 0.74 1.1 | g g |
| 1860 | VINYL FLUORIDE, INHIBITED | 2F | (1),(2),(3),(5) |  | 25.0 | 10 | 0.64 | a,f,g,n |
| 1911 | DIBORANE, COMPRESSED | 1TF | (1),(5) |  | 25.0 | 5 | 0.072 | e,f,l |
| 1912 | METHYLCHLORIDE AND METHYLENE CHLORIDE MIXTURE | 2F | (1),(2),(3),(5) |  | 1.7 | 10 | 0.81 | a,n |
| 1952 | CARBON DIOXIDE AND ETHYLENE OXIDE MIXTURE with not more than 9% ethylene oxide | 2A | (1),(2),(3),(5) (1),(2),(3),(5) |  | 19 25 | 10 10 | 0.66 0.75 | n n |
| 1953 | COMPRESSED GAS, TOXIC, FLAMMABLE, N.O.S. | 1TF | (1),(2),(3),(5) | 1.5 |  | 5 | 2/3 T.P. | z |
| 1954 | COMPRESSED GAS, FLAMMABLE, N.O.S. | 1F | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. | z |
| 1955 | COMPRESSED GAS, TOXIC, N.O.S. | 1T | (1),(2),(3),(5) | 1.5 |  | 5 | 2/3 T.P. | z |
| 1956 | COMPRESSED GAS, N.O.S. | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. | z |
| 1957 | DEUTERIUM, COMPRESSED | 1F | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1958 | DICHLOROTETRAFLUORO-ETHANE (REFRIGERANT GAS R114) | 2A | (1),(2),(3),(5) |  | 1.0 | 10 | 1.30 | n |
| 1959 | 1,1-DIFLUOROETHYLENE (REFRIGERANT GAS R1132a) | 2F | (1),(2),(3),(5) |  | 25 | 10 | 0.77 | g,n |
| 1962 | ETHYLENE, COMPRESSED | 1F | (1),(2),(3),(5) (1),(2),(3),(5) |  | 22.5 30 | 10 10 | 0.34 0.37 | g g |
| 1964 | HYDROCARBON GAS MIXTURE, COMPRESSED, N.O.S. | 1F | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. | z |
| 1965 | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S. MIXTURE A MIXTURE AO1 MIXTURE AO2 MIXTURE AO MIXTURE A1 MIXTURE B1 MIXTURE B2 MIXTURE B MIXTURE C | 2F | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 1.0 1.5 1.5 1.5 2.0 2.5 2.5 2.5 3.0 | 10 10 10 10 10 10 10 10 10 10 | 2/ 0.50 0.49 0.48 0.47 0.46 0.45 0.44 0.43 0.42 | m,n,z |
| 1967 | INSECTICIDE GAS, TOXIC, N.O.S. | 2T | (1),(2),(3),(5) |  |  | 5 |  | z |
| 1968 | INSECTICIDE GAS, N.O.S. | 2A | (1),(2),(3),(5) |  |  | 10 |  | n,z |
| 1969 | ISOBUTANE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.49 | n |
| 1971 | METHANE, COMPRESSED or NATURAL GAS, COMPRESSED with high methane content | 1F | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P |  |
| 1973 | CHLORODIFLUOROMETHANE AND CHLOROPENTAFLUORO-ETHANE MIXTURE with fixed boiling point, with approximately 49% chlorodifluoromethane (REFRIGERANT GAS R502) | 2A | (1),(2),(3),(5) |  | 3.1 | 10 | 1.05 | n |
| 1974 | CHLORODIFLUOROBROMO-METHANE (R12B1) | 2A | (1),(2),(3),(5) |  | 1.0 | 10 | 1.61 | n |
| 1975 | NITRIC OXIDE AND DINITROGEN TETROXIDE MIXTURE (NITRIC OXIDE AND NITROGEN DIOXIDE MIXTURE) | 2TOC | (1),(2),(3),(5) |  |  | 3 |  | e,j,l |
| 1976 | OCTAFLUOROCYCLOBUTANE (REFRIGERANT GAS RC318) | 2A | (1),(2),(3),(5) |  | 1.1 | 10 | 1.34 | n |
| 1978 | PROPANE | 2F | (1),(2),(3),(5) |  | 2.5 | 10 | 0.42 | n |
| 1979 | RARE GASES MIXTURE, COMPRESSED | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1980 | RARE GASES AND OXYGEN MIXTURE, COMPRESSED | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P |  |
| 1981 | RARE GASES AND NITROGEN MIXTURE, COMPRESSED | 1A | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 1982 | TETRAFLUOROMETHANE, COMPRESSED (REFRIGERANT GAS R14, COMPRESSED) | 1A | (1),(2),(3),(5) (1),(2),(3),(5) |  | 20 30 | 10 | 0.62 0.94 | g g |
| 1983 | 1-CHLORO-2,2,2-TRIFLUOROETHANE (REFRIGERANT GAS R133a) | 2A | (1),(2),(3),(5) |  | 1.0 | 10 | 1.18 | n |
| 1984 | TRIFLUOROMETHANE (REFRIGERANT GAS R23) | 2A | (1),(2),(3),(5) (1),(2),(3),(5) |  | 19.0 25.0 | 10 10 | 0.87 0.95 | g,n g,n |
| 2034 | HYDROGEN AND METHANE MIXTURE, COMPRESSED | 1F | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. |  |
| 2035 | 1,1,1-TRIFLUOROETHANE (REFRIGERANT GAS R143a) | 2F | (1),(2),(3),(5) |  | 3.5 | 10 | 0.75 | n |
| 2036 | XENON, COMPRESSED | 1A | (1),(2),(3),(5) |  | 13 | 10 | 1.24 | g |
| 2044 | 2,2-DIMETHYLPROPANE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.53 | n |
| 2073 | AMMONIA SOLUTION, relative density less than 0.88 at 15C with more than 35% and not more than 40% ammonia with more than 40% and not more than 50% ammonia | 4A | (1),(2),(3),(5) (1),(2),(3),(5) |  | 1.0 1.0 | 5 5 | 0.80 0.77 |  |
| 2188 | ARSINE | 2TF | (1),(5) |  | 4.2 | 5 | 1.10 | e,l |
| 2189 | DICHLOROSILANE | 2TFC | (1),(2),(3),(5) |  | 1 | 3 | 0.90 |  |
| 2190 | OXYGEN DIFLUORIDE | 1TOC | (1),(5) |  | 20.0 | 3 | 2.8 | a,d,e,l |
| 2191 | SULPHURYL FLUORIDE | 2T | (1),(2),(3),(5) |  | 5.0 | 5 | 1.10 | k |
| 2192 | GERMANE 3/ | 2TF | (1),(5) |  | 25.0 | 5 | 1.02 | e,g,l,n |
| 2193 | HEXAFLUOROETHANE, COMPRESSED (REFRIGERANT GAS R116, COMPRESSED) | 1A | (1),(2),(3),(5) |  | 20 | 10 | 1.10 | g |
| 2194 | SELENIUM HEXAFLUORIDE | 2TC | (1),(5) |  | 3.6 | 3 | 1.46 | e,g,l,n |
| 2195 | TELLURIUM HEXAFLUORIDE | 2TC | (1),(5) |  | 2.0 | 3 | 1.0 | e,l,n |
| 2196 | TUNGSTEN HEXAFLUORIDE | 2TC | (1),(5) |  | 1.0 | 3 | 2.70 | a,e,l,n |
| 2197 | HYDROGEN IODIDE, ANHYDROUS | 2TC | (1),(2),(3),(5) |  | 2.3 | 3 | 2.25 | a,n |
| 2198 | PHOSPHORUS PENTAFLUORIDE, COMPRESSED | 1TC | (1),(5) (1),(5) |  | 20 30 | 3 | 0.9 1.34 | e,g,l e,g,l |
| 2199 | PHOSPHINE 3/ | 2TF | (1),(5) |  | 22.5 | 5 | 0.30 | e,g,l |
| 2200 | PROPADIENE, INHIBITED | 2F | (1),(2),(3),(5) |  | 2.2 | 10 | 0.50 | f,n |
| 2202 | HYDROGEN SELENIDE, ANHYDROUS | 2TF | (1),(5) |  | 3.1 | 5 | 1.60 | e,l |
| 2203 | SILANE, COMPRESSED 3/ | 1F | (1),(2),(3),(5) (1),(2),(3),(5) |  | 22.5 25.0 | 10 10 | 0.32 0.41 | e,g,l e,g,l |
| 2204 | CARBONYL SULPHIDE | 2TF | (1),(2),(3),(5) |  | 2.6 | 5 | 0.84 | k,n |
| 2417 | CARBONYL FLUORIDE, COMPRESSED | 1TC | (1),(2),(3),(5) (1),(2),(3),(5) |  | 20 30 | 3 | 0.47 0.7 | g g |
| 2418 | SULPHUR TETRAFLUORIDE | 2TC | (1),(5) |  | 3.0 | 3 | 0.91 | e,l,n |
| 2419 | BROMOTRIFLUORO-ETHYLENE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 1.19 | n |
| 2420 | HEXAFLUOROACETONE | 2TC | (1),(2),(3),(5) |  | 2.2 | 3 | 1.08 | n |
| 2422 | OCTAFLUOROBUT-2-ENE (REFRIGERANT GAS R1318) | 2A | (1),(2),(3),(5) |  | 1.2 | 10 | 1.34 | n |
| 2424 | OCTAFLUOROPROPANE (REFRIGERANT GAS R218) | 2A | (1),(2),(3),(5) |  | 2.5 | 10 | 1.09 | n |
| 2451 | NITROGEN TRIFLUORIDE | 1O | (1),(2),(3),(5) (1),(2),(3),(5) |  | 20 30 | 10 | 0.5 0.75 | g g |
| 2452 | ETHYLACETYLENE, INHIBITED | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.57 | c,f,n |
| 2453 | ETHYL FLUORIDE (REFRIGERANT GAS R161) | 2F | (1),(2),(3),(5) |  | 3.0 | 10 | 0.57 | n |
| 2454 | METHYL FLUORIDE (REFRIGERANT GAS R41) | 2F | (1),(2),(3),(5) |  | 30.0 | 10 | 0.36 | n |
| 2517 | 1-CHLORO-1,1-DIFLUOROETHANE (REFRIGERANT GAS R142(b) | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.99 | n |
| 2534 | METHYLCHLOROSILANE | 2TFC | (1),(2),(3),(5) |  |  | 3 |  | j,n |
| 2548 | CHLORINE PENTAFLUORIDE | 2TOC | (1),(5) |  | 1.3 | 3 | 1.49 | a,e,l |
| 2599 | CHLOROTRIFLUORO-METHANE AND TRIFLUOROMETHANE, AZEOTROPIC MIXTURE with approximately 60% chlorotrifluoromethane (REFRIGERANT GAS R503) | 2A | (1),(2),(3),(5) (1),(2),(3),(5) (1),(2),(3),(5) |  | 4.2 10.0 10.0 | 10 10 10 | 0.20 0.66 0.66 | n |
| 2600 | CARBON MONOXIDE AND HYDROGEN MIXTURE, COMPRESSED | 1TF | (1),(2),(3),(5) | 1.5 |  | 5 | 2/3 T.P. | k |
| 2601 | CYCLOBUTANE | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.63 | n |
| 2602 | DICHLORODIFLUORO-METHANE AND 1,1-DIFLUOROETHANE, AZEOTROPIC MIXTURE with approximately 74% dichlorodifluoromethane (REFRIGERANT GAS R500) | 2A | (1),(2),(3),(5) |  | 2.2 | 10 | 1.01 | n |
| 2676 | STIBINE | 2TF | (1),(5) |  | 2.0 | 5 | 1.2 | e,l,n |
| 2901 | BROMINE CHLORIDE | 2TOC | (1),(2),(3),(5) |  | 1.0 | 3 | 1.5 | a |
| 3057 | TRIFLUOROACETYL CHLORIDE | 2TC | (1),(2),(3),(5) |  | 1.7 | 3 | 1.17 | n |
| 3070 | ETHYLENE OXIDE AND DICHLORODIFLUORO-METHANE MIXTURE with not more than 12.5% ethylene oxide | 2A | (1),(2),(3),(5) |  | 1.8 | 10 | 1.09 | n |
| 3083 | PERCHLORYL FLUORIDE | 2TO | (1),(2),(3),(5) |  | 3.3 | 5 | 1.21 | k |
| 3153 | PERFLUORO(METHYL VINYL ETHER) | 2F | (1),(2),(3),(5) |  | 2.0 | 10 | 0.75 | n |
| 3154 | PERFLUORO(ETHYL VINYL ETHER) | 2F | (1),(2),(3),(5) |  | 1.0 | 10 | 0.98 | n |
| 3156 | COMPRESSED GAS, OXIDIZING, N.O.S. | 1O | (1),(2),(3),(5) | 1.5 |  | 10 | 2/3 T.P. | z |
| 3157 | LIQUEFIED GAS, OXIDIZING, N.O.S. | 2O | (1),(2),(3),(5) |  |  | 10 |  | z |
| 3159 | 1,1,1,2-TETRAFLUOROETHANE (REFRIGERNAT GAS R134a) | 2A | (1),(2),(3),(5) |  | 2.2 | 10 | 1.04 | n |
| 3160 | LIQUEFIED GAS, TOXIC, FLAMMABLE, N.O.S. | 2TF | (1),(2),(3),(5) |  |  | 5 |  | n,z |
| 3161 | LIQUEFIED GAS, FLAMMABLE, N.O.S. | 2F | (1),(2),(3),(5) |  |  | 10 |  | n,z |
| 3162 | LIQUEFIED GAS, TOXIC, N.O.S. | 2T | (1),(2),(3),(5) |  |  | 5 |  | z |
| 3163 | LIQUEFIED GAS, N.O.S. | 2A | (1),(2),(3),(5) |  |  | 10 |  | n,z |
| 3220 | PENTAFLUOROETHANE (REFRIGERANT GAS R125) | 2A | (1),(2),(3),(5) (1),(2),(3),(5) |  | 4.9 3.6 | 10 10 | 0.95 0.72 | g,n g,n |
| 3252 | DIFLUOROMETHANE (REFRIGERANT GAS R32) | 2F | (1),(2),(3),(5) |  | 4.8 | 10 | 0.78 | n |
| 3296 | HEPTAFLUOROPROPANE (REFRIGERANT GAS R227) | 2A | (1),(2),(3),(5) |  | 1.5 | 10 | 1.2 | n |
| 3297 | ETHYLENE OXIDE AND CHLOROTETRAFLUORO-ETHANE MIXTURE with not more than 8.8% ethylene oxide | 2A | (1),(2),(3),(5) |  | 1.0 | 10 | 1.16 | n |
| 3298 | ETHYLENE OXIDE AND PENTAFLUOROETHANE MIXTURE with not more than 7.9% ethylene oxide | 2A | (1),(2),(3),(5) |  | 2.6 | 10 | 1.02 | n |
| 3299 | ETHYLENE OXIDE AND TETRAFLUOROETHANE MIXTURE with not more than 5.6% ethylene oxide | 2A | (1),(2),(3),(5) |  | 1.7 | 10 | 1.03 | n |
| 3300 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with more than 87% ethylene oxide | 2TF | (1),(2),(3),(5) |  | 2.8 | 5 | 0.73 | f,n |
| 3303 | COMPRESSED GAS, TOXIC, OXIDIZING, N.O.S. | 1TO | (1),(2),(3),(5) | 1.5 |  | 5 | 2/3 T.P. | z |
| 3304 | COMPRESSED GAS, TOXIC, CORROSIVE, N.O.S. | 1TC | (1),(2),(3),(5) | 1.5 |  | 3 | 2/3 T.P. | z |
| 3305 | COMPRESSED GAS, TOXIC, FLAMMABLE, CORROSIVE, N.O.S. | 1TFC | (1),(2),(3),(5) | 1.5 |  | 3 | 2/3 T.P. | z |
| 3306 | COMPRESSED GAS, TOXIC, OXIDIZING, CORROSIVE, N.O.S. | 1TOC | (1),(2),(3),(5) | 1.5 |  | 3 | 2/3 T.P. | z |
| 3307 | LIQUEFIED GAS, TOXIC, OXIDIZING, N.O.S. | 2TO | (1),(2),(3),(5) |  |  | 5 |  | z |
| 3308 | LIQUEFIED GAS, TOXIC, CORROSIVE, N.O.S. | 2TC | (1),(2),(3),(5) |  |  | 3 |  | z,n |
| 3309 | LIQUEFIED GAS, TOXIC, FLAMMABLE, CORROSIVE, N.O.S. | 2TFC | (1),(2),(3),(5) |  |  | 3 |  | n,z |
| 3310 | LIQUEFIED GAS, TOXIC, OXIDIZING, CORROSIVE, N.O.S. | 2TOC | (1),(2),(3),(5) |  |  | 3 |  | z |
| 3318 | AMMONIA SOLUTION, relative density less than 0.880 at 15C in water, with more than 50% ammonia | 4TC | (1),(2),(3),(5) |  |  | 5 |  | j |
| 3337 | REFRIGERANT GAS R404A | 2A | (1),(2),(3),(5) |  | 3.5 | 10 | 0.84 | n |
| 3338 | REFRIGERANT GAS R407A | 2A | (1),(2),(3),(5) |  | 3.5 | 10 | 0.95 | n |
| 3339 | REFRIGERANT GAS R407B | 2A | (1),(2),(3),(5) |  | 3.7 | 10 | 0.95 | n |
| 3340 | REFRIGERANT GAS R407C | 2A | (1),(2),(3),(5) |  | 3.4 | 10 | 0.95 | n |
| 3354 | INSECTICIDE GAS, FLAMMABLE, N.O.S. | 2F | (1),(2),(3),(5) |  |  | 10 |  | n,z |
| 3355 | INSECTICIDE GAS, TOXIC, FLAMMABLE, N.O.S. | 2TF | (1),(2),(3),(5) |  |  | 5 |  | n,z |

1/ 	Not applicable for receptacles made of composite materials.

2/ 	For mixtures of UN No. 1965, the maximum permissible filling mass per litre of capacity is as follows:

3/ 	Considered as pyrophoric.

P201 PACKING INSTRUCTION P201

This instruction applies to UN Nos. 3167, 3168 and 3169.

The following packagings are authorized: (1) Compressed gas cylinders and gas receptacles conforming to the construction, testing and filling requirements approved by the competent authority; (2) For non-toxic gases, combination packagings with hermetically sealed inner packagings of glass or metal with a maximum capacity of 5 litres per package which meet the packing group III performance level; (3) For toxic gases, combination packagings with hermetically sealed inner packagings of glass or metal with a maximum capacity of 1 litre per package which meet the packing group III performance level.

P202 PACKING INSTRUCTION P202

This instruction applies to UN No. 3353.

The following packagings are authorized: Packagings conforming to the packing group III performance level. Air bag inflators or modules or seat belts pretensioners may be carried unpackaged in dedicated handling devices, vehicles or closed vehicles or containers when moved from where they are manufactured to an assembly plant.

Additional requirements: 1. The packaging shall be designed and constructed to prevent inadvertent operation during normal conditions of carriage. 2. The pressure vessel shall be in accordance with the requirements of the competent authority for the gas(es) contained in the pressure vessel.

P203 PACKING INSTRUCTION P203

Type of packagings: Cryogenic receptacles General instructions: (1) The special packing provisions of 4.1.6 shall be met. (2) The receptacles shall be so insulated that they cannot become coated with dew or hoar-frost. (3) In the case of receptacles intended for the carriage of gases of classification code 3O, the material used to ensure the leakproofness of the joints or for the maintenance of the closures shall be compatible with the contents. Particular instructions for closed cryogenic receptacles: (4) The receptacles shall be fitted with safety valves. (5) For refrigerated liquefied gases of classification codes 3A and 3O the degree of filling, at the filling temperature and at a pressure of 0.1 MPa (1 bar) shall not exceed 98% of the capacity. (6) For refrigerated liquefied gases of classification code 3F the degree of filling shall remain below the level at which, if the contents were raised to the temperature at which the vapour pressure equalled the opening pressure of the relief valve, the volume would reach 95% of the capacity at that temperature. (7) Receptacles shall be subjected to periodic inspections in accordance with the provisions of 6.2.1.6. (8) Periodic inspections shall be carried out every 10 years. By derogation from this date, the periodic inspection of receptacles which make use of composite materials (composite receptacles) may be carried out at intervals determined by the competent authority of the Contracting Party to ADR which has approved the technical code for the design and construction. Particular instructions for open cryogenic receptacles: (9) Open cryogenic receptacles are not allowed for flammable refrigerated liquefied gases of classification code 3F, and UN No. 2187 carbon dioxide, refrigerated liquid and its mixtures. (10) The receptacles shall be equipped with devices which prevent the liquid from splashing out. (11) Glass receptacles shall be double-walled vacuum insulated and surrounded by an absorbent insulating material; they shall be protected by iron-wire baskets and placed in metal cases. The metal cases for the glass receptacles and the other receptacles shall be fitted with means of handling. (12) The openings of the receptacles shall be fitted with devices allowing gases to escape, preventing any splashing out of the liquid, and so fixed that they cannot fall out. (13) In the case of UN No. 1073 oxygen refrigerated liquid and mixtures thereof, the devices referred to above and the absorbent insulating material surrounding the glass receptacles shall be made of incombustible materials. Reference to standards (reserved)

P204 PACKING INSTRUCTION P204

This packing instruction applies to UN No. 1950 aerosols and UN No. 2037 receptacles, small, containing gas (gas cartridges)

(1) The special packing provisions of 4.1.6 shall be met when applicable. (2) Receptacles shall be so closed and leakproof as to prevent escape of the gases. (3) For UN No. 1950 aerosols and UN No. 2037 receptacles, small, containing gas (gas cartridges): (a) the internal pressure at 50 °C shall exceed neither two-thirds of the test pressure nor 1.32 MPa (13.2 bar). (b) they shall be so filled that at 50 °C the liquid phase does not exceed 95% of their capacity. (c) they shall satisfy a tightness (leakproofness) test in a hot-water bath: - The temperature of the bath and the duration of the test shall be such that the internal pressure of each receptacle reaches at least 90% of the internal pressure that would be reached at 55 °C; - However, if the contents are sensitive to heat or if the receptacles are made of a plastics material which softens at this temperature, the temperature of the bath shall be from 20 °C to 30 °C; in addition, one receptacle out of every 2000 shall be tested at the temperature prescribed in the foregoing indent; - No leakage or permanent deformation shall occur. The provision concerning permanent deformation is not applicable to receptacles which, being made of plastics material, soften. The requirements of instruction P204(3)(c) are deemed to be met if the following standards are complied with: - for aerosol dispensers (UN No. 1950 aerosols): Annex to Council Directive 75/324/EEC(as amended by Commission Directive 94/1/EC((; - for UN No. 2037 gas cartridges containing UN No. 1965 hydrocarbon gas mixture, liquefied: EN 417:1992 Non-refillable metallic gas cartridges for liquefied petroleum gases, with or without a valve, for use with portable appliances - Construction, inspection, testing and marking. (4) For UN No. 1950 aerosols, only non-pyrophoric and non-toxic gases may be used as propellants, as constituents of propellants, or as filler gases. (5) All compressed and liquefied gases, except the pyrophoric gases and very toxic gases (gases with an LC50 lower than 200ppm), shall be accepted as filling gases for UN No. 2037 gas cartridges. (6) Aerosols and gas cartridges shall be placed in wooden boxes or strong fibreboard or metal boxes; UN No. 1950 aerosols made of glass or synthetic material and liable to shatter shall be separated from one another by interposed sheets of fibreboard or of another suitable material. (7) A package shall not weigh more than 50kg if fibreboard boxes are used or more than 75kg if other packagings are used. (8) In the case of carriage by full load, metal articles may also be packed as follows: the articles shall be grouped together in units on trays and held in position with an appropriate plastics cover; these units shall be stacked and suitably secured on pallets.

P205 PACKING INSTRUCTION P205

This packing instruction applies to UN No. 1057 lighters or lighter refills

(1) The special packing provisions of 4.1.6.1 shall be met when applicable. (2) The articles shall comply with the provisions of the country in which they were filled. (3) Lighters and lighter refills shall be provided with protection against inadvertent discharge. (4) The liquid portion of the gas shall not exceed 85% of the capacity of the receptacle at 15 °C. (5) The receptacles, including the closures, shall be capable of withstanding an internal pressure of the liquefied petroleum gas at 55 °C. (6) The valve mechanisms and ignition devices shall be securely sealed, taped or otherwise fastened or designed to prevent operation or leakage of the contents during carriage. (7) The lighters or lighter refills shall be tightly packed to prevent inadvertent operation of the release devices. (8) Lighters shall contain not more than 10g of liquefied petroleum gas. Lighter refills shall contain not more than 65g of liquefied petroleum gas. (9) The lighters and lighter refills shall be packed in strong outer packagings conforming to 6.1.4 consisting of natural wood boxes (4C1, 4C2), plywood boxes (4D) or reconstituted wood boxes (4F) with a maximum gross mass of 75kg, or fibreboard boxes (4G) with a maximum gross mass of 40kg. The packagings shall be tested and approved in accordance with Chapter 6.1 for packing group II. Nevertheless, if these packagings have a maximum gross mass of not more than 2kg, compliance with the general provisions of 4.1.1.1, 4.1.1.2 and 4.1.1.5 to 4.1.1.7.

P206 PACKING INSTRUCTION 206

This packing instruction applies to UN No. 3150 devices, small, hydrocarbon gas powered or hydrocarbon gas refills for small devices

(1) The special packing provisions of 4.1.6 when applicable shall be met. (2) The articles shall comply with the provisions of the country in which they were filled. (3) The devices and refills shall be packed in outer packagings conforming to 6.1.4 tested and approved in accordance with Chapter 6.1 for packing group II.

P300 PACKING INSTRUCTION P300

This instruction applies to UN No. 3064.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: Combination packagings consisting of inner metal cans of not more than 1 litre capacity each and outer wooden boxes (4C1, 4C2, 4D or 4F) containing not more than 5 litres of solution.

Additional requirements: 1. Metal cans shall be completely surrounded with absorbent cushioning material. 2. Wooden boxes shall be completely lined with suitable material impervious to water and nitroglycerin.

P301 PACKING INSTRUCTION P301

This instruction applies to UN No. 3165.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: (1) Aluminium pressure vessel made from tubing and having welded heads. Primary containment of the fuel within this vessel shall consist of a welded aluminium bladder having a maximum internal volume of 46 litres. The outer vessel shall have a minimum design gauge pressure of 1275 kPa and a minimum burst gauge pressure of 2 755 kPa. Each vessel shall be leak checked during manufacture and before dispatch and shall be found leakproof. The complete inner unit shall be securely packed in non-combustible cushioning material, such as vermiculite, in a strong outer tightly closed metal packaging which will adequately protect all fittings. Maximum quantity of fuel per unit and package is 42 litres; (2) Aluminium pressure vessel. Primary containment of the fuel within this vessel shall consist of a welded vapour tight fuel compartment with an elastomeric bladder having a maximum internal volume of 46 litres. The pressure vessel shall have a minimum design gauge pressure of 2860 kPa and a minimum burst gauge pressure of 5170 kPa. Each vessel shall be leak-checked during manufacture and before dispatch and shall be securely packed in non-combustible cushioning material such as vermiculite, in a strong outer tightly closed metal packaging which will adequately protect all fittings. Maximum quantity of fuel per unit and package is 42 litres.

P302 PACKING INSTRUCTION P302

This instruction applies to UN No. 3269.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: Combination packagings which meet the packing group II or III performance level according to the criteria for Class 3, applied to the base material. The base material and the activator (organic peroxide) shall be each separately packed in inner packagings. The components may be placed in the same outer packaging provided they will not interact dangerously in the event of a leakage. The activator shall have a maximum quantity of 125 ml per inner packaging if liquid, and 500 grams per inner packaging if solid.

P400 PACKING INSTRUCTION P400

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met (see also the Table in 4.1.4.4): (1) Steel gas cylinders and gas receptacles, which shall comply with the appropriate requirements in the Table of 4.1.4.4. Valves shall be protected with steel valve protection caps or collars or the gas cylinders or receptacles shall be overpacked in strong wood, fibreboard or plastics boxes. Cylinders and gas receptacles shall be secured to prevent movement in the box and shall be packaged and carried so that the pressure relief devices remain in the vapour space of the cylinder during normal conditions of handling and carriage; (2) Boxes (4A, 4B, 4C1, 4C2, 4D, 4F or 4G), drums (1A2, 1B2, 1N2, 1D or 1G) or jerricans (3A2 or 3B2) enclosing hermetically sealed metal cans with inner packagings of glass or metal, with a capacity of not more than 1 litre each, having threaded closures with gaskets. Inner packagings shall be cushioned on all sides with dry, absorbent, non-combustible material in a quantity sufficient to absorb the entire contents. Inner packagings shall not be filled to more than 90% of their capacity. Outer packagings shall have a maximum net mass of 125 kg; (3) Steel, aluminium or metal drums (1A2, 1B2 or 1N2), jerricans (3A2 or 3B2) or boxes (4A or 4B) with a maximum net mass of 150 kg each with hermetically sealed inner metal cans not more than 4 litre capacity each, with threaded closures fitted with gaskets. Inner packagings shall be cushioned on all sides with dry, absorbent, non-combustible material in a quantity sufficient to absorb the entire contents. Each layer of inner packagings shall be separated by a dividing partition in addition to cushioning material. Inner packagings shall not be filled to more than 90% of their capacity.

P401 PACKING INSTRUCTION P401

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met (see also the Table in 4.1.4.4): (1) Steel gas cylinders and gas receptacles, which shall comply with the appropriate requirements in the Table of 4.1.4.4. Valves shall be protected with steel valve protection caps or collars or the gas cylinders or receptacles shall be overpacked in strong wood, fibreboard or plastics boxes. Cylinders and gas receptacles shall be secured to prevent movement in the box and shall be packaged and carried so that the pressure relief devices remain in the cylinder during normal conditions of handling and carriage; Inner packaging Outer packaging (2) Combination packagings with inner 1 l 30 kg packagings of glass metal or plastics maximum net mass which have threaded closures surrounded in inert cushioning and absorbent material in a quantity sufficient to absorb the entire contents.

P402 PACKING INSTRUCTION P402

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met (see also the Table in 4.1.4.4): (1) Steel gas cylinders and gas receptacles, which shall comply with the appropriate requirements in the Table of 4.1.4.4. Valves shall be protected with steel valve protection caps or collars or the gas cylinders or receptacles shall be overpacked in strong wood, fibreboard or plastics boxes. Cylinders and gas receptacles shall be secured to prevent movement in the box and shall be packaged and transported so that the pressure relief devices remain in the vapour space of the cylinder during normal conditions of handling and carriage. Filling shall not be greater than 90% of the capacity of the cylinder; Inner packaging Outer packaging maximum net mass (2) Combination packagings with inner packagings 10 kg (glass) 125 kg of glass, metal or plastics which have threaded 15 kg (metal or plastics) 125 kg closures surrounded in inert cushioning and absorbent material in a quantity sufficient to absorb the entire contents.

Special packing provision PP78 For UN No. 3130, the openings of receptacles shall be tightly closed by means of two devices in series, one of which shall be screwed or secured in an equivalent manner.

| P403 PACKING INSTRUCTION P403 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: |  |  |
| Combination packagings: |  |  |
| Inner packagings | Outer packagings | Maximum net mass |
| Glass 2 kg Plastics 15 kg Metal 20 kg Inner packagings shall have threaded closures | Drums steel (1A2) aluminium (1B2) metal, other than steel or aluminium (1N2) plastics (1H2) plywood (1D) fibre (1G) | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg |
|  | Boxes steel (4A) aluminium (4B) natural wood (4C1) natural wood with sift proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) expanded plastics (4H1) solid plastics (4H2) | 400 kg 400 kg 250 kg 250 kg 250 kg 125 kg 125 kg 60 kg 250 kg |
|  | Jerricans steel (3A2) aluminium (3B2) plastics (3H2) | 120 kg 120 kg 120 kg |
| Single packagings: |  | Maximum net mass |
| Drums steel(1A1, 1A2) aluminium (1B1, 1B2) metal other than steel or aluminium (1N1, 1N2) plastics (1H1, 1H2) |  | 250 kg 250 kg 250 kg 250 kg |
| Jerricans steel (3A1, 3A2) aluminium (3B1, 3B2) plastics (3H1, 3H2) |  | 120 kg 120 kg 120 kg |
| Composite packagings |  |  |
| plastics receptacle with outer steel or aluminium drums (6HA1 or 6HB1) |  | 250 kg |
| plastics receptacle with outer fibre, plastics or plywood drums (6HG1, 6HH1 or 6HD1) |  | 75 kg |
| plastics receptacle with outer steel or aluminium crate or box or with outer wooden, plywood, fibreboard or solid plastics boxes (6HA2, 6HB2, 6HC, 6HD2, 6HG2 or 6HH2) |  | 75 kg |
| Additional requirement: Packagings shall be hermetically sealed. |  |  |
| P404 PACKING INSTRUCTION P404 |
| This instruction applies to pyrophoric solids: UN Nos: 1370, 1383, 1854, 1855, 2005, 2008, 2545, 2546, 2846, 2881, 3052, 3200 and 3203. |
| The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: (1) Combination packagings Outer packagings: (1A2, 1B2, 1N2, 1H2, 1D, 4A, 4B, 4C1, 4C2, 4D, 4F or 4H2) Inner packagings: Metal packagings with a capacity of not more than 15kg each. Inner packagings shall be hermetically sealed and have threaded closures; (2) Metal packagings: (1A1, 1A2, 1B1, 1N1, 1N2, 3A1, 3A2, 3B1 and 3B2) Maximum gross mass: 150kg; (3) Composite packagings: Plastics receptacle with outer steel or aluminium drum (6HA1 or 6HB1) Maximum gross mass: 150kg. |

P405 PACKING INSTRUCTION P405

This instruction applies to UN No. 1381.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: (1) For UN No. 1381, phosphorus, wet: (a) Combination packagings Outer packagings: (4A, 4B, 4C1, 4C2, 4D or 4F) Maximum net mass: 75kg Inner packagings: (i) hermetically sealed metal cans, with a maximum net mass of 15kg; or (ii) glass inner packagings cushioned on all sides with dry, absorbent, non-combustible material in a quantity sufficient to absorb the entire contents with a maximum net mass of 2 kg; or (b) Drums (1A1, 1A2, 1B1, 1B2, 1N1 or 1N2); maximum net mass: 400 kg Jerricans (3A1 or 3B1); maximum net mass: 120kg. These packagings shall be capable of passing the leakproofness test specified in 6.1.5.4 at the packing group II performance level; (2) For UN No. 1381, dry phosphorus: (a) When fused, drums (1A2, 1B2 or 1N2) with a maximum net mass of 400 kg; or (b) In projectiles or hard cased articles when carried without Class 1 components: as specified by the competent authority.

P406 PACKING INSTRUCTION P406

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met:

(1) Combination packagings outer packagings: (4C1, 4C2, 4D, 4F, 4G, 4H1, 4H2, 1G, 1D, 1H2 or 3H2) inner packagings: water-resistant packagings; (2) Plastics, plywood or fibreboard drums (1H2, 1D or 1G) or boxes (4A, 4B, 4C1, 4D, 4F, 4C2 4G and 4H2) with a water resistant inner bag, plastics film lining or water resistant coating; (3) Metal drums (1A1, 1A2, 1B1, 1B2, 1N1 or 1N2), plastics drums (1H1 or 1H2), metal jerricans (3A1, 3A2, 3B1 or 3B2), plastics jerricans (3H1 or 3H2), plastics receptacle with outer steel or aluminium drums (6HA1 or 6HB1), plastics receptacle with outer fibre, plastics or plywood drums (6HG1, 6HH1 or 6HD1), plastics receptacle with outer steel or aluminium crate or box or with outer wooden, plywood, fibreboard or solid plastics boxes (6HA2, 6HB2, 6HC, 6HD2, 6HG2 or 6HH2).

Additional requirements: 1. Packagings shall be designed and constructed to prevent the loss of water or alcohol content or the content of the phlegmatizer. 2. Packagings shall be so constructed and closed so as to avoid an explosive overpressure or pressure build-up of more than 300 kPa (3 bar). 3. The type of packaging and maximum permitted quantity per packaging are limited when this packing instruction is applied in accordance with special provisions 15 or 18 of Chapter 3.3.

Special packing provisions: PP24 For UN No. 2852, the quantity carried shall not exceed 500 g per package. PP25 For UN No. 1347, the quantity carried shall not exceed 15 kg per package. PP26 For UN Nos. 1310, 1320, 1321, 1322, 1344, 1347, 1348, 1349, 1517, 2907, 3317 and 3344 packagings shall be lead free.

P407 PACKING INSTRUCTION P407

This instruction applies to UN Nos. 1331, 1944, 1945 and 2254.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met:

Combination packagings comprising securely closed inner packagings to prevent accidental ignition under normal conditions of transport. The maximum net mass of the outer packagings shall not exceed 45 kg except for fibreboard boxes which shall not exceed 30 kg.

Additional requirement: Matches shall be tightly packed.

Special packing provision: PP27 UN No. 1331, Strike-anywhere matches shall not be packed in the same outer packaging with any other dangerous goods other than safety matches or wax Vesta matches, which shall be packed in separate inner packagings. Inner packagings shall not contain more than 700 strike-anywhere matches.

P408 PACKING INSTRUCTION P408

This instruction applies to UN No. 3292.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met:

(1) For cells: Outer packagings with sufficient cushioning material to prevent contact between cells and between cells and the internal surfaces of the outer packaging and to ensure that no dangerous movement of the cells within the outer packaging occurs during carriage. Packagings shall conform to the packing group II performance level; (2) For batteries: Batteries may be carried unpacked or in protective enclosures (e.g. in fully enclosed or wooden slatted crates). The terminals shall not support the weight of other batteries or materials packed with the batteries.

Additional requirement: Batteries shall be protected against short circuit and shall be isolated in such a manner as to prevent short circuits.

P409 PACKING INSTRUCTION P409

This instruction applies to UN Nos. 2956, 3242 and 3251.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met:

(1) Fibre drum (1G) which may be fitted with a liner or coating; maximum net mass: 50kg; (2) Combination packagings: Fibreboard box (4G) with a single inner plastic bag; maximum net mass: 50kg; (3) Combination packagings: Fibreboard box (4G) or fibre drum (1G) with plastics inner packagings each containing a maximum of 5 kg; maximum net mass: 25kg.

| P410 PACKING INSTRUCTION P410 |  |  |  |
| --- | --- | --- | --- |
| The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: |  |  |  |
| Combination packagings: |  |  |  |
| Inner packagings | Outer packagings | Maximum net mass |  |
|  |  | Packing group II | Packing group III |
| Glass 10 kg Plastics 1/ 30 kg Metal 40 kg Paper 1/ 2/ 10 kg Fibre 1/ 2/ 10 kg 1/ Packagings shall be sift-proof. 2/ These inner packagings shall not be used when the substances being carried may become liquid during carriage. | Drums steel (1A2) aluminium (1B2) metal other than steel or aluminium (1N2) plastics (1H2) plywood (1D) fibre (1G) 1/ | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg |
|  | Boxes steel (4A) aluminium (4B) natural wood (4C1) natural wood with sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G)1/ expanded plastics (4H1) solid plastics (4H2) | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 60 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 60 kg 400 kg |
|  | Jerricans steel (3A2) aluminium (3B2) plastics (3H2) | 120 kg 120 kg 120 kg | 120 kg 120 kg 120 kg |
| Single packagings: |  |  |
| Drums steel (1A1 or 1A2) aluminium (1B1 or 1B2) metal other than steel or aluminium (1N1 or 1N2) plastics (1H1 or 1H2) | 400 kg 400 kg 400 kg 400 kg | 400 kg 400 kg 400 kg 400 kg |
| Jerricans steel (3A1 or 3A2) aluminium (3B1 or 3B2) plastics (3H1 or 3H2) | 120 kg 120 kg 120 kg | 120 kg 120 kg 120 kg |
| P410 PACKING INSTRUCTION (cont’d) P410 |  |  |
| Single packagings (cont’d): | Packing group II | Packing group III |
| Boxes steel (4A) 3/ aluminium (4B) 3/ natural wood (4C1) 3/ plywood (4D) 3/ reconstituted wood (4F) 3/ natural wood with sift-proof walls (4C2) 3/ fibreboard (4G) 3/ solid plastics (4H2) 3/ | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg | 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg 400 kg |
| Bags Bags (5H3, 5H4, 5L3, 5M2) 3/ 4/ | 50 kg | 50 kg |
| Composite packagings plastics receptacle with outer steel, aluminium, plywood, fibre or plastics drum (6HA1, 6HB1, 6HG1, 6HD1, or 6HH1) | 400 kg | 400 kg |
| plastics receptacle with outer steel or aluminium crate or box, or outer wooden, plywood, fibreboard or solid plastics box (6HA2, 6HB2, 6HC, 6HD2, 6HG2 or 6HH2) | 75 kg | 75 kg |
| glass receptacle with outer steel, aluminium, plywood or fibre drum (6PA1, 6PB1, 6PD1 or 6PG1) or outer steel or aluminium crate or box or with outer wooden or fibreboard box or with outer wickerwork hamper (6PA2, 6PB2, 6PC, 6PD2, or 6PG2) or with outer solid or expanded plastics packaging (6PH1 or 6PH2) | 75 kg | 75 kg |
| 3/ These packagings shall not be used when the substances being carried may become liquid during carriage. 4/ These packagings shall only be used for packing group II substances when carried in a closed vehicle or container. |  |  |
| Special packing provisions: PP 39 For UN No. 1378, for metal packagings a venting device is required. PP 40 For UN Nos. 1326, 1352, 1358, 1395, 1396, 1404, 1436, 1437, 1485, 1495, 1871, 2805, 3182 and 3247, packing group II, bags are not allowed. |  |  |

P411 PACKING INSTRUCTION P411

This instruction applies to UN No. 3270.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met:

(1) Fibreboard box with a maximum gross mass of 30kg; (2) Other packagings, provided that explosion is not possible by reason of increased internal pressure. Maximum net mass shall not exceed 30kg.

P500 PACKING INSTRUCTION P500

This instruction applies to UN No. 3356.

The general provisions of 4.1.1 and 4.1.3 shall be met.

Packagings shall conform to the packing group II performance level. The generator(s) shall be carried in a package which meets the following requirements when one generator in the package is actuated: (a) Other generators in the package will not be actuated; (b) Packaging material will not ignite; and (c) The outside surface temperature of the completed package shall not exceed 100 °C.

P501 PACKING INSTRUCTION P501

This instruction applies to UN No. 2015.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met:

Combination packagings: Inner packaging Outer packaging maximum capacity maximum net mass

(1) Boxes (4A, 4B, 4C1, 4C2, 4D, 4H2) 5 l 125 kg or drums (1A2, 1B2, 1N2, 1H2, 1D) or jerricans (3A2, 3B2, 3H2) with glass, plastics or metal inner packagings (2) Fibreboard box (4G) or fibre drum (1G), 2 l 50 kg with plastics or metal inner packagings each in a plastics bag

Single packagings: Maximum capacity

Drums steel (1A1) 250 l aluminium (1B1) metal other than steel or aluminium (1N1) plastics (1H1)

Jerricans

steel (3A1) 60 l aluminium (3B1) plastics (3H1)

Composite packagings

plastics receptacle with outer steel or aluminium drum (6HA1, 6HB1) 250 l plastics receptacle with outer fibre, plastics or plywood drum (6HG1, 6HH1, 6HD1) 250 l plastics receptacle with outer steel or aluminium crate or box or plastics receptacle with outer wooden, plywood, fibreboard or solid plastics box (6HA2, 6HB2, 6HC, 6HD2, 6HG2 or 6HH2) 60 l glass receptacle with outer steel, aluminium, fibre, plywood, solid plastics or expanded plastics drum (6PA1, 6PB1, 6PG1, 6PD1, 6PH1 or 6PH2) or with outer steel or aluminium crate or box or with outer wooden or fibreboard box or with outer wickerwork hamper (6PA2, 6PB2, 6PC, 6PG2 or 6PD2) 60 l

Additional requirements: 1. Packagings shall have a maximum filling degree of 90%. 2. Packagings shall be vented.

| P502 PACKING INSTRUCTION P502 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: |  |  |
| Combination packagings: |
| Inner packagings | Outer packagings | Maximum net mass |
| Glass 5 l Metal 5 l Plastics 5 l | Drums steel (1A2) aluminium (1B2) metal other than steel or aluminium (1N2) plastics (1H2) plywood (1D) fibre (1G) | 125 kg 125 kg 125 kg 125 kg 125 kg 125 kg |
|  | Boxes steel (4A) aluminium (4B) natural wood (4C1) natural wood with sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) expanded plastics (4H1) solid plastics (4H2) | 125 kg 125 kg 125 kg 125 kg 125 kg 125 kg 125 kg 60 kg 125 kg |
| Single packagings: Maximum capacity |  |  |
| Drums steel (1A1) 250 l aluminium (1B1) plastics (1H1) Jerricans steel (3A1) 60 l aluminium (3B1) plastics (3H1) |  |  |
| Composite packagings |  |  |
| plastics receptacle with outer steel or aluminium drum (6HA1, 6HB1) 250 l plastics receptacle with outer fibre, plastics or plywood drum (6HG1, 6HH1, 6HD1) 250 l plastics receptacle with outer steel or aluminium crate or box or plastics receptacle with outer wooden, plywood, fibreboard or solid plastics box (6HA2, 6HB2, 6HC, 6HD2, 6HG2 or 6HH2) 60 l glass receptacle with outer steel, aluminium, fibre, plywood, solid plastics or expanded plastics drum (6PA1, 6PB1, 6PG1, 6PD1, 6PH1 or 6PH2) or with outer steel or aluminium crate or box or with outer wooden or fibreboard box or with outer wickerwork hamper (6PA2, 6PB2, 6PC, 6PG2 or 6PD2) 60 l |  |  |
| Special packing provision: PP28 For UN No. 1873, only glass inner packagings are authorized for combination packagings. |  |  |
| P503 PACKING INSTRUCTION P503 |  |  |
| The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: |  |  |
| Combination packagings: |
| Inner packagings | Outer packagings | Maximum net mass |
| Glass 5 kg. Metal 5 kg Plastics 5 kg | Drums steel (1A2) aluminium (1B2) metal other than steel or aluminium (1N2) plastics (1H2) plywood (1D) fibre (1G) | 125kg 125kg 125kg 125kg 125kg 125kg |
|  | Boxes steel (4A) aluminium (4B) natural wood (4C1) natural wood with sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) expanded plastics (4H1) solid plastics (4H2) | 125 kg 125 kg 125 kg 125 kg 125 kg 125 kg 40 kg 60 kg 125 kg |
| Single packagings: |  |  |
| Metal drums (1A1, 1A2, 1B1, 1B2, 1N1 or 1N2) with a maximum net mass of 250 kg. |  |  |
| Fibreboard (1G) or plywood drums (1D) fitted with inner liners with a maximum net mass of 200 kg. |  |  |

| P504 PACKING INSTRUCTION P504 |  |
| --- | --- |
| The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3 are met: |  |
| Combination packagings: | Maximum net mass |
| (1) Glass receptacles with a maximum capacity of 5 litres in 1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H2 outer packagings (2) Plastics receptacles with a maximum capacity of 30 litres in 1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H2 outer packagings (3) Metal receptacles with a maximum capacity of 40 litres in 1G, 4F or 4G outer packagings (4) Metal receptacles with a maximum capacity of 40 litres in 1A2, 1B2, 1N2, 1H2, 1D, 4A, 4B, 4C1, 4C2, 4D, 4H2 outer packagings | 75 kg 75 kg 125 kg 225 kg |
| Single packagings: | Maximum capacity |
| Drums |  |
| steel, non-removable head (1A1) | 250 l |
| steel, removable head (1A2) aluminium, non-removable head (1B1) aluminium, removable head (1B2) | 250 l 250 l 250 l |
| metal other than steel or aluminium, non-removable head (1N1) metal other than steel or aluminium, removable head (1N2) | 250 l 250 l |
| plastics, non-removable head (1H1) plastics, removable head (3H2) | 250 l 250 l |
| Jerricans |  |
| steel, non-removable head (3A1) | 60 l |
| aluminium, non-removable head (3B1) | 60 l |
| plastics, non-removable head (3H1) | 60 l |
| Composite packagings: |  |
| plastics receptacle with outer steel or aluminium drum (6HA1, 6HB1) | 250 l |
| plastics receptacle with outer fibre, plastics or plywood drum (6HG1, 6HH1, 6HD1) | 120 l |
| plastics receptacle with outer steel or aluminium crate or box or plastics receptacle with outer wooden, plywood, fibreboard or solid plastics box (6HA2, 6HB2, 6HC, 6HD2, 6HG2 or 6HH2) | 60 l |
| glass receptacle with outer steel, aluminium, fibre, plywood, solid plastics or expanded plastics drum (6PA1, 6PB1, 6PG1, 6PD1, 6PH1 or 6PH2) or with outer steel or aluminium crate or box or with outer wooden fibreboard box or with outer wickerwork hamper (6PA2, 6PB2, 6PC, 6PG2 or 6PD2) | 60 l |
| Special packing provisions: PP10 For UN No. 2014 PG II and UN No. 2984 PG III, the packaging shall be vented. PP29 For UN No. 2014, maximum degree of filling shall be 90%. |  |

| P520 PACKING INSTRUCTION P520 |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| This instruction applies to organic peroxides of Class 5.2 and self-reactive substances of Class 4.1 |  |  |  |  |  |  |  |  |
| The packagings listed below are authorized provided the general provisions of 4.1.1 and 4.1.3 and special provisions of 4.1.7 are met. The packing methods are designated OP1 to OP8. The packing methods appropriate for the individual currently assigned organic peroxides and self-reactive substances are listed in 4.1.7.1.3, 2.2.41.4 and 2.2.52.4. The quantities specified for each packing method are the maximum quantities authorized per package. The following packagings are authorized: (1) Combination packagings with outer packagings comprising boxes (4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H1 and 4H2), drums (1A2, 1B2, 1G, 1H2 and 1D), jerricans (3A2, 3B2 and 3H2); (2) Single packagings consisting of drums (1A1, 1A2, 1B1, 1B2, 1G, 1H1, 1H2 and 1D) and jerricans (3A1, 3A2, 3B1, 3B2, 3H1 and 3H2); (3) Composite packagings with plastics inner receptacles (6HA1, 6HA2, 6HB1, 6HB2, 6HC, 6HD1, 6HD2, 6HG1, 6HG2, 6HH1 and 6HH2). |  |  |  |  |  |  |  |  |
| Maximum quantity per packaging/package 1/ for packing methods OP1 to OP8 |  |  |  |  |  |  |  |  |
| Packing Method Maximum Quantity | OP1 | OP2 1/ | OP3 | OP4 1/ | OP5 | OP6 | OP7 | OP8 |
| Maximum mass (kg) for solids and for combination packagings (liquid and solid) | 0.5 | 0.5/10 | 5 | 5/25 | 25 | 50 | 50 | 200 2/ |
| Maximum contents in litres for liquids 3/ | 0.5 | - | 5 | - | 30 | 60 | 60 | 225 4/ |
| 1/ If two values are given, the first applies to the maximum net mass per inner packaging and the second to the maximum net mass of the complete package. 2/ 60 kg for jerricans/ 100 kg for boxes. 3/ Viscous substances shall be treated as solids when they do not meet the criteria provided in the definition for “liquids” presented in 1.2.1. 4/ 60 litres for jerricans. |  |  |  |  |  |  |  |  |
| Additional requirements: 1. Metal packagings, including inner packagings of combination packagings and outer packagings of combination or composite packagings may only be used for packing methods OP7 and OP8. 2. In combination packagings, glass receptacles may only be used as inner packagings with maximum contents of 0.5 kg or 0.5 litre. 3. In combination packagings, cushioning materials shall not be readily combustible. 4. The packaging of an organic peroxide or self-reactive substance required to bear an “EXPLOSIVE” subsidiary risk label shall also comply with the provisions given in 4.1.5.10 and 4.1.5.11. |  |  |  |  |  |  |  |  |
| Special packing provisions: PP21 For certain self-reactive substances of types B or C, UN Nos. 3221, 3222, 3223, 3224, 3231, 3232, 3233 and 3234, a smaller packaging than that allowed by packing methods OP5 or OP6 respectively shall be used (see 4.1.6 and 2.2.41.4). PP22 UN No. 3241, 2-Bromo-2-nitropropane-1, 3-diol, shall be packed in accordance with packing method OP6. |  |  |  |  |  |  |  |  |

P600 PACKING INSTRUCTION P600

This instruction applies to UN Nos. 1700, 2016 and 2017.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: Outer packagings (1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H2) meeting the packing group II performance level. The articles shall be individually packaged and separated from each other using partitions, dividers, inner packagings or cushioning material to prevent inadvertent discharge during normal conditions of carriage. Maximum net mass: 75 kg

P601 PACKING INSTRUCTION P601

The following packagings are authorized provided the general provisions of 4.1.1 and 4.1.3 are met (see also the Table of 4.1.4.4): (1) Combination packagings consisting of glass inner packagings not exceeding 1 litre in capacity packed with absorbent material sufficient to absorb the entire contents and inert cushioning material placed in metal receptacles which are individually packed in 1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G or 4H2 outer packagings with a maximum gross mass of 15 kg. Inner packagings shall not be filled to more than 90% of their capacity. The closure of each inner packaging shall be physically held in place by any means capable of preventing back-off or loosening of the closure by impact or vibration during carriage; (2) Combination packagings consisting of metal inner packagings or additionally, for UN No. 1744 only, in polyvinylidene fluoride (PVDF) inner packagings, not exceeding 5 litres in capacity individually packed with absorbent material sufficient to absorb the contents and inert cushioning material in 1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G or 4H2 outer packagings with a maximum gross mass of 75 kg. Inner packagings shall not be filled to more than 90% of their capacity. The closure of each inner packaging shall be physically held in place by any means capable of preventing back-off or loosening of the closure by impact or vibration during carriage; (3) Combination packagings: Outer packagings: Plastic or steel drums, removable head (1A2 or 1H2) tested in accordance with the test requirements in 6.1.5 as combination packagings as assembled for carriage; Inner packagings: Drums and composite packagings (1A1, 1B1, 1N1, 1H1 or 6HA1) meeting the requirements of Chapter 6.1 for single packagings, subject to the following conditions: (a) The hydraulic pressure test shall be conducted at a pressure of at least 0.3 MPa (gauge pressure); (b) The design and production leakproofness tests shall be conducted at a test pressure of 30 kPa; (c) They shall be isolated from the outer drum by the use of inert shock-mitigating cushioning material which surrounds the inner packaging on all sides; (d) Their capacity shall not exceed 125 litres; and (e) Closures shall be of a screw cap type that are: (i) physically held in place by any means capable of preventing back-off or loosening of the closure by impact or vibration during carriage; and (ii) provided with a cap seal; (f) The inner packaging shall be tested periodically at least every 5 years according to (a) and (b); (g) The complete packaging shall be visually inspected to the satisfaction of the competent authority at least every 3 years; (h) The outer and inner packaging shall bear in clearly legible and durable characters: (i) the date (month, year) of the initial test and the latest periodic test and inspection; (ii) The stamp of the expert who carried out the test and inspection; (4) Gas cylinders and gas receptacles, which shall comply with the appropriate requirements of the Table of 4.1.4.4.

P602 PACKING INSTRUCTION P602

The following packagings are authorised provided the general provisions of 4.1.1 and 4.1.3 are met: (1) Combination packagings consisting of glass inner packagings packed with absorbent material sufficient to absorb the entire contents and inert cushioning material placed in metal receptacles which are individually packed in 1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G or 4H2 outer packagings with a maximum gross mass of 50 kg. Inner packagings shall not be filled to more than 90% of their capacity. The closure of each inner packaging shall be physically held in place by any means capable of preventing back-off or loosening of the closure by impact or vibration during carriage. Inner packagings shall not exceed 1 litre in capacity; (2) Combination packagings consisting of metal inner packagings individually packed with absorbent material sufficient to absorb the entire contents and inert cushioning material in 1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G or 4H2 outer packagings with a maximum gross mass of 75 kg. Inner packagings shall not be filled to more than 90% of their capacity. The closure of each inner packaging shall be physically held in place by any means capable of preventing back-off or loosening of the closure by impact or vibration during carriage. Inner packagings shall not exceed 5 litres in capacity; (3) Drums and composite packagings (1A1, 1B1, 1N1, 1H1 or 6HA1), subject to the following conditions: (a) The hydraulic pressure test shall be conducted at a pressure of at least 0.3 MPa (gauge pressure); (b) The design and production leakproofness tests shall be conducted at a test pressure of 30 kPa; and (c) Closures shall be of a screw cap type that are: (i) physically held in place by any means capable of preventing back-off or loosening of the closure by impact or vibration during carriage; and (ii) provided with a cap seal; (4) Gas cylinders and gas receptacles with a minimum test pressure of 1 MPa (gauge pressure) conforming to the provisions of P200. No cylinder may be equipped with any pressure relief device. Gas cylinders and gas receptacles shall have their valves protected.

P620 PACKING INSTRUCTION P620

This instruction applies to UN Nos. 2814 and 2900.

The following packagings are authorized provided the special packing provisions of 4.1.8 are met:

Packagings meeting the requirements of Chapter 6.3 and approved accordingly consisting of: (a) Inner packagings comprising: (i) leakproof primary receptacle(s); (ii) a leakproof secondary packaging; (iii) other than for solid infectious substances, an absorbent material in sufficient quantity to absorb the entire contents placed between the primary receptacle(s) and the secondary packaging; if multiple primary receptacles are placed in a single secondary packaging, they shall be individually wrapped so as to prevent contact between them; (b) An outer packaging of adequate strength for its capacity, mass and intended use. The smallest external dimension shall be at least 100 mm.

Additional requirements: 1. Inner packagings containing infectious substances shall not be consolidated with inner packagings containing unrelated types of goods. Complete packages may be overpacked in accordance with the provisions of 1.2.1 and 5.1.2; such an overpack may contain dry ice. 2. Other than for exceptional consignments, e.g. whole organs which require special packaging, the following additional requirements shall apply: (a) Lyophilized substances: Primary receptacles shall be flame-sealed glass ampoules or rubber-stoppered glass vials fitted with metal seals; (b) Liquid or solid substances: (i) Substances consigned at ambient temperatures or at a higher temperature. Primary receptacles shall be of glass, metal or plastics. Positive means of ensuring a leakproof seal shall be provided, e.g. a heat seal, a skirted stopper or a metal crimp seal. If screw caps are used, they shall be reinforced with adhesive tape; (ii) Substances consigned refrigerated or frozen. Ice, dry ice or other refrigerant shall be placed around the secondary packaging(s) or alternatively in an overpack with one or more complete packages marked in accordance with 6.3.1.1. Interior supports shall be provided to secure secondary packaging(s) or packages in position after the ice or dry ice has dissipated. If ice is used, the outer packaging or overpack shall be leakproof. If dry ice is used, the outer packaging or overpack shall permit the release of carbon dioxide gas. The primary receptacle and the secondary packaging shall maintain their integrity at the temperature of the refrigerant used; (iii) Substances consigned in liquid nitrogen. Plastics primary receptacles capable of withstanding very low temperature shall be used. The secondary packaging shall also be capable of withstanding very low temperatures, and in most cases will need to be fitted over the primary receptacle individually. Provisions for the consignment of liquid nitrogen shall also be fulfilled in accordance with the requirements of P200. The primary receptacle and the secondary packaging shall maintain their integrity at the temperature of the liquid nitrogen. 3. Whatever the intended temperature of the consignment, the primary receptacle or the secondary packaging shall be capable of withstanding without leakage an internal pressure producing a pressure differential of not less than 95 kPa and temperatures in the range -40 °C to +55 °C.

P621 PACKING INSTRUCTION P621

This instruction applies to UN No. 3291.

The following packagings are authorized provided the general provisions of 4.1.1 and 4.1.3 are met: (1) Rigid, leakproof packagings meeting the requirements of Chapter 6.1 for solids, at the packing group II performance level, provided there is sufficient absorbent material to absorb the entire amount of liquid present and the packaging is capable of retaining liquids; (2) For packages containing larger quantities of liquid, rigid packagings meeting the requirements of Chapter 6.1 at the packing group II performance level for liquids.

Additional requirement: Packagings intended to contain sharp objects such as broken glass and needles shall be resistant to puncture and retain liquids under the performance test conditions in Chapter 6.1.

P650 PACKING INSTRUCTION P650

This instruction applies to diagnostic specimens

Diagnostic specimens may be carried in either: (1) Packagings that meet the following conditions: (a) The primary receptacles do not contain more than 100ml; (b) The outer packaging does not contain more than 500ml; (c) The primary receptacles are leakproof; and (d) The packagings are in accordance with P620. However, it need not be subjected to the tests; or (2) Packagings that comply with standard EN 829:1996.

| P800 PACKING INSTRUCTION P800 |  |
| --- | --- |
| This instruction applies to UN Nos. 2809 and 2803. |  |
| The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: (1) Cylinders in accordance with P200; or (2) Steel flasks or bottles with threaded closures with a capacity not exceeding 2.5 l; or (3) Combination packagings which conform to the following requirements: (a) Inner packagings shall comprise glass, metal or rigid plastics intended to contain liquids with a maximum net mass of 15 kg each; (b) The inner packagings shall be packed with sufficient cushioning material to prevent breakage; (c) Either the inner packagings or the outer packagings shall have inner liners or bags of strong leakproof and puncture-resistant material impervious to the contents and completely surrounding the contents to prevent it from escaping from the package irrespective of its position or orientation; (d) The following outer packagings and maximum net masses are authorized: |  |
| Outer packaging: | Maximum net mass |
| Drums steel (1A2) metal other than steel or aluminium (1N2) plastics (1H2) plywood (1D) fibre (1G) | 400 kg 400 kg 400 kg 400 kg 400 kg |
| Boxes steel (4A) natural wood (4C1) natural wood with sift-proof walls (4C2) plywood (4D) reconstituted wood (4F) fibreboard (4G) expanded plastics (4H1) solid plastics (4H2) | 400 kg 250 kg 250 kg 250 kg 125 kg 125 kg 60 kg 125 kg |
| Special packing provision: PP41 For UN No. 2803, when it is necessary to carry gallium at low temperatures in order to maintain it in a completely solid state, the above packagings may be overpack ed in a strong, water-resistant outer packaging which contains dry ice or other means of refrigeration. If a refrigerant is used, all of the above materials used in the packaging of gallium shall be chemically and physically resistant to the refrigerant and shall have impact resistance at the low temperatures of the refrigerant employed. If dry ice is used, the outer packaging shall permit the release of carbon dioxide gas. |  |

P801 PACKING INSTRUCTION P801

This instruction applies to new batteries assigned to UN Nos. 2794, 2795 or 3028.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: (1) Rigid outer packagings; (2) Wooden slatted crates; (3) Pallets.

Additional requirements: 1. Batteries shall be protected against short circuits. 2. Batteries stacked shall be adequately secured in tiers separated by a layer of non conductive material. 3. Battery terminals shall not support the weight of other superimposed elements. 4. Batteries shall be packaged or secured to prevent inadvertent movement. Any cushioning material used shall be inert.

P801a PACKING INSTRUCTION P801a

This instruction applies to used batteries of UN Nos. 2794, 2795 and 3028.

Stainless steel or solid plastics battery boxes of a capacity of up to 1m3 are authorized provided the following provisions are met: (a) The battery boxes shall be resistant to the corrosive substances contained in the storage batteries; (b) Under normal conditions of carriage, no corrosive substance shall leak from the battery boxes and no other substance (e.g. water) shall enter the battery boxes. No dangerous residues of corrosive substances contained in the storage batteries shall adhere to the outside of the battery boxes; (c) The battery boxes shall not be loaded with storage batteries to a height greater than the height of their sides; (d) No storage battery containing substances or other dangerous goods which may react dangerously with one another shall be placed in a battery box; (e) The battery boxes shall be either: (i) covered; or (ii) carried in closed or sheeted vehicles or containers.

P802 PACKING INSTRUCTION P802

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: (1) Combination packagings: Outer packagings: 1A2, 1B2, 1N2, 1H2, 1D, 4A, 4B, 4C1, 4C2, 4D, 4F, or 4H2; maximum net mass: 75 kg. Inner packagings: glass or plastics; maximum capacity: 10 litres; (2) Combination packagings: Outer packagings: 1A2, 1B2, 1N2, 1H2, 1D, 1G, 4A, 4B, 4C1, 4C2, 4D, 4F, 4G or 4H2; maximum net mass: 125 kg. Inner packagings: metal; maximum capacity: 40 litres; (3) Composite packagings: Glass receptacle with outer steel, aluminium, plywood or solid plastics drum (6PA1, 6PB1, 6PD1, or 6PH2) or with outer steel or aluminium crate or box or with outer wooden box or with outer wickerwork hamper (6PA2, 6PB2, 6PC or 6PD2); maximum capacity: 60 litres; (4) Austenitic steel drums (1A1) with a maximum capacity of 250 litres; (5) Gas cylinders conforming to the construction, testing and filling requirements approved by the competent authority.

P803 PACKING INSTRUCTION P803

This instruction applies to UN No. 2028.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: (1) Drums (1A2, 1B2, 1N2, 1H2, 1D, 1G); (2) Boxes ( 4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H2). Maximum net mass: 75kg. The articles shall be individually packaged and separated from each other using partitions, dividers, inner packagings or cushioning material to prevent inadvertent discharge during normal conditions of carriage.

P900 PACKING INSTRUCTION P900

(Reserved)

P901 PACKING INSTRUCTION P901

This instruction applies to UN No. 3316.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: Packagings conforming to the performance level consistent with the packing group assigned to the kit as a whole (see 3.3.1, special provision 251). Maximum quantity of dangerous goods per outer packaging: 10 kg.

Additional requirement: Dangerous goods in kits shall be packed in inner packagings which shall not exceed either 250 ml or 250 g and shall be protected from other materials in the kit.

P902 PACKING INSTRUCTION P902

This instruction applies to UN No. 3268.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: Packagings conforming to the packing group III performance level. Each packaging shall conform to special provision 235 (see 3.3.1) and shall conform to the packing group III performance level. The packaging shall be designed and constructed to prevent movement of the articles and inadvertent discharge during normal conditions of carriage. The articles may also be carried unpackaged in dedicated handling devices, vehicles or containers when moved from where they are manufactured to an assembly plant.

P903 PACKING INSTRUCTION P903

This instruction applies to UN Nos. 3090 and 3091.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: Packagings conforming to the packing group II performance level. When lithium cells and batteries are packed with equipment, they shall be packed in inner fibreboard packagings that meet the requirements for packing group II. When lithium cells and batteries included in Class 9 are contained in equipment, the equipment shall be packed in strong outer packagings in such a manner as to prevent accidental operation during carriage.

Additional requirement: Batteries shall be protected against short circuit.

P903a PACKING INSTRUCTION P903a

This instruction applies to used cells and batteries of UN Nos. 3090 and 3091.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: Packagings conforming to the packing group II performance level. Non-approved packagings shall, however, be permitted provided that: - they meet the general provisions of 4.1.1 and 4.1.3; - the cells and batteries are packed and stowed so as to prevent any risk of short circuits; - the packages weigh not more than 30 kg.

Additional requirement: Batteries shall be protected against short circuit.

P904 PACKING INSTRUCTION P904

This instruction applies to UN No. 3245.

The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: (1) Packagings according to P001 or P002; (2) Outer packagings, which need not conform to the packaging test requirements of Part 6, but conforming to the following: (a) An inner packaging comprising: (i) a watertight primary receptacle(s); (ii) a watertight secondary packaging which is leakproof; (iii) absorbent material in sufficient quantity to absorb the entire contents placed between the primary receptacle(s) and the secondary packaging; if several primary receptacles are placed in a single secondary packaging, they shall be individually wrapped so as to prevent contact between them; (b) An outer packaging of adequate strength for its capacity, mass and intended use, and with a minimum external dimension of 100mm; (3) For substances consigned in liquid nitrogen: Plastics primary receptacles capable of withstanding very low temperatures shall be used. The secondary packaging shall also be capable of withstanding very low temperatures, and in most cases will need to be fitted over the primary receptacle individually. Provisions for the consignment of liquid nitrogen shall also be fulfilled in accordance with the requirements of P200. The primary receptacle and the secondary packaging shall maintain their integrity at the temperature of the liquid nitrogen.

P905 PACKING INSTRUCTION P905

This instruction applies to UN Nos. 3072 and 2990.

Any suitable packaging is authorized, provided the general provisions of 4.1.1 and 4.1.3 are met, except that packagings need not conform to the requirements of Part 6. When the life saving appliances are constructed to incorporate or are contained in rigid outer weatherproof casings (such as for lifeboats), they may be carried unpackaged.

Additional requirements: 1. All dangerous substances and articles contained as equipment within the appliances shall be secured to prevent inadvertent movement and in addition: (a) Signal devices of Class 1 shall be packed in plastics or fibreboard inner packagings; (b) Gases shall be contained in cylinders as specified by the competent authority, which may be connected to the appliance; (c) Electric storage batteries (Class 8) and lithium batteries (Class 9) shall be disconnected or electrically isolated and secured to prevent any spillage of liquid; and (d) Small quantities of other dangerous substances (for example in Classes 3, 4.1 and 5.2) shall be packed in strong inner packagings. 2. Preparation for transport and packaging shall include provisions to prevent any accidental inflation of the appliance.

| P906 PACKING INSTRUCTION P906 |
| --- |
| This instruction applies to UN Nos. 2315, 3151 and 3152. |
| The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 are met: (1) For liquids and solids containing or contaminated with PCBs: Packagings in accordance with P001 or P002, as appropriate; (2) For transformers and condensers and other devices: Leakproof packagings which are capable of containing, in addition to the devices, at least 1.25 times the volume of the liquid PCBs present in them. There shall be sufficient absorbent material in the packagings to absorb at least 1.1 times the volume of liquid which is contained in the devices. In general, transformers and condensers shall be carried in leakproof metal packagings which are capable of holding, in addition to the transformers and condensers, at least 1.25 times the volume of the liquid present in them. Notwithstanding the above, liquids and solids not packaged in accordance with P001 and P002 and unpackaged transformers and condensers may be carried in cargo transport units fitted with a leakproof metal tray to a height of at least 800mm, containing sufficient inert absorbent material to absorb at least 1.1 times the volume of any free liquid. |
| Additional requirement: Adequate provisions shall be taken to seal the transformers and condensers to prevent leakage during normal conditions of carriage. |
| R001 PACKING INSTRUCTION R001 |  |  |  |
| The following packagings are authorized provided the general provisions of 4.1.1 and 4.1.3 are met: |  |  |  |
| Light gauge metal packagings | Maximum capacity/maximum net mass |  |  |
|  | Packing group I | Packing group II | Packing group III |
| non-removable head (0A1) | Not allowed | 40l/50kg | 40l/50kg |
| removable head (0A2)*/ | Not allowed | 40l/50kg | 40l/50kg |
| */ not allowed for UN No. 1261 NITROMETHANE |  |  |  |
| NOTE 1: This instruction applies to solids and liquids (provided the design type is tested and marked appropriately). NOTE 2: For Class 3, packing group II, these packagings may be used only for substances with no subsidiary risk and a vapour pressure of not more than 110 kPa at 50 °C and for slightly toxic pesticides. |  |  |  |
| Special packing provision: RR03 For UN Nos. 1204 and 3256, light gauge metal packagings are not permitted. |  |  |  |

4.1.4.2	Packing instructions concerning the use of IBCs

IBC01 PACKING INSTRUCTION IBC01

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: Metal (31A, 31B and 31N).

Additional requirement: Only liquids with a vapour pressure less than or equal to 110 kPa at 50 °C, or 130 kPa at 55 °C, are authorized.

Special packing provision: B12 For UN No. 3130, the openings of receptacles for this substance shall be tightly closed by means of two devices in series, one of which shall be screwed or secured in an equivalent manner.

IBC02 PACKING INSTRUCTION IBC02

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: (1) Metal (31A, 31B and 31N); (2) Rigid plastics (31H1 and 31H2); (3) Composite (31HZ1).

Additional requirement: Only liquids with a vapour pressure less than or equal to 110 kPa at 50 °C, or 130 kPa at 55 °C, are authorized.

Special packing provisions: B5 For UN Nos. 1791, 2014 and 3149, IBCs shall be provided with a device to allow venting during carriage. The inlet to the venting device shall be sited in the vapour space of the IBC under maximum filling conditions during carriage. B7 For UN Nos. 1222 and 1865, IBCs with a capacity greater than 450 litres are not permitted due to the substance’s potential for explosion when carried in large volumes. B8 The pure form of this substance shall not be transported in IBCs since it is known to have a vapour pressure of more than 110 kPa at 50 °C or 130 kPa at 55 °C. B11 Bottom openings are permitted provided they are fitted with two closure devices in series.

IBC03 PACKING INSTRUCTION IBC03

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: (1) Metal (31A, 31B and 31N); (2) Rigid plastics (31H1 and 31H2); (3) Composite (31HZ1, 31HA2, 31HB2, 31HN2, 31HD2 and 31HH2).

Additional requirement: Only liquids with a vapour pressure less than or equal to 110 kPa at 50 °C, or 130 kPa at 55 °C, are authorized.

Special packing provision: B8 The pure form of this substance shall not be carried in IBCs since it is known to have a vapour pressure of more than 110 kPa at 50 °C or 130 kPa at 55 °C.

IBC04 PACKING INSTRUCTION IBC04

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: Metal (11A, 11B, 11N, 21A, 21B, 21N, 31A, 31B and 31N).

Special packing provision: B1 For packing group I substances, IBCs shall be carried in closed vehicles or containers.

IBC05 PACKING INSTRUCTION IBC05

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: (1) Metal (11A, 11B, 11N, 21A, 21B, 21N, 31A, 31B and 31N); (2) Rigid plastics (11H1, 11H2, 21H1, 21H2, 31H1 and 31H2); (3) Composite (11HZ1, 21HZ1 and 31HZ1).

Special packing provision: B1 For packing group I substances, IBCs shall be carried in closed vehicles or containers. B2 For packing group II solid substances, IBCs other than metal or rigid plastics IBCs shall be carried in closed vehicles or containers.

IBC06 PACKING INSTRUCTION IBC06

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: (1) Metal (11A, 11B, 11N, 21A, 21B, 21N, 31A, 31B and 31N); (2) Rigid plastics (11H1, 11H2, 21H1, 21H2, 31H1 and 31H2); (3) Composite (11HZ1, 11HZ2, 21HZ1, 21HZ2, 31HZ1 and 31HZ2).

Additional requirement: Composite IBCs 11HZ2, 21HZ2 and 31HZ2 shall not be used when the substances being carried may become liquid during carriage.

Special packing provisions: B1 For packing group I substances, IBCs shall be transported in closed vehicles or containers. B2 For packing group II solid substances, IBCs other than metal or rigid plastics IBCs shall be carried in closed vehicles or containers.

IBC07 PACKING INSTRUCTION IBC07

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: (1) Metal (11A, 11B, 11N, 21A, 21B, 21N, 31A, 31B and 31N); (2) Rigid plastics (11H1, 11H2, 21H1, 21H2, 31H1 and 31H2); (3) Composite (11HZ1, 11HZ2, 21HZ1, 21HZ2, 31HZ1 and 31HZ2); (4) Wooden (11C, 11D and 11F).

Additional requirement: Liners of wooden IBCs shall be sift-proof.

Special packing provisions: B1 For packing group I substances, IBCs shall be carried in closed vehicles or containers. B2 For packing group II solid substances, IBCs other than metal or rigid plastics IBCs shall be carried in closed vehicles or containers.

IBC08 PACKING INSTRUCTION IBC08

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: (1) Metal (11A, 11B, 11N, 21A, 21B, 21N, 31A, 31B and 31N); (2) Rigid plastics (11H1, 11H2, 21H1, 21H2, 31H1 and 31H2); (3) Composite (11HZ1, 11HZ2, 21HZ1, 21HZ2, 31HZ1 and 31HZ2); (4) Fibreboard (11G); (5) Wooden (11C, 11D and 11F); (6) Flexible (13H1, 13H2, 13H3, 13H4, 13H5, 13L1, 13L2, 13L3, 13L4, 13M1 or 13M2).

Special packing provisions: B2 For packing group II solid substances, IBCs other than metal or rigid plastics IBCs shall be carried in closed vehicles or containers. B3 Flexible IBCs shall be sift-proof and water-resistant or shall be fitted with a sift-proof and water-restistant liner. B4 Flexible, fibreboard or wooden IBCs shall be sift-proof and water-resistant or shall be fitted with a sift-proof and water-resistant liner. B6 For UN Nos. 1363, 1364, 1365, 1386, 1841, 2211, 2217, 2793 and 3314, IBCs are not required to meet the IBC testing requirements of Chapter 6.5.

IBC99 PACKING INSTRUCTION IBC99

Only IBCs which are approved by the competent authority may be used.

IBC100 PACKING INSTRUCTION IBC100

This instruction applies to UN Nos. 0082, 0241, 0331 and 0332.

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 and special provisions of 4.1.5 are met: (1) Metal (11A, 11B, 11N, 21A, 21B, 21N, 31A, 31B and 31N); (2) Flexible (13H2, 13H3, 13H4, 13L2, 13L3, 13L4 and 13M2); (3) Rigid plastics (11H1, 11H2, 21H1, 21H2, 31H1 and 31H2); (4) Composite (11HZ1, 11HZ2, 21HZ1, 21HZ2, 31HZ1 and 31HZ2).

Additional requirements: 1. IBCs shall only be used for free flowing substances. 2. Flexible IBCs shall only be used for solids.

Special packing provisions: B9 For UN No. 0082, this packing instruction may only be used when the substances are mixtures of ammonium nitrate or other inorganic nitrates with other combustible substances which are not explosive ingredients. Such explosives shall not contain nitroglycerin, similar liquid organic nitrates, or chlorates. Metal IBCs are not authorized. B10 For UN No. 0241, this packing instruction may only be used for substances which consist of water as an essential ingredient and high proportions of ammonium nitrate or other oxidizing substances some or all of which are in solution. The other constituents may include hydrocarbons or aluminium powder, but shall not include nitro-derivatives such as trinitrotoluene. Metal IBCs are not authorized.

| IBC 520 PACKING INSTRUCTION IBC520 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| This instruction applies to organic peroxides and self-reactive substances of type F. |  |  |  |  |  |
| The IBCs listed below are authorized for the formulations listed, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 and special provisions of 4.1.7.2 are met. For formulations not listed below, only IBCs which are approved by the competent authority may be used (see 4.1.7.2.2). |  |  |  |  |  |
| UN No. | Organic peroxide | Type of IBC | Maximum quantity (litres) | Control temper- ature | Emer- gency temper- ature |
| 3109 | ORGANIC PEROXIDE, TYPE F, LIQUID tert-Butyl hydroperoxide, not more than 72% with water | 31A | 1250 |  |  |
|  | tert-Butyl peroxyacetate, not more than 32% in diluent type A | 31A 31HA1 | 1250 1000 |  |  |
|  | tert-Butyl peroxy-3,5,5-trimethylhexanoate, not more than 32% in diluent type A | 31A 31HA1 | 1250 1000 |  |  |
|  | Cumyl hydroperoxide, not more than 90% in diluent type A | 31HA1 | 1250 |  |  |
|  | Dibenzoyl peroxide, not more than 42% as a stable dispersion in water | 31H1 | 1000 |  |  |
|  | Di-tert-butyl peroxide, not more than 52% in diluent type A | 31A 31HA1 | 1250 1000 |  |  |
|  | 1,1-Di-(tert-butylperoxy) cyclohexane, not more than 42% in diluent type A | 31H1 | 1000 |  |  |
|  | Dilauroyl peroxide, not more than 42%, stable dispersion, in water | 31HA1 | 1000 |  |  |
|  | Isopropyl cumyl hydroperoxide, not more than 72% in diluent type A | 31HA1 | 1250 |  |  |
|  | p-Menthyl hydroperoxide, not more than 72% in diluent type A | 31HA1 | 1250 |  |  |
|  | Peroxyacetic acid, stabilized, not more than 17% | 31H1 31HA1 31A | 1500 1500 1500 |  |  |
| IBC 520 (cont’d) PACKING INSTRUCTION IBC520 |  |  |  |  |  |
| 3119 | ORGANIC PEROXIDE, TYPE F, LIQUID, TEMPERATURE CONTROLLED tert-Butyl peroxy-2-ethylhexanoate, not more than 32% in diluent type B | 31HA1 31A | 1000 1250 | +30 °C +30 °C | +35 °C +35 °C |
|  | tert-Butyl peroxyneodecanoate, not more than 32% in diluent type A stable dispersion, in water | 31A | 1250 | 0 °C | +10 °C |
|  | tert-Butyl peroxyneodecanoate, not more than 42% stable dispersion, in water | 31A | 1250 | - 5 °C | +5 °C |
|  | tert-Butyl peroxypivalate, not more than 27% in diluent type B | 31HA1 31A | 1000 1250 | +10 °C +10 °C | +15 °C +15 °C |
|  | Cumyl peroxyneodecanoate, not more than 52%, stable dispersion, in water | 31A | 1250 | - 15 °C | - 5 °C |
|  | Di-(4-tert-butylcyclohexyl) peroxydicarbonate, not more than 42%, stable dispersion, in water | 31HA1 | 1000 | +30 °C | +35 °C |
|  | Dicetyl peroxydicarbonate, not more than 42%, stable dispersion, in water | 31HA1 | 1000 | +30 °C | +35 °C |
|  | Di-(2-ethylhexyl) peroxydicarbonate, not more than 52%, stable dispersion, in water | 31A | 1250 | - 20 °C | - 10 °C |
|  | Dimyristyl peroxydicarbonate, not more than 42%, stable dispersion, in water | 31HA1 | 1000 | +15 °C | +20 °C |
|  | Di-(3,5,5-trimethylhexanoyl) peroxide, not more than 38% in diluent type A | 31HA1 31A | 1000 1250 | +10 °C +10 °C | +15 °C +15 °C |
|  | Di-(3,5,5-trimethylhexanoyl) peroxide, not more than 52%, stable dispersion, in water | 31A | 1250 | +10 °C | +15 °C |
|  | 1,1,3,3-Tetramethylbutyl peroxyneodecanoate, not more than 52%, stable dispersion, in water | 31A | 1250 | - 5 °C | + 5 °C |
| Additional requirements: 1. IBCs shall be provided with a device to allow venting during carriage. The inlet to the pressure-relief device shall be sited in the vapour space of the IBC under maximum filling conditions during carriage. 2. To prevent explosive rupture of metal IBCs or composite IBCs with complete metal casing, the emergency-relief devices shall be designed to vent all the decomposition products and vapours evolved during self-accelerating decomposition or during a period of not less than one hour of fire-engulfment as calculated by the formula in 4.2.1.13.8. The control and emergency temperatures specified in this packing instruction are based on a non-insulated IBC. When consigning an organic peroxide in an IBC in accordance with this instruction, it is the responsibility of the consignor to ensure that: (a) the pressure and emergency relief devices installed on the IBC are designed to take appropriate account of the self-accelerating decomposition of the organic peroxide and of fire-engulfment; and (b) when applicable, the control and emergency temperatures indicated are appropriate, taking into account the design (e.g. insulation) of the IBC to be used. |  |  |  |  |  |

IBC620 PACKING INSTRUCTION IBC620

This instruction applies to UN No. 3291.

The following IBCs are authorized, provided the general provisions of 4.1.1, 4.1.2 and 4.1.3 are met: Rigid, leakproof IBCs conforming to the packing group II performance level.

Additional requirements: 1. There shall be sufficient absorbent material to absorb the entire amount of liquid present in the IBC. 2. IBCs shall be capable of retaining liquids. 3. IBCs intended to contain sharp objects such as broken glass and needles shall be resistant to puncture.

4.1.4.3	Packing instructions concerning the use of large packagings

| LP01 PACKING INSTRUCTION (LIQUIDS) LP01 |
| --- |
| The following large packagings are authorized provided the general provision of 4.1.1 and 4.1.3 are met: |
| Inner packagings | Large outer packagings | Packing group I | Packing group II | Packing group III |
| Glass 10 litre Plastics 30 litre Metal 40 litre | Steel (50A) Aluminium (50B) Metal other than steel or aluminium (50N) Rigid plastics (50H) Natural wood (50C) Plywood (50D) Reconstituted wood (50F) Fibreboard (50G) | Not allowed | Not allowed | Maximum capacity: 3 m3 |

| LP02 PACKING INSTRUCTION (SOLIDS) LP02 |  |  |  |  |
| --- | --- | --- | --- | --- |
| The following large packagings are authorized provided the general provisions of 4.1.1 and 4.1.3 are met: |  |  |  |  |
| Inner packagings | Large outer packagings | Packing group I | Packing group II | Packing group III |
| Glass 10kg Plastics 2/ 50kg Metal 50 kg Paper 1/ 2/ 50 kg Fibre 1/ 2/ 50 kg | Steel (50A) Aluminium (50B) Metal other than steel or aluminium (50N) Rigid plastics (50H) Natural wood (50C) Plywood (50D) Reconstituted wood (50F) Fibreboard (50G) | Not allowed | Not allowed | Maximum capacity: 3 m3 |
| 1/ These inner packagings shall not be used when the substances being carried may become liquid during carriage. 2/ These inner packagings shall be sift-proof. |  |  |  |  |

LP99 PACKING INSTRUCTION LP99

Only large packagings which are approved by the Competent Authority may be used (see 4.1.3.7).

| LP101 PACKING INSTRUCTION LP101 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 and special provisions of 4.1.5 are met: |  |  |
| Inner packagings | Intermediate packagings | Large packagings |
| Not necessary | Not necessary | Steel (50A) Aluminium (50B) Metal other than steel or aluminium (50N) Rigid plastics (50H) Natural wood (50C) Plywood (50D) Reconstituted wood (50F) Fibreboard (50G) |
| Special packing provision: L1 For UN Nos. 0006, 0009, 0010, 0015, 0016, 0018, 0019, 0034, 0035, 0038, 0039, 0048, 0056, 0137, 0138, 0168, 0169, 0171, 0181, 0182, 0183, 0186, 0221, 0243, 0244, 0245, 0246, 0254, 0280, 0281, 0286, 0287, 0297, 0299, 0300, 0301, 0303, 0321, 0328, 0329, 0344, 0345, 0346, 0347, 0362, 0363, 0370, 0412, 0424, 0425, 0434, 0435, 0436, 0437, 0438, 0451, 0488 and 0502: Large and robust explosives articles, normally intended for military use, without their means of initiation or with their means of initiation containing at least two effective protective features, may be carried unpackaged. When such articles have propelling charges or are self-propelled, their ignition systems shall be protected against stimuli encountered during normal conditions of carriage. A negative result in Test Series 4 on an unpackaged article indicates that the article can be considered for carriage unpackaged. Such unpackaged articles may be fixed to cradles or contained in crates or other suitable handling devices. |

| LP102 PACKING INSTRUCTION LP102 |  |  |
| --- | --- | --- |
| The following packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 and special provisions of 4.1.5 are met: |  |  |
| Inner packagings | Intermediate packagings | Outer packagings |
| Bags water resistant Receptacles fibreboard metal plastics wood Sheets fibreboard, corrugated Tubes fibreboard | Not necessary | Steel (50A) Aluminium (50B) Metal other than steel or aluminium (50N) Rigid plastics (50H) Natural wood (50C) Plywood (50D) Reconstituted wood (50F) Fibreboard (50G) |
| LP621 PACKING INSTRUCTION LP621 |
| This instruction applies to UN No. 3291. |
| The following large packagings are authorized, provided the general provisions of 4.1.1 and 4.1.3 and the special provisions of 4.1.8 are met: (1) For clinical waste placed in inner packagings: Rigid, leakproof large packagings conforming to the requirements of Chapter 6.6 for solids, at the packing group II performance level, provided there is sufficient absorbent material to absorb the entire amount of liquid present and the large packaging is capable of retaining liquids; (2) For packages containing larger quantities of liquid: Large rigid packagings conforming to the requirements of Chapter 6.6, at the packing group II performance level, for liquids. |
| Additional requirement: Large packagings intended to contain sharp objects such as broken glass and needles shall be resistant to puncture and retain liquids under the performance test conditions in Chapter 6.6. |

4.1.4.4	 	Particular requirements applicable to gas cylinders and gas receptacles

When gas cylinders or gas receptacles are used as packaging for substances assigned to packing instructions P400, P401, P402 or P601, they shall be constructed, tested, filled and marked according to the corresponding requirements (PR1 to PR6) as mentioned in the table below for each UN number.

TABLE

LIST OF PARTICULAR REQUIREMENTS (PR)

FOR GAS CYLINDERS AND RECEPTACLES

| Pressure receptacle requirements | UN Nos. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR1 | 1366 1370 1380 1389 1391 1411 1421 1928 2003 2445 2845 2870 3049 3050 3051 3052 3053 3076 3129 3130 3148 3194 3203 3207 3254 | The substances classified under these UN numbers shall be packed in hermetically closing metal receptacles which are not affected by the contents and have a capacity of not more than 450 litres. The receptacles shall be subjected to the initial test and periodic tests every five years at a pressure of not less than 1MPa (10 bar) (gauge pressure). The receptacles shall not be filled to more than 90% of their capacity; however, a space of at least 5% shall remain empty for safety when the liquid is at an average temperature of 50 °C. During carriage, the liquid shall be under a layer of inert gas the gauge pressure of which shall be not less than 50 kPa (0.5 bar). The receptacles shall carry a data plate with the following particulars entered in a durable form: - substance or substances 1/ accepted for carriage; - tare 2/ of the receptacle, including accessories; - test pressure 2/ (gauge pressure); - date (month, year) of the last test undergone; - stamp of the expert who carried out the test; - capacity 2/ of the receptacle; - maximum mass of filling allowed 2/ |

| Pressure receptacle requirements | UN Nos. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR2 | 1183 1242 1295 2988 | The substances classified under these UN number shall be packed in corrosion-resistant steel receptacles with a maximum capacity of 450 litres. The closing device of the receptacle shall be protected by a cap. The receptacles shall be subjected to the initial test and periodic tests every five years at a pressure of not less than 0.4 MPa (4 bar) (gauge pressure). The maximum permissible mass of filling per litre of capacity for trichlorosilane, ethyldichlorosilane and methyldichlorosilane shall not exceed 1.14 kg, 0.93 kg or 0.95 kg respectively, if the filling is carried out by mass; if the filling is by volume, the degree of filling shall not exceed 85%. The receptacles shall also carry a plate showing the following particulars in a durable form: - description of the substance(s) accepted for carriage, or for chlorosilanes : « chlorosilanes, Class 4.3 »; - tare 2/ of the receptacle, including accessories; - test pressure 2/ (gauge pressure); - date (month, year) of the last test undergone; - stamp of the expert who carried out the test; - capacity 2/ of the receptacle; - maximum degree of filling allowed by mass 2/ for each substance accepted for carriage. |

| Pressure receptacle requirements | UN Nos. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR3 | 1092 1251 1259 1605 1613 1994 3294 | The substances classified under these UN numbers shall be packed in metal receptacles fitted with completely leakproof closing devices which shall, if necessary, be secured against mechanical damage by protective caps. Steel receptacles of a capacity not exceeding 150 litres shall have a minimum wall thickness of 3 mm, and larger steel receptacles and receptacles made of other materials shall have walls at least thick enough to guarantee equivalent mechanical strength. The maximum capacity of receptacles permitted shall be 250 litres. The mass of the contents shall be not more than 1 kg of liquid per litre of capacity. Before being used for the first time, the receptacles shall undergo a hydraulic pressure test at a pressure of not less than 1 MPa (10 bar) (gauge pressure). The pressure test shall be repeated every five years and shall include a meticulous inspection of the inside of the receptacle and a check of the tare. The receptacles shall bear the following particulars in clearly legible and durable characters: - substance or substances 1/ accepted for carriage; - the name of the owner of the receptacle; - the tare 2/ of the receptacle, including such fittings and accessories as valves, protective caps, etc; - the date (month, year) of the initial test and of the most recent test, and the stamp of the expert who carried out the test; - the maximum permissible mass of the contents of the receptacle in kg; - the internal pressure (test pressure) to be applied in the hydraulic pressure test. |

| Pressure receptacle requirements | UN Nos. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR4 | 1185 | The substances classified under this UN number shall be packed in steel receptacles of sufficient thickness, which shall be closed by a screw-threaded bung and a screw-threaded protective cap or equivalent device leakproof both to liquid and to vapour. The receptacles shall initially and periodically, at least every five years, be tested at a pressure of at least 1 MPa (10 bar) (gauge pressure) in accordance with 6.2.1.5 and 6.2.1.6. The mass of the contents shall not exceed 0.67 kg per litre of capacity. A package shall not weigh more than 75 kg. Receptacles shall bear, in clearly legible and durable characters: - the name or mark of the manufacturer and the number of the receptacle; - the word "ethyleneimine"; - the tare 2/ of the receptacle and its maximum permitted mass 2/ when filled; - the date (month and year) of the initial test and of the most recent test undergone; - the stamp of the expert who carried out the tests and examinations. |

| Pressure receptacle requirements | UN Nos. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR5 | 2480 2481 | The substances classified under this UN number shall be packed in receptacles made of pure aluminium having a wall thickness of not less than 5 mm or in receptacles of stainless steel. The receptacles shall be fully welded. They shall initially and periodically, at least every five years, be tested at a pressure of at least 0.5 MPa (5 bar) (gauge pressure) in accordance with 6.2.1.5 and 6.2.1.6. They shall be so closed as to be leakproof by means of two closures one above the other, one of which shall be screw-threaded or secured in an equally effective manner. The degree of filling shall be not more than 90 %. Drums weighing more than 100 kg shall be fitted with rolling hoops or stiffening ribs. The receptacles shall bear, in clearly legible and durable characters: - the name or mark of the manufacturer and the number of the receptacle; - substance or substances 1/ accepted for carriage; - the tare 2/ of the receptacle and its maximum permitted mass when filled; - the date (month and year) of the initial test and of the most recent test undergone; - the stamp of the expert who carried out the tests and examinations. |

| Pressure receptacle requirements | UN No. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR6 | 1744 | Bromine containing less than 0.005% water, or between 0.005% and 0.2% water, provided that in the latter case measures are taken to prevent corrosion of the lining of the receptacles, may be carried in receptacles satisfying the following conditions: (a) The receptacles shall be made of steel and be equipped with a leakproof lining made of lead or of some other material affording equivalent protection and with a hermetic closure; receptacles made of monel metal or nickel, or with a nickel lining, shall also be permitted; (b) The capacity of the receptacles shall not exceed 450 litres; (c) The receptacles shall not be filled to more than 92% of their capacity or more than 2.86 kg per litre of capacity; (d) The receptacles shall be welded and designed for a calculation pressure of not less than 2.1 MPa (21 bar) gauge pressure. The materials and workmanship shall in other respects meet the relevant requirements of Chapter 6.2. The initial test of unlined steel receptacles shall be subject to the requirements of 6.2.1.5; (e) The closures shall project as little as possible from the receptacle and be fitted with protective caps. The closures and caps shall be fitted with gaskets made of a material not capable of being attacked by bromine. The closures shall be in the upper part of the receptacles in such a manner that they can in no case be in permanent contact with the liquid phase; (f) The receptacles shall be provided with fittings enabling them to stand stably upright, and with lifting attachments (rings, flanges, etc.) at the top, which shall be tested at twice the working load. Before being put into service, the receptacles shall be subjected to a leakproofness test at a pressure of at least 200 kPa (2 bar) gauge pressure. |

.

| Pressure receptacle requirements | UN No. | Applicable construction, testing, filling and marking requirements |
| --- | --- | --- |
| PR6 (cont'd) |  | The leakproofness test shall be repeated every two years and shall be accompanied by an internal inspection of the receptacle and a check of its tare 2/. The test and the inspection shall be carried out under the supervision of an expert approved by the competent authority. The receptacles shall bear, in clearly legible and durable characters: - the name of the manufacturer or the manufacturing mark and the number of the receptacle, - the word "Bromine", - tare 2/ mass of the receptacle and the permissible maximum mass 2/ of the filled receptacle, - date (month, year) of the initial test and of the latest periodical test, - stamp of the expert who carried out the tests and inspections. |

______________________________________

1/	The name may be replaced by a generic description covering substances of a similar nature and also compatible with the characteristics of the receptacle.

2/	The units of measurement to be added each time after the numerical values.

4.1.5	Special packing provisions for goods of Class 1

4.1.5.1	The general provisions of section 4.1.1 shall be met.

4.1.5.2	All packagings for Class 1 goods shall be so designed and constructed that:

(a)	They will protect the explosives, prevent them escaping and cause no increase in the risk of unintended ignition or initiation when subjected to normal conditions of carriage including foreseeable changes in temperature, humidity and pressure;

(b)	The complete package can be handled safely in normal conditions of carriage; and

(c)	The packages will withstand any loading imposed on them by foreseeable stacking to which they will be subject during carriage so that they do not add to the risk presented by the explosives, the containment function of the packagings is not harmed, and they are not distorted in a way or to an extent which will reduce their strength or cause instability of a stack.

4.1.5.3	All explosive substances and articles, as prepared for carriage, shall have been classified in

accordance with the procedures detailed in 2.2.1.

4.1.5.4	Class 1 goods shall be packed in accordance with the appropriate packing instruction shown in

Column 8 of the Dangerous Goods List, as detailed in 4.1.4.

4.1.5.5	Packagings, including IBCs and large packagings shall conform to the requirements of

Chapter 6.1, 6.5 or 6.6, respectively, and shall meet the test requirements of 6.1.5, 6.5.4 or 6.6.5,

respectively, for Packing Group II, subject to 4.1.1.13, 6.1.2.4 and 6.5.1.4.4. Packagings other than

metal packagings meeting the test criteria of Packing Group I may be used. To avoid unnecessary

confinement, metal packagings of Packing Group I shall not be used.

4.1.5.6	The closure device of packagings containing liquid explosives shall ensure a double

protection against leakage.

4.1.5.7	The closure device of metal drums shall include a suitable gasket; if a closure device includes

a screw-thread, the ingress of explosive substances into the screw-thread shall be prevented.

4.1.5.8	Packagings for water soluble substances shall be water resistant. Packagings for desensitized

or phlegmatized substances shall be closed to prevent changes in concentration during carriage.

4.1.5.9	When the packaging includes a double envelope filled with water which may freeze during

transport, a sufficient quantity of an anti-freeze agent shall be added to the water to prevent freezing.

Anti-freeze that could create a fire hazard because of its inherent flammability shall not be used.

4.1.5.10	Nails, staples and other closure devices made of metal without protective covering shall not

penetrate to the inside of the outer packaging unless the inner packaging adequately protects the

explosives against contact with the metal.

4.1.5.11	Inner packagings, fittings and cushioning materials and the placing of explosive substances or

articles in packages shall be accomplished in a manner which prevents the explosive substances or

articles  from becoming loose in the outer packaging under normal conditions of carriage. Metallic components of articles shall be prevented from making contact with metal packagings. Articles containing explosive substances not enclosed in an outer casing shall be separated from each other in order to prevent friction and impact. Padding, trays, partitioning in the inner or outer packaging, mouldings or receptacles may be used for this purpose.

4.1.5.12	Packagings shall be made of materials compatible with, and impermeable to, the explosives

contained in the package, so that neither interaction between the explosives and the packaging materials, nor leakage, causes the explosive to become unsafe to carriage, or the hazard division or compatibility group to change.

4.1.5.13	The ingress of explosive substances into the recesses of seamed metal packagings shall be

prevented.

4.1.5.14	Plastics packagings shall not be liable to generate or accumulate sufficient static electricity so

that a discharge could cause the packaged explosive substances or articles to initiate, ignite or function.

4.1.5.15	Large and robust explosives articles, normally intended for military use, without their means

of initiation or with their means of initiation containing at least two effective protective features, may

be carried unpackaged. When such articles have propelling charges or are self-propelled, their ignition

systems shall be protected against stimuli encountered during normal conditions of carriage. A negative result in Test Series 4 on an unpackaged article indicates that the article can be considered for carriage unpackaged. Such unpackaged articles may be fixed to cradles or contained in crates or other suitable handling, storage or launching devices in such a way that they will not become loose during normal conditions of carriage.

Where such large explosive articles are as part of their operational safety and  suitability tests subjected

to test regimes that meet the intentions of ADR and such tests have been successfully undertaken, the

competent authority may approve such articles to be carried under these Regulations.

4.1.5.16	Explosive substances shall not be packed in inner or outer packagings where the differences

in internal and external pressures, due to thermal or other effects, could cause an explosion or rupture

of the package.

4.1.5.17	Whenever loose explosive substances or the explosive substance of an uncased or partly cased

article may come into contact with the inner surface of metal packagings (1A2, 1B2, 4A, 4B and metal

receptacles), the metal packaging shall be provided with an inner liner or coating (see 4.1.1.2).

4.1.5.18	Packing instruction P101 may be used for any explosive provided the packaging has been

approved by a competent authority regardless of whether the packaging complies with the packing

instruction assignment in column 8 of Table A of Chapter 3.2.

4.1.6	Special packing provisions for goods of Class 2

4.1.6.1  	Receptacles, including their closures, shall be selected to contain a gas or a mixture of gases according to the requirements of 6.2.1.2 "Materials of receptacles" and the requirements of the relevant packing instructions of 4.1.4.

4.1.6.2  	A change of use of a refillable receptacle shall include emptying, purging and evacuation operations to the extent necessary for safe operation (see also table of standards at the end of this section).

NOTE 1: Refillable receptacles for the transport of gases of Class 2 shall be periodically inspected according to the periodicity set out in the relevant packing instructions (P200 or P203) and according to the provisions detailed in 6.2.1.6 “Periodic inspection”.

2:. Receptacles ready for shipment shall be marked and labelled according to the provisions set out in chapter 5.2

4.1.6.3 	Receptacles except open cryogenic receptacles, including their closures, shall conform to

the design, construction, inspection and testing requirements detailed in Chapter 6.2. When outer packagings are prescribed, the receptacles shall be firmly secured therein. Unless otherwise specified in the relevant packing instructions, receptacles may be enclosed in outer packagings either singly or in groups.

4.1.6.4 	Valves (cocks) shall be effectively protected from damage which could cause gas release if the receptacle falls, and during carriage and stacking. This requirement is deemed to be complied with if one or more of the following conditions are fulfilled (see also table of standards at the end of this section):

(a)	Valves are placed inside the neck of the receptacle and protected by a screw-                    threaded plug;

(b)	Valves are protected by caps. Caps shall possess vent-holes of sufficient cross-sectional area to evacuate gases if leakage occurs at the valves;

(c)	Valves are protected by shrouds or guards;

(d)	Valves are designed and constructed in such a way that their ability to withstand damage without leakage of product has been demonstrated;

(e)	Valves are placed inside a protective frame;

(f)	Receptacles are carried in protective boxes or frames.

4.1.6.5 	Receptacles, containing pyrophoric gases or very toxic gases (gases with an LC50 lower than 200 ppm) shall have their valve(s) openings fitted with gas-tight plugs or cap nuts which shall be made of a material not liable to attack by the contents of the receptacle.

4.1.6.6 	Receptacles may be carried after the expiry of the time-limit set for the periodic test prescribed for the purpose of undergoing the test.

4.1.6.7 	Requirements of the following packing provisions are considered to have been complied with if the following standards, as relevant, are applied:

| Applicable paragraphs | Reference | Title of document |
| --- | --- | --- |
| 4.1.6.2 | EN 1795:1997 | Gas cylinders (excluding LPG) - Procedures for change of gas service. |
| 4.1.6.4 | EN 962:1996 | Valve protection caps and valve guards for industrial and medical gas cylinders - Design, construction and tests |

4.1.7	Special packing provisions for organic peroxides (Class 5.2) and self-reactive substances of Class 4.1

4.1.7.1	Use of packagings

4.1.7.1.1	Packagings for organic peroxides and self-reactive substances shall meet the requirements of Chapter 6.1 or of Chapter 6.6 at the packing group II performance level. To avoid unnecessary confinement, metal packagings meeting the test criteria of packing group I shall not be used.

4.1.7.1.2	The packing methods for organic peroxides and self-reactive substances are listed in packing instruction 520 and are designated OP1 to OP8. The quantities specified for each packing method are the maximum quantities authorized per package.

4.1.7.1.3	The packing methods appropriate for the individual currently assigned organic peroxides and self-reactive substances are listed in 2.2.41.4 and 2.2.52.4.

4.1.7.1.4	For new organic peroxides, new self-reactive substances or new formulations of currently assigned organic peroxides or self-reactive substances, the following procedure shall be used to assign the appropriate packing method:

(a)	ORGANIC PEROXIDE, TYPE B or SELF-REACTIVE SUBSTANCE, TYPE B:

Packing method OP5 shall be assigned, provided that the organic peroxide (or self-reactive substance) satisfies the criteria of 20.4.3 (b) (resp. 20.4.2 (b)) of the Manual of Tests and Criteria in a packaging authorized by  the packing method.  If the organic peroxide (or self-reactive substance) can only satisfy these criteria in a smaller packaging than those authorized by packing method OP5 (viz. one of the packagings listed for OP1 to OP4), then the corresponding packing method with the lower OP number is assigned;

(b)	ORGANIC PEROXIDE, TYPE C or SELF-REACTIVE SUBSTANCE, TYPE C:

Packing method OP6 shall be assigned, provided that the organic peroxide (or self-reactive substance) satisfies the criteria of 20.4.3 (c) (resp. 20.4.2 (c)) of the Manual of Tests and Criteria in a packaging authorized by the packing method.  If the organic peroxide (or self-reactive substance) can only satisfy these criteria in a smaller packaging than those authorized by packing method OP6 then the corresponding packing method with the lower OP number is assigned;

(c)	ORGANIC PEROXIDE, TYPE D or SELF-REACTIVE SUBSTANCE, TYPE D:

Packing method OP7 shall be assigned to this type of organic peroxide or self-reactive substance;

(d)	ORGANIC PEROXIDE, TYPE E or SELF-REACTIVE SUBSTANCE, TYPE E:

Packing method OP8 shall be assigned to this type of organic peroxide or self-reactive substance;

(e)	ORGANIC PEROXIDE, TYPE F or SELF-REACTIVE SUBSTANCE, TYPE F:

Packing method OP8 shall be assigned to this type of organic peroxide or self-reactive substance.

4.1.7.2	Use of intermediate bulk containers

4.1.7.2.1	The currently assigned organic peroxides specifically listed in the table of 2.2.52.4 and indicated with the letter “N” in the “Packing Method” column of that table may be carried in IBCs in accordance with packing instruction IBC 520.

4.1.7.2.2	Other organic peroxides and self-reactive substances of type F may be carried in IBCs under conditions established by the competent authority of the country of origin when, on the basis of the appropriate tests, that competent authority is satisfied that such carriage may be safely conducted. The tests undertaken shall include those necessary:

(a)	To prove that the organic peroxide (or self-reactive substance) complies with the principles for classification given in 20.4.3 (f) (resp. 20.4.2 (f) of the Manual of Tests and Criteria, exit box F of Figure 20.1 (b) of the Manual;

(b)	To prove the compatibility of all materials normally in contact with the substance during carriage;

(c)	To determine, when applicable, the control and emergency temperatures associated with the carriage of the product in the IBC concerned as derived from the SADT;

(d)	To design, when applicable, pressure and emergency relief devices; and

(e)	To determine if any special provisions are necessary for safe carriage of the substance.

If the country of origin is not Contracting Party to ADR, the classification and transport conditions shall be recognized by the competent authority of the first country contracting Party to ADR reached by the consignment.

4.1.8	Special packing provisions for infectious substances (Class 6.2)

4.1.8.1	Consignors of infectious substances shall ensure that packages are prepared in such a manner that they arrive at their destination in good condition and present no hazard to persons or animals during carriage.

4.1.8.2	The definitions in 1.2.1 and the general provisions of 4.1.1.1 to 4.1.1.14, except 4.1.1.3 and 4.1.1.9 to 4.1.1.12, apply to infectious substances packages.

4.1.8.3	An itemized list of contents shall be enclosed between the secondary packaging and the outer packaging.

4.1.8.4	Before an empty packaging is returned to the consignor, or sent elsewhere, it shall be thoroughly disinfected or sterilized and any label or marking indicating that it had contained an infectious substance shall be removed or obliterated.

4.1.9	Special packing provisions for Class 7

4.1.9.1 	General

4.1.9.1.1	Radioactive material, packagings and packages shall meet the requirements of Chapter 6.4.  The quantity of radioactive material in a package shall not exceed the limits specified in  2.2.7.7.1.

4.1.9.1.2	The non-fixed contamination on the external surfaces of any package shall be kept as low as practicable and, under routine conditions of transport, shall not exceed the following limits:

(a)	4 Bq/cm2 for beta and gamma emitters and low toxicity alpha emitters; and

(b) 	0.4 Bq/cm2 for all other alpha emitters.

These limits are applicable when averaged over any area of 300 cm2 of any part of the surface.

4.1.9.1.3	A package shall not contain any other items except such articles and documents as are necessary for the use of the radioactive material. This requirement shall not preclude the carriage of low specific activity material or surface contaminated objects with other items. The carriage of such articles and documents in a package, or of low specific activity material or surface contaminated objects with other items may be permitted provided that there is no interaction between them and the packaging or its radioactive contents that would reduce the safety of the package.

4.1.9.1.4 	Except as provided in 7.5.11, CV33, the level of non-fixed contamination on the external and internal surfaces of overpacks, containers, tanks and intermediate bulk containers shall not exceed the limits specified in 4.1.9.1.2.

4.1.9.1.5 	Radioactive material with a subsidiary risk shall be carried in packagings, IBCs or tanks fully complying with the requirements of the relevant chapters of Part 6 as appropriate, as well as applicable requirements of chapters 4.1 or 4.2 for that subsidiary risk.

4.1.9.2 	Requirements and controls for carriage of LSA material and SCO

4.1.9.2.1 	The quantity of LSA material or SCO in a single Industrial package Type 1 (Type IP-1), Industrial package Type 2 (Type IP-2), Industrial package Type 3 (Type IP-3), or object or collection of objects, whichever is appropriate, shall be so restricted that the external radiation level at 3 m from the unshielded material or object or collection of objects does not exceed 10 mSv/h.

4.1.9.2.2 	LSA material and SCO which is or contains fissile material shall meet the applicable requirements of 7.5.11, CV33 and 6.4.11.1.

4.1.9.2.3 	LSA material and SCO in groups LSA-I and SCO-I may be carried unpackaged under the following conditions:

(a)	All unpackaged material other than ores containing only naturally occurring radionuclides shall be carried in such a manner that under routine conditions of carriage there will be no escape of the radioactive contents from the conveyance nor will there be any loss of shielding;

(b)	Each conveyance shall be under exclusive use, except when only carrying SCO-I on which the contamination on the accessible and the inaccessible surfaces is not greater than ten times the applicable level specified in 2.2.7.2; and

(c)	For SCO-I where it is suspected that non-fixed contamination exists on inaccessible surfaces in excess of the values specified in 2.2.7.5(a)(i), measures shall be taken to ensure that the radioactive material is not released into the vehicle.

4.1.9.2.4 	LSA material and SCO, except as otherwise specified in 4.1.9.2.3, shall be packaged in accordance with the table below:

Industrial package requirements for LSA material and SCO

| Radioactive contents | Industrial package type |  |
| --- | --- | --- |
|  | Exclusive use | Not under exclusive use |
| LSA-I Solid a/ Liquid | Type IP-1 Type IP-1 | Type IP-1 Type IP-2 |
| LSA-II Solid Liquid and gas | Type IP-2 Type IP-2 | Type IP-2 Type IP-3 |
| LSA-III | Type IP-2 | Type IP-3 |
| SCO-I a/ | Type IP-1 | Type IP-1 |
| SCO-II | Type IP-2 | Type IP-2 |

a/   	Under the conditions specified in 4.1.9.2.3, LSA-I material and SCO-I may be carried unpackaged.

4.1.10	Special provisions for mixed packing

4.1.1.10.1	When mixed packing is permitted in accordance with the provisions of this section, different dangerous goods or dangerous goods and other goods may be packed together in combination packagings conforming to 6.1.4.2.1, provided that they do not react dangerously with one another and that all other relevant provisions of this Chapter are complied with.

NOTE 1: See also 4.1.1.5 and 4.1.1.6.

NOTE 2: For goods of Class 7, see 4.1.9.

4.1.10.2	Except for packages containing Class 1 goods only or Class 7 goods only, if wooden or fibreboard boxes are used as outer packagings, a package containing different goods packed together shall not weigh more than 100 kg.

4.1.10.3	Unless otherwise prescribed by a special provision applicable according to 4.1.10.4, dangerous goods of the same class and the same classification code may be packed together.

4.1.10.4	When indicated for a given entry in column (9b) of table A of Chapter 3.2, the following special provisions shall apply to the mixed packing of the goods assigned to that entry with other goods in the same package.

MP 1 	May only be packed together with goods of the same type within the same compatibility group.

MP 2	Shall not be packed together with other goods.

MP 3	Mixed packing of UN No. 1873 with UN No. 1802 is permitted.

MP 4	Shall not be packed together with goods of other classes or with goods which are not subject to the requirements of ADR. However, if this organic peroxide is a hardener or compound system for Class 3 substances, mixed packing is permitted with these substances of Class 3.

MP 5	UN No. 2814 and UN No. 2900 may be packed together in a combination packaging in conformity with P620. They shall not be packed together with other goods; this does not apply to diagnostic specimens packed in accordance with P621 or to substances added as coolants, e.g. ice, dry ice or deeply refrigerated liquid nitrogen.

MP 6	Shall not be packed together with other goods. This does not apply to substances added as coolants, e.g. ice, dry ice or deeply refrigerated liquid nitrogen.

MP 7	May – in quantities not exceeding 5 litres per inner packaging – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 8	May – in quantities not exceeding 3 litres per inner packaging – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 9	May be packed together in an outer packaging for combination packagings in accordance with 6.1.4.21:

-	with other goods of Class 2;

-	with goods of other classes, when the mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 10	May – in quantities not exceeding 5 kg per inner packaging – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 11	May – in quantities not exceeding 5 kg per inner packaging – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes (except substances of packing group I or II of Class 5.1) when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 12	May – in quantities not exceeding 5 kg per inner packaging – be packed together in a combination packaging conforming to sub-section 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes (except substances of packing group I or II of Class 5.1) when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

Packagings shall not weigh more than 45 kg. If fibreboard boxes are used as outer pacagings however, a package shall not weigh more than 27 kg.

MP 13	May – in quantities not exceeding 3 kg per inner packaging and per package – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 14	May – in quantities not exceeding 6 kg per inner packaging – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 15	May – in quantities not exceeding 3 litres per inner packaging – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 16	May – in quantities not exceeding 3 litres per inner packaging and per package – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 17	May – in quantities not exceeding 0,5 litre per inner packaging and 1 litre per package – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of other classes, except Class 7, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 18	May – in quantities not exceeding 0,5 kg per inner packaging and 1 kg per package – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods or articles of other classes, except Class 7, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 19	May – in quantities not exceeding 5 litres per inner packaging – be packed together in a combination packaging conforming to 6.1.4.21:

-	with goods of the same class covered by other classification codes or with goods of other classes, when mixed packing is also permitted for these; or

-	with goods which are not subject to the requirements of ADR,

provided they do not react dangerously with one another.

MP 20	May be packed together with substances covered by the same UN number.

Shall not be packed together with goods and articles of Class 1 having different UN numbers.

Shall not be packed together with goods of other classes or with goods which are not subject to the requirements of ADR.

MP 21	May be packed together with articles covered by the same UN number.

Shall not be packed together with goods of Class 1 having different UN numbers, except for

(a)	their own means of ignition, provided that

(i)	the means of ignition will not function under normal conditions of carriage; or

(ii)	such means have at least two effective protective features which prevent explosion of an article in the event of accidental functioning of the means of initiation; or

(iii)	when such means do not have two effective protective features (i.e. means of initiation assigned to compatibility group B), in the opinion of the competent authority of the country of origin, the accidental functioning of the means of initiation does not cause the explosion of an article under normal conditions of carriage;

(b)	articles of compatibility groups C, D and E.

Shall not be packed together with goods of other classes or with goods which are not subject to the requirements of ADR.

When goods are packed together in accordance with this special provision, account shall be taken of a possible amendment of the classification of packages in accordance with 2.2.1.1. For the description of the goods in the transport document, see 5.4.1.2.1 (b).

MP 22	May be packed together with articles covered by the same UN number.

Shall not be packed together with goods of Class 1 having different UN numbers, except for

(a)	their own means of ignition, provided that the means of ignition will not function under normal conditions of carriage;

(b)	articles of compatibility groups C, D and E.

Shall not be packed together with goods of other classes or with goods which are not subject to the requirements of ADR.

When goods are packed together in accordance with this special provision, account shall be taken of a possible amendment of the classification of packages in accordance with 2.2.1.1. For the description of the goods in the transport document, see 5.4.1.2.1 (b).

MP 23	May be packed together with articles covered by the same UN number.

Shall not be packed together with goods and articles of Class 1 having different UN numbers ; however, exception is made for their own means of ignition, provided that the means of ignition will not function under normal conditions of carriage.

Shall not be packed together with goods of other classes or with goods which are not subject to the requirements of ADR.

When goods are packed together in accordance with this special provision, account shall be taken of a possible amendment of the classification of packages in accordance with 2.2.1.1. For the description of the goods in the transport document, see 5.4.1.2.1 (b).

MP 24	May be packed together with goods with the UN numbers shown in the table below, under the following conditions :

-	if a letter A is indicated in the table, the goods with those UN numbers may be included in the same package without any special limitation of mass;

-	 if a letter B is indicated in the table, the goods with those UN numbers may be included in the same package up to a total mass of 50 kg of explosive substances.

When goods are packed together in accordance with this special provision, account shall be taken of a possible amendment of the classification of packages in accordance with 2.2.1.1. For the description of the goods in the transport document, see 5.4.1.2.1 (b).

| UN No. | 0012 | 0014 | 0027 | 0028 | 0044 | 0054 | 0160 | 0161 | 0186 | 0191 | 0194 | 0195 | 0197 | 0238 | 0240 | 0312 | 0333 | 0334 | 0335 | 0336 | 0337 | 0373 | 0405 | 0428 | 0429 | 0430 | 0431 | 0432 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0012 |  | A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0014 | A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0027 |  |  |  | B | B |  | B | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0028 |  |  | B |  | B |  | B | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0044 |  |  | B | B |  |  | B | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0054 |  |  |  |  |  |  |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0160 |  |  | B | B | B |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0161 |  |  | B | B | B |  | B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0186 |  |  |  |  |  | B |  |  |  | B | B | B | B | B | B | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0191 |  |  |  |  |  | B |  |  | B |  | B | B | B | B | B | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0194 |  |  |  |  |  | B |  |  | B | B |  | B | B | B | B | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0195 |  |  |  |  |  | B |  |  | B | B | B |  | B | B | B | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0197 |  |  |  |  |  | B |  |  | B | B | B | B |  | B | B | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0238 |  |  |  |  |  | B |  |  | B | B | B | B | B |  | B | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0240 |  |  |  |  |  | B |  |  | B | B | B | B | B | B |  | B |  |  |  |  |  | B | B | B | B | B | B | B |
| 0312 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B |  |  |  |  |  |  | B | B | B | B | B | B | B |
| 0333 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | A | A | A | A |  |  |  |  |  |  |  |
| 0334 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | A |  | A | A | A |  |  |  |  |  |  |  |
| 0335 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | A | A |  | A | A |  |  |  |  |  |  |  |
| 0336 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | A | A | A |  | A |  |  |  |  |  |  |  |
| 0337 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | A | A | A | A |  |  |  |  |  |  |  |  |
| 0373 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  |  | B | B | B | B | B | B |
| 0405 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  | B |  | B | B | B | B | B |
| 0428 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  | B | B |  | B | B | B | B |
| 0429 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  | B | B | B |  | B | B | B |
| 0430 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  | B | B | B | B |  | B | B |
| 0431 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  | B | B | B | B | B |  | B |
| 0432 |  |  |  |  |  | B |  |  | B | B | B | B | B | B | B | B |  |  |  |  |  | B | B | B | B | B | B |  |

# Footnotes

Relative density (d) is considered to be synonymous with specific gravity (SG) and will be used throughout this Chapter.

( 	European Communities Council Directive 75/324/EEC of 20 May 1975 on the approximation of the laws of the Member States (of the European Communities) concerning packagings for aerosols, published in the Official Journal of the European Communities No. L147 of 9 June 1975.

(( 	European Commission Directive 94/1/EC of 6 January 1994 to align with Directive 75/324/EEC on the approximation of the laws of the Member States (of the European Union) concerning aerosol packagings to technical progress, published in the Official Journal of the European Communities No. L23 of 28 January 1994.

If the country of origin is not Contracting Party to ADR, the approval shall require validation by the competent authority of the first country Contracting Party to ADR reached by the consignment.

# Text boxes

E

Economic and Social

Council

propane

Commercial

utane

Commercial b

kg/l

Density  at 50 °C in

Maximum permissible mass of contents per litre of capacity

0.525

0.516

0.505

0.495

0.485

0.474

0.463

0.450

0.440

0.50

0.49

0.48

0.47

0.46

0.45

0.44

0.43

0.42

A

A01

A02

A0

A1

B1

B2

B

C

TRANS/WP.15/159/Add.3

page 110