| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1113 | AMYL NITRITE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1114 | BENZENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1120 | BUTANOLS | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1120 | BUTANOLS | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1123 | BUTYL ACETATES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1123 | BUTYL ACETATES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1125 | n-BUTYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1126 | 1-BROMOBUTANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1127 | CHLOROBUTANES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1128 | n-BUTYL FORMATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1129 | BUTYRALDEHYDE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1130 | CAMPHOR OIL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1131 | CARBON DISULPHIDE | 3 | FT1 | I | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1133 | ADHESIVES containing flammable liquid (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1133 | ADHESIVES containing flammable liquid (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1133 | ADHESIVES containing flammable liquid (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1133 | ADHESIVES containing flammable liquid (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1133 | ADHESIVES containing flammable liquid | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1133 | ADHESIVES containing flammable liquid (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1133 | ADHESIVES containing flammable liquid (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1133 | ADHESIVES containing flammable liquid (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1134 | CHLOROBENZENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1135 | ETHYLENE CHLOROHYDRIN | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1136 | COAL TAR DISTILLATES, FLAMMABLE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1136 | COAL TAR DISTILLATES, FLAMMABLE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1139 | COATING SOLUTION (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1139 | COATING SOLUTION (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1139 | COATING SOLUTION (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1139 | COATING SOLUTION (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1139 | COATING SOLUTION | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1139 | COATING SOLUTION (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1139 | COATING SOLUTION (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1139 | COATING SOLUTION (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1143 | CROTONALDEHYDE, STABILIZED | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1144 | CROTONYLENE | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1145 | CYCLOHEXANE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1146 | CYCLOPENTANE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1147 | DECAHYDRO-NAPHTHALENE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1148 | DIACETONE ALCOHOL | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1148 | DIACETONE ALCOHOL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1149 | DIBUTYL ETHERS | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1150 | 1,2-DICHLOROETHYLENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1152 | DICHLOROPENTANES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1153 | ETHYLENE GLYCOL DIETHYL ETHER | 3 | F1 | II | 3 |  | LQ4 | [T] | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1153 | ETHYLENE GLYCOL DIETHYL ETHER | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1154 | DIETHYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1155 | DIETHYL ETHER (ETHYL ETHER) | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1156 | DIETHYL KETONE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1157 | DIISOBUTYL KETONE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1158 | DIISOPROPYLAMINE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1159 | DIISOPROPYL ETHER | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1160 | DIMETHYLAMINE AQUEOUS SOLUTION | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1161 | DIMETHYL CARBONATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1162 | DIMETHYLDICHLORO- SILANE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1163 | DIMETHYLHYDRAZINE, UNSYMMETRICAL | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1164 | DIMETHYL SULPHIDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1165 | DIOXANE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1166 | DIOXOLANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1167 | DIVINYL ETHER, STABILIZED | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1169 | EXTRACTS, AROMATIC, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1170 | ETHANOL (ETHYL ALCOHOL) or ETHANOL SOLUTION (ETHYL ALCOHOL SOLUTION) | 3 | F1 | II | 3 | 144 | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1170 | ETHANOL SOLUTION (ETHYL ALCOHOL SOLUTION) | 3 | F1 | III | 3 | 144 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1171 | ETHYLENE GLYCOL MONOETHYL ETHER | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1172 | ETHYLENE GLYCOL MONOETHYL ETHER ACETATE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1173 | ETHYL ACETATE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1175 | ETHYLBENZENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1176 | ETHYL BORATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1177 | 2-ETHYLBUTYL ACETATE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1178 | 2-ETHYLBUTYRALDEHYDE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1179 | ETHYL BUTYL ETHER | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1180 | ETHYL BUTYRATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1181 | ETHYL CHLOROACETATE | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1182 | ETHYL CHLOROFORMATE | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1183 | ETHYLDICHLOROSILANE | 4.3 | WFC | I | 4.3+3+8 |  | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 1184 | ETHYLENE DICHLORIDE | 3 | FT1 | II | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1185 | ETHYLENEIMINE, STABILIZED | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1188 | ETHYLENE GLYCOL MONOMETHYL ETHER | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1189 | ETHYLENE GLYCOL MONOMETHYL ETHER ACETATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1190 | ETHYL FORMATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1191 | OCTYL ALDEHYDES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1192 | ETHYL LACTATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1193 | ETHYL METHYL KETONE (METHYL ETHYL KETONE) | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1194 | ETHYL NITRITE SOLUTION | 3 | FT1 | I | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1195 | ETHYL PROPIONATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1196 | ETHYLTRICHLOROSILANE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1197 | EXTRACTS, FLAVOURING, LIQUID (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1197 | EXTRACTS, FLAVOURING, LIQUID (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1197 | EXTRACTS, FLAVOURING, LIQUID (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1197 | EXTRACTS, FLAVOURING, LIQUID (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1197 | EXTRACTS, FLAVOURING, LIQUID | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1197 | EXTRACTS, FLAVOURING, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1197 | EXTRACTS, FLAVOURING, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1197 | EXTRACTS, FLAVOURING, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1198 | FORMALDEHYDE SOLUTION, FLAMMABLE | 3 | FC | III | 3+8 |  | LQ7 | T | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 1199 | FURALDEHYDES | 6.1 | TF1 | II | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1201 | FUSEL OIL | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1201 | FUSEL OIL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1202 | GAS OIL or DIESEL FUEL or HEATING OIL, LIGHT (flash-point not more than 61 °C) | 3 | F1 | III | 3 | 640K | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1202 | DIESEL FUEL complying with standard EN 590:1993 or GAS OIL or HEATING OIL, LIGHT with a flash-point as specified in EN 590:1993 | 3 | F1 | III | 3 | 640L | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1202 | GAS OIL or DIESEL FUEL or HEATING OIL, LIGHT (flash-point more than 61 °C and not more than 100 °C) | 3 | F1 | III | 3 | 640M | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1203 | MOTOR SPIRIT or GASOLINE or PETROL | 3 | F1 | II | 3 | 534 | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1204 | NITROGLYCERIN SOLUTION IN ALCOHOL with not more than 1% nitroglycerin | 3 | D | II | 3 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1206 | HEPTANES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1207 | HEXALDEHYDE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1208 | HEXANES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 163 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 163 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 163 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 163 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable | 3 | F1 | III | 3 | 163 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 163 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa) | 3 | F1 | III | 3 | 163 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1210 | PRINTING INK, flammable or PRINTING INK RELATED MATERIAL (including printing ink thinning or reducing compound), flammable (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 163 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1212 | ISOBUTANOL (ISOBUTYL ALCOHOL) | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1213 | ISOBUTYL ACETATE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1214 | ISOBUTYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1216 | ISOOCTENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1218 | ISOPRENE, STABILIZED | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1219 | ISOPROPANOL (ISOPROPYL ALCOHOL) | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1220 | ISOPROPYL ACETATE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1221 | ISOPROPYLAMINE | 3 | FC | I | 3+8 |  | LQ3 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1222 | ISOPROPYL NITRATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1223 | KEROSENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1224 | KETONES, LIQUID, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 274 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1224 | KETONES, LIQUID, N.O.S. (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 274 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1224 | KETONES, LIQUID, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1228 | MERCAPTANS, LIQUID, FLAMMABLE, TOXIC, N.O.S. or MERCAPTAN MIXTURE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | II | 3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1228 | MERCAPTANS, LIQUID, FLAMMABLE, TOXIC, N.O.S. or MERCAPTAN MIXTURE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | III | 3+6.1 | 274 802 | LQ7 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 1229 | MESITYL OXIDE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1230 | METHANOL | 3 | FT1 | II | 3+6.1 | 279 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1231 | METHYL ACETATE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1233 | METHYLAMYL ACETATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1234 | METHYLAL | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1235 | METHYLAMINE, AQUEOUS SOLUTION | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1237 | METHYL BUTYRATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1238 | METHYL CHLOROFORMATE | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1239 | METHYL CHLORO-METHYL ETHER | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1242 | METHYLDICHLOROSILANE | 4.3 | WFC | I | 4.3+3+8 |  | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 1243 | METHYL FORMATE | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1244 | METHYLHYDRAZINE | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1245 | METHYL ISOBUTYL KETONE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1246 | METHYL ISOPROPENYL KETONE, STABILIZED | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1247 | METHYL METHACRYLATE MONOMER, STABILIZED | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1248 | METHYL PROPIONATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1249 | METHYL PROPYL KETONE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1250 | METHYLTRICHLOROSILANE | 3 | FC | I | 3+8 |  | LQ3 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1251 | METHYL VINYL KETONE, STABILIZED | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1259 | NICKEL CARBONYL | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1261 | NITROMETHANE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1262 | OCTANES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 163 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 163 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 163 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 163 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) | 3 | F1 | III | 3 | 163 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) (having a flash-point below 23 °C and viscous according to 2.2.3.1. | 3 | F1 | III | 3 | 163 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) (having a flash-point below 23 °C and viscous according to 2.2.3.1. | 3 | F1 | III | 3 | 163 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1263 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) (having a flash-point below 23 °C and viscous according to 2.2.3.1. | 3 | F1 | III | 3 | 163 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1264 | PARALDEHYDE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1265 | PENTANES, liquid | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1265 | PENTANES, liquid | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1266 | PERFUMERY PRODUCTS with flammable solvents (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1267 | PETROLEUM CRUDE OIL (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1267 | PETROLEUM CRUDE OIL (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1267 | PETROLEUM CRUDE OIL (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1267 | PETROLEUM CRUDE OIL (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1267 | PETROLEUM CRUDE OIL | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 274 640A | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 274 640B | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 274 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 274 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1272 | PINE OIL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1274 | n-PROPANOL (PROPYL ALCOHOL, NORMAL) | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1274 | n-PROPANOL (PROPYL ALCOHOL, NORMAL) | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1275 | PROPIONALDEHYDE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1276 | n-PROPYL ACETATE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1277 | PROPYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1278 | PROPYL CHLORIDE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1279 | 1,2-DICHLOROPROPANE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1280 | PROPYLENE OXIDE | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1281 | PROPYL FORMATES | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1282 | PYRIDINE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1286 | ROSIN OIL (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1286 | ROSIN OIL (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1286 | ROSIN OIL (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1286 | ROSIN OIL (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1286 | ROSIN OIL | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1286 | ROSIN OIL (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1286 | ROSIN OIL (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1286 | ROSIN OIL (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1287 | RUBBER SOLUTION (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1287 | RUBBER SOLUTION (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1287 | RUBBER SOLUTION (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1287 | RUBBER SOLUTION (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1287 | RUBBER SOLUTION | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1287 | RUBBER SOLUTION (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1287 | RUBBER SOLUTION (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1287 | RUBBER SOLUTION (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1288 | SHALE OIL | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1288 | SHALE OIL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1289 | SODIUM METHYLATE SOLUTION in alcohol | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1289 | SODIUM METHYLATE SOLUTION in alcohol | 3 | FC | III | 3+8 |  | LQ7 | T | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 1292 | TETRAETHYL SILICATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1293 | TINCTURES, MEDICINAL | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1293 | TINCTURES, MEDICINAL | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1294 | TOLUENE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1295 | TRICHLOROSILANE | 4.3 | WFC | I | 4.3+3+8 |  | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 1296 | TRIETHYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1297 | TRIMETHYLAMINE, AQUEOUS SOLUTION, not more than 50% trimethylamine, by mass | 3 | FC | I | 3+8 |  | LQ3 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1297 | TRIMETHYLAMINE, AQUEOUS SOLUTION, not more than 50% trimethylamine, by mass | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1297 | TRIMETHYLAMINE, AQUEOUS SOLUTION, not more than 50% trimethylamine, by mass | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 1298 | TRIMETHYLCHLORO-SILANE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1299 | TURPENTINE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1300 | TURPENTINE SUBSTITUTE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1300 | TURPENTINE SUBSTITUTE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1301 | VINYL ACETATE, STABILIZED | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1302 | VINYL ETHYL ETHER, STABILIZED | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1303 | VINYLIDENE CHLORIDE, STABILIZED | 3 | F1 | I | 3 |  | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1304 | VINYL ISOBUTYL ETHER, STABILIZED | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1305 | VINYLTRICHLOROSILANE, STABILIZED | 3 | FC | I | 3+8 |  | LQ3 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1306 | WOOD PRESERVATIVES, LIQUID (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1306 | WOOD PRESERVATIVES, LIQUID (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1306 | WOOD PRESERVATIVES, LIQUID | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1306 | WOOD PRESERVATIVES, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1306 | WOOD PRESERVATIVES, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1306 | WOOD PRESERVATIVES, LIQUID (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1307 | XYLENES | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1307 | XYLENES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | F3 | II | 4.1 |  | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1310 | AMMONIUM PICRATE, WETTED with not less than 10% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1312 | BORNEOL | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1313 | CALCIUM RESINATE | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1314 | CALCIUM RESINATE, FUSED | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1318 | COBALT RESINATE, PRECIPITATED | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1320 | DINITROPHENOL, WETTED with not less than 15% water, by mass | 4.1 | DT | I | 4.1+6.1 | 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 1321 | DINITROPHENOLATES, WETTED with not less than 15% water, by mass | 4.1 | DT | I | 4.1+6.1 | 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 1322 | DINITRORESORCINOL, WETTED with not less than 15% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1323 | FERROCERIUM | 4.1 | F3 | II | 4.1 | 249 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1324 | FILMS, NITROCELLULOSE BASE, gelatin coated, except scrap | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 | F1 | II | 4.1 | 274 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 | F1 | III | 4.1 | 274 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1326 | HAFNIUM POWDER, WETTED with not less than 25% water | 4.1 | F3 | II | 4.1 | 586 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1327 | Hay, Straw or Bhusa | 4.1 | F1 |  |  |  | NOT SUBJECT TO ADN |  |  |  |  |  |  |
| 1328 | HEXAMETHYLENETE-TRAMINE | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1330 | MANGANESE RESINATE | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1331 | MATCHES, 'STRIKE ANYWHERE' | 4.1 | F1 | III | 4.1 | 293 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1332 | METALDEHYDE | 4.1 | F1 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1333 | CERIUM, slabs, ingots or rods | 4.1 | F3 | II | 4.1 |  | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1334 | NAPHTHALENE, CRUDE or NAPHTHALENE, REFINED | 4.1 | F1 | III | 4.1 | 501 | LQ9 | B | PP |  | CO01 |  |  | 0 |  |
| 1336 | NITROGUANIDINE (PICRITE), WETTED with not less than 20% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1337 | NITROSTARCH, WETTED with not less than 20% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1338 | PHOSPHORUS, AMORPHOUS | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1339 | PHOSPHORUS HEPTASULPHIDE, free from yellow and white phosphorus | 4.1 | F3 | II | 4.1 | 602 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1340 | PHOSPHORUS PENTASULPHIDE, free from yellow and white phosphorus | 4.3 | WF2 | II | 4.3+4.1 | 602 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 1341 | PHOSPHORUS SESQUISULPHIDE, free from yellow and white phosphorus | 4.1 | F3 | II | 4.1 | 602 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1343 | PHOSPHORUS TRISULPHIDE, free from yellow and white phosphorus | 4.1 | F3 | II | 4.1 | 602 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1344 | TRINITROPHENOL, WETTED with not less than 30% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1345 | RUBBER SCRAP or RUBBER SHODDY, powdered or granulated | 4.1 | F1 | II | 4.1 |  | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1346 | SILICON POWDER, AMORPHOUS | 4.1 | F3 | III | 4.1 | 32 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1347 | SILVER PICRATE, WETTED with not less than 30% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1348 | SODIUM DINITRO-o-CRESOLATE, WETTED with not less than 15% water, by mass | 4.1 | DT | I | 4.1+6.1 | 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 1349 | SODIUM PICRAMATE, WETTED with not less than 20% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1350 | SULPHUR | 4.1 | F3 | III | 4.1 | 242 | LQ9 | B | PP |  |  |  |  | 0 |  |
| 1352 | TITANIUM POWDER, WETTED with not less than 25% water | 4.1 | F3 | II | 4.1 | 586 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1353 | FIBRES or FABRICS IMPREGNATED WITH WEAKLY NITRATED NITROCELLULOSE, N.O.S. | 4.1 | F1 | III | 4.1 | 274 502 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1354 | TRINITROBENZENE, WETTED with not less than 30% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1355 | TRINITROBENZOIC ACID, WETTED with not less than 30% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1356 | TRINITROTOLUENE (TNT), WETTED with not less than 30% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1357 | UREA NITRATE, WETTED with not less than 20% water, by mass | 4.1 | D | I | 4.1 | 227 | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1358 | ZIRCONIUM POWDER, WETTED with not less than 25% water | 4.1 | F3 | II | 4.1 | 586 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1360 | CALCIUM PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 1361 | CARBON, animal or vegetable origin | 4.2 | S2 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1361 | CARBON, animal or vegetable origin | 4.2 | S2 | III | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1362 | CARBON, ACTIVATED | 4.2 | S2 | III | 4.2 | 646 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1363 | COPRA | 4.2 | S2 | III | 4.2 |  | LQ0 | B | PP |  |  |  | IN01, IN02 | 0 | IN01 and IN02 apply only when this substance is carried in bulk or without packaging |
| 1364 | COTTON WASTE, OILY | 4.2 | S2 | III | 4.2 |  | LQ0 | B | PP |  |  |  |  | 0 |  |
| 1365 | COTTON, WET | 4.2 | S2 | III | 4.2 |  | LQ0 | B | PP |  |  |  |  | 0 |  |
| 1366 | DIETHYLZINC | 4.2 | SW | I | 4.2+4.3 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1369 | p-NITROSODIMETHYL- ANILINE | 4.2 | S2 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1370 | DIMETHYLZINC | 4.2 | SW | I | 4.2+4.3 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1372 | Fibres, animal or fibres, vegetal burnt, wet or damp | 4.2 | S2 | NOT SUBJECT TO ADN |
| 1373 | FIBRES or FABRICS, ANIMAL or VEGETABLE or SYNTHETIC, N.O.S. with oil | 4.2 | S2 | III | 4.2 | 274 | LQ0 | B | PP |  |  |  |  | 0 |  |
| 1374 | FISH MEAL (FISH SCRAP), UNSTABILIZED | 4.2 | S2 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1376 | IRON OXIDE, SPENT or IRON SPONGE, SPENT obtained from coal gas purification | 4.2 | S4 | III | 4.2 | 592 | LQ0 | B | PP |  |  |  |  | 0 |  |
| 1378 | METAL CATALYST, WETTED with a visible excess of liquid | 4.2 | S4 | II | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1379 | PAPER, UNSATURATED OIL TREATED, incompletely dried (including carbon paper) | 4.2 | S2 | III | 4.2 |  | LQ0 | B | PP |  |  |  |  | 0 |  |
| 1380 | PENTABORANE | 4.2 | ST3 | I | 4.2+6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1381 | PHOSPHORUS, WHITE or YELLOW, UNDER WATER or IN SOLUTION | 4.2 | ST3 | I | 4.2+6.1 | 503 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1381 | PHOSPHORUS, WHITE or YELLOW, DRY | 4.2 | ST4 | I | 4.2+6.1 | 503 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1382 | POTASSIUM SULPHIDE, ANHYDROUS or POTASSIUM SULPHIDE with less than 30% water of crystallization | 4.2 | S4 | II | 4.2 | 504 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1383 | PYROPHORIC METAL, N.O.S. or PYROPHORIC ALLOY, N.O.S. | 4.2 | S4 | I | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1384 | SODIUM DITHIONITE (SODIUM HYDROSULPHITE) | 4.2 | S4 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1385 | SODIUM SULPHIDE, ANHYDROUS or SODIUM SULPHIDE with less than 30% water of crystallization | 4.2 | S4 | II | 4.2 | 504 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1386 | SEED CAKE with more than 1.5% oil and not more than 11% moisture | 4.2 | S2 | III | 4.2 | 800 | LQ0 | B | PP |  |  |  | IN01, IN02 | 0 | IN01 and IN02 apply only when this substance is carried in bulk or without packaging |
| 1387 | Wool waste, wet | 4.2 | S2 | NOT SUBJECT TO ADN |
| 1389 | ALKALI METAL AMALGAM | 4.3 | W2 | I | 4.3 | 182 274 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1390 | ALKALI METAL AMIDES | 4.3 | W2 | II | 4.3 | 182 274 505 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION | 4.3 | W1 | I | 4.3 | 182 183 274 282 506 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1392 | ALKALINE EARTH METAL AMALGAM | 4.3 | W2 | I | 4.3 | 183 274 506 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1393 | ALKALINE EARTH METAL ALLOY, N.O.S. | 4.3 | W2 | II | 4.3 | 183 274 506 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1394 | ALUMINIUM CARBIDE | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1395 | ALUMINIUM FERROSILICON POWDER | 4.3 | WT2 | II | 4.3+6.1 | 802 | LQ11 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | W2 | II | 4.3 |  | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | W2 | III | 4.3 |  | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1397 | ALUMINIUM PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 507 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 | W2 | III | 4.3 | 37 | LQ12 | B | PP, EX, A | VE01, VE03 | LO03 | HA07, HA08 | IN01, IN03 | 0 | VE03, LO03, HA07, IN01 and IN03 apply only when this substance is carried in bulk or without packaging |
| 1400 | BARIUM | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1401 | CALCIUM | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1402 | CALCIUM CARBIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1402 | CALCIUM CARBIDE | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1403 | CALCIUM CYANAMIDE with more than 0.1% calcium carbide | 4.3 | W2 | III | 4.3 | 38 | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1404 | CALCIUM HYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1405 | CALCIUM SILICIDE | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1405 | CALCIUM SILICIDE | 4.3 | W2 | III | 4.3 |  | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1407 | CAESIUM | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | WT2 | III | 4.3+6.1 | 39 802 | LQ12 | B | PP, EP, EX, TOX, A | VE01, VE02, VE03 | LO03 | HA07, HA08 | IN01, IN02, IN03 | 0 | VE03, LO03, HA07, IN01, IN02 and IN03 apply only when this substance is carried in bulk or without packaging |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | W2 | I | 4.3 | 274 508 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | W2 | II | 4.3 | 274 508 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1410 | LITHIUM ALUMINIUM HYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1411 | LITHIUM ALUMINIUM HYDRIDE, ETHEREAL | 4.3 | WF1 | I | 4.3+3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 1413 | LITHIUM BOROHYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1414 | LITHIUM HYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1415 | LITHIUM | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1417 | LITHIUM SILICON | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | WS | I | 4.3+4.2 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | WS | II | 4.3+4.2 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | WS | III | 4.3+4.2 |  | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1419 | MAGNESIUM ALUMINIUM PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 1420 | POTASSIUM METAL ALLOYS | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1421 | ALKALI METAL ALLOY, LIQUID, N.O.S. | 4.3 | W1 | I | 4.3 | 182 274 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1422 | POTASSIUM SODIUM ALLOYS | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1423 | RUBIDIUM | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1426 | SODIUM BOROHYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1427 | SODIUM HYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1428 | SODIUM | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1431 | SODIUM METHYLATE | 4.2 | SC4 | II | 4.2+8 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1432 | SODIUM PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 1433 | STANNIC PHOSPHIDES | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 1435 | ZINC ASHES | 4.3 | W2 | III | 4.3 |  | LQ12 | B | PP, EX, A | VE01, VE03 | LO03 | HA07, HA08 | IN01, IN03 | 0 | VE03, LO03, HA07, IN01 and IN03 apply only when this substance is carried in bulk or without packaging |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | WS | I | 4.3+4.2 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | WS | II | 4.3+4.2 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | WS | III | 4.3+4.2 |  | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1437 | ZIRCONIUM HYDRIDE | 4.1 | F3 | II | 4.1 |  | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1438 | ALUMINIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1439 | AMMONIUM DICHROMATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1442 | AMMONIUM PERCHLORATE | 5.1 | O2 | II | 5.1 | 152 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 1444 | AMMONIUM PERSULPHATE | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1445 | BARIUM CHLORATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 1446 | BARIUM NITRATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 1447 | BARIUM PERCHLORATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 1448 | BARIUM PERMANGANATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 1449 | BARIUM PEROXIDE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 1450 | BROMATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 604 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1451 | CAESIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1452 | CALCIUM CHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1453 | CALCIUM CHLORITE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1454 | CALCIUM NITRATE | 5.1 | O2 | III | 5.1 | 208 | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1455 | CALCIUM PERCHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1456 | CALCIUM PERMANGANATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1457 | CALCIUM PEROXIDE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1461 | CHLORATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 605 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1462 | CHLORITES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 509 606 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1463 | CHROMIUM TRIOXIDE, ANHYDROUS | 5.1 | OC2 | II | 5.1+8 | 510 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1465 | DIDYMIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1466 | FERRIC NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1467 | GUANIDINE NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1469 | LEAD NITRATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 1470 | LEAD PERCHLORATE | 5.1 | OT2 | II | 5.1+6.1 | 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 1471 | LITHIUM HYPOCHLORITE, DRY or LITHIUM HYPOCHLORITE MIXTURE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1472 | LITHIUM PEROXIDE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1473 | MAGNESIUM BROMATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1474 | MAGNESIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1475 | MAGNESIUM PERCHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1476 | MAGNESIUM PEROXIDE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 511 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 511 | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1479 | OXIDIZING SOLID, N.O.S. | 5.1 | O2 | I | 5.1 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1479 | OXIDIZING SOLID, N.O.S. | 5.1 | O2 | II | 5.1 | 274 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1479 | OXIDIZING SOLID, N.O.S. | 5.1 | O2 | III | 5.1 | 274 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 608 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 608 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1484 | POTASSIUM BROMATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1485 | POTASSIUM CHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1486 | POTASSIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1487 | POTASSIUM NITRATE AND SODIUM NITRITE MIXTURE | 5.1 | O2 | II | 5.1 | 607 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1488 | POTASSIUM NITRITE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1489 | POTASSIUM PERCHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1490 | POTASSIUM PERMANGANATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1491 | POTASSIUM PEROXIDE | 5.1 | O2 | I | 5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1492 | POTASSIUM PERSULPHATE | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1493 | SILVER NITRATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1494 | SODIUM BROMATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1495 | SODIUM CHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1496 | SODIUM CHLORITE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1498 | SODIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1499 | SODIUM NITRATE AND POTASSIUM NITRATE MIXTURE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1500 | SODIUM NITRITE | 5.1 | OT2 | III | 5.1+6.1 | 802 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1502 | SODIUM PERCHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1503 | SODIUM PERMANGANATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1504 | SODIUM PEROXIDE | 5.1 | O2 | I | 5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1505 | SODIUM PERSULPHATE | 5.1 | O2 | III | 5.1 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1506 | STRONTIUM CHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1507 | STRONTIUM NITRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | B | PP |  | CO02, LO04 |  |  | 0 | CO02 and LO04 apply only when this substance is carried in bulk or without packaging |
| 1508 | STRONTIUM PERCHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1509 | STRONTIUM PEROXIDE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1510 | TETRANITROMETHANE | 5.1 | OT1 | I | 5.1+6.1 | 609 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1511 | UREA HYDROGEN PEROXIDE | 5.1 | OC2 | III | 5.1+8 |  | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1512 | ZINC AMMONIUM NITRITE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1513 | ZINC CHLORATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1514 | ZINC NITRATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1515 | ZINC PERMANGANATE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1516 | ZINC PEROXIDE | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1517 | ZIRCONIUM PICRAMATE, WETTED with not less than 20% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 1541 | ACETONE CYANOHYDRIN, STABILIZED | 6.1 | T1 | I | 6.1 | 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 43 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 43 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1545 | ALLYL ISOTHIOCYANATE, STABILIZED | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1546 | AMMONIUM ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1547 | ANILINE | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1548 | ANILINE HYDROCHLORIDE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1549 | ANTIMONY COMPOUND, INORGANIC, SOLID, N.O.S. | 6.1 | T5 | III | 6.1 | 45 274 512 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1550 | ANTIMONY LACTATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1551 | ANTIMONY POTASSIUM TARTRATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1553 | ARSENIC ACID, LIQUID | 6.1 | T4 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1554 | ARSENIC ACID, SOLID | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1555 | ARSENIC BROMIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T4 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T4 | II | 6.1 | 43 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T4 | III | 6.1 | 43 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T5 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T5 | II | 6.1 | 43 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T5 | III | 6.1 | 43 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1558 | ARSENIC | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1559 | ARSENIC PENTOXIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1560 | ARSENIC TRICHLORIDE | 6.1 | T4 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1561 | ARSENIC TRIOXIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1562 | ARSENICAL DUST | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 177 274 513 587 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 177 274 513 587 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1565 | BARIUM CYANIDE | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 274 514 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 274 514 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1567 | BERYLLIUM POWDER | 6.1 | TF3 | II | 6.1+4.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1569 | BROMOACETONE | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1570 | BRUCINE | 6.1 | T2 | I | 6.1 | 43 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1571 | BARIUM AZIDE, WETTED with not less than 50% water, by mass | 4.1 | DT | I | 4.1+6.1 | 568 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 1572 | CACODYLIC ACID | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1573 | CALCIUM ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1574 | CALCIUM ARSENATE AND CALCIUM ARSENITE MIXTURE, SOLID | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1575 | CALCIUM CYANIDE | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1577 | CHLORODINITRO- BENZENES, LIQUID | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1577 | CHLORODINITRO- BENZENES, SOLID | 6.1 | T2 | II | 6.1 | 279 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1578 | CHLORONITROBENZENES, liquid | 6.1 | T2 | II | 6.1 | 279 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1578 | CHLORONITROBENZENES, solid | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1580 | CHLOROPICRIN | 6.1 | T1 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1581 | CHLOROPICRIN AND METHYL BROMIDE MIXTURE with more than 2% chloropicrin | 2 | 2T |  | 2.3 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1582 | CHLOROPICRIN AND METHYL CHLORIDE MIXTURE | 2 | 2T |  | 2.3 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 | T1 | I | 6.1 | 274 515 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 | T1 | II | 6.1 | 274 515 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 | T1 | III | 6.1 | 274 515 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1585 | COPPER ACETOARSENITE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1586 | COPPER ARSENITE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1587 | COPPER CYANIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | T5 | I | 6.1 | 47 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | T5 | II | 6.1 | 47 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | T5 | III | 6.1 | 47 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1589 | CYANOGEN CHLORIDE, STABILIZED | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1590 | DICHLOROANILINES, LIQUID | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1590 | DICHLOROANILINES, SOLID | 6.1 | T2 | II | 6.1 | 279 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1591 | o-DICHLOROBENZENE | 6.1 | T1 | III | 6.1 | 279 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1593 | DICHLOROMETHANE | 6.1 | T1 | III | 6.1 | 516 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1594 | DIETHYL SULPHATE | 6.1 | T1 | II | 6.1 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1595 | DIMETHYL SULPHATE | 6.1 | TC1 | I | 6.1+8 | 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1596 | DINITROANILINES | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1597 | DINITROBENZENES, LIQUID | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1597 | DINITROBENZENES, SOLID | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1598 | DINITRO-o-CRESOL | 6.1 | T2 | II | 6.1 | 43 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1599 | DINITROPHENOL SOLUTION | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, A |  |  |  |  | 2 |  |
| 1599 | DINITROPHENOL SOLUTION | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, A |  |  |  |  | 0 |  |
| 1600 | DINITROTOLUENES, MOLTEN | 6.1 | T1 | II | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | T2 | I | 6.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | T2 | II | 6.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | T2 | III | 6.1 | 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | I | 6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | II | 6.1 | 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | III | 6.1 | 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1603 | ETHYL BROMOACETATE | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1604 | ETHYLENEDIAMINE | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1605 | ETHYLENE DIBROMIDE | 6.1 | T1 | I | 6.1 | 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1606 | FERRIC ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1607 | FERRIC ARSENITE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1608 | FERROUS ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1611 | HEXAETHYL TETRAPHOSPHATE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1612 | HEXAETHYL TETRAPHOSPHATE AND COMPRESSED GAS MIXTURE | 2 | 1T |  | 2.3 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1613 | HYDROCYANIC ACID, AQUEOUS SOLUTION (HYDROGEN CYANIDE, AQUEOUS SOLUTION) with not more than 20% hydrogen cyanide | 6.1 | TF1 | I | 6.1+3 | 48 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1614 | HYDROGEN CYANIDE, STABILIZED, containing less than 3% water and absorbed in a porous inert material | 6.1 | TF1 | I | 6.1+3 | 603 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1616 | LEAD ACETATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1617 | LEAD ARSENATES | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1618 | LEAD ARSENITES | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1620 | LEAD CYANIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1621 | LONDON PURPLE | 6.1 | T5 | II | 6.1 | 43 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1622 | MAGNESIUM ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1623 | MERCURIC ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1624 | MERCURIC CHLORIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1625 | MERCURIC NITRATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1626 | MERCURIC POTASSIUM CYANIDE | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1627 | MERCUROUS NITRATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1629 | MERCURY ACETATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1630 | MERCURY AMMONIUM CHLORIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1631 | MERCURY BENZOATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1634 | MERCURY BROMIDES | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1636 | MERCURY CYANIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1637 | MERCURY GLUCONATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1638 | MERCURY IODIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1639 | MERCURY NUCLEATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1640 | MERCURY OLEATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1641 | MERCURY OXIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1642 | MERCURY OXYCYANIDE, DESENSITIZED | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1643 | MERCURY POTASSIUM IODIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1644 | MERCURY SALICYLATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1645 | MERCURY SULPHATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1646 | MERCURY THIOCYANATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1647 | METHYL BROMIDE AND ETHYLENE DIBROMIDE MIXTURE, LIQUID | 6.1 | T1 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1648 | ACETONITRILE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1649 | MOTOR FUEL ANTI-KNOCK MIXTURE | 6.1 | T3 | I | 6.1 | 162 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1650 | beta-NAPHTHYLAMINE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1651 | NAPHTHYLTHIOUREA | 6.1 | T2 | II | 6.1 | 43 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1652 | NAPHTHYLUREA | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1653 | NICKEL CYANIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1654 | NICOTINE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 43 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 43 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1656 | NICOTINE HYDROCHLORIDE, liquid or NICOTINE HYDROCHLORIDE SOLUTION | 6.1 | T1 | II | 6.1 | 43 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1656 | NICOTINE HYDROCHLORIDE, solid | 6.1 | T2 | II | 6.1 | 43 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1657 | NICOTINE SALICYLATE, solid | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1658 | NICOTINE SULPHATE, SOLUTION | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, A |  |  |  |  | 2 |  |
| 1658 | NICOTINE SULPHATE, SOLID | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1659 | NICOTINE TARTRATE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1660 | NITRIC OXIDE, COMPRESSED | 2 | 1TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1661 | NITROANILINES (o-, m-, p-) | 6.1 | T2 | II | 6.1 | 279 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1662 | NITROBENZENE | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1663 | NITROPHENOLS (o-, m-, p-) | 6.1 | T2 | III | 6.1 | 279 802 | LQ9 | T | PP, EP |  |  |  |  | 0 |  |
| 1664 | NITROTOLUENES, LIQUID | 6.1 | T1 | II | 6.1 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1664 | NITROTOLUENES, SOLID | 6.1 | T2 | II | 6.1 | 802 | LQ18 | T | PP, EP |  |  |  |  | 2 |  |
| 1665 | NITROXYLENES, LIQUID | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1665 | NITROXYLENES, SOLID | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1669 | PENTACHLOROETHANE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1670 | PERCHLOROMETHYL MERCAPTAN | 6.1 | T1 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1671 | PHENOL, SOLID | 6.1 | T2 | II | 6.1 | 279 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1672 | PHENYLCARBYLAMINE CHLORIDE | 6.1 | T1 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1673 | PHENYLENEDIAMINES (o-, m-, p-) | 6.1 | T2 | III | 6.1 | 279 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1674 | PHENYLMERCURIC ACETATE | 6.1 | T3 | II | 6.1 | 43 802 | LQ18 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1677 | POTASSIUM ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1678 | POTASSIUM ARSENITE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1679 | POTASSIUM CUPROCYANIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1680 | POTASSIUM CYANIDE | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1683 | SILVER ARSENITE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1684 | SILVER CYANIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1685 | SODIUM ARSENATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1686 | SODIUM ARSENITE, AQUEOUS SOLUTION | 6.1 | T4 | II | 6.1 | 43 802 | LQ17 |  | PP, EP |  |  |  |  | 2 |  |
| 1686 | SODIUM ARSENITE, AQUEOUS SOLUTION | 6.1 | T4 | III | 6.1 | 43 802 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1687 | SODIUM AZIDE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1688 | SODIUM CACODYLATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1689 | SODIUM CYANIDE | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1690 | SODIUM FLUORIDE | 6.1 | T5 | III | 6.1 | 802 | LQ9 | B | PP, EP |  |  |  |  | 0 |  |
| 1691 | STRONTIUM ARSENITE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1692 | STRYCHNINE or STRYCHNINE SALTS | 6.1 | T2 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1693 | TEAR GAS SUBSTANCE, LIQUID, N.O.S. | 6.1 | T1 | I | 6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1693 | TEAR GAS SUBSTANCE, LIQUID, N.O.S. | 6.1 | T1 | II | 6.1 | 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1694 | BROMOBENZYL CYANIDES, LIQUID | 6.1 | T1 | I | 6.1 | 138 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1694 | BROMOBENZYL CYANIDES, SOLID | 6.1 | T2 | I | 6.1 | 138 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1695 | CHLOROACETONE, STABILIZED | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1697 | CHLOROACETOPHENONE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1698 | DIPHENYLAMINE CHLOROARSINE | 6.1 | T3 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1699 | DIPHENYLCHLOROARSINE, LIQUID | 6.1 | T3 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1699 | DIPHENYLCHLOROARSINE, SOLID | 6.1 | T3 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1700 | TEAR GAS CANDLES | 6.1 | TF3 | II | 6.1+4.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1701 | XYLYL BROMIDE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1702 | 1,1,2,2-TETRACHLOROETHANE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1704 | TETRAETHYL DITHIOPYROPHOSPHATE | 6.1 | T2 | II | 6.1 | 43 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1707 | THALLIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 43 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1708 | TOLUIDINES, LIQUID | 6.1 | T1 | II | 6.1 | 279 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1708 | TOLUIDINES, SOLID | 6.1 | T2 | II | 6.1 | 279 802 | LQ18 | T | PP, EP |  |  |  |  | 2 |  |
| 1709 | 2,4-TOLUYLENEDIAMINE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1710 | TRICHLOROETHYLENE | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1711 | XYLIDINES, LIQUID | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1711 | XYLIDINES, SOLID | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1712 | ZINC ARSENATE, ZINC ARSENITE or ZINC ARSENATE AND ZINC ARSENITE MIXTURE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1713 | ZINC CYANIDE | 6.1 | T5 | I | 6.1 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1714 | ZINC PHOSPHIDE | 4.3 | WT2 | I | 4.3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 1715 | ACETIC ANHYDRIDE | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1716 | ACETYL BROMIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1717 | ACETYL CHLORIDE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1718 | BUTYL ACID PHOSPHATE | 8 | C3 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1719 | CAUSTIC ALKALI LIQUID, N.O.S. | 8 | C5 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1719 | CAUSTIC ALKALI LIQUID, N.O.S. | 8 | C5 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1722 | ALLYL CHLOROFORMATE | 6.1 | TFC | I | 6.1+3+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1723 | ALLYL IODIDE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1724 | ALLYLTRICHLOROSILANE, STABILIZED | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1725 | ALUMINIUM BROMIDE, ANHYDROUS | 8 | C2 | II | 8 | 588 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1726 | ALUMINIUM CHLORIDE, ANHYDROUS | 8 | C2 | II | 8 | 588 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1727 | AMMONIUM HYDROGENDIFLUORIDE, SOLID | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1728 | AMYLTRICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1729 | ANISOYL CHLORIDE | 8 | C3 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1730 | ANTIMONY PENTACHLORIDE, LIQUID | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1731 | ANTIMONY PENTACHLORIDE SOLUTION | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1731 | ANTIMONY PENTACHLORIDE SOLUTION | 8 | C1 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1732 | ANTIMONY PENTAFLUORIDE | 8 | CT1 | II | 8+6.1 | 802 | LQ22 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1733 | ANTIMONY TRICHLORIDE | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1736 | BENZOYL CHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1737 | BENZYL BROMIDE | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1738 | BENZYL CHLORIDE | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1739 | BENZYL CHLOROFORMATE | 8 | C9 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | C2 | II | 8 | 274 517 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | C2 | III | 8 | 274 517 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 1741 | BORON TRICHLORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX | 8 | C3 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1744 | BROMINE or BROMINE SOLUTION | 8 | CT1 | I | 8+6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1745 | BROMINE PENTAFLUORIDE | 5.1 | OTC | I | 5.1+6.1+8 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1746 | BROMINE TRIFLUORIDE | 5.1 | OTC | I | 5.1+6.1+8 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1747 | BUTYLTRICHLOROSILANE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | O2 | II | 5.1 | 589 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 1749 | CHLORINE TRIFLUORIDE | 2 | 2TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1750 | CHLOROACETIC ACID SOLUTION | 6.1 | TC1 | II | 6.1+8 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1751 | CHLOROACETIC ACID, SOLID | 6.1 | TC2 | II | 6.1+8 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1752 | CHLOROACETYL CHLORIDE | 6.1 | TC1 | I | 6.1+8 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1753 | CHLOROPHENYL- TRICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1754 | CHLOROSULPHONIC ACID (with or without sulphur trioxide) | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1755 | CHROMIC ACID SOLUTION | 8 | C1 | II | 8 | 518 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1755 | CHROMIC ACID SOLUTION | 8 | C1 | III | 8 | 518 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1756 | CHROMIC FLUORIDE, SOLID | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1757 | CHROMIC FLUORIDE SOLUTION | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1757 | CHROMIC FLUORIDE SOLUTION | 8 | C1 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1758 | CHROMIUM OXYCHLORIDE | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | C10 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | C10 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | C10 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | I | 8 | 274 | LQ20 | T | PP, EP |  |  |  |  | 0 |  |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1760 | CORROSIVE LIQUID, N.O.S. | 8 | C9 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1761 | CUPRIETHYLENEDIAMINE SOLUTION | 8 | CT1 | II | 8+6.1 | 802 | LQ22 |  | PP, EP, A |  |  |  |  | 2 |  |
| 1761 | CUPRIETHYLENEDIAMINE SOLUTION | 8 | CT1 | III | 8+6.1 | 802 | LQ19 |  | PP, EP, A |  |  |  |  | 0 |  |
| 1762 | CYCLOHEXENYLTRI- CHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1763 | CYCLOHEXYLTRICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1764 | DICHLOROACETIC ACID | 8 | C3 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1765 | DICHLOROACETYL CHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1766 | DICHLOROPHENYL- TRICHLOROSILANE | 8 | C3 | II | 8 |  | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 1767 | DIETHYLDICHLOROSILANE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1768 | DIFLUOROPHOSPHORIC ACID, ANHYDROUS | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1769 | DIPHENYLDICHLORO-SILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1770 | DIPHENYLMETHYL BROMIDE | 8 | C10 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1771 | DODECYLTRICHLORO- SILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1773 | FERRIC CHLORIDE, ANHYDROUS | 8 | C2 | III | 8 | 590 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 1774 | FIRE EXTINGUISHER CHARGES, corrosive liquid | 8 | C11 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1775 | FLUOROBORIC ACID | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1776 | FLUOROPHOSPHORIC ACID, ANHYDROUS | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1777 | FLUOROSULPHONIC ACID | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1778 | FLUOROSILICIC ACID | 8 | C1 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1779 | FORMIC ACID | 8 | C3 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1780 | FUMARYL CHLORIDE | 8 | C3 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1781 | HEXADECYLTRICHLORO- SILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1782 | HEXAFLUORO- PHOSPHORIC ACID | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1783 | HEXAMETHYLENE- DIAMINE SOLUTION | 8 | C7 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1783 | HEXAMETHYLENE- DIAMINE SOLUTION | 8 | C7 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1784 | HEXYLTRICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1786 | HYDROFLUORIC ACID AND SULPHURIC ACID MIXTURE | 8 | CT1 | I | 8+6.1 | 802 | LQ20 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1787 | HYDRIODIC ACID | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1787 | HYDRIODIC ACID | 8 | C1 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1788 | HYDROBROMIC ACID | 8 | C1 | II | 8 | 519 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1788 | HYDROBROMIC ACID | 8 | C1 | III | 8 | 519 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1789 | HYDROCHLORIC ACID | 8 | C1 | II | 8 | 520 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1789 | HYDROCHLORIC ACID | 8 | C1 | III | 8 | 520 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1790 | HYDROFLUORIC ACID with more than 85% hydrofluoric acid | 8 | CT1 | I | 8+6.1 | 640J 802 | LQ20 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1790 | HYDROFLUORIC ACID with more than 60% but not more than 85% hydrofluoric acid | 8 | CT1 | I | 8+6.1 | 640I 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1790 | HYDROFLUORIC ACID with not more than 60% hydrofluoric acid | 8 | CT1 | II | 8+6.1 | 802 | LQ22 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1791 | HYPOCHLORITE SOLUTION | 8 | C9 | II | 8 | 521 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1791 | HYPOCHLORITE SOLUTION | 8 | C9 | III | 8 | 521 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1792 | IODINE MONOCHLORIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1793 | ISOPROPYL ACID PHOSPHATE | 8 | C3 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1794 | LEAD SULPHATE with more than 3% free acid | 8 | C2 | II | 8 | 591 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1796 | NITRATING ACID MIXTURE with more than 50% nitric acid | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1796 | NITRATING ACID MIXTURE with not more than 50% nitric acid | 8 | CO1 | I | 8+5.1 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1798 | NITROHYDROCHLORIC ACID | 8 | COT |  |  |  |  | forbidden |  |  |  |  |  |  |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1799 | NONYLTRICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1800 | OCTADECYLTRICHLORO- SILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1801 | OCTYLTRICHLOROSILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1802 | PERCHLORIC ACID with not more than 50% acid, by mass | 8 | CO1 | II | 8+5.1 | 522 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1803 | PHENOLSULPHONIC ACID, LIQUID | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1804 | PHENYLTRICHLORO- SILANE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1805 | PHOSPHORIC ACID, LIQUID | 8 | C1 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1805 | PHOSPHORIC ACID, SOLID | 8 | C2 | III | 8 |  | LQ24 | T | PP, EP |  |  |  |  | 0 |  |
| 1806 | PHOSPHORUS PENTACHLORIDE | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1807 | PHOSPHORUS PENTOXIDE | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1808 | PHOSPHORUS TRIBROMIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1809 | PHOSPHORUS TRICHLORIDE | 6.1 | TC3 | I | 6.1+8 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1810 | PHOSPHORUS OXYCHLORIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1811 | POTASSIUM HYDROGENDIFLUORIDE | 8 | CT2 | II | 8+6.1 | 802 | LQ23 |  | PP, EP |  |  |  |  | 2 |  |
| 1812 | POTASSIUM FLUORIDE | 6.1 | T5 | III | 6.1 | 802 | LQ9 | B | PP, EP |  |  |  |  | 0 |  |
| 1813 | POTASSIUM HYDROXIDE, SOLID | 8 | C6 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1814 | POTASSIUM HYDROXIDE SOLUTION | 8 | C5 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1814 | POTASSIUM HYDROXIDE SOLUTION | 8 | C5 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1815 | PROPIONYL CHLORIDE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1816 | PROPYLTRICHLOROSILANE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1817 | PYROSULPHURYL CHLORIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1818 | SILICON TETRACHLORIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1819 | SODIUM ALUMINATE SOLUTION | 8 | C5 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1819 | SODIUM ALUMINATE SOLUTION | 8 | C5 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1823 | SODIUM HYDROXIDE, SOLID | 8 | C6 | II | 8 |  | LQ23 | T | PP, EP |  |  |  |  | 0 |  |
| 1824 | SODIUM HYDROXIDE SOLUTION | 8 | C5 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1824 | SODIUM HYDROXIDE SOLUTION | 8 | C5 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1825 | SODIUM MONOXIDE | 8 | C6 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1826 | NITRATING ACID MIXTURE, SPENT, with more than 50% nitric acid | 8 | C1 | II | 8 | 113 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1826 | NITRATING ACID MIXTURE, SPENT, with not more than 50% nitric acid | 8 | CO1 | I | 8+5.1 | 113 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1827 | STANNIC CHLORIDE, ANHYDROUS | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1828 | SULPHUR CHLORIDES | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1829 | SULPHUR TRIOXIDE, STABILIZED | 8 | C1 | I | 8 | 623 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1830 | SULPHURIC ACID with more than 51% acid | 8 | C1 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1831 | SULPHURIC ACID, FUMING | 8 | CT1 | I | 8+6.1 | 802 | LQ20 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1832 | SULPHURIC ACID, SPENT | 8 | C1 | II | 8 | 113 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 1833 | SULPHUROUS ACID | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1834 | SULPHURYL CHLORIDE | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1835 | TETRAMETHYL- AMMONIUM HYDROXIDE | 8 | C7 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1836 | THIONYL CHLORIDE | 8 | C1 | I | 8 |  | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1837 | THIOPHOSPHORYL CHLORIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1838 | TITANIUM TETRACHLORIDE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1839 | TRICHLOROACETIC ACID | 8 | C4 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1840 | ZINC CHLORIDE SOLUTION | 8 | C1 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1841 | ACETALDEHYDE AMMONIA | 9 | M11 | III | 9 |  | LQ27 |  | PP |  |  |  |  | 0 |  |
| 1843 | AMMONIUM DINITRO-o-CRESOLATE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1845 | Carbon dioxide, solid (Dry ice) | 9 | M11 |  |  |  |  | free |  |  |  |  |  |  |  |
| 1846 | CARBON TETRACHLORIDE | 6.1 | T1 | II | 6.1 | 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1847 | POTASSIUM SULPHIDE, HYDRATED with not less than 30% water of crystallization | 8 | C6 | II | 8 | 523 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1848 | PROPIONIC ACID | 8 | C3 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 1849 | SODIUM SULPHIDE, HYDRATED with not less than 30% water | 8 | C6 | II | 8 | 523 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | II | 6.1 | 221 274 601 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | III | 6.1 | 221 274 601 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1854 | BARIUM ALLOYS, PYROPHORIC | 4.2 | S4 | I | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1855 | CALCIUM, PYROPHORIC or CALCIUM ALLOYS, PYROPHORIC | 4.2 | S4 | I | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1856 | Rags, oily | 4.2 | S2 | NOT SUBJECT TO ADN |
| 1857 | Textile waste, wet | 4.2 | S2 | NOT SUBJECT TO ADN |
| 1858 | HEXAFLUOROPROPYLENE (REFRIGERANT GAS R 1216) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1859 | SILICON TETRAFLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1860 | VINYL FLUORIDE, STABILIZED | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1862 | ETHYL CROTONATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 1863 | FUEL, AVIATION, TURBINE ENGINE (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1863 | FUEL, AVIATION, TURBINE ENGINE (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1863 | FUEL, AVIATION, TURBINE ENGINE (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1863 | FUEL, AVIATION, TURBINE ENGINE (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1863 | FUEL, AVIATION, TURBINE ENGINE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1865 | n-PROPYL NITRATE | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1866 | RESIN SOLUTION, flammable (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 640A | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1866 | RESIN SOLUTION, flammable (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 640B | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1866 | RESIN SOLUTION, flammable (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 640C | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1866 | RESIN SOLUTION, flammable (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 640D | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1866 | RESIN SOLUTION, flammable | 3 | F1 | III | 3 | 640E | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1866 | RESIN SOLUTION, flammable (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | III | 3 | 640F | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1866 | RESIN SOLUTION, flammable (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 640G | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1866 | RESIN SOLUTION, flammable (having a flash-point below 23 °C and viscous according to 2.2.3.1.4) (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | III | 3 | 640H | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1868 | DECABORANE | 4.1 | FT2 | II | 4.1+6.1 | 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 1869 | MAGNESIUM or MAGNESIUM ALLOYS with more than 50% magnesium in pellets, turnings or ribbons | 4.1 | F3 | III | 4.1 | 59 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 1870 | POTASSIUM BOROHYDRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 1871 | TITANIUM HYDRIDE | 4.1 | F3 | II | 4.1 |  | LQ8 |  | PP |  |  |  |  | 1 |  |
| 1872 | LEAD DIOXIDE | 5.1 | OT2 | III | 5.1+6.1 | 802 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 1873 | PERCHLORIC ACID with more than 50% but not more than 72% acid, by mass | 5.1 | OC1 | I | 5.1+8 | 60 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 1884 | BARIUM OXIDE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 1885 | BENZIDINE | 6.1 | T2 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 1886 | BENZYLIDENE CHLORIDE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1887 | BROMOCHLOROMETHANE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1888 | CHLOROFORM | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1889 | CYANOGEN BROMIDE | 6.1 | TC2 | I | 6.1+8 | 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 1891 | ETHYL BROMIDE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1892 | ETHYLDICHLOROARSINE | 6.1 | T3 | I | 6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1894 | PHENYLMERCURIC HYDROXIDE | 6.1 | T3 | II | 6.1 | 802 | LQ18 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1895 | PHENYLMERCURIC NITRATE | 6.1 | T3 | II | 6.1 | 802 | LQ18 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1897 | TETRACHLOROETHYLENE | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 1898 | ACETYL IODIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1902 | DIISOOCTYL ACID PHOSPHATE | 8 | C3 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 | C9 | I | 8 | 274 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 | C9 | II | 8 | 274 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 | C9 | III | 8 | 274 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1905 | SELENIC ACID | 8 | C2 | I | 8 |  | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 1906 | SLUDGE ACID | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1907 | SODA LIME with more than 4% sodium hydroxide | 8 | C6 | III | 8 | 62 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 1908 | CHLORITE SOLUTION | 8 | C9 | II | 8 | 521 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 1908 | CHLORITE SOLUTION | 8 | C9 | III | 8 | 521 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 1910 | Calcium oxide | 8 | C6 |  |  |  |  | free |  |  |  |  |  |  |  |
| 1911 | DIBORANE | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1912 | METHYL CHLORIDE AND METHYLENE CHLORIDE MIXTURE | 2 | 2F |  | 2.1 | 228 | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1913 | NEON, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1914 | BUTYL PROPIONATES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1915 | CYCLOHEXANONE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1916 | 2,2'-DICHLORODIETHYL ETHER | 6.1 | TF1 | II | 6.1+3 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1917 | ETHYL ACRYLATE, STABILIZED | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1918 | ISOPROPYLBENZENE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1919 | METHYL ACRYLATE, STABILIZED | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1920 | NONANES | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |