| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2784 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2784 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2785 | 4-THIAPENTANAL | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2787 | ORGANOTIN PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2787 | ORGANOTIN PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2788 | ORGANOTIN COMPOUND, LIQUID, N.O.S. | 6.1 | T3 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2788 | ORGANOTIN COMPOUND, LIQUID, N.O.S. | 6.1 | T3 | II | 6.1 | 43 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2788 | ORGANOTIN COMPOUND, LIQUID, N.O.S. | 6.1 | T3 | III | 6.1 | 43 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2789 | ACETIC ACID, GLACIAL or ACETIC ACID SOLUTION, more than 80% acid, by mass | 8 | CF1 | II | 8+3 |  | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2790 | ACETIC ACID SOLUTION, not less than 50% but not more than 80% acid, by mass | 8 | C3 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2790 | ACETIC ACID SOLUTION, more than 10% and less than 50% acid, by mass | 8 | C3 | III | 8 | 597 647 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2793 | FERROUS METAL BORINGS, SHAVINGS, TURNINGS or CUTTINGS in a form liable to self-heating | 4.2 | S4 | III | 4.2 | 592 | LQ0 | B | PP |  | LO02 |  |  | 0 | LO02 applies only when this substance is carried in bulk or without packaging |
| 2794 | BATTERIES, WET, FILLED WITH ACID, electric storage | 8 | C11 |  | 8 | 295 598 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 2795 | BATTERIES, WET, FILLED WITH ALKALI, electric storage | 8 | C11 |  | 8 | 295 598 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 2796 | SULPHURIC ACID with not more than 51% acid or BATTERY FLUID, ACID | 8 | C1 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2797 | BATTERY FLUID, ALKALI | 8 | C5 | II | 8 |  | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 2798 | PHENYLPHOSPHORUS DICHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2799 | PHENYLPHOSPHORUS THIODICHLORIDE | 8 | C3 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2800 | BATTERIES, WET, NON-SPILLABLE, electric storage | 8 | C11 |  | 8 | 238 295 598 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 2801 | DYE, LIQUID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, LIQUID, CORROSIVE, N.O.S. | 8 | C9 | I | 8 | 274 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 2801 | DYE, LIQUID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, LIQUID, CORROSIVE, N.O.S. | 8 | C9 | II | 8 | 274 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2801 | DYE, LIQUID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, LIQUID, CORROSIVE, N.O.S. | 8 | C9 | III | 8 | 274 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2802 | COPPER CHLORIDE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2803 | GALLIUM | 8 | C10 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2805 | LITHIUM HYDRIDE, FUSED SOLID | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2806 | LITHIUM NITRIDE | 4.3 | W2 | I | 4.3 |  | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2807 | Magnetized material | 9 | M11 | NOT SUBJECT TO ADN |
| 2809 | MERCURY | 8 | C9 | III | 8 | 599 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. | 6.1 | T1 | I | 6.1 | 274 614 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. | 6.1 | T1 | II | 6.1 | 274 614 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. | 6.1 | T1 | III | 6.1 | 274 614 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | T2 | I | 6.1 | 274 614 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | T2 | II | 6.1 | 274 614 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | T2 | III | 6.1 | 274 614 802 | LQ9 | T | PP, EP |  |  |  |  | 0 |  |
| 2812 | Sodium aluminate, solid | 8 | C6 | NOT SUBJECT TO ADN |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | W2 | I | 4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | W2 | II | 4.3 | 274 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | W2 | III | 4.3 | 274 | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2814 | INFECTIOUS SUBSTANCE, AFFECTING HUMANS (risk groups 3 and 4) | 6.2 | I1 |  | 6.2 | 274 634 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2814 | INFECTIOUS SUBSTANCE, AFFECTING HUMANS (risk group 2) | 6.2 | I1 |  | 6.2 | 274 634 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2815 | N-AMINOETHYL- PIPERAZINE | 8 | C7 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2817 | AMMONIUM HYDROGENDIFLUORIDE SOLUTION | 8 | CT1 | II | 8+6.1 | 802 | LQ22 |  | PP, EP |  |  |  |  | 2 |  |
| 2817 | AMMONIUM HYDROGENDIFLUORIDE SOLUTION | 8 | CT1 | III | 8+6.1 | 802 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2818 | AMMONIUM POLYSULPHIDE SOLUTION | 8 | CT1 | II | 8+6.1 | 802 | LQ22 |  | PP, EP |  |  |  |  | 2 |  |
| 2818 | AMMONIUM POLYSULPHIDE SOLUTION | 8 | CT1 | III | 8+6.1 | 802 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2819 | AMYL ACID PHOSPHATE | 8 | C3 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2820 | BUTYRIC ACID | 8 | C3 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2821 | PHENOL SOLUTION | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2821 | PHENOL SOLUTION | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2822 | 2-CHLOROPYRIDINE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2823 | CROTONIC ACID | 8 | C4 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2826 | ETHYL CHLOROTHIOFORMATE | 8 | CF1 | II | 8+3 |  | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2829 | CAPROIC ACID | 8 | C3 | III | 8 |  | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 2830 | LITHIUM FERROSILICON | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2831 | 1,1,1-TRICHLOROETHANE | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2834 | PHOSPHOROUS ACID | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2835 | SODIUM ALUMINIUM HYDRIDE | 4.3 | W2 | II | 4.3 |  | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2837 | BISULPHATES, AQUEOUS SOLUTION | 8 | C1 | II | 8 | 274 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2837 | BISULPHATES, AQUEOUS SOLUTION | 8 | C1 | III | 8 | 274 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2838 | VINYL BUTYRATE, STABILIZED | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 2839 | ALDOL | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2840 | BUTYRALDOXIME | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2841 | DI-n-AMYLAMINE | 3 | FT1 | III | 3+6.1 | 802 | LQ7 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2842 | NITROETHANE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 | W2 | III | 4.3 |  | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2845 | PYROPHORIC LIQUID, ORGANIC, N.O.S. | 4.2 | S1 | I | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2846 | PYROPHORIC SOLID, ORGANIC, N.O.S. | 4.2 | S2 | I | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2849 | 3-CHLOROPROPANOL-1 | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2850 | PROPYLENE TETRAMER | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2851 | BORON TRIFLUORIDE DIHYDRATE | 8 | C1 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2852 | DIPICRYL SULPHIDE, WETTED with not less than 10% water, by mass | 4.1 | D | I | 4.1 | 545 | LQ0 |  | PP |  |  |  |  | 1 |  |
| 2853 | MAGNESIUM FLUOROSILICATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2854 | AMMONIUM FLUOROSILICATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2855 | ZINC FLUOROSILICATE | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2856 | FLUOROSILICATES, N.O.S. | 6.1 | T5 | III | 6.1 | 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2857 | REFRIGERATING MACHINES containing non-flammable, non-toxic, liquefied gas or ammonia solutions (UN 2672) | 2 | 6A |  | 2.2 | 119 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2858 | ZIRCONIUM, DRY, coiled wire, finished metal sheets, strip (thinner than 254 microns but not thinner than 18 microns) | 4.1 | F3 | III | 4.1 | 546 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2859 | AMMONIUM METAVANADATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2861 | AMMONIUM POLYVANADATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2862 | VANADIUM PENTOXIDE, non-fused form | 6.1 | T5 | III | 6.1 | 600 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2863 | SODIUM AMMONIUM VANADATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2864 | POTASSIUM METAVANADATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2865 | HYDROXYLAMINE SULPHATE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | C2 | II | 8 |  | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2870 | ALUMINIUM BOROHYDRIDE | 4.2 | SW | I | 4.2+4.3 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2870 | ALUMINIUM BOROHYDRIDE IN DEVICES | 4.2 | SW | I | 4.2+4.3 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2871 | ANTIMONY POWDER | 6.1 | T5 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2872 | DIBROMOCHLORO- PROPANES | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2872 | DIBROMOCHLORO-PROPANES | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2873 | DIBUTYLAMINOETHANOL | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2874 | FURFURYL ALCOHOL | 6.1 | T1 | III | 6.1 | 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2875 | HEXACHLOROPHENE | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2876 | RESORCINOL | 6.1 | T2 | III | 6.1 | 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 2878 | TITANIUM SPONGE GRANULES or TITANIUM SPONGE POWDERS | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2879 | SELENIUM OXYCHLORIDE | 8 | CT1 | I | 8+6.1 | 802 | LQ20 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED, or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% but not more than 16% water | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 2881 | METAL CATALYST, DRY | 4.2 | S4 | I | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2881 | METAL CATALYST, DRY | 4.2 | S4 | II | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2881 | METAL CATALYST, DRY | 4.2 | S4 | III | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2900 | INFECTIOUS SUBSTANCE, AFFECTING ANIMALS only (risk group 2) | 6.2 | I2 |  | 6.2 | 274 634 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2900 | INFECTIOUS SUBSTANCE, AFFECTING ANIMALS only (risk groups 3 and 4) | 6.2 | I2 |  | 6.2 | 274 634 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2901 | BROMINE CHLORIDE | 2 | 2TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2902 | PESTICIDE, LIQUID, TOXIC, N.O.S. | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2902 | PESTICIDE, LIQUID, TOXIC, N.O.S. | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2902 | PESTICIDE, LIQUID, TOXIC, N.O.S. | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2903 | PESTICIDE, LIQUID, TOXIC, FLAMMABLE, N.O.S., flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2903 | PESTICIDE, LIQUID, TOXIC, FLAMMABLE, N.O.S., flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2903 | PESTICIDE, LIQUID, TOXIC, FLAMMABLE, N.O.S., flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 2904 | CHLOROPHENOLATES, LIQUID or PHENOLATES, LIQUID | 8 | C9 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 2905 | CHLOROPHENOLATES, SOLID or PHENOLATES, SOLID | 8 | C10 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2907 | ISOSORBIDE DINITRATE MIXTURE with not less than 60% lactose, mannose, starch or calcium hydrogen phosphate | 4.1 | D | II | 4.1 | 127 | LQ8 |  | PP |  |  |  |  | 0 |  |
| 2908 | RADIOACTIVE MATERIAL, EXCEPTED PACKAGE - EMPTY PACKAGING | 7 |  |  |  | 290 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2909 | RADIOACTIVE MATERIAL, EXCEPTED PACKAGE - ARTICLES MANUFACTURED FROM NATURAL URANIUM or DEPLETED URANIUM or NATURAL THORIUM | 7 |  |  |  | 290 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2910 | RADIOACTIVE MATERIAL, EXCEPTED PACKAGE - LIMITED QUANTITY OF MATERIAL | 7 |  |  |  | 290 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2911 | RADIOACTIVE MATERIAL, EXCEPTED PACKAGE - INSTRUMENTS or ARTICLES | 7 |  |  |  | 290 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2912 | RADIOACTIVE MATERIAL, LOW SPECIFIC ACTIVITY (LSA-I), non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 | B | PP |  |  |  | RA01 | 2 |  |
| 2913 | RADIOACTIVE MATERIAL, SURFACE CONTAMINATED OBJECTS (SCO-I or SCO-II), non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 | B | PP |  |  |  | RA02, RA03 | 2 |  |
| 2915 | RADIOACTIVE MATERIAL, TYPE A PACKAGE, non-special form, non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 2916 | RADIOACTIVE MATERIAL, TYPE B(U) PACKAGE, non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 2917 | RADIOACTIVE MATERIAL, TYPE B(M) PACKAGE, non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 2919 | RADIOACTIVE MATERIAL, TRANSPORTED UNDER SPECIAL ARRANGEMENT, non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 2920 | CORROSIVE LIQUID, FLAMMABLE, N.O.S. | 8 | CF1 | I | 8+3 | 274 | LQ20 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2920 | CORROSIVE LIQUID, FLAMMABLE, N.O.S. | 8 | CF1 | II | 8+3 | 274 | LQ22 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | CF2 | I | 8+4.1 | 274 | LQ21 |  | PP, EP |  |  |  |  | 1 |  |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | CF2 | II | 8+4.1 | 274 | LQ23 |  | PP, EP |  |  |  |  | 1 |  |
| 2922 | CORROSIVE LIQUID, TOXIC, N.O.S. | 8 | CT1 | I | 8+6.1 | 274 802 | LQ20 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2922 | CORROSIVE LIQUID, TOXIC, N.O.S. | 8 | CT1 | II | 8+6.1 | 274 802 | LQ22 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2922 | CORROSIVE LIQUID, TOXIC, N.O.S. | 8 | CT1 | III | 8+6.1 | 274 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | CT2 | I | 8+6.1 | 274 802 | LQ21 |  | PP, EP |  |  |  |  | 2 |  |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | CT2 | II | 8+6.1 | 274 802 | LQ23 |  | PP, EP |  |  |  |  | 2 |  |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | CT2 | III | 8+6.1 | 274 802 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | 3 | FC | I | 3+8 | 274 | LQ3 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | 3 | FC | II | 3+8 | 274 | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | 3 | FC | III | 3+8 | 274 | LQ7 | T | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | FC1 | II | 4.1+8 | 274 | LQ0 |  | PP |  |  |  |  | 1 |  |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | FC1 | III | 4.1+8 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | FT1 | II | 4.1+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | FT1 | III | 4.1+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2927 | TOXIC LIQUID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | TC1 | I | 6.1+8 | 274 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2927 | TOXIC LIQUID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | TC1 | II | 6.1+8 | 274 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | TC2 | I | 6.1+8 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | TC2 | II | 6.1+8 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | TF1 | I | 6.1+3 | 274 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | TF1 | II | 6.1+3 | 274 802 | LQ17 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | TF3 | I | 6.1+4.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | TF3 | II | 6.1+4.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2931 | VANADYL SULPHATE | 6.1 | T5 | II | 6.1 | 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 2933 | METHYL 2-CHLOROPROPIONATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2934 | ISOPROPYL 2-CHLOROPROPIONATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2935 | ETHYL 2-CHLOROPROPIONATE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2936 | THIOLACTIC ACID | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2937 | alpha-METHYLBENZYL ALCOHOL | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2940 | 9-PHOSPHABICYCLONO- NANES (CYCLOOCTADIENE PHOSPHINES) | 4.2 | S2 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2941 | FLUOROANILINES | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2942 | 2-TRIFLUOROMETHYL- ANILINE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2943 | TETRAHYDROFURFURY- LAMINE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2945 | N-METHYLBUTYLAMINE | 3 | FC | II | 3+8 |  | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2946 | 2-AMINO-5-DIETHYLAMINOPENTANE | 6.1 | T1 | III | 6.1 | 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2947 | ISOPROPYL CHLOROACETATE | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 2948 | 3-TRIFLUOROMETHYL- ANILINE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2949 | SODIUM HYDROSULPHIDE with not less than 25% water of crystallization | 8 | C6 | II | 8 | 523 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 | W2 | III | 4.3 |  | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2956 | 5-tert-BUTYL-2,4,6-TRINITRO-m-XYLENE (MUSK XYLENE) | 4.1 | SR1 | III | 4.1 | 638 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2965 | BORON TRIFLUORIDE DIMETHYL ETHERATE | 4.3 | WFC | I | 4.3+3+8 |  | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 2966 | THIOGLYCOL | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2967 | SULPHAMIC ACID | 8 | C2 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 | W2 | III | 4.3 | 547 | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 2969 | CASTOR BEANS or CASTOR MEAL or CASTOR POMACE or CASTOR FLAKE | 9 | M11 | II | 9 | 141 | LQ25 | B | PP |  |  |  |  | 0 |  |
| 2977 | RADIOACTIVE MATERIAL, URANIUM HEXAFLUORIDE, FISSILE | 7 |  |  | 7X+7E+8 | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 2978 | RADIOACTIVE MATERIAL, URANIUM HEXAFLUORIDE, non fissile or fissile-excepted | 7 |  |  | 7X+8 | 172 | LQ0 | B | PP |  |  |  | RA01 | 2 |  |
| 2983 | ETHYLENE OXIDE AND PROPYLENE OXIDE MIXTURE, not more than 30% ethylene oxide | 3 | FT1 | I | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2984 | HYDROGEN PEROXIDE, AQUEOUS SOLUTION with not less than 8% but less than 20% hydrogen peroxide (stabilized as necessary) | 5.1 | O1 | III | 5.1 | 65 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 2985 | CHLOROSILANES, FLAMMABLE, CORROSIVE, N.O.S. | 3 | FC | II | 3+8 | 274 548 | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2986 | CHLOROSILANES, CORROSIVE, FLAMMABLE, N.O.S. | 8 | CF1 | II | 8+3 | 274 548 | LQ22 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 2987 | CHLOROSILANES, CORROSIVE, N.O.S. | 8 | C3 | II | 8 | 274 548 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | 4.3 | WFC | I | 4.3+3+8 | 274 549 | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | F3 | II | 4.1 |  | LQ8 |  | PP |  |  |  |  | 1 |  |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | F3 | III | 4.1 |  | LQ9 |  | PP |  |  |  |  | 0 |  |
| 2990 | LIFE-SAVING APPLIANCES, SELF-INFLATING | 9 | M5 |  | 9 | 296 635 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 2991 | CARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2991 | CARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2991 | CARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 2992 | CARBAMATE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2992 | CARBAMATE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2992 | CARBAMATE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2993 | ARSENICAL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2993 | ARSENICAL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2993 | ARSENICAL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 2994 | ARSENICAL PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2994 | ARSENICAL PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2994 | ARSENICAL PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2995 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2995 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2995 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 2996 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2996 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2996 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 2997 | TRIAZINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2997 | TRIAZINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 2997 | TRIAZINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 2998 | TRIAZINE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2998 | TRIAZINE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 2998 | TRIAZINE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3005 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3005 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3005 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3006 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3006 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3006 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3009 | COPPER BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3009 | COPPER BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3009 | COPPER BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3010 | COPPER BASED PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3010 | COPPER BASED PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3010 | COPPER BASED PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3011 | MERCURY BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3011 | MERCURY BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3011 | MERCURY BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3012 | MERCURY BASED PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3012 | MERCURY BASED PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3012 | MERCURY BASED PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3013 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3013 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3013 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3014 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3014 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3014 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3015 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3015 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3015 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3016 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3016 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3016 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3017 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3017 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3017 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3018 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3018 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3018 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 3019 | ORGANOTIN PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3019 | ORGANOTIN PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3019 | ORGANOTIN PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3020 | ORGANOTIN PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3020 | ORGANOTIN PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3020 | ORGANOTIN PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3021 | PESTICIDE, LIQUID, FLAMMABLE, TOXIC, N.O.S., flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3021 | PESTICIDE, LIQUID, FLAMMABLE, TOXIC, N.O.S., flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3022 | 1,2-BUTYLENE OXIDE, STABILIZED | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3023 | 2-METHYL-2-HEPTANETHIOL | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3024 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3024 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3025 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3025 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3025 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3026 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3026 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3026 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3028 | BATTERIES, DRY, CONTAINING POTASSIUM HYDROXIDE SOLID, electric storage | 8 | C11 |  | 8 | 295 304 598 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 3048 | ALUMINIUM PHOSPHIDE PESTICIDE | 6.1 | T7 | I | 6.1 | 61 153 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3049 | METAL ALKYL HALIDES, WATER-REACTIVE, N.O.S. or METAL ARYL HALIDES, WATER-REACTIVE, N.O.S. | 4.2 | SW | I | 4.2+4.3 | 274 527 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3050 | METAL ALKYL HYDRIDES, WATER-REACTIVE, N.O.S. or METAL ARYL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.2 | SW | I | 4.2+4.3 | 274 527 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3051 | ALUMINIUM ALKYLS | 4.2 | SW | I | 4.2+4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3052 | ALUMINIUM ALKYL HALIDES, LIQUID | 4.2 | SW | I | 4.2+4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3052 | ALUMINIUM ALKYL HALIDES, SOLID | 4.2 | SW | I | 4.2+4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3053 | MAGNESIUM ALKYLS | 4.2 | SW | I | 4.2+4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3054 | CYCLOHEXYL MERCAPTAN | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3055 | 2-(2-AMINOETHOXY) ETHANOL | 8 | C7 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 3056 | n-HEPTALDEHYDE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3057 | TRIFLUOROACETYL CHLORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3064 | NITROGLYCERIN, SOLUTION IN ALCOHOL with more than 1% but not more than 5% nitroglycerin | 3 | D | II | 3 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3065 | ALCOHOLIC BEVERAGES, with more than 70% alcohol by volume | 3 | F1 | II | 3 |  | LQ5 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3065 | ALCOHOLIC BEVERAGES, with more than 24% but not more than 70% alcohol by volume | 3 | F1 | III | 3 | 144 145 247 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3066 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) | 8 | C9 | II | 8 | 163 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 3066 | PAINT (including paint, lacquer, enamel, stain, shellac, varnish, polish, liquid filler and liquid lacquer base) or PAINT RELATED MATERIAL (including paint thinning and reducing compound) | 8 | C9 | III | 8 | 163 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 3070 | ETHYLENE OXIDE AND DICHLORODIFLUORO- METHANE MIXTURE with not more than 12.5% ethylene oxide | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3071 | MERCAPTANS, LIQUID, TOXIC, FLAMMABLE, N.O.S. or MERCAPTAN MIXTURE, LIQUID, TOXIC, FLAMMABLE, N.O.S. | 6.1 | TF1 | II | 6.1+3 | 274 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3072 | LIFE-SAVING APPLIANCES NOT SELF-INFLATING containing dangerous goods as equipment | 9 | M5 |  | 9 | 296 635 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3073 | VINYLPYRIDINES, STABILIZED | 6.1 | TFC | II | 6.1+3+8 | 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3076 | ALUMINIUM ALKYL HYDRIDES | 4.2 | SW | I | 4.2+4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3077 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S. | 9 | M7 | III | 9 | 274 | LQ27 | T | PP |  |  |  |  | 0 |  |
| 3078 | CERIUM, turnings or gritty powder | 4.3 | W2 | II | 4.3 | 550 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3079 | METHACRYLONITRILE, STABILIZED | 3 | FT1 | I | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3080 | ISOCYANATES, TOXIC, FLAMMABLE, N.O.S. or ISOCYANATE SOLUTION, TOXIC, FLAMMABLE, N.O.S. | 6.1 | TF1 | II | 6.1+3 | 274 551 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3082 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S. | 9 | M6 | III | 9 | 274 | LQ28 | T | PP |  |  |  |  | 0 |  |
| 3083 | PERCHLORYL FLUORIDE | 2 | 2TO |  | 2.3+5.1 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | CO2 | I | 8+5.1 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | CO2 | II | 8+5.1 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | OC2 | I | 5.1+8 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | OC2 | II | 5.1+8 | 274 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | OC2 | III | 5.1+8 | 274 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | TO2 | I | 6.1+5.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | TO2 | II | 6.1+5.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | OT2 | I | 5.1+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | OT2 | II | 5.1+6.1 | 274 802 | LQ11 |  | PP |  |  |  |  | 2 |  |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | OT2 | III | 5.1+6.1 | 274 802 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | S2 | II | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | S2 | III | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | F3 | II | 4.1 | 274 552 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | F3 | III | 4.1 | 274 552 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 3090 | LITHIUM BATTERIES | 9 | M4 | II | 9 | 188 230 310 636 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3091 | LITHIUM BATTERIES CONTAINED IN EQUIPMENT or LITHIUM BATTERIES PACKED WITH EQUIPMENT | 9 | M4 | II | 9 | 188 230 636 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3092 | 1-METHOXY-2-PROPANOL | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3093 | CORROSIVE LIQUID, OXIDIZING, N.O.S. | 8 | CO1 | I | 8+5.1 | 274 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 3093 | CORROSIVE LIQUID, OXIDIZING, N.O.S. | 8 | CO1 | II | 8+5.1 | 274 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 3094 | CORROSIVE LIQUID, WATER-REACTIVE, N.O.S. | 8 | CW1 | I | 8+4.3 | 274 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 3094 | CORROSIVE LIQUID, WATER-REACTIVE, N.O.S. | 8 | CW1 | II | 8+4.3 | 274 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | CS2 | I | 8+4.2 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | CS2 | II | 8+4.2 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | CW2 | I | 8+4.3 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | CW2 | II | 8+4.3 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3097 | FLAMMABLE SOLID, OXIDIZING, N.O.S. | 4.1 | FO |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3098 | OXIDIZING LIQUID, CORROSIVE, N.O.S. | 5.1 | OC1 | I | 5.1+8 | 274 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 3098 | OXIDIZING LIQUID, CORROSIVE, N.O.S. | 5.1 | OC1 | II | 5.1+8 | 274 | LQ10 |  | PP, EP |  |  |  |  | 0 |  |
| 3098 | OXIDIZING LIQUID, CORROSIVE, N.O.S. | 5.1 | OC1 | III | 5.1+8 | 274 | LQ13 |  | PP, EP |  |  |  |  | 0 |  |
| 3099 | OXIDIZING LIQUID, TOXIC, N.O.S. | 5.1 | OT1 | I | 5.1+6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3099 | OXIDIZING LIQUID, TOXIC, N.O.S. | 5.1 | OT1 | II | 5.1+6.1 | 274 802 | LQ10 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3099 | OXIDIZING LIQUID, TOXIC, N.O.S. | 5.1 | OT1 | III | 5.1+6.1 | 274 802 | LQ13 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3100 | OXIDIZING SOLID, SELF-HEATING, N.O.S. | 5.1 | OS |  |  |  | CARRIAGE FORBIDDEN |  |  |  |  |  |  |
| 3101 | ORGANIC PEROXIDE TYPE B, LIQUID | 5.2 | P1 |  | 5.2+1 | 122 181 274 | LQ14 |  | PP, EX, A | VE01 |  | HA01, HA10 |  | 3 |  |
| 3102 | ORGANIC PEROXIDE TYPE B, SOLID | 5.2 | P1 |  | 5.2+1 | 122 181 274 | LQ15 |  | PP, EX, A | VE01 |  | HA01, HA10 |  | 3 |  |
| 3103 | ORGANIC PEROXIDE TYPE C, LIQUID | 5.2 | P1 |  | 5.2 | 122 274 | LQ14 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3104 | ORGANIC PEROXIDE TYPE C, SOLID | 5.2 | P1 |  | 5.2 | 122 274 | LQ15 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3105 | ORGANIC PEROXIDE TYPE D, LIQUID | 5.2 | P1 |  | 5.2 | 122 274 | LQ16 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3106 | ORGANIC PEROXIDE TYPE D, SOLID | 5.2 | P1 |  | 5.2 | 122 274 | LQ11 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3107 | ORGANIC PEROXIDE TYPE E, LIQUID | 5.2 | P1 |  | 5.2 | 122 274 | LQ16 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3108 | ORGANIC PEROXIDE TYPE E, SOLID | 5.2 | P1 |  | 5.2 | 122 274 | LQ11 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3109 | ORGANIC PEROXIDE TYPE F, LIQUID | 5.2 | P1 |  | 5.2 | 122 274 | LQ16 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3110 | ORGANIC PEROXIDE TYPE F, SOLID | 5.2 | P1 |  | 5.2 | 122 274 | LQ11 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3111 | ORGANIC PEROXIDE TYPE B, LIQUID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2+1 | 122 181 274 | LQ0 |  | PP, EX, A | VE01 |  | HA01, HA10 |  | 3 |  |
| 3112 | ORGANIC PEROXIDE TYPE B, SOLID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2+1 | 122 181 274 | LQ0 |  | PP, EX, A | VE01 |  | HA01, HA10 |  | 3 |  |
| 3113 | ORGANIC PEROXIDE TYPE C, LIQUID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3114 | ORGANIC PEROXIDE TYPE C, SOLID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3115 | ORGANIC PEROXIDE TYPE D, LIQUID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3116 | ORGANIC PEROXIDE TYPE D, SOLID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3117 | ORGANIC PEROXIDE TYPE E, LIQUID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3118 | ORGANIC PEROXIDE TYPE E, SOLID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3119 | ORGANIC PEROXIDE TYPE F, LIQUID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3120 | ORGANIC PEROXIDE TYPE F, SOLID, TEMPERATURE CONTROLLED | 5.2 | P2 |  | 5.2 | 122 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3121 | OXIDIZING SOLID, WATER-REACTIVE, N.O.S. | 5.1 | OW |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3122 | TOXIC LIQUID, OXIDIZING, N.O.S. | 6.1 | TO1 | I | 6.1+5.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3122 | TOXIC LIQUID, OXIDIZING, N.O.S. | 6.1 | TO1 | II | 6.1+5.1 | 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3123 | TOXIC LIQUID, WATER-REACTIVE, N.O.S. | 6.1 | TW1 | I | 6.1+4.3 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3123 | TOXIC LIQUID, WATER-REACTIVE, N.O.S. | 6.1 | TW1 | II | 6.1+4.3 | 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | TS | I | 6.1+4.2 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | TS | II | 6.1+4.2 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | TW2 | I | 6.1+4.3 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | TW2 | II | 6.1+4.3 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | SC2 | II | 4.2+8 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | SC2 | III | 4.2+8 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S | 4.2 | SO |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | ST2 | II | 4.2+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | ST2 | III | 4.2+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | WC1 | I | 4.3+8 | 274 | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | WC1 | II | 4.3+8 | 274 | LQ10 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | WC1 | III | 4.3+8 | 274 | LQ13 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | WT1 | I | 4.3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | WT1 | II | 4.3+6.1 | 274 802 | LQ10 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 2 |  |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | WT1 | III | 4.3+6.1 | 274 802 | LQ13 |  | PP, EP, EX, TOX, A | VE01, VE02 |  | HA08 |  | 0 |  |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | WC2 | I | 4.3+8 | 274 | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | WC2 | II | 4.3+8 | 274 | LQ11 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | WC2 | III | 4.3+8 | 274 | LQ12 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 0 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | WF2 |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3133 | WATER-REACTIVE SOLID, OXIDIZING, N.O.S. | 4.3 | WO |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | WT2 | I | 4.3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 2 |  |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | WT2 | II | 4.3+6.1 | 274 802 | LQ11 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 2 |  |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | WT2 | III | 4.3+6.1 | 274 802 | LQ12 |  | PP, EP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | WS |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3136 | TRIFLUOROMETHANE, REFRIGERATED LIQUID | 2 | 3A |  | 2.2 | 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3137 | OXIDIZING SOLID, FLAMMABLE, N.O.S. | 5.1 | OF |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3138 | ETHYLENE, ACETYLENE AND PROPYLENE MIXTURE, REFRIGERATED LIQUID containing at least 71.5% ethylene with not more than 22.5% acetylene and not more than 6% propylene | 2 | 3F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3139 | OXIDIZING LIQUID, N.O.S. | 5.1 | O1 | I | 5.1 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3139 | OXIDIZING LIQUID, N.O.S. | 5.1 | O1 | II | 5.1 | 274 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 3139 | OXIDIZING LIQUID, N.O.S. | 5.1 | O1 | III | 5.1 | 274 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 3140 | ALKALOIDS, LIQUID, N.O.S. or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 | T1 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3140 | ALKALOIDS, LIQUID, N.O.S. or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 | T1 | II | 6.1 | 43 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3140 | ALKALOIDS, LIQUID, N.O.S. or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 | T1 | III | 6.1 | 43 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3141 | ANTIMONY COMPOUND, INORGANIC, LIQUID, N.O.S. | 6.1 | T4 | III | 6.1 | 45 274 512 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | I | 6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | II | 6.1 | 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | III | 6.1 | 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | T2 | I | 6.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | T2 | II | 6.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | T2 | III | 6.1 | 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 | T1 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 | T1 | II | 6.1 | 43 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 | T1 | III | 6.1 | 43 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | I | 8 | 274 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | T3 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | T3 | II | 6.1 | 43 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | T3 | III | 6.1 | 43 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | C10 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | C10 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | C10 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 | W1 | I | 4.3 | 274 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 | W1 | II | 4.3 | 274 | LQ10 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 | W1 | III | 4.3 | 274 | LQ13 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3149 | HYDROGEN PEROXIDE AND PEROXYACETIC ACID MIXTURE with acid(s), water and not more than 5% peroxyacetic acid, STABILIZED | 5.1 | OC1 | II | 5.1+8 | 196 553 | LQ10 |  | PP, EP |  |  |  |  | 0 |  |
| 3150 | DEVICES, SMALL, HYDROCARBON GAS POWERED or HYDROCARBON GAS REFILLS FOR SMALL DEVICES with release device | 2 | 6F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3151 | POLYHALOGENATED BIPHENYLS, LIQUID or POLYHALOGENATED TERPHENYLS, LIQUID | 9 | M2 | II | 9 | 203 305 802 | LQ29 |  | PP, EP |  |  |  |  | 0 |  |
| 3152 | POLYHALOGENATED BIPHENYLS, SOLID or POLYHALOGENATED TERPHENYLS, SOLID | 9 | M2 | II | 9 | 203 305 802 | LQ29 |  | PP, EP |  |  |  |  | 0 |  |
| 3153 | PERFLUORO(METHYL VINYL ETHER) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3154 | PERFLUORO(ETHYL VINYL ETHER) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3155 | PENTACHLOROPHENOL | 6.1 | T2 | II | 6.1 | 43 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3156 | COMPRESSED GAS, OXIDIZING, N.O.S. | 2 | 1O |  | 2.2+5.1 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3157 | LIQUEFIED GAS, OXIDIZING, N.O.S. | 2 | 2O |  | 2.2+5.1 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3158 | GAS, REFRIGERATED LIQUID, N.O.S. | 2 | 3A |  | 2.2 | 274 593 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3159 | 1,1,1,2-TETRAFLUOROETHANE (REFRIGERANT GAS R 134a) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3160 | LIQUEFIED GAS, TOXIC, FLAMMABLE, N.O.S. | 2 | 2TF |  | 2.3+2.1 | 274 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3161 | LIQUEFIED GAS, FLAMMABLE, N.O.S. | 2 | 2F |  | 2.1 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3162 | LIQUEFIED GAS, TOXIC, N.O.S. | 2 | 2T |  | 2.3 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3163 | LIQUEFIED GAS, N.O.S. | 2 | 2A |  | 2.2 | 274 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3164 | ARTICLES, PRESSURIZED, PNEUMATIC or HYDRAULIC (containing non-flammable gas) | 2 | 6A |  | 2.2 | 283 594 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3165 | AIRCRAFT HYDRAULIC POWER UNIT FUEL TANK (containing a mixture of anhydrous hydrazine and methylhydrazine) (M86 fuel) | 3 | FTC | I | 3+6.1+8 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3166 | Engine, internal combustion or vehicle, flammable gas powered or vehicle, flammable liquid powered | 9 | M11 |  |  |  |  | free |  |  |  |  |  |  |  |
| 3167 | GAS SAMPLE, NON-PRESSURIZED, FLAMMABLE, N.O.S., not refrigerated liquid | 2 | 7F |  | 2.1 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3168 | GAS SAMPLE, NON-PRESSURIZED, TOXIC, FLAMMABLE, N.O.S., not refrigerated liquid | 2 | 7TF |  | 2.3+2.1 | 274 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3169 | GAS SAMPLE, NON-PRESSURIZED, TOXIC, N.O.S., not refrigerated liquid | 2 | 7T |  | 2.3 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | W2 | II | 4.3 | 244 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | W2 | III | 4.3 | 244 | LQ12 | B | PP, EX, A | VE01, VE03 | LO03 | HA07, HA08 | IN01, IN02, IN03 | 0 | VE03, LO03, HA07, IN01, IN02 and IN03 apply only when this substance is carried in bulk or without packaging |
| 3171 | Battery-powered vehicle or Battery-powered equipment | 9 | M11 |  |  |  |  | free |  |  |  |  |  |  |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 | T1 | I | 6.1 | 210 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 | T1 | II | 6.1 | 210 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 | T1 | III | 6.1 | 210 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 210 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 210 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 210 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3174 | TITANIUM DISULPHIDE | 4.2 | S4 | III | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3175 | SOLIDS or mixtures of solids (such as preparations and wastes) CONTAINING FLAMMABLE LIQUID, N.O.S. having a flash-point up to 61°C | 4.1 | F1 | II | 4.1 | 216 274 800 | LQ8 | TB | PP, EX, A | VE01, VE03 |  |  | IN01, IN02 | 1 | VE03, IN01and IN02 apply only when this substance is carried in bulk or without packaging |
| 3176 | FLAMMABLE SOLID, ORGANIC, MOLTEN, N.O.S. | 4.1 | F2 | II | 4.1 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3176 | FLAMMABLE SOLID, ORGANIC, MOLTEN, N.O.S. | 4.1 | F2 | III | 4.1 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | F3 | II | 4.1 | 274 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | F3 | III | 4.1 | 274 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | FT2 | II | 4.1+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | FT2 | III | 4.1+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | FC2 | II | 4.1+8 | 274 | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | FC2 | III | 4.1+8 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | F3 | II | 4.1 | 274 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | F3 | III | 4.1 | 274 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 | F3 | II | 4.1 | 274 554 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 | F3 | III | 4.1 | 274 554 | LQ9 |  | PP |  |  |  |  | 0 |  |
| 3183 | SELF-HEATING LIQUID, ORGANIC, N.O.S. | 4.2 | S1 | II | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3183 | SELF-HEATING LIQUID, ORGANIC, N.O.S. | 4.2 | S1 | III | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3184 | SELF-HEATING LIQUID, TOXIC, ORGANIC, N.O.S. | 4.2 | ST1 | II | 4.2+6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3184 | SELF-HEATING LIQUID, TOXIC, ORGANIC, N.O.S. | 4.2 | ST1 | III | 4.2+6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3185 | SELF-HEATING LIQUID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | SC1 | II | 4.2+8 | 274 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 3185 | SELF-HEATING LIQUID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | SC1 | III | 4.2+8 | 274 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 3186 | SELF-HEATING LIQUID, INORGANIC, N.O.S. | 4.2 | S3 | II | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3186 | SELF-HEATING LIQUID, INORGANIC, N.O.S. | 4.2 | S3 | III | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3187 | SELF-HEATING LIQUID, TOXIC, INORGANIC, N.O.S. | 4.2 | ST3 | II | 4.2+6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3187 | SELF-HEATING LIQUID, TOXIC, INORGANIC, N.O.S. | 4.2 | ST3 | III | 4.2+6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3188 | SELF-HEATING LIQUID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | SC3 | II | 4.2+8 | 274 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 3188 | SELF-HEATING LIQUID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | SC3 | III | 4.2+8 | 274 | LQ0 |  | PP, EP |  |  |  |  | 0 |  |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | S4 | II | 4.2 | 274 555 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | S4 | III | 4.2 | 274 555 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | S4 | II | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | S4 | III | 4.2 | 274 | LQ0 | B | PP |  |  |  |  | 0 |  |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | ST4 | II | 4.2+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | ST4 | III | 4.2+6.1 | 274 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | SC4 | II | 4.2+8 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | SC4 | III | 4.2+8 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3194 | PYROPHORIC LIQUID, INORGANIC, N.O.S. | 4.2 | S3 | I | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3200 | PYROPHORIC SOLID, INORGANIC, N.O.S. | 4.2 | S4 | I | 4.2 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3203 | PYROPHORIC ORGANOMETALLIC COMPOUND, WATER-REACTIVE, N.O.S., liquid | 4.2 | SW | I | 4.2+4.3 | 274 527 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3203 | PYROPHORIC ORGANOMETALLIC COMPOUND, WATER-REACTIVE, N.O.S., solid | 4.2 | SW | I | 4.2+4.3 | 274 527 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | S4 | II | 4.2 | 183 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | S4 | III | 4.2 | 183 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | SC4 | II | 4.2+8 | 182 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | SC4 | III | 4.2+8 | 183 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3207 | ORGANOMETALLIC COMPOUND or ORGANOMETALLIC COMPOUND SOLUTION or ORGANOMETALLIC COMPOUND DISPERSION, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | WF1 | I | 4.3+3 | 274 556 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 3207 | ORGANOMETALLIC COMPOUND or ORGANOMETALLIC COMPOUND SOLUTION or ORGANOMETALLIC COMPOUND DISPERSION, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | WF1 | II | 4.3+3 | 274 556 | LQ10 |  | PP, EX, A | VE01 |  | HA08 |  | 1 |  |
| 3207 | ORGANOMETALLIC COMPOUND or ORGANOMETALLIC COMPOUND SOLUTION or ORGANOMETALLIC COMPOUND DISPERSION, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | WF1 | III | 4.3+3 | 274 556 | LQ13 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | W2 | I | 4.3 | 274 557 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | W2 | II | 4.3 | 274 557 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | W2 | III | 4.3 | 274 557 | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | WS | I | 4.3+4.2 | 274 557 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | WS | II | 4.3+4.2 | 274 557 | LQ11 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | WS | III | 4.3+4.2 | 274 557 | LQ12 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3210 | CHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 605 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 3210 | CHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 605 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 3211 | PERCHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 3211 | PERCHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 3212 | HYPOCHLORITES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 559 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 3213 | BROMATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 604 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 3213 | BROMATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 604 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 3214 | PERMANGANATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 608 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 3215 | PERSULPHATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 | LQ12 |  | PP |  |  |  |  | 0 |  |
| 3216 | PERSULPHATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 3218 | NITRATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 270 274 511 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 3218 | NITRATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 270 274 511 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 3219 | NITRITES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 103 274 | LQ10 |  | PP |  |  |  |  | 0 |  |
| 3219 | NITRITES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 103 274 | LQ13 |  | PP |  |  |  |  | 0 |  |
| 3220 | PENTAFLUOROETHANE (REFRIGERANT GAS R 125) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3221 | SELF-REACTIVE LIQUID TYPE B | 4.1 | SR1 |  | 4.1+1 | 181 194 274 | LQ14 |  | PP |  |  | HA01, HA10 |  | 3 |  |
| 3222 | SELF-REACTIVE SOLID TYPE B | 4.1 | SR1 |  | 4.1+1 | 181 194 274 | LQ15 |  | PP |  |  | HA01, HA10 |  | 3 |  |
| 3223 | SELF-REACTIVE LIQUID TYPE C | 4.1 | SR1 |  | 4.1 | 194 274 | LQ14 |  | PP |  |  |  |  | 0 |  |
| 3224 | SELF-REACTIVE SOLID TYPE C | 4.1 | SR1 |  | 4.1 | 194 274 | LQ15 |  | PP |  |  |  |  | 0 |  |
| 3225 | SELF-REACTIVE LIQUID TYPE D | 4.1 | SR1 |  | 4.1 | 194 274 | LQ16 |  | PP |  |  |  |  | 0 |  |
| 3226 | SELF-REACTIVE SOLID TYPE D | 4.1 | SR1 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3227 | SELF-REACTIVE LIQUID TYPE E | 4.1 | SR1 |  | 4.1 | 194 274 | LQ16 |  | PP |  |  |  |  | 0 |  |
| 3228 | SELF-REACTIVE SOLID TYPE E | 4.1 | SR1 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3229 | SELF-REACTIVE LIQUID TYPE F | 4.1 | SR1 |  | 4.1 | 194 274 | LQ16 |  | PP |  |  |  |  | 0 |  |
| 3230 | SELF-REACTIVE SOLID TYPE F | 4.1 | SR1 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3231 | SELF-REACTIVE LIQUID TYPE B, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1+1 | 181 194 274 | LQ0 |  | PP |  |  | HA01, HA10 |  | 3 |  |
| 3232 | SELF-REACTIVE SOLID TYPE B, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1+1 | 181 194 274 | LQ0 |  | PP |  |  | HA01, HA10 |  | 3 |  |
| 3233 | SELF-REACTIVE LIQUID TYPE C, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3234 | SELF-REACTIVE SOLID TYPE C, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3235 | SELF-REACTIVE LIQUID TYPE D, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3236 | SELF-REACTIVE SOLID TYPE D, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3237 | SELF-REACTIVE LIQUID TYPE E, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3238 | SELF-REACTIVE SOLID TYPE E, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3239 | SELF-REACTIVE LIQUID TYPE F, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3240 | SELF-REACTIVE SOLID TYPE F, TEMPERATURE CONTROLLED | 4.1 | SR2 |  | 4.1 | 194 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3241 | 2-BROMO-2-NITROPROPANE-1,3-DIOL | 4.1 | SR1 | III | 4.1 | 638 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3242 | AZODICARBONAMIDE | 4.1 | SR1 | II | 4.1 | 215 638 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3243 | SOLIDS CONTAINING TOXIC LIQUID, N.O.S. | 6.1 | T9 | II | 6.1 | 217 274 802 | LQ18 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3244 | SOLIDS CONTAINING CORROSIVE LIQUID, N.O.S. | 8 | C10 | II | 8 | 218 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3245 | GENETICALLY MODIFIED MICRO-ORGANISMS | 9 | M8 |  | 9 | 219 634 637 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3246 | METHANESULPHONYL CHLORIDE | 6.1 | TC1 | I | 6.1+8 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3247 | SODIUM PEROXOBORATE, ANHYDROUS | 5.1 | O2 | II | 5.1 |  | LQ11 |  | PP |  |  |  |  | 0 |  |
| 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | II | 3+6.1 | 220 221 274 601 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | III | 3+6.1 | 220 221 274 601 802 | LQ7 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | T2 | II | 6.1 | 221 274 601 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | T2 | III | 6.1 | 221 274 601 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3250 | CHLOROACETIC ACID, MOLTEN | 6.1 | TC1 | II | 6.1+8 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3251 | ISOSORBIDE-5-MONONITRATE | 4.1 | SR1 | III | 4.1 | 226 638 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3252 | DIFLUOROMETHANE (REFRIGERANT GAS R 32) | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3253 | DISODIUM TRIOXOSILICATE | 8 | C6 | III | 8 |  | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 3254 | TRIBUTYLPHOSPHANE | 4.2 | S1 | I | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3255 | tert-BUTYL HYPOCHLORITE | 4.2 | SC1 |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 61 °C, at or above its flash-point | 3 | F2 | III | 3 | 274 560 | LQ0 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3257 | ELEVATED TEMPERATURE LIQUID, N.O.S., at or above 100 °C and below its flash-point (including molten metals, molten salts, etc.) | 9 | M9 | III | 9 | 274 580 643 | LQ0 | T | PP |  |  |  |  | 0 |  |
| 3258 | ELEVATED TEMPERATURE SOLID, N.O.S., at or above 240 °C | 9 | M10 | III | 9 | 274 580 643 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | C8 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | C8 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | C8 | III | 8 | 274 | LQ24 | T | PP, EP |  |  |  |  | 0 |  |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | C2 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | C2 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | C2 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | C4 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | C4 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | C4 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | C6 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | C6 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | C6 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | C8 | I | 8 | 274 | LQ21 |  | PP, EP |  |  |  |  | 0 |  |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | C8 | II | 8 | 274 | LQ23 |  | PP, EP |  |  |  |  | 0 |  |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | C8 | III | 8 | 274 | LQ24 |  | PP, EP |  |  |  |  | 0 |  |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | I | 8 | 274 | LQ20 | T | PP, EP |  |  |  |  | 0 |  |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | 8 | C1 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | I | 8 | 274 | LQ20 | T | PP, EP |  |  |  |  | 0 |  |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | 8 | C3 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | I | 8 | 274 | LQ20 | T | PP, EP |  |  |  |  | 0 |  |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | 8 | C5 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | I | 8 | 274 | LQ20 | T | PP, EP |  |  |  |  | 0 |  |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | II | 8 | 274 | LQ22 | T | PP, EP |  |  |  |  | 0 |  |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | 8 | C7 | III | 8 | 274 | LQ19 | T | PP, EP |  |  |  |  | 0 |  |
| 3268 | AIR BAG INFLATORS, or AIR BAG MODULES, or SEAT-BELT PRETENSIONERS | 9 | M5 | III | 9 | 280 289 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3269 | POLYESTER RESIN KIT | 3 | F1 | II | 3 | 236 | LQ6 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3269 | POLYESTER RESIN KIT | 3 | F1 | III | 3 | 236 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3269 | POLYESTER RESIN KIT (viscous according to 2.2.3.1.4) (vapour pressure at 50 ºC more than 175 kPa) | 3 | F1 | III | 3 | 236 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3269 | POLYESTER RESIN KIT (viscous according to 2.2.3.1.4) (vapour pressure at 50 ºC more than 110 kPa but not more than 175 kPa) | 3 | F1 | III | 3 | 236 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3269 | POLYESTER RESIN KIT (viscous according to 2.2.3.1.4) (vapour pressure at 50 ºC not more than 110 kPa) | 3 | F1 | III | 3 | 236 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3270 | NITROCELLULOSE MEMBRANE FILTERS, with not more than 12.6% nitrogen, by dry mass | 4.1 | F1 | II | 4.1 | 237 286 | LQ8 |  | PP |  |  |  |  | 1 |  |
| 3271 | ETHERS, N.O.S. | 3 | F1 | II | 3 | 274 | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3271 | ETHERS, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3272 | ESTERS, N.O.S. | 3 | F1 | II | 3 | 274 | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3272 | ESTERS, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3273 | NITRILES, FLAMMABLE, TOXIC, N.O.S. | 3 | TF1 | I | 3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3273 | NITRILES, FLAMMABLE, TOXIC, N.O.S. | 3 | TF1 | II | 3+6.1 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3274 | ALCOHOLATES SOLUTION, N.O.S., in alcohol | 3 | FC | II | 3+8 | 274 | LQ4 |  | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 3275 | NITRILES, TOXIC, FLAMMABLE, N.O.S. | 6.1 | TF1 | I | 6.1+3 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3275 | NITRILES, TOXIC, FLAMMABLE, N.O.S. | 6.1 | TF1 | II | 6.1+3 | 274 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3276 | NITRILES, TOXIC, N.O.S. | 6.1 | T1 | I | 6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3276 | NITRILES, TOXIC, N.O.S. | 6.1 | T1 | II | 6.1 | 274 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3276 | NITRILES, TOXIC, N.O.S. | 6.1 | T1 | III | 6.1 | 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3277 | CHLOROFORMATES, TOXIC, CORROSIVE, N.O.S. | 6.1 | TC1 | II | 6.1+8 | 274 561 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., liquid | 6.1 | T1 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., liquid | 6.1 | T1 | II | 6.1 | 43 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., liquid | 6.1 | T1 | III | 6.1 | 43 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | T2 | I | 6.1 | 43 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | T2 | II | 6.1 | 43 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | T2 | III | 6.1 | 43 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3279 | ORGANOPHOSPHORUS COMPOUND, TOXIC, FLAMMABLE, N.O.S. | 6.1 | TF1 | I | 6.1+3 | 43 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3279 | ORGANOPHOSPHORUS COMPOUND, TOXIC, FLAMMABLE, N.O.S. | 6.1 | TF1 | II | 6.1+3 | 43 274 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., liquid | 6.1 | T3 | I | 6.1 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., liquid | 6.1 | T3 | II | 6.1 | 274 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., liquid | 6.1 | T3 | III | 6.1 | 274 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | T3 | I | 6.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | T3 | II | 6.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | T3 | III | 6.1 | 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3281 | METAL CARBONYLS, N.O.S., liquid | 6.1 | T3 | I | 6.1 | 274 562 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3281 | METAL CARBONYLS, N.O.S., liquid | 6.1 | T3 | II | 6.1 | 274 562 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3281 | METAL CARBONYLS, N.O.S., liquid | 6.1 | T3 | III | 6.1 | 274 562 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | T3 | I | 6.1 | 274 562 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | T3 | II | 6.1 | 274 562 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | T3 | III | 6.1 | 274 562 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., liquid | 6.1 | T3 | I | 6.1 | 274 562 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., liquid | 6.1 | T3 | II | 6.1 | 274 562 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., liquid | 6.1 | T3 | III | 6.1 | 274 562 802 | LQ9 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | T3 | I | 6.1 | 274 562 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | T3 | II | 6.1 | 274 562 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | T3 | III | 6.1 | 274 562 802 | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | T5 | I | 6.1 | 274 563 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 274 563 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 274 563 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | T5 | I | 6.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | T5 | I | 6.1 | 274 564 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 274 564 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 274 564 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. | 3 | FTC | I | 3+6.1+8 | 274 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. | 3 | FTC | II | 3+6.1+8 | 274 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. | 6.1 | T4 | I | 6.1 | 274 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. | 6.1 | T4 | II | 6.1 | 274 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. | 6.1 | T4 | III | 6.1 | 274 802 | LQ19 | T | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | T5 | I | 6.1 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | T5 | II | 6.1 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | T5 | III | 6.1 | 274 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3289 | TOXIC LIQUID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | TC3 | I | 6.1+8 | 274 802 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3289 | TOXIC LIQUID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | TC3 | II | 6.1+8 | 274 802 | LQ17 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | TC4 | I | 6.1+8 | 274 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | TC4 | II | 6.1+8 | 274 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3291 | CLINICAL WASTE, UNSPECIFIED, N.O.S. or (BIO) MEDICAL WASTE, N.O.S. or REGULATED MEDICAL WASTE, N.O.S. | 6.2 | I3 | II | 6.2 | 565 634 802 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3292 | BATTERIES, CONTAINING SODIUM, or CELLS, CONTAINING SODIUM | 4.3 | W3 | II | 4.3 | 239 295 | LQ0 |  | PP, EX, A | VE01 |  | HA08 |  | 0 |  |
| 3293 | HYDRAZINE, AQUEOUS SOLUTION with not more than 37% hydrazine, by mass | 6.1 | T4 | III | 6.1 | 566 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3294 | HYDROGEN CYANIDE, SOLUTION IN ALCOHOL with not more than 45% hydrogen cyanide | 6.1 | TF1 | I | 6.1+3 | 610 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. (vapour pressure at 50 °C more than 175 kPa) | 3 | F1 | I | 3 | 274 640A | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | I | 3 | 274 640B | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 274 640C | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 274 640D | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3296 | HEPTAFLUOROPROPANE (REFRIGERANT GAS R 227) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3297 | ETHYLENE OXIDE AND CHLOROTETRAFLUORO- ETHANE MIXTURE with not more than 8.8% ethylene oxide | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3298 | ETHYLENE OXIDE AND PENTAFLUOROETHANE MIXTURE with not more than 7.9% ethylene oxide | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3299 | ETHYLENE OXIDE AND TETRAFLUOROETHANE MIXTURE with not more than 5.6% ethylene oxide | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3300 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with more than 87% ethylene oxide | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3301 | CORROSIVE LIQUID, SELF-HEATING, N.O.S. | 8 | CS1 | I | 8+4.2 | 274 | LQ20 |  | PP, EP |  |  |  |  | 0 |  |
| 3301 | CORROSIVE LIQUID, SELF-HEATING, N.O.S. | 8 | CS1 | II | 8+4.2 | 274 | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 3302 | 2-DIMETHYLAMINOETHYL ACRYLATE | 6.1 | T1 | II | 6.1 | 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3303 | COMPRESSED GAS, TOXIC, OXIDIZING, N.O.S. | 2 | 1TO |  | 2.3+5.1 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3304 | COMPRESSED GAS, TOXIC, CORROSIVE, N.O.S. | 2 | 1TC |  | 2.3+8 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3305 | COMPRESSED GAS, TOXIC, FLAMMABLE, CORROSIVE, N.O.S. | 2 | 1TFC |  | 2.3+2.1+8 | 274 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3306 | COMPRESSED GAS, TOXIC, OXIDIZING, CORROSIVE, N.O.S. | 2 | 1TOC |  | 2.3+5.1+8 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3307 | LIQUEFIED GAS, TOXIC, OXIDIZING, N.O.S. | 2 | 2TO |  | 2.3+5.1 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3308 | LIQUEFIED GAS, TOXIC, CORROSIVE, N.O.S. | 2 | 2TC |  | 2.3+8 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3309 | LIQUEFIED GAS, TOXIC, FLAMMABLE, CORROSIVE, N.O.S. | 2 | 2TFC |  | 2.3+2.1+8 | 274 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3310 | LIQUEFIED GAS, TOXIC, OXIDIZING, CORROSIVE, N.O.S. | 2 | 2TOC |  | 2.3+5.1+8 | 274 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3311 | GAS, REFRIGERATED LIQUID, OXIDIZING, N.O.S. | 2 | 3O |  | 2.2+5.1 | 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3312 | GAS, REFRIGERATED LIQUID, FLAMMABLE, N.O.S. | 2 | 3F |  | 2.1 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | S2 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | S2 | III | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3314 | PLASTICS MOULDING COMPOUND in dough, sheet or extruded rope form evolving flammable vapour | 9 | M3 | III | none | 207 633 | LQ27 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 3315 | CHEMICAL SAMPLE, TOXIC, liquid or solid | 6.1 | T8 | I | 6.1 | 250 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3316 | CHEMICAL KIT or FIRST AID KIT | 9 | M11 | II | 9 | 251 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3316 | CHEMICAL KIT or FIRST AID KIT | 9 | M11 | III | 9 | 251 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3317 | 2-AMINO-4,6-DINITROPHENOL, WETTED with not less than 20% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3318 | AMMONIA SOLUTION | 2 | 4TC |  | 2.3+8 | 23 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3319 | NITROGLYCERIN MIXTURE, DESENSITIZED, SOLID, N.O.S. with more than 2% but not more than 10% nitroglycerin, by mass | 4.1 | D | II | 4.1 | 272 274 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3320 | SODIUM BOROHYDRIDE AND SODIUM HYDROXIDE SOLUTION, with not more than 12% sodium borohydride and not more than 40% sodium hydroxide by mass | 8 | C5 | II | 8 |  | LQ22 |  | PP, EP |  |  |  |  | 0 |  |
| 3320 | SODIUM BOROHYDRIDE AND SODIUM HYDROXIDE SOLUTION, with not more than 12% sodium borohydride and not more than 40% sodium hydroxide by mass | 8 | C5 | III | 8 |  | LQ19 |  | PP, EP |  |  |  |  | 0 |  |
| 3321 | RADIOACTIVE MATERIAL, LOW SPECIFIC ACTIVITY (LSA-II), non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3322 | RADIOACTIVE MATERIAL, LOW SPECIFIC ACTIVITY (LSA-III), non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3323 | RADIOACTIVE MATERIAL, TYPE C PACKAGE, non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3324 | RADIOACTIVE MATERIAL, LOW SPECIFIC ACTIVITY (LSA-II), FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3325 | RADIOACTIVE MATERIAL, LOW SPECIFIC ACTIVITY, (LSA-III), FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3326 | RADIOACTIVE MATERIAL, SURFACE CONTAMINATED OBJECTS (SCO-I or SCO-II), FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3327 | RADIOACTIVE MATERIAL, TYPE A PACKAGE, FISSILE, non-special form | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3328 | RADIOACTIVE MATERIAL, TYPE B(U) PACKAGE, FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3329 | RADIOACTIVE MATERIAL, TYPE B(M) PACKAGE, FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3330 | RADIOACTIVE MATERIAL, TYPE C PACKAGE, FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3331 | RADIOACTIVE MATERIAL, TRANSPORTED UNDER SPECIAL ARRANGEMENT, FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3332 | RADIOACTIVE MATERIAL, TYPE A PACKAGE, SPECIAL FORM, non fissile or fissile-excepted | 7 |  |  | 7X | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3333 | RADIOACTIVE MATERIAL, TYPE A PACKAGE, SPECIAL FORM, FISSILE | 7 |  |  | 7X+7E | 172 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3334 | Aviation regulated liquid, n.o.s. | 9 | M11 |  |  |  |  | free |  |  |  |  |  |  |  |
| 3335 | Aviation regulated solid, n.o.s. | 9 | M11 |  |  |  |  | free |  |  |  |  |  |  |  |
| 3336 | MERCAPTANS, LIQUID, FLAMMABLE, N.O.S. or MERCAPTAN MIXTURE, LIQUID, FLAMMABLE, N.O.S. | 3 | F1 | I | 3 | 274 | LQ3 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3336 | MERCAPTANS, LIQUID, FLAMMABLE, N.O.S. or MERCAPTAN MIXTURE, LIQUID, FLAMMABLE, N.O.S. (vapour pressure at 50 °C more than 110 kPa but not more than 175 kPa) | 3 | F1 | II | 3 | 274 640C | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3336 | MERCAPTANS, LIQUID, FLAMMABLE, N.O.S. or MERCAPTAN MIXTURE, LIQUID, FLAMMABLE, N.O.S. (vapour pressure at 50 °C not more than 110 kPa) | 3 | F1 | II | 3 | 274 640D | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3336 | MERCAPTANS, LIQUID, FLAMMABLE, N.O.S. or MERCAPTAN MIXTURE, LIQUID, FLAMMABLE, N.O.S. | 3 | F1 | III | 3 | 274 | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3337 | REFRIGERANT GAS R 404A (Pentafluoroethane, 1,1,1-trifluoroethane, and 1,1,1,2-tetrafluoroethane zeotropic mixture with approximately 44% pentafluoroethane and 52% 1,1,1-trifluoroethane) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3338 | REFRIGERANT GAS R 407A (Difluoromethane, pentafluoroethane, and 1,1,1,2-tetrafluoroethane zeotropic mixture with approximately 20% difluoromethane and 40% pentafluoroethane) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3339 | REFRIGERANT GAS R 407B (Difluoromethane, pentafluoroethane, and 1,1,1,2-tetrafluoroethane zeotropic mixture with approximately 10% difluoromethane and 70% pentafluoroethane | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3340 | REFRIGERANT GAS R 407C (Difluoromethane, pentafluoroethane, and 1,1,1,2-tetrafluoroethane zeotropic mixture with approximately 23%difluoromethane and 25% pentafluoroethane) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 3341 | THIOUREA DIOXIDE | 4.2 | S2 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3341 | THIOUREA DIOXIDE | 4.2 | S2 | III | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3342 | XANTHATES | 4.2 | S2 | II | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3342 | XANTHATES | 4.2 | S2 | III | 4.2 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3343 | NITROGLYCERIN MIXTURE, DESENSITIZED, LIQUID, FLAMMABLE, N.O.S. with not more than 30% nitroglycerin, by mass | 3 | D |  | 3 | 274 278 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 3344 | PENTAERYTHRITE TETRANITRATE MIXTURE, DESENSITIZED, SOLID, N.O.S. with more than 10% but not more than 20% PETN, by mass | 4.1 | D | II | 4.1 | 272 274 | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3346 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3346 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3347 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3347 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3347 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3348 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3348 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3348 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | T7 | I | 6.1 | 61 802 | LQ0 |  | PP, EP |  |  |  |  | 2 |  |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | T7 | II | 6.1 | 61 802 | LQ18 |  | PP, EP |  |  |  |  | 2 |  |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | T7 | III | 6.1 | 61 802 | LQ9 |  | PP, EP |  |  |  |  | 0 |  |
| 3350 | PYRETHROID PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | I | 3+6.1 | 61 802 | LQ3 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3350 | PYRETHROID PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash-point less than 23 °C | 3 | FT2 | II | 3+6.1 | 61 802 | LQ4 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3351 | PYRETHROID PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | I | 6.1+3 | 61 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3351 | PYRETHROID PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | II | 6.1+3 | 61 802 | LQ17 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3351 | PYRETHROID PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash-point not less than 23 °C | 6.1 | TF2 | III | 6.1+3 | 61 802 | LQ19 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 0 |  |
| 3352 | PYRETHROID PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | I | 6.1 | 61 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3352 | PYRETHROID PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | II | 6.1 | 61 802 | LQ17 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3352 | PYRETHROID PESTICIDE, LIQUID, TOXIC | 6.1 | T6 | III | 6.1 | 61 802 | LQ19 |  | PP, EP, TOX, A | VE02 |  |  |  | 0 |  |
| 3354 | INSECTICIDE GAS, FLAMMABLE, N.O.S. | 2 | 2F |  | 2.1 | 274 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3355 | INSECTICIDE GAS, TOXIC, FLAMMABLE, N.O.S. | 2 | 2TF |  | 2.3+2.1 | 274 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 3356 | OXYGEN GENERATOR, CHEMICAL | 5.1 | O3 | II | 5.1 | 284 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 3357 | NITROGLYCERIN MIXTURE, DESENSITIZED, LIQUID, N.O.S. with not more than 30% nitroglycerin, by mass | 3 | D | II | 3 | 274 288 | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3358 | REFRIGERATING MACHINES containing flammable, non-toxic, liquefied gas | 2 | 6F |  | 2.1 | 291 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3359 | FUMIGATED UNIT | 9 | M11 |  |  | 302 |  |  |  |  |  |  |  |  |  |
| 3360 | Fibres, vegetable, dry | 4.1 | F1 | NOT SUBJECT TO ADN |  |  |  |  |  |
| 3361 | CHLOROSILANES, TOXIC, CORROSIVE, N.O.S. | 6.1 | TC1 | II | 6.1+8 | 274 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 3362 | CHLOROSILANES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | TFC | II | 6.1+3+8 | 274 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01 VE02 |  |  |  | 2 |  |
| 3363 | Dangerous goods in machinery or dangerous goods in apparatus | 9 | M11 | NOT SUBJECT TO ADN [see also 1.1.3.1 b)] |  |  |  |  |  |
| 3364 | TRINITROPHENOL (PICRIC ACID), dry or wetted with less than 30% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 3364 | TRINITROPHENOL (PICRIC ACID) wetted with not less than 10% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3365 | TRINITROCHLOROBENZENE (PICRYL CHLORIDE) | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 3365 | TRINITROCHLOROBENZENE (PICRYL CHLORIDE) wetted with not less than 10% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3366 | TRINITROTOLUENE (TNT), wetted with not less than 10% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3367 | TRINITROBENZENE, dry or wetted with less than 30% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 3367 | TRINITROBENZENE, wetted with not less than 10% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3368 | TRINITROBENZOIC ACID, dry or wetted with less than 30% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 3368 | TRINITROBENZOIC ACID, wetted with not less than 10% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3369 | SODIUM DINITRO-o-CRESOLATE, dry or wetted with less than 15% water, by mass | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 3369 | SODIUM DINITRO-o-CRESOLATE, WETTED with not less than 10% water, by mass | 4.1 | DT | I | 4.1+6.1 | 802 | LQ0 |  | PP |  |  |  |  | 2 |  |
| 3370 | UREA NITRATE, dry or wetted with less than 20% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 3370 | UREA NITRATE, wetted with not less than 10% water, by mass | 4.1 | D | I | 4.1 |  | LQ0 |  | PP |  |  |  |  | 1 |  |
| 3371 | 2-METHYLBUTANAL | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | WF2 | I | 4.3+4.1 | 274 | LQ0 | [forbidden] |  |  |  |  |  |  |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | WF2 | II | 4.3+4.1 | 274 | LQ11 | [forbidden] |  |  |  |  |  |  |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | WF3 | III | 4.3+4.1 | 274 | LQ12 | [forbidden] |  |  |  |  |  |  |
| 3373 | DIAGNOSTIC SPECIMENS | 6.2 | I4 |  |  |  | LQ0 |  |  |  |  |  |  |  |  |
| 3374 | ACETYLENE, SOLVENT FREE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 3375 | AMMONIUM NITRATE EMULSION, A SUSTENSION or GEL, intermediate for blasting explosives | 5.1 | O1 | II | 5.1 | 306 309 | LQ11 |  | PP |  |  |  |  | 0 |  |
| 3376 | 4-NITROPHENYL HYDRAZINE, with not less than 30% water, by mass | 4.1 | D | II | 4.1 | 28 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 9000 | AMMONIA, DEEPLY REFRIGERATED | 2 | 3TC |  | 2.3+8 |  |  | T | PP |  |  |  |  | 2 | Admitted only for carriage in tank vehicles |
| 9001 | SUBSTANCES WITH A FLASH-POINT ABOVE 61 ºC which are carried heated within a limiting range of 15K below their flash-point | 3 |  |  | none |  |  | T | PP |  |  |  |  | 0 | Dangerous only when carried in tank vehicles |
| 9002 | SUBSTANCES WITH AN AUTO-IGNITION TEMPERATURE OF 200 ºC AND BELOW WHICH ARE NOT LISTED ELSEWHERE | 3 |  |  | none |  |  | T | PP |  |  |  |  | 0 | Dangerous only when carried in tank vehicles |
| 9003 | SUBSTANCES WITH A FLASH-POINT ABOVE 61 ºC AND NOT MORE THAN 100 ºC, WHICH DO NOT BELONG TO ANOTHER CLASS | 9 |  |  | none |  |  | T | PP |  |  |  |  | 0 | Dangerous only when carried in tank vehicles |
| 9004 | DIPHENYLMETHANE-4, 4'-DIISOCYANATE | 9 |  |  | none |  |  | T | PP |  |  |  |  | 0 | Dangerous only when carried in tank vehicles |

___________________