Distr.

GENERAL

TRANS/WP.29/GRE/2002/2

25 January 2002

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Lighting and Light-Signalling (GRE)

(Forty-eighth session, 9-12 April 2002,

agenda item 1.1.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 48

(Installation of lighting and light-signalling devices)

Transmitted by the Expert from Japan

Note:  The text reproduced below was proposed by the expert from Japan and distributed without a symbol (informal document No. 16) during the forty-seventh session of GRE (TRANS/WP.29/GRE/47, para. 26).

_________

_____________

Note:  This document is distributed to the Experts on Lighting and Light-Signalling only.

GE.02-20362

Paragraph 6.2.9., amend to read:

"6.2.9.	Other requirements

The requirements of ... when these headlamps are installed.

For dipped beam headlamps with an additional light source for bend lighting purpose, the combination of such dipped beam headlamp and the lamp with the additional light source shall be considered as "a single lamp" described in paragraph 2.16.1., provided it meets other relevant requirements specified in this Regulation."

___________