Informal document No.    11

(43rd GRPE, 15-18. January 2002,

agenda item 1.1.)

# PROPOSAL FOR DRAFT AMENDMENTS

# TO THE 03 SERIES OF AMENDMENTS TO REGULATION No. 49

(Emissions of C.I., NG, and P.I (LPG) engines)

Transmitted by the expert from the Czech Republic

Justification:  The wording of Annexes 2A and 2B has not been harmonised with the implementation of the new test procedure.  The proposed amendment harmonises wording of ECE Regulation No. 49 with 1999/96/EC.

*     *     *

Proposal:

Annex 2A, item 10, amend to read:

"10.	Emission levels of the engine/parent engine

10.1.	ESC-test (if applicable):

CO:	g/kWh

THC:	g/kWh

NOx:		g/kWh

PT:	g/kWh

10.2.	ELR-test (if applicable):

Smoke value:	m-1

10.3.	ETC-test (if applicable):

CO:	g/kWh

THC:	g/kWh

NMHC:	g/kWh

CH4:	g/kWh

NOx:	g/kWh

PT:	g/kWh"

Annex 2B, item 9., amend to read:

"9.	Emission levels of the engine/parent engine

9.1.	ESC-test (if applicable):

CO:		g/kWh

THC:	g/kWh

NOx:	g/kWh

PT:	g/kWh

9.2.	ELR-test (if applicable):

Smoke value:	m-1

9.3.	ETC-test (if applicable):

CO:	g/kWh

THC:	g/kWh

NMHC:	g/kWh

CH4:	g/kWh

NOx:	g/kWh

PT:	g/kWh"

__________