Informal document No. 19

(82nd GRSG, 29 April - 3 May 2002

agenda item 8.6.)

The Netherlands

Proposal to amend TRANS/WP.292002/14 relating to Regulation No. 34 on Fire Risks

In order to resolve the problem of the chained filler cap in relation to the spillage of fuel two proposals are suggested:

Proposal 1:

Add at the end of paragraph 5.9.1.1.3 a new sentence reading:

"However, use of a tethered or chained filler cap by itself is not sufficient for vehicles other than M1 and N1."

Proposal 2:

Replace paragraph 5.9.1. to 5.9.1.1.3. by a new paragraph 5.9.1., reading:

"5.9.1.	The vehicle must be designed such that it cannot be driven without the fuel cap in the closed position unless the vehicle is equipped with a design feature to prevent excess evaporative emissions and fuel spillage caused by a missing or open filler cap."

The Netherlands can accept both proposals