Attachment 3

# Specifications of Head Form Impactors

|  |  | Child Head Impactor | Adult Head Impactor |
| --- | --- | --- | --- |
| Specification | Weight | 3.5 +/- [0.1] kg | 4.5 +/- [0.1] kg |
|  | Diameter | 165 +/- [3.3] mm |
|  | Inertia moment | [0.01 kgm2] | [0.012 kgm2] |
|  | Center of gravity | +/- [2mm] from the geometric center of the sphere |
|  | Accelerometer position | +/- [1mm] from the geometric center of the sphere |
| Calibration*2 | Dynamic Test Drop height: [376mm] Thickness of the dropped surface: [50mm] Size of the dropped surface: [600 mm2] Surface condition: [0.2 – 2.0]μm Temperature: [20 +/- 2 degrees C.] Humidity: [10 – 70%] | [245 – 300] G | [225 – 275] G |
|  | Impact Test Weight of test impactor: [1 +/- 0.1kg] Diameter of the impact surface: [70 +/- 1 mm] Curvature of the edge: [5 +/- 0.5 mm] Surface condition: [2.0]μm Temperature: [20 +/- 2 degrees C.] Humidity: [10 – 70%] Impact velocity: [7.0 +/- 0.1 m/s] Tolerance between center of impact surface and geometric center of impactor: [+/- 5 mm] | [300 – 330] G | [300 – 330] G |

*1: The values in square brackets are tentative.

*2: Either the Dynamic test or Impact test could be selected as the calibration for the certification test, except for the development of the impactor.

# Text boxes

.

BLE

50

deg

600

mm

Straight Edge

(1

m)

BLE

BLE

Figure 4-1 General

Figure 4-4 In the case that the top point of the straight edge

contacts the vehicle front structure

Figure 4-2 In the case that the bottom point of the straight edge

contacts the vehicle front structure.

Figure 4-5 In the case that the straight edge contacts the bumper.

WAD 1000mm

Figure 4-3 In the case that the straight edge is tangential to the

vehicle front structure.

40

deg

.

50

deg

.

BLE

Contact with Bumper

BLE