Informal document N° 6

(32nd GRSP, 10-13 December 2002

agenda item B.2)

## ISOFIX – AMENDMENTS TO REGULATION 44

##### OICA contribution to document TRANS/WP29/GRSP/2001/16/Rev.2

Paragraph 7.1.4.1.9, amend to read:

"7.1.4.1.9	A child restraint with a support leg shall be tested as follows:

- In the case of semi-universal category … to both its maximum and minimum adjustments compatible with the positioning on the trolley floor pan. During the tests ..."

- unchanged

- unchanged

Justification: The current text could force all support legs to have a specific identical length for the trolley floor pan. The OICA proposal would allow more flexibility, thereby ensuring an increased universality of the child restraint system.

Paragraph 7.1.4.1.10 (Proposal C), amend to read:

"7.1.4.1.10	In the case of a child restraint making use of an ISOFIX anchorage system and a top tether strap or another anti-rotation device, the dynamic test shall be carried out with the top tether strap or the anti-rotation device in function."

Paragraphs 7.1.4.1.10.1 and 7.1.4.1.10.2 (Proposal C), delete.

Justification: OICA is of the opinion that, when systems are provided, these systems should also be used in the regulatory testing, as is already the case in many other ECE Regulations.

____________