UNITED

# NATIONS

# Distr.

# GENERAL

# TRANS/WP.15/AC.1/2003/56/Add.3

# 20 June 2003

# ENGLISH

Original: ENGLISH AND FRENCH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

HARMONIZATION WITH THE UN RECOMMENDATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

Report of the Working Group on the Harmonization of RID/ADR/ADN 
 with the UN Recommendations on the Transport of Dangerous Goods */

# Addendum 3

Proposals of amendments to Part 3 of RID/ADR/ADN

PART 3

Chapter 3.1

3.1.2.2 (b)	Replace the existing text with the following:

"UN 2793 FERROUS METAL BORINGS, SHAVINGS, TURNINGS or CUTTINGS in a form liable to self-heating. The proper shipping name is the most appropriate of the following combinations:

FERROUS METAL BORINGS

FERROUS METAL SHAVINGS

FERROUS METAL TURNINGS

FERROUS METAL CUTTINGS".

3.1.2.4	Replace the existing paragraph with the following text:

"3.1.2.4	Many substances have an entry for both the liquid and solid state (see definitions for liquid and solid in 1.2.1), or for the solid and solution. These are allocated separate UN numbers which are not necessarily adjacent to each other1."

3.1.2.8.1.3	Replace "UN 2003 METAL ALKYL, WATER-REACTIVE, N.O.S (trimethylgallium)" with "UN 3394 ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC, WATER-REACTIVE  (trimethylgallium)".

### Chapter 3.2

[3.2.1	Column (10):	Amend the title to read as follows: "UN portable tanks and bulk containers instructions".

Add the following sentence at the end of the current text, after the note:

"Alphanumeric codes starting with the letters "BK" refer to types of bulk containers used for the carriage of bulk goods described in Chapter 6.11."].

Column (11): 	Amend the title to read as follows: "UN portable tanks and bulk containers special provisions".

Table A

Amend the heading applicable to columns (10) and (11) to read: "UN Portable tanks and bulk containers".

For UN No. 1704, replace "P002 IBC08" with "P001 IBC02" in column (8) and delete "B4" in column (9a).

For UN Nos. 1611 and 1704, add "T7" and "TP2" in column (10) and (11) respectively.

In Table A, assign "TP5" in column (11) to each refrigerated liquid gas that is assigned "T75" in column (10). (Apply to UN Nos. 1003, 1038, 1073, 1913, 1951, 1961, 1963, 1966, 1970, 1972, 1977, 2187, 2201, 2591, 3136, 3138, 3158, 3311 and 3312).

For UN Nos 0331, 0332 and 3375, insert "T1" in column (10) and "TP1", "TP17" and "TP32" in column (11).

For UN Nos 1334, 1350, 1438, 1454, 1474, 1486, 1495, 1498, 1499, 1942, 2067, 2213, 2969, 3170 (PG II and III), 3175, 3243 and 3244, insert "BK1, BK2" in column (10) and for UN Nos. 1376, 1408 and 2950, insert "BK2" in the same column.

For the liquid, packing group I entries of UN Nos. 1583, 2810, 2927, 2929, 3122, 3123, 3275, 3276, 3278, 3279, 3280, 3281, 3287 and 3289, insert "315" in column (6).

For all the UN Nos. containing the words "fissile-excepted" in lower case in column (2), insert "317" in column (6). (Apply to UN Nos.: 2912, 2913, 2915, 2916, 2917, 2919, 2978, 3321, 3322, 3323 and 3332).

For UN Nos. 1366, 1370, 2005, 2445, 3051, 3052, 3053 and 3076, add "320" in column (6).

Assign TP9 to all N.O.S entries of Classes 4.2, 6.1 and 8, packing group I to which a T code has been assigned in column (10).

UN No. 1010	Amend the name in column (2) to read as follows: " BUTADIENES, STABILIZED or BUTADIENES AND HYDROCARBON MIXTURE, STABILIZED containing more than 40% butadienes [and having a vapour pressure at 70 °C not exceeding 1.1 MPa (11 bar) and a density at 50 °C not lower than 0.525 kg/l]".

UN No. 1052	Add "V14/W14"  in column (16) and "CV34" in column (18).

[UN No. 1057	Add "201" in column (6), replace "P205" with "P002" in column (8) and add "PP84" in column (9a)].

UN No. 1203	The first amendment does not apply to the English version.

Add "243" in column (6).

UN No. 1389	Add ", LIQUID" in column (2), replace "W2" with "W1" in column (3b) and (for RID/ADR) delete "P403" in column (8) and "B1" in column (9a).

UN No. 1392	Add ", LIQUID" in column (2), replace "W2" with "W1" in column (3b) and (for RID/ADR) delete "P403 IBC04" in column (8).

UN No. 1408	(RID/ADR) Insert "B6" in column (9a).

UN No. 1420	Add ", LIQUID" in column (2), replace "W2" with "W1" in column (3b) and (for RID/ADR) replace "P403 IBC04" with "P402" in column (8).

UN No. 1422	Add ", LIQUID" in column (2), replace "W2" with "W1" in column (3b) and (for RID/ADR) replace "P403 IBC04" with "P402" in column (8).

UN No. 1445	Add ", SOLID" in column (2).

UN No. 1447	Add ", SOLID" in column (2).

UN No. 1459	Add ", SOLID" in column (2).

UN No. 1470	Add ", SOLID" in column (2).

UN No. 1578	Replace "solid" with "SOLID" in column (2).

UN No. 1579	Add ", SOLID" in column (2).

UN No. 1605	(RID/ADR) Replace "P601" with "P602" in column (8).

UN No. 1650	Add ", SOLID" in column (2).

UN No. 1680	Add ", SOLID" in column (2).

UN No. 1689	Add ", SOLID" in column (2).

UN No. 1690	Add ", SOLID" in column (2).

UN No. 1697	Add ", SOLID" in column (2); replace "T1" with "T2" in column (3b) and "LQ17" with "LQ18" in column (7);

(RID/ADR) add "SGAH" in column (12);

(RID only) Replace "CE5" with "CE9" in column (19).

UN No. 1701	Add ", LIQUID" in column (2).

UN No. 1709	Add ", SOLID" in column (2).

UN No. 1729	Replace "C3" with "C4" in column (4) and "LQ22" with "LQ23" in column (7);

(RID/ADR): replace "P001 IBC02" with "P002 IBC08" in column (8); insert "B4" in column (9a); replace "MP15" with "MP10" in column (9b); replace "T7" with "T3" and "TP2" with "TP33" in columns (10) and (11), respectively and insert "SGAN" before "L4BN" in column (12) and W11/V11 in column (16);

(RID only): replace "CE6" with "CE10" in column (19).

UN No. 1742	Add ", LIQUID" in column (2).

UN No. 1743	Add ", LIQUID" in column (2).

UN No. 1744		Add "PP82" in column (9a).

UN No. 1805	In column (2), replace "LIQUID" with "SOLUTION".

UN No. 1811	Amend the name in column (2) to read "POTASSIUM HYDROGENDIFLUORIDE SOLID".

UN No. 1812	Add ", SOLID" in column (2).

UN No. 1843	Add ", SOLID" in column (2) and (for RID/ADR) delete "T7" and "TP2" in columns (10) and (11) respectively.

UN No. 1963	(RID/ADR) Add "TP34" in column (11).

UN No. 1966	(RID/ADR) Add "TP34" in column (11).

UN No. 2003	Delete.

UN No. 2014	Delete "PP29" in column (9a).

UN No. 2074	Add ", SOLID" in column (2).

UN No. 2077	(RID/ADR) Replace "T3" and "TP1" with "T1" and "TP33" in columns (10) and (11) respectively.

UN No. 2208	Add "313" and "314" in column (6) and (for RID/ADR) "PP85" and "B13" in column (9a) and "CV35" in column (18).

UN No. 2235	Add ", LIQUID" in column (2) and replace "T2" with "T1" in column (3b) and "LQ9" with "LQ19" in column (7).

(RID/ADR) Replace "MP10" with "MP15" in column (9b), delete "SGAH" in column (12) and "VW9/VV9" in column (17).

(RID only) Replace "CE11" with "CE8".

UN No. 2236	Add ", LIQUID" in column (2) and replace "T2" with "T1" in column (3b) and "LQ18" with "LQ17" in column (7).

(RID/ADR) Replace "MP10" with "MP15" in column (9b) and delete "SGAH" in column (12).

(RID only) Replace "CE9" with "CE5".

UN No. 2239	Replace "solid" with "SOLID" in column (2) and delete the entry for the liquid substance.

UN No. 2261	Replace "solid" with "SOLID" in column (2) and delete the entry for the liquid substance.

UN No. 2305	(RID/ADR) Add "T3", "TP33" in columns (10) and (11) respectively.

UN No. 2306	Replace "liquid" with "LIQUID" in column (2) and delete the entry for the solid substance.

UN No. 2315	Add ", LIQUID" in column (2).

UN No. 2445	Add ", LIQUID" in column (2).

UN No. 2446	Replace "solid" with "SOLID" in column (2).

UN No. 2511 (first entry): 	Delete ",SOLUTION" in column (2).

Delete the entry for "2-CHLOROPROPIONIC ACID, SOLID".

UN No. 2552	Add ", LIQUID" in column (2).

UN No. 2662	Add ", SOLID" in column (2).

UN No. 2669	Delete the entry for the solid substance.

UN No. 2729	(RID/ADR) Add "T1" and "TP33" in columns (10) and (11) respectively.

UN No. 2813	(RID/ADR) For packing groups I, II and III, add "PP83" in column (9a).

UN No. 2814	In the first entry, delete the text in lower case in column (2) and replace "274" with "318" in column (6).  Delete the second entry.

UN No. 2823	(RID/ADR) Replace "P001 IBC03 LP01" with "P002 IBC08 LP02" in column (8).

UN No. 2857	Amend the name in column (2) to read as follows:  "REFRIGERATING MACHINES containing non-flammable, non-toxic gases or ammonia solutions (UN 2672)".

UN No. 2900	In the first entry, delete the text in lower case in column (2), replace "274" with "318" in column (6) and add "BK1 BK2" in column (10). 	Delete the second entry.

UN No. 2937	Add ", LIQUID" in column (2).

UN No. 3049	Delete.

UN No. 3050	Delete.

UN No. 3052	(RID/ADR): In the entry for the liquid substance, add "TP9" in column (11).

[UN No. 3077	Add "179" in column (6)].

[UN No. 3082	Add "179" in column (6)].

UN No. 3149	(for RID/ADR) Add "PP10" in column (9a).

UN No. 3176	(RID/ADR) Delete "TP9" in column (11) (2 entries).

UN No. 3203	Delete (2 entries).

UN No. 3207	Delete (3 entries).

UN No. 3276	Amend the name in column (2) to read as follows: "NITRILES, TOXIC, LIQUID, N.O.S". (3 entries).

UN No. 3278	Amend the name in column (2) for the liquid substance to read as follows: "ORGANOPHOSPHORUS COMPOUND, TOXIC, LIQUID, N.O.S" (3 entries).

Delete the entries for the solid substance.

UN No. 3280	Amend the name in column (2) for the liquid substance to read as follows: "ORGANOARSENIC COMPOUND, LIQUID, N.O.S" (3 entries).

Delete the entries for the solid substance.

UN No. 3281	Amend the name in column (2) for the liquid substance to read as follows: "METAL CARBONYLS, LIQUID, N.O.S" (3 entries).

Delete the entries for the solid substance.

UN No. 3282	Amend the name in column (2) for the liquid substance to read as follows: "ORGANOMETALLIC COMPOUND, TOXIC, LIQUID, N.O.S" (3 entries).

Delete the entries for the solid substance.

UN No. 3283	Amend the name in column (2) to read as follows: "SELENIUM COMPOUND, SOLID, N.O.S" (3 entries).

UN No. 3315	In column (2), delete ", liquid or solid".

UN No. 3372	Delete (3 entries).

UN No. 3373	Amend the name in column (2) to read as follows: "DIAGNOSTIC SPECIMENS or CLINICAL SPECIMENS" and add "319" in column (6) [, "BK1, BK2" in column (10), "L4BH" in column (12), "TU15 TE15 TE19" in column (13), "AT" in column (14), "2" in column (15), "S3" in column (19) and "606" in column (20)].

UN No. 3375	Delete "306" in column (6).

Amend the following entries to read as follows:

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings | UN Portable tanks and bulk containers | ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Mixed packing provisions | Portable tank instruction | Portable tank special provisions | Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |
| 1597 | DINITROBENZENES LIQUID | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 CV31 | S9 S19 | 60 |
| 1597 | DINITROBENZENES LIQUID | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 CV31 | S9 | 60 |
| 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 | T1 | II | 6.1 | 43 | LQ17 | P001 IBC02 |  | MP15 |  |  | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 CV31 | S9 S19 | 60 |
| 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 | T1 | III | 6.1 | 43 | LQ19 | P001 IBC03 LP01 R001 |  | MP15 |  |  | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 CV31 | S9 | 60 |
| 1658 | NICOTINE SULPHATE SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 CV31 | S9 S19 | 60 |
| 1658 | NICOTINE SULPHATE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 CV31 | S9 | 60 |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | O2 | II | 5.1 | 313 314 589 | LQ11 | P002 IBC08 | PP85 B4, B13 | MP10 |  |  | SGAN | TU3 | AT | 2 | V11 |  | CV24 CV35 |  | 50 |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | O2 | III | 5.1 | 316 589 | LQ12 | P002 IBC08 R001 | PP85 B4 | MP10 |  |  | SGAV | TU3 | AT | 3 |  |  | CV24 CV35 |  | 50 |
| 1835 | TETRAMETHYL-AMMONIUM HYDROXIDE SOLUTION | 8 | C7 | II | 8 |  | LQ22 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BN |  | AT | 2 |  |  |  |  | 80 |
| 1835 | TETRAMETHYL-AMMONIUM HYDROXIDE SOLUTION | 8 | C7 | III | 8 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 | L4BN |  | AT | 3 |  |  |  |  | 80 |
| 1938 | BROMOACETIC ACID SOLUTION | 8 | C3 | II | 8 |  | LQ22 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BN |  | AT | 2 |  |  |  |  | 80 |
| 1938 | BROMOACETIC ACID SOLUTION | 8 | C3 | III | 8 |  | LQ19 | P001 IBC02 LP01 R001 |  | MP15 | T7 | TP2 | L4BN |  | AT | 3 |  |  |  |  | 80 |
| 2669 | CHLOROCRESOLS SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 2669 | CHLOROCRESOLS SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE HYDRATED MIXTURE, with not less than 5.5% but not more than 16% water | 5.1 | O2 | II | 5.1 | 313 314 | LQ11 | P002 IBC08 | PP85 B4, B13 | MP10 |  |  | SGAN | TU3 | AT | 2 | V11 |  | CV24 CV35 |  | 50 |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE HYDRATED MIXTURE, with not less than 5.5% but not more than 16% water | 5.1 | O2 | III | 5.1 | 316 | LQ12 | P002 IBC08 R001 | PP85 B4 | MP10 |  |  | SGAV | TU3 | AT | 3 |  | VV8 | CV24 CV35 |  | 50 |

Add the following new entries:

(Note: When two UN numbers appear in column (1) of the table below, the number in italics corresponds to a current entry in the Table A for the same substance in solid, liquid or solution state and is given only for reference.).

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings | UN Portable tanks and bulk containers | ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Mixed packing provisions | Portable tank instruction | Portable tank special provisions | Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |
| 3377 | SODIUM PERBORATE MONOHYDRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 BK1 BK2 | TP33 | SGAV | TU3 | AT | 3 |  | VV8 | CV24 |  | 50 |
| 3378 | SODIUM CARBONATE PEROXYHYDRATE | 5.1 | O2 | II | 5.1 |  | LQ11 | P002 IBC08 | B4 | MP10 | T3 BK1 BK2 | TP33 | SGAV | TU3 | AT | 2 | V11 | VV8 | CV24 |  | 50 |
| 3378 | SODIUM CARBONATE PEROXYHYDRATE | 5.1 | O2 | III | 5.1 |  | LQ12 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 BK1 BK2 | TP33 | SGAV | TU3 | AT | 3 |  | VV8 | CV24 |  | 50 |
| 3379 | DESENSITIZED EXPLOSIVE, LIQUID, N.O.S. | 3 | D | I | 3 | 274 311 | LQ0 | P099 |  | MP2 |  |  |  |  |  | 1 |  |  |  | S2 S20 | (RID 33) |
| 3380 | DESENSITIZED EXPLOSIVE, SOLID, N.O.S. | 4.1 | D | I | 4.1 | 274 311 | LQ0 | P099 |  | MP2 |  |  |  |  |  | 1 |  |  |  | S17 | (RID 40) |
| 3381 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | [T1 or T4] | I | 6.1 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3382 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | [T1 or T4] | I | 6.1 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3383 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | TF1 | I | 6.1 +3 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | FL | 1 |  |  | CV1 CV13 CV28 | S2 S9 S17 | 663 |
| 3384 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | TF1 | I | 6.1 +3 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | FL | 1 |  |  | CV1 CV13 CV28 | S2 S9 S17 | 663 |
| 3385 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | TW1 | I | 6.1 +4.3 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 623 |
| 3386 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | TW1 | I | 6.1 +4.3 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 623 |
| 3387 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | TO1 | I | 6.1 +5.1 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 665 |
| 3388 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | TO1 | I | 6.1 +5.1 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 665 |
| 3389 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | 6.1 | [TC1 or TC3] | I | 6.1 +8 | 274 | LQ0 | P601 |  | MP8 MP17 | T22 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 668 |
| 3390 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | 6.1 | [TC1 or TC3] | I | 6.1 +8 | 274 | LQ0 | P602 |  | MP8 MP17 | T20 | TP2 TP9 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 668 |
| 3391 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC | 4.2 | S5 | I | 4.2 | 274 | LQ0 | P404 | PP86 | MP2 | T21 | TP7 TP33 | L21DH | TU4 TU14 TU22 TC1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | 333 |
| 3392 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC | 4.2 | S5 | I | 4.2 | 274 | LQ0 | P400 | PP86 | MP2 | T21 | TP2 TP7 | L21DH | TU4 TU14 TU22 TC1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | 333 |
| 3393 | ORGANOMETALLIC SUBSTANCE, SOLID, PYROPHORIC, WATER-REACTIVE | 4.2 | SW | I | 4.2 +4.3 | 274 | LQ0 | P404 | PP86 | MP2 | T21 | TP7 TP33 | L21DH | TU4 TU14 TU22 TC1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 |
| 3394 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC, WATER-REACTIVE | 4.2 | SW | I | 4.2 +4.3 | 274 | LQ0 | P400 | PP86 | MP2 | T21 | TP2 TP7 | L21DH | TU4 TU14 TU22 TC1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 | W2 | I | 4.3 | 274 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 | S10AN L10DH | TU4 TU14 TU22 TE21 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 | W2 | II | 4.3 | 274 | LQ11 | P410 IBC04 |  | MP14 | T3 | TP33 | SGAN L4DH | TU14 TE21 TM2 | AT | 2 | V1 |  | CV23 |  | 423 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 | W2 | III | 4.3 | 274 | LQ12 | P410 IBC06 |  | MP14 | T1 | TP33 | SGAN L4DH | TU14 TE21 TM2 | AT | 3 | V1 |  | CV23 |  | 423 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | WF2 | I | 4.3 +4.1 | 274 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 | S10AN L10DH | TU4 TU14 TU22 TE21 TM2 | AT | 0 | V1 |  | CV23 |  | X423 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | WF2 | II | 4.3 +4.1 | 274 | LQ11 | P410 IBC04 |  | MP14 | T3 | TP33 | SGAN L4DH | TU14 TE21 TM2 | AT | 0 | V1 |  | CV23 |  | 423 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | WF2 | III | 4.3 +4.1 | 274 | LQ12 | P410 IBC06 |  | MP14 | T1 | TP33 | SGAN L4DH | TU14 TE21 TM2 | AT | 0 | V1 |  | CV23 |  | 423 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | WS | I | 4.3 +4.2 | 274 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 | S10AN L10DH | TU14 TE21 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | WS | II | 4.3 +4.2 | 274 | LQ11 | P410 IBC04 |  | MP14 | T3 | TP33 | SGAN L4DH |  | AT | 2 | V1 |  | CV23 |  | 423 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | WS | III | 4.3 +4.2 | 274 | LQ12 | P410 IBC06 |  | MP14 | T1 | TP33 | SGAN L4DH |  | AT | 3 | V1 |  | CV23 |  | 423 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 | W1 | I | 4.3 | 274 | LQ0 | P402 |  | MP2 | T13 | TP2 TP7 | L10DH | TU4 TU14 TU22 TE21 TM2 | AT | 0 | V1 |  | CV23 | S20 | X323 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 | W1 | II | 4.3 | 274 | LQ10 | P001 IBC01 |  | MP15 | T7 | TP2 TP7 | L4DH | TU14 TE21 TM2 | AT | 0 | V1 |  | CV23 |  | 323 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 | W1 | III | 4.3 | 274 | LQ13 | P001 IBC02 |  | MP15 | T7 | TP2 TP7 | L4DH | TU14 TE21 TM2 | AT | 0 | V1 |  | CV23 |  | 323 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | WF1 | I | 4.3 +3 | 274 | LQ0 | P402 |  | MP2 | T13 | TP2 TP7 | L10DH | TU4 TU14 TU22 TE21 TM2 | FL | 0 | V1 |  | CV23 | S2 S20 | X323 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | WF1 | II | 4.3 +3 | 274 | LQ10 | P001 IBC01 |  | MP15 | T7 | TP2 TP7 | L4DH | TU4 TU14 TU22 TE21 TM2 | FL | 0 | V1 |  | CV23 | S2 | 323 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | WF1 | III | 4.3 +3 | 274 | LQ13 | P001 IBC02 R001 |  | MP15 | T7 | TP2 TP7 | L4DH | TU14 TE21 TM2 | FL | 0 | V1 |  | CV23 | S2 | 323 |
| 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING | 4.2 | S5 | II | 4.2 | 274 | LQ18 | P410 IBC06 |  | MP14 | T3 | TP33 | SGAN L4BN |  | AT | 2 | V1 V12 |  |  |  | 40 |
| 3400 | ORGANOMETALLIC SUBSTANCE, SOLID, SELF-HEATING | 4.2 | S5 | III | 4.2 | 274 | LQ11 | P002 IBC08 |  | MP14 | T1 | TP33 | SGAN L4BN |  | AT | 3 | V1 |  |  |  | 40 |
| 3401 1389 | ALKALI METAL AMALGAM, SOLID | 4.3 | W2 | I | 4.3 | 182 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 | L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 |
| 3402 1392 | ALKALINE EARTH METAL AMALGAM, SOLID | 4.3 | W2 | I | 4.3 | 183 506 | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 | L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 |
| 3403 1420 | POTASSIUM METAL ALLOYS, SOLID | 4.3 | W2 | I | 4.3 |  | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 | L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 |
| 3404 1422 | Potassium sodium alloys, SOLID | 4.3 | W2 | I | 4.3 |  | LQ0 | P403 |  | MP2 | T9 | TP7 TP33 | L10BN(+) | TU1 TE5 TT3 TM2 | AT | 1 | V1 |  | CV23 | S20 | X423 |
| 3405 1445 | BARIUM CHLORATE SOLUTION | 5.1 | OT1 | II | 5.1 +6.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 | L4BN | TU3 | AT | 2 |  |  | CV24 CV28 |  | 56 |
| 3405 1445 | BARIUM CHLORATE SOLUTION | 5.1 | OT1 | III | 5.1 +6.1 |  | LQ13 | P001 IBC02 |  | MP2 | T4 | TP1 | LGBV | TU3 | AT | 3 |  |  | CV24 CV28 |  | 56 |
| 3406 1447 | BARIUM PERCHLORATE SOLUTION | 5.1 | OT1 | II | 5.1 +6.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 | L4BN | TU3 | AT | 2 |  |  | CV24 CV28 |  | 56 |
| 3406 1447 | BARIUM PERCHLORATE SOLUTION | 5.1 | OT1 | III | 5.1 +6.1 |  | LQ13 | P001 IBC02 |  | MP2 | T4 | TP1 | LGBV | TU3 | AT | 3 |  |  | CV24 CV28 |  | 56 |
| 3407 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE SOLUTION | 5.1 | O1 | II | 5.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 | L4BN | TU3 | AT | 2 |  |  | CV24 |  | 50 |
| 3407 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE SOLUTION | 5.1 | O1 | III | 5.1 |  | LQ13 | P504 IBC02 |  | MP2 | T4 | TP1 | LGBV | TU3 | AT | 3 |  |  | CV24 |  | 50 |
| 3408 1470 | LEAD PERCHLORATE SOLUTION | 5.1 | OT1 | II | 5.1 +6.1 |  | LQ10 | P504 IBC02 |  | MP2 | T4 | TP1 | L4BN | TU3 | AT | 2 |  |  | CV24 CV28 |  | 56 |
| 3408 1470 | LEAD PERCHLORATE SOLUTION | 5.1 | OT1 | III | 5.1 +6.1 |  | LQ13 | P001 IBC02 |  | MP2 | T4 | TP1 | LGBV | TU3 | AT | 3 |  |  | CV24 CV28 |  | 56 |
| 3409 1578 | CHLORONITRO-BENZENES, LIQUID | 6.1 | T1 | II | 6.1 | 279 | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3410 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3411 1650 | beta-NAPHTHYLAMINE SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3411 1650 | beta-NAPHTHYLAMINE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3413 1680 | POTASSIUM CYANIDE SOLUTION | 6.1 | T4 | I | 6.1 |  | LQ0 | P001 |  | MP8 MP17 | T14 | TP2 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3413 1680 | POTASSIUM CYANIDE SOLUTION | 6.1 | T4 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T11 | TP2 TP27 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3413 1680 | POTASSIUM CYANIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 TP28 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3414 1689 | SODIUM CYANIDE SOLUTION | 6.1 | T4 | I | 6.1 |  | LQ0 | P001 |  | MP8 MP17 | T14 | TP2 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3414 1689 | SODIUM CYANIDE SOLUTION | 6.1 | T4 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T11 | TP2 TP27 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3414 1689 | SODIUM CYANIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T7 | TP2 TP28 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3415 1690 | SODIUM FLUORIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3416 1697 | CHLOROACETO-PHENONE, LIQUID | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3417 1701 | XYLYL BROMIDE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3418 1709 | 2,4-TOLUYLENE-DIAMINE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3419 1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX, SOLID | 8 | C4 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAN L4BN |  | AT | 2 | V11 |  |  |  | 80 |
| 3420 1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, SOLID | 8 | C4 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAN L4BN |  | AT | 2 | V11 |  |  |  | 80 |
| 3421 1811 | POTASSIUM HYDROGENDI-FLUORIDE SOLUTION | 8 | CT1 | II | 8 +6.1 |  | LQ22 | P001 IBC02 |  | MP15 | T7 | TP2 | L4DH | TU14 TE21 | AT | 2 |  |  | CV13 CV28 |  | 86 |
| 3421 1811 | POTASSIUM HYDROGENDI-FLUORIDE SOLUTION | 8 | CT1 | III | 8 +6.1 |  | LQ19 | P001 IBC03 R001 |  | MP15 | T4 | TP1 | L4DH | TU14 TE21 | AT | 3 |  |  | CV13 CV28 |  | 86 |
| 3422 1812 | POTASSIUM FLUORIDE SOLUTION | 6.1 | T4 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3423 1835 | TETRAMETHYL-AMMONIUM HYDROXIDE, SOLID | 8 | C8 | II | 8 |  | LQ24 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAN L4BN |  | AT | 2 | V11 |  |  |  | 80 |
| 3424 1843 | AMMONIUM DINITRO-o-CRESOLATE SOLUTION | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3424 1843 | AMMONIUM DINITRO-o-CRESOLATE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3425 1938 | BROMOACETIC ACID, SOLID | 8 | C4 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAN L4BN |  | AT | 2 | V11 |  |  |  | 80 |
| 3426 2074 | ACRYLAMIDE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3427 2235 | CHLOROBENZYL CHLORIDES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3428 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3429 2239 | CHLORO-TOLUIDINES, LIQUID | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3430 2261 | XYLENOLS, LIQUID | 6.1 | T1 | II | 6.1 |  | LQ17 | P001 IBC02 |  | MP15 | T7 | TP2 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3431 2306 | NITROBENZO-TRIFLUORIDES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3432 2315 | POLYCHLORINATED BIPHENYLS, SOLID | 9 | M2 | II | 9 | 305 | LQ25 | P906 IBC08 |  | MP10 | T3 | TP33 | S4AH L4BH | TU15 TE15 | AT | 0 | V1 |  | CV1 CV13 CV28 | S19 | 90 |
| 3433 2445 | LITHIUM ALKYLS, SOLID | 4.2 | SW | I | 4.2 +4.3 | 320 | LQ0 | P400 |  | MP2 | T21 | TP7 TP33 | L21DH | TU4 TU14 TU22 TC1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 |
| 3434 2446 | NITROCRESOLS, LIQUID | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3435 2662 | HYDROQUINONE SOLUTION | 6.1 | T1 | III | 6.1 |  | LQ19 | P001 IBC03 LP01 R001 |  | MP15 | T4 | TP1 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3436 2552 | HEXAFLUORO-ACETONE HYDRATE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3437 2669 | CHLOROCRESOLS, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3438 2937 | alpha-METHYLBENZYL ALCOHOL, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 | S10AH L10CH | TU14 TU15 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3439 3276 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 274 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | I | 6.1 | 563 | LQ0 | P001 |  | MP8 MP17 | T14 | TP2 TP9 TP27 | L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | II | 6.1 | 563 | LQ17 | P001 IBC02 |  | MP15 | T11 | TP2 TP27 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3440 3283 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | III | 6.1 | 563 | LQ19 | P001 IBC03 |  | MP15 | T7 | TP1 TP28 | L4BH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 | 60 |
| 3468 | HYDROGEN IN A METAL HYDRIDE STORAGE SYSTEM | 2 | 1F |  | 2.1 | 321 | LQ0 | P099 |  | MP9 |  |  |  |  |  | 2 | V7 |  | CV9 CV10 | S2 S20 | (RID:23) |

Add the following new entries for the solid form of substances previously covered by the UN number indicated in italics in column (1):

| UN No. | Name and description | Class | Classification Code | Packing group | Labels | Special provisions | Limited quantities | Packagings | UN Portable tanks and bulk containers | ADR tank | Vehicle for tank carriage | Transport category | Special provisions for carriage | Hazard identification No. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special packing provisions | Mixed packing provisions | Portable tank instruction | Portable tank special provisions | Tank code | Special provisions |  |  | Packages | Bulk | Loading, unloading and handling | Operation |  |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9a) | (9b) | (10) | (11) | (12) | (13) | (14) | (15) | (16) | (17) | (18) | (19) | (20) |
| 3441 1577 | CHLORODINITRO-BENZENES, SOLID | 6.1 | T2 | II | 6.1 | 279 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3442 1590 | DICHLOROANILINES, SOLID | 6.1 | T2 | II | 6.1 | 279 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3443 1597 | DINITROBENZENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 R001 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3444 1656 | NICOTINE HYDROCHLORIDE, SOLID | 6.1 | T2 | II | 6.1 | 43 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH | TU15 TE15 TE19 | AT | 2 |  |  | CV13 CV28 | S9 S19 | 60 |
| 3445 1658 | NICOTINE SULPHATE, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3446 1664 | NITROTOLUENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3447 1665 | NITROXYLENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3448 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 274 | LQ0 | P002 |  | MP18 | T6 | TP9 TP33 | S10AH L10CH | TU14 TU15 TE19 TE21 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3448 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3449 1694 | Bromobenzyl cyanides, solid | 6.1 | T2 | I | 6.1 | 138 | LQ0 | P002 |  | MP18 | T6 | TP33 | S10AH L10CH | TU15 TE19 | AT | 1 |  |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3450 1699 | DIPHENYL-CHLOROARSINE, SOLID | 6.1 | T3 | I | 6.1 |  | LQ0 | P002 IBC07 |  | MP18 | T6 | TP33 | S10AH | TU15 TE19 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3451 1708 | Toluidines, SOLID | 6.1 | T2 | II | 6.1 | 279 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3452 1711 | XYLIDINES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3453 1805 | PHOSPHORIC ACID SOLID | 8 | C2 | III | 8 |  | LQ24 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAV L4BN |  | AT | 3 |  | VV9b | CV28 |  | 80 |
| 3454 2038 | DINITROTOLUENES, SOLID | 6.1 | T2 | II | 6.1 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3455 2076 | CRESOLS, SOLID | 6.1 | TC2 | II | 6.1 +8 |  | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 68 |
| 3456 2308 | NITROSYL-SULPHURIC ACID, SOLID | 8 | C2 | II | 8 |  | LQ23 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAN L4BN |  | AT | 2 | V11 |  |  |  | X80 |
| 3457 2433 | CHLORONITRO-TOLUENES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3458 2730 | NITROANISOLES, SOLID | 6.1 | T2 | III | 6.1 | 279 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3459 2732 | NITROBROMO-BENZENES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3460 2753 | N-ETHYLBENZYL-TOLUIDINES, SOLID | 6.1 | T2 | III | 6.1 |  | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3461 3052 | ALUMINIUM ALKYL HALIDES, SOLID | 4.2 | SW | I | 4.2 +4.3 | 274 320 | LQ0 | P404 |  | MP2 | T21 | TP7 TP33 | L21DH | TU4 TU14 TU22 TC1 TE21 TM1 | AT | 0 | V1 |  |  | S20 | X333 |
| 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 210 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 | S10AH L10CH | TU15 TE19 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 210 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3462 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 210 274 | LQ9 | P002 IBC08 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 43 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 | S10AH L10CH | TU14 TU15 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 43 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3464 3278 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 43 274 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 | T3 | I | 6.1 | 274 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 | S10AH L10CH | TU14 TU15 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 | T3 | II | 6.1 | 274 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3465 3280 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 | T3 | III | 6.1 | 274 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 | T3 | I | 6.1 | 274 562 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 | S10AH L10CH | TU14 TU15 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 | T3 | II | 6.1 | 274 562 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3466 3281 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 | T3 | III | 6.1 | 274 562 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |
| 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T3 | I | 6.1 | 274 562 | LQ0 | P002 IBC07 |  | MP18 | T6 | TP9 TP33 | S10AH L10CH | TU14 TU15 TE19 TE21 | AT | 1 | V10 V12 |  | CV1 CV13 CV28 | S9 S17 | 66 |
| 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T3 | II | 6.1 | 274 562 | LQ18 | P002 IBC08 | B4 | MP10 | T3 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 | V11 |  | CV13 CV28 | S9 S19 | 60 |
| 3467 3282 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 | T3 | III | 6.1 | 274 562 | LQ9 | P002 IBC08 LP02 R001 | B3 | MP10 | T1 | TP33 | SGAH L4BH | TU15 TE15 TE19 | AT | 2 |  | VV9b | CV13 CV28 | S9 | 60 |

Rationalized approach for assignment of tank instructions for solids:

| Class | Labels | PG | Tank Instruction | Tank prov. | Apply to |
| --- | --- | --- | --- | --- | --- |
| 4.1 |  | I | Not Authorized |  | All UN Nos. in this group |
|  |  | II | T3 | TP33 | 1309, 1323, 1325 (replace "TP1" with "TP33"), 1326, 1339, 1341, 1343, 1345, 1352, 1358, 1437, 1868, 1871, 2925, 2926, 2989, 3089, 3175, 3178, 3179, 3180, 3181, 3182, 3242 |
|  |  | III | T1 | TP33 | 1309,1312, 1313, 1314, 1318, 1325 (replace "TP1" with "TP33"), 1328, 1330, 1332, 1334, 1338, 1346, 1350 (replace "TP1" with "TP33"), 1869, 2001, 2213, 2538, 2687, 2714, 2715, 2717, 2878, 2925, 2926, 2989, 3089, 3097, 3178, 3179, 3180, 3181, 3182 |
| 4.2 |  | I | T21 | TP7 TP33 | 1383, 1854, 2005, 2008, 2870, 2881, 3200, 3254 |
|  |  | II | T3 | TP33 | 1361, 1369, 1374, 1378, 1382, 1384, 1385, 1431, 1923, 1929, 2004, 2008, 2318, 2545, 2546, 2881, 2940, 3088, 3126, 3127, 3128, 3189, 3190, 3191, 3192, 3205, 3206, 3313, 3341, 3342 |
|  |  | III | T1 | TP33 | 1361, 1362, 1373, 1376, 1932, 2008, 2210, 2545, 2546, 2881, 3088, 3126, 3127, 3128, 3174, 3189, 3190, 3191, 3192, 3205, 3206, 3313, 3341, 3342 |
| 4.3 | 4.3 +6.1 | I | Not Authorized |  | All UN Nos. in this group |
|  |  | I | T9 | TP7 TP33 | 1402, 1428 (replace "TP3 TP31" with "TP33") and 2257 (replace "TP3 TP31" with "TP33") |
|  |  | II | T3 | TP33 | 1340, 1390, 1393, 1394, 1395, 1396, 1400, 1401, 1402, 1405, 1409, 1417, 1418, 1436, 2624, 2805, 2813, 2830, 2835, 3078, 3131, 3132, 3134, 3135, 3170, 3208, 3209, 3372 |
|  |  | III | T1 | TP33 | 1396, 1398, 1403, 1405, 1408, 1418, 1435, 1436, 2813, 2844, 2950, 2968, 3131, 3132, 3134, 3135, 3170, 3208, 3209, 3372 |
| 5.1 |  | I | Not Authorized |  | All UN Nos. in this group |
|  |  | II | T3 | TP33 | 1439, 1442, 1445 (replace "T4" with "T3" and "TP1" with "TP33"), 1446, 1447 (replace "T4" with "T3" and "TP1" with "TP33"), 1448, 1449, 1450, 1452, 1453, 1455, 1456, 1457, 1458, 1459 (replace "T4" with "T3" and "TP1" with "TP33", 1461, 1462, 1463, 1469, 1470 (replace "T4" with "T3" and "TP1" with "TP33"), 1472, 1473, 1475, 1476, 1477, 1479, 1481, 1482, 1483, 1484, 1485, 1487, 1488, 1489, 1490, 1493, 1494, 1495, 1496, 1502, 1503, 1506, 1508, 1509, 1512, 1513, 1514, 1515, 1516, 2464, 2465, 2468, 2573, 2626, 2627, 2719, 2721, 2723, 2741, 3085, 3087, 3212, 3247 |
|  |  | III | T1 | TP33 | 1438, 1444, 1451, 1454, 1458, 1459 (replace "T4" with "T1" and "TP1" with "TP33"), 1465, 1466, 1467, 1474, 1477, 1479, 1481, 1482, 1483, 1486, 1492, 1498, 1499, 1500, 1505, 1507, 1511, 1872, 1942, 2067, 2469, 2720, 2722, 2724, 2725, 2726, 2728, 3085, 3087, 3215 |
| 5.2 |  |  | T23 | TP33 | 3110, 3120 |
| 6.1 |  | I | T6 | TP33 | 1544, 1557, 1565, 1570, 1575, 1588, 1601, 1626, 1655, 1680 (replace "T14" with "T6" and "TP2 TP13" with "TP33"), 1689 (replace "T14" with "T6" and "TP2 TP13" with "TP33"), 1692, 1698, 1713, 1889, 2025, 2026, 2316, 2471, 2570, 2588, 2628, 2629, 2630, 2642, 2757, 2759, 2761, 2763, 2771, 2775, 2777, 2779, 2781, 2783, 2786, 2811, 2928, 2930, 3027, 3048, 3086, 3124, 3125, 3143, 3146, 3283 (replace "T14" with "T6" and "TP2 TP27" with "TP33"), 3284 (replace "T14" with "T6" and "TP2 TP27" with "TP33"), 3285 (replace "T14" with "T6" and "TP2 TP27" with "TP33"), 3288, 3290, 3345, 3349 |
|  |  | II | T3 | TP33 | 1544, 1546, 1554, 1555, 1557, 1558, 1559, 1561, 1562, 1564, 1566, 1567, 1569 (replace "T10" with "T3" and "TP2 TP13" with "TP33"), 1572, 1573, 1574, 1578 (replace "T7" with "T3" and "TP2" with "TP33"), 1585, 1586, 1587, 1588, 1596 (replace "T7" with "T3" and "TP2" with "TP33"), 1598 (replace "T7" with "T3" and "TP2" with "TP33"), 1601, 1606, 1607, 1608, 1617, 1618, 1620, 1621, 1622, 1623, 1624, 1625, 1627, 1629, 1630, 1631, 1634, 1636, 1637, 1638, 1639, 1640, 1641, 1642, 1643, 1644, 1645, 1646, 1650 (replace "T7" with "T3" and "TP2" with "TP33"), 1651, 1652, 1653, 1655, 1657, 1659, 1661 (replace "T7" with "T3" and "TP2" with "TP33"), 1671 (replace "T6" with "T3" and "TP2" with "TP33"), 1674, 1677, 1678, 1679, 1683, 1684, 1685, 1688, 1691, 1697 (replace "T7" with "T3" and "TP2 TP13" with "TP33"), 1707, 1712, 1751, 1843, 1885, 1894, 1895, 2018 (replace "T7" with "T3" and "TP2" with "TP33"), 2025, 2026, 2027, 2250 (replace "T7" with "T3" and "TP2" with "TP33"), 2261 (replace "T7" with "T3" and "TP2" with "TP33"), 2567, 2570, 2587, 2588, 2645, 2647, 2649, 2657, 2671, 2673, 2727, 2757, 2759, 2761, 2763, 2771, 2775, 2777, 2779, 2781, 2783, 2786, 2811, 2859, 2861, 2863, 2864, 2928, 2930, 2931, 3027, 3086, 3124, 3125, 3143, 3146, 3155, 3243, 3249, 3283 (replace "T11" with "T3" and "TP2 TP27" with "TP33"), 3284(replace "T11" with "T3" and "TP2 TP27" with "TP33"), 3285 (replace "T11" with "T3" and "TP2 TP27" with "TP33"), 3288, 3290, 3345, 3349 |
|  |  | III | T1 | TP33 | 1544, 1548, 1549, 1550, 1551, 1557, 1564, 1566, 1579 (replace "T4" with "T1" and "TP1" with "TP33"), 1588, 1601, 1616, 1655, 1663 (replace "T4" with "T1" and "TP3" with "TP33"), 1673 (replace "T7" with "T1" and "TP1" with "TP33"), 1690 (replace "T4" with "T1" and "TP1" with "TP33"), 1709 (replace "T4" with "T1" and "TP1" with "TP33"), 1812 (replace "T4" with "T1" and "TP1" with "TP33"), 1884, 2020, 2025, 2026, 2074 (replace "T4" with "T1" and "TP1" with "TP33"), 2233, 2237, 2239 (replace "T4" with "T1" and "TP1" with "TP33"), 2291, 2446, 2473, 2505, 2512, 2516, 2570, 2588, 2651 (replace "T4" with "T1" and "TP1" with "TP33"), 2655, 2659, 2660, 2662 (replace "T4" with "T1" and "TP1" with "TP33"), 2674, 2713, 2716, 2729, 2757, 2759, 2761, 2763, 2771, 2775, 2777, 2779, 2781, 2783, 2786, 2811, 2853, 2854, 2855, 2856, 2862, 2871, 2875, 2876, 3027, 3143, 3146, 3249, 3283 (replace "T7" with "T1"and "TP1 TP28" with "TP33"), 3284 (replace "T7" with "T1" and "TP1 TP28" with "TP33"), 3285 (replace "T7" with "T1" and "TP1 TP28" with "TP33"), 3288, 3345, 3349 |
| 8 |  | I | T6 | TP33 | 1759, 1905, 2430 (replace "T10" with "T1" and "TP2 TP28" with "TP33"), 2921, 2923, 3084, 3095, 3096, 3147, 3259, 3260, 3261, 3262, 3263 |
|  |  | II | T3 | TP33 | 1725, 1726, 1727, 1740, 1756, 1759, 1770, 1794, 1806, 1807, 1811 (replace "T7" with "T3" and "TP2" with "TP33"), 1813, 1823, 1825, 1839, 1847, 1849 (replace "T7" with "T3" and "TP2" with "TP33"), 1939 (replace "T7" with "T3" and "TP2" with "TP33"), 2033, 2430 (replace "TP2" with "TP33"), 2439, 2506, 2509, 2583, 2670, 2678, 2680, 2682, 2691, 2869, 2921, 2923, 3084, 3095, 3096, 3147, 3244, 3259, 3260, 3261, 3262, 3263 |
|  |  | III | T1 | TP33 | 1740, 1759, 1773, 1907, 1910, 2214 (replace "T4" with "T1" and "TP3" with "TP33"), 2215 (replace "T4" with "T1" and "TP1" with "TP33"), 2280 (replace "T4" with "T1" and "TP3" with "TP33"), 2331, 2430 (replace "T3" with "T1" and "TP1" with "TP33"), 2440, 2475, 2503, 2507, 2508, 2578, 2579 (replace "T4" with "T1" and "TP1 TP30" with "TP33"), 2585, 2698, 2802, 2803, 2812, 2823 (replace "T4" with "T1" and "TP1" with "TP33"), 2834 (replace "T3" with "T1" and "TP1" with "TP33"), 2865, 2869, 2905, 2923, 2967, 3147, 3253, 3259, 3260, 3261, 3262, 3263 |
| 9 |  | II | T3 | TP33 | 2212, 2969, 3152 |
|  |  | III | T1 | TP33 | 1841, 1931, 2211, 2216, 2590, 3077 |

Chapter 3.3

Amend the following special provisions as follows:

SP203		Replace the existing text with the following:

"This entry shall not be used for polychlorinated biphenyls, liquid, UN No. 2315 and polychlorinated biphenyls, solid, UN No. 3432."

SP215	Add the following text at the end:

"Homogeneous mixtures containing not more than 35 % by mass of azocarbonamide and at least 65 % of inert substance are not subject to RID/ADR/ADN unless criteria of other classes are met.".

SP219		Amend to read as follows:

"Genetically modified micro-organisms and genetically modified organisms which meet the definition of an infectious substance and the criteria for inclusion in Class 6.2 in accordance with section 2.2.62 shall be carried as UN No. 2814, UN No. 2900 or UN No. 3373, as appropriate.".

SP296	Replace the existing text with the following:

"These entries apply for life-saving appliances such as life rafts, personal flotation devices and self-inflating slides. UN No. 2990 applies for self-inflating appliances and UN No. 3072 applies for life-saving appliances that are not self-inflating.  Life-saving appliances may contain:

(a) 	Signal devices (Class 1) which may include smoke and illumination signal flares packed in packagings that prevent them from being inadvertently activated;

(b) 	For UN No. 2990 only, cartridges, power device of Division 1.4, compatibility group S, may be contained for purposes of the self-inflating mechanism and provided that the quantity of explosives per appliance does not exceed 3.2 g;

(c) 	Class 2 compressed gases, group A or O, according to 2.2.2.1.3;

(d) 	Electric storage batteries (Class 8) and lithium batteries (Class 9);

(e) 	First aid kits or repair kits containing small quantities of dangerous goods (e.g.: Class 3, 4.1, 5.2, 8 or 9 substances); or

(f) 	"Strike anywhere" matches packed in packagings that prevent them from being inadvertently activated.".

SP309 	Amend the last sentence to read as follows:

"Substances shall pass Test Series 8 of the Manual of Tests and Criteria, Part I, Section 18."

SP513	Replace the fourth sentence with the following:

"UN No. 1445 barium chlorate, solid, UN No. 1446 barium nitrate, UN No. 1447 barium perchlorate, solid, UN No. 1448 barium permanganate, UN No. 1449 barium peroxide, UN No. 2719 barium bromate, UN No. 2741 barium hypochlorite with more than 22% available chlorine, UN No. 3405 barium chlorate, solution and UN No. 3406 barium perchlorate, solution, are substances of Class 5.1."

SP517	Replace the existing text with the following:

"UN No. 1690 sodium fluoride, solid, UN No. 1812 potassium fluoride, solid, UN No. 2505 ammonium fluoride, UN No. 2674 sodium fluorosilicate, UN No. 2856 fluorosilicates, n.o.s., UN No. 3415 sodium fluoride, solution and UN No. 3422 potassium fluoride, solution, are substances of Class 6.1."

SP527	Delete this special provision.

SP535	Replace the existing text with the following:

"UN No. 1469 lead nitrate, UN No. 1470 lead perchlorate, solid and UN No. 3408 lead perchlorate, solution are substances of Class 5.1."

Add the following new special provisions:

[179		"This designation may also be used for wastes not otherwise subject to RID/ADR/ADN but which are covered under the Basel Convention on the Control of Transboundary Movements of Hazardous Wastes and their Disposal".].

[201	Lighters and lighter refills shall comply with the provisions of the country in which they were filled.  They shall be provided with protection against inadvertent discharge.  The liquid portion of the gas shall not exceed 85% of the capacity of the receptacle at 15 °C. The receptacles, including the closures, shall be capable of withstanding an internal pressure of twice the pressure of the liquefied petroleum gas at 55 °C.  The valve mechanisms and ignition devices shall be securely sealed, taped or otherwise fastened or designed to prevent operation or leakage of the contents during carriage.  Lighters shall not contain more than 10 g of liquefied petroleum gas.  Lighter refills shall not contain more than 65 g of liquefied petroleum gas.].

243	"Gasoline, motor spirit and petrol for use in spark-ignition engines (e.g. in automobiles, stationary engines and other engines) shall be assigned to this entry regardless of variations in volatility.".

311	Substances shall not be carried under this entry unless approved by the competent authority on the basis of the results of appropriate tests according to Part I of the Manual of Tests and Criteria. Packaging shall ensure that the percentage of diluent does not fall below that stated in the competent authority approval, at any time during carriage.

313	Substances and mixtures meeting the criteria for Class 8 shall bear a subsidiary risk label conforming to model No. 8 (see 5.2.2.2.2).

314	a) 	These substances are liable to exothermic decomposition at elevated temperatures. Decomposition can be initiated by heat or by impurities (e.g. powdered metals (iron, manganese, cobalt, magnesium) and their compounds);

b)	During the course of carriage, these substances shall be shaded from direct sunlight and all sources of heat and be placed in adequately ventilated areas.

315	This entry shall not be used for Class 6.1 substances which meet the inhalation toxicity criteria for packing group I described in 2.2.61.1.8.

316	This entry applies only to calcium hypochlorite, dry or hydrated, when carried in non friable tablet form.

317	"Fissile-excepted" applies only to those packages complying with 6.4.11.2.

318	For the purposes of documentation, the proper shipping name shall be supplemented with the technical name (see 3.1.2.8). When the infectious substances to be carried are unknown, but suspected of meeting the criteria for inclusion in category A and assignment to UN No. 2814 or 2900, the words "suspected category A infectious substance" shall be shown, in parentheses, following the proper shipping name on the transport document.

319	This entry applies to human or animal material including, but not limited to, excreta, secreta, blood and its components, tissue and tissue fluids, and body parts being carried for purposes such as research, diagnosis, investigational activities, disease treatment or prevention.  Substances packed and marked in accordance with packing instruction P650 are not subject to any other requirements of RID/ADR/ADN.

320	It is intended that this entry will be deleted from RID/ADR/ADN on 1 January 2007. Irrespective of 2.1.2, in the interim period, this entry or the appropriate generic entry may be used.

321	These storage systems shall always be considered as containing hydrogen.".

---------------------------------

# Footnotes

*/ 	Circulated by the Central Office for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT-III/2003/56/Add.3.

"1 	Details are provided in the alphabetical index (Table B of 3.2.2), e.g.:

NITROXYLENES, LIQUID 	6.1 	1665

NITROXYLENES, SOLID	6.1	3447"

# Text boxes

Economic and Social

Council

E