## Proposal of amendment of ADR/RID - 	Annex 1

| LPG CYLINDERS REQUALIFICATION WITHIN EU/CEN COUNTRIES |
| --- |
| COUNTRY | 15 years acceptance/date | Comments | Type of tests | Authority requests |
|  |  |  | Ext. Insp. | Int. Insp. | Pres. test | Others |  |
| AUSTRIA | Yes |  | Yes |  | Yes |  | Quality management system + accordance to EN 1439 and 1440 |
| SWITZERLAND | Yes/1997 |  | Yes |  | Yes |  | Accordance to EN 1440. Yearly audit. |
| GERMANY | Yes | Cylinders manufactured from 1969. Under expertise for oldest cylinders. | Yes | Yes | Yes |  | Product and operation management system requested |
| BELGIUM | Yes |  | Yes | No | Yes | Pneumatic pressure test allowed | Accordance to EN 1439 and 1440. Periodical audit by qualified body. Date of the next requalification on the cylinder |
| France | Yes/1984 | Cylinders manufactured after about 1960-1965. 5 years interval for older cylinders | Yes | No | Yes | Periodical burst tests on samples. Pneumatic test on camping cylinders | Possibility of self assessment Quality management system + periodical audit |
| SPAIN | Waiting for a response of the authority |  |  |  |  |  |  |
| PORTUGAL | Yes | From date of manufacture for “(” cylinders. From last requalification date for others. | Yes | No | Yes |  |  |
| UNITED KINGDOM | Yes |  | Yes | Yes | Yes/No | Pressure test according to company practices | Accordance to EN 1440 |
| IRELAND | Yes |  | Yes | Yes | No |  | None. Professional code of practice in accordance with EN 1440. New or refurbished valve. |
| ITALY | Possible, but not applied | 10 years interval applied | Yes | No | Yes |  | Accordance to EN 1440 ? |
| DENMARK | Possible, but not applied | 10 years interval applied. 5 years interval for cylinders manufactured before 1956. | Yes | Yes | Yes |  | Accordance to EU directive 1999/36: Approved quality management system in accordance to 1999/36/EEC or EN 45004. Accordance to EN 1440. |
| FINLAND | Yes |  | Yes | Yes | Yes | Not more than 5% loss in weight | Accordance to EN 1440. New valve to be fitted |
| SWEDEN | No |  | Yes | Yes | Yes | Not more than 5% loss in weight | Accordance to EN 1440. New valve to be fitted |