INF.57

### ECONOMIC COMMISSION FOR EUROPE

#### INLAND TRANSPORT COMMITTEE

##### Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods.

(Bonn, 13-17 October 2003

agenda item 3(a))

# Part 7 of ADR

Revised Proposal based on 2003/2 and 2003/51

##### Proposal:

1.	Insert a new “CV/CW xy” in Table A for all substances of Class 2

“CV/CW xy	Packages shall preferably be loaded in open vehicles/wagons or open containers. If this is not feasible and packages are carried in closed vehicles/wagons or containers, the cargo doors of the vehicles/wagons or containers shall be marked with the following in letters not less than 25 mm high:

“NO VENTILATION

OPEN WITH CAUTION”

Placards shall be affixed to closed vehicles, see 5.3.1.5.3. [This sentence in ADR only] Sources of ignition shall not be present in a closed vehicle/wagon or closed container when flammable gases are carried.”

- Insert the following text in 5.3.1.5: [ADR only]

“5.3.1.5.3	For closed vehicles carrying packages of substances which have special provision CVxy in column (18) of table A of Chapter 3.2, placards shall be affixed to both sides and at the rear of the vehicle.”

----------------------------------