Informal Document No. 5

(53rd GRRF, 3 – 7 February 2003,

agenda Item 1.5.)

PROPOSAL TO AMEND UNECE REGULATION 13

(Braking)

Transmitted by the Expert from the United Kingdom on behalf of Ad-hoc Working Group on HVG Compatibility

A.	Proposal

In Regulation 13, Annex 10, add a new paragraph 1.3. to read:

  - Validation of the development of braking force.

    - At the time of type approval it shall be checked that the development of braking on an axle of each independent axle group */ shall be within the following pressure ranges:

Laden vehicles:

At least one axle shall commence to develop a braking force when the pressure at the coupling head is within the pressure range 0.2 to 1.0 bar.

At least one axle of any other axle group shall commence to develop a braking force when the pressure at the coupling head is at a pressure ≤ [1.2 bar].

Unladen vehicles:

At least one axle shall commence to develop a braking force when the pressure at the coupling head is within the pressure range 0.2 to 1.0 bar.

*/ 	An axle group is where a number of axles have a maximum axle spread of 2m.

      - With the wheel(s) of the axle(s) raised off the ground and free to rotate, apply an increasing brake demand and measure the coupling head pressure corresponding to when the wheel(s) can no longer be rotated by hand. This condition is defined as the development of the braking force.

In Regulation 13, Annex 10, amend paragraph 7.5. to read:

  - Electronically controlled brake force distribution systems that cannot fulfil the requirements of paragraphs 7.1., 7.2., 7.3. and 7.4. above shall have a self-checking procedure of the functions which influence brake force distribution. In addition, when the vehicle is stationary, it must be possible to carry out the checks defined in paragraph 1.3.1. above by generating the nominal demand pressure value associated with the commencement of braking for both the laden and the unladen conditions.

In Regulation 13, Annex 10, amend paragraph 8. to read:

- Vehicle testing

During the type approval testing of a vehicle, the technical inspection authority  At the time of type approval the technical service shall verify conformity with the requirements contained in the present within this Annex and carry out any further tests considered necessary to this end. The results of on any further additional tests shall be recorded and appended to the type approval report.

### B.	Justification

Paragraph 1.3.: Whilst the majority of brake applications occur at low pressure, to date no defined test procedure exist enabling the compatibility requirements to be verified and therefore the addition of paragraph 1.3. within Annex 10 addresses this issue by:

- Defining a standard procedure by which the reference values (development of a braking force) referred to in Annex 10, paragraph 1.2. can be easily verified.

- Controlling/improving the differentials in brake performance that can exist between motor vehicles and their trailers and so aiding the issue to brake compatibility.

Paragraph 7.5.:  For vehicles with EBS, the addition of the second sentence ensures that the coupling head nominal demand pressure value associated with the commencement of braking fulfils the requirements as defined within Annex 10, paragraph 1.2.

Paragraph 8.:  Alignment of terminology with supplement 6 of the 09 series of amendments to this Regulation.