HARMONIZATION OF MOTORCYCLE BRAKING REQUIREMENTS

Transmitted by the expert from Canada

An informal working group meeting regarding the harmonization of motorcycle braking

requirement was held this past July.  A study to determine the most stringent requirements was

conducted by Canada and was compared to a similar study made by IMMA.  A summery of that

comparison and other documents presented during that meeting can be obtain from on the ECE

web site at the following address.

http://www.unece.org/trans/main/wp29/wp29wgs/wp29grrf/grrf-infmotobrake1.html

To date, the testing of five motorcycles, (2001 BMW C1 Executive 125, 2003 Harley Davidson

Dyna Super Glide FXD, 2002 Honda ST1100A, 2002 Honda Interceptor VFR 800 and a 2002

Suzuki Marauder GZ 250) to three world motorcycle brake system regulations has been

completed (ECE 78, FMVSS 122 and JSS 12-61).  Additional Anti-Lock Brake System (ABS)

testing was also conducted on the two Honda’s and the BMW. The final report for this work

should be submitted to NHTSA this October.

Additional braking tests on the Honda VFR 800, Yamaha FJR 1300, BMW F650CS and the

BMW R1150R are underway for the purposes of comparing the performances of ABS and

non-ABS equipped motorcycles, both in the loaded and unloaded conditions.

A date for the next informal group meeting has not yet been set, however, one will likely be held

at the end of winter or beginning of spring 2004.  For other questions please contact Mr. Bergevin

at bergema@tc.gc.ca or  Mr. D. Brault at braultd@tc.gc.ca

_________________