Informal document No. GRSG-87-18

(87th GRSG, 12-15 October 2004,

agenda item 3.)

## Proposal for draft amendments to Document TRANS/WP.29/GRSG/2003/22/Rev.1 regarding Regulation No. 107

Transmitted by the expert from Germany

### PROPOSAL

7.11.2.2	amend to read:

“7.11.2.2.	When applying the procedure described in paragraph 7.11.2.1, only such hand-rails and handholds shall be considered as are not less than 800 mm and not more than 1950 mm above the floor.”

JUSTIFICATION

Presently it would not be possible to provide hand-rails in certain positions above the gangway and to meet the requirements for the height of the gangway of 1900 mm without using strap hangers. The new text clarifies the situation.

_______________