| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRSG/2005/5 31 January 2005 Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

(Eighty-eighth session, 18 - 22 April 2005,

agenda item 2.1.)

## PROPOSAL FOR DRAFT CORRIGENDUM TO REGULATIONS Nos. 18 and 116

(Protection against unauthorized use)

# Transmitted by the expert from the Netherlands

Note:  The text reproduced below was prepared by the expert from the Netherlands in order to delete Annex 5 .

____________

_______________

Note: This document is distributed to the Experts on General Safety Provisions only.

A.	PROPOSALS FOR ECE-regulation Nos. 18 and 116

List of Annexes, "Annex 5   Electrically powered system test", amend to read:
"Annex 5	(Reserved)".

Annex 5, amend to read:

"Annex 5

(Reserved)"

*     *     *

B.	JUSTIFICATION

These Regulations contain no reference to Annex 5.  Initially Annex 5 was introduced by paragraph 20. of the draft proposal (TRANS/WP.29/GRSG/R.288) of GRSG in 1995.  However, in its seventieth session, GRSG decided to eliminate all requirements applicable to vehicle door locks, inclusive of paragraph 20.  Annex 5 should have been deleted as well.  In addition to that, the tests prescribed in Annex 5 are already covered by other requirements of the Regulations, but with different parameters like time, voltages, etc.  Maintaining this annex would lead to confusion.  As Regulation No. 18 has been used for drafting the new Regulation No. 116, the Netherlands suggest to replace the present text of Annex 5 by "(Reserved)" in both regulations.

__________