| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.6/2005/1 8 December 2004 Original: ENGLISH |
| ECONOMIC COMMISSION FOR EUROPE |

INLAND TRANSPORT COMMITTEE

##### Working Party on Transport Statistics

(Fifty-sixth session, 8-10 June 2005)

GLOSSARY FOR TRANSPORT STATISTICS: UPDATE

INLAND WATERWAYS

### Note by the secretariat

Following the adoption of a new classification of navigable inland waterways in 1992 by the United Nations Economic Commission for Europe (UNECE) (resolution No.30) and the European Conference of Ministers of Transport (ECMT) (CEMT/CM(92)6 Final), the Intersecretariat Working Group (IWG), during its meeting on 25-26 November 2004 in Paris, agreed to introduce this update in the Glossary for Transport Statistics.

The IWG proposes that the Working Party adopt this document without alterations.

* * *

CATEGORIES OF NAVIGABLE INLAND WATERWAYS

Current Glossary for Transport Statistics definition C.I.03 is replaced by the following:

C.I.03.	Categories of navigable inland waterways

Taking into account the 1992 UNECE/ECMT Classification of European Inland Waterways, canals, navigable rivers and lakes the different categories are to be defined as follows:

By horizontal dimensions of vessels and pushed convoys

Class		(length/beam)

I to III		Up to 80/9 m.

IV		80-85/9.50 m.

V a		95-110/11.40 m.

V b		172-175/11.40 m.

VI a		95-110/22.80 m.

VI b		185-195/22.80 m.

VI c		270-280/22.80 or 193-200/33-34.20 m.

VII		285/33-34.20 m and over.

In some cases the "carrying capacity of vessels" may be used to classify the navigable inland waterways.

_______________