| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.15/AC.1/2006/30 29 June 2006 ENGLISH Original: FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the
Working Party on the Transport of Dangerous Goods

Geneva, 11-15 September 2006
Agenda item 5

# Proposals for amendments to RID/ADR/ADN*

## Carriage of liquid or solid substances in pressure receptacles

## Proposal submitted by the Government of Germany

SUMMARY Executive summary: As of 1 January 2007, new requirements for the carriage of liquid or solid substances in pressure receptacles (new subsection 4.1.3.6) will be introduced in RID/ADR/ADN. Among others, the substances listed in subsection 4.1.4.4 are excluded from those requirements. The present document is aimed at introducing the necessary provisions of 4.1.4.4 in the new system.

Action to be taken: Amendments to the relevant packing instructions for certain substances and deletion of subsection 4.1.4.4. Relevant documents: TRANS/WP.15/AC.1/2005/42/Add.1-OCTI/RID/GT-III/2005/42/Add.1, INF.16 (CEFIC) of the Joint Meeting of September 2005, TRANS/WP.15/AC.1/100-OCTI/RID/GT-III/2005-B, para. 53.

1.	The non-restructured RID/ADR/ADN had already required the use of pressure receptacles for the carriage of liquid or solid substances other than those of class 2.

2.	Those requirements were moved to subsection 4.1.4.4 of the restructured RID/ADR/ADN by introducing special requirements applicable to the use of pressure receptacles for substances other than those of class 2.

3.	With the amendments to the thirteenth edition of the United Nations Recommendations, similar provisions were introduced into the United Nations Model Regulations, but they still differed from those of RID/ADR/ADN.

4.	The ad hoc working group on the harmonization of RID/ADR/ADN with the fourteenth edition of the United Nations Recommendations discussed the provisions on the carriage of liquid or solid substances in pressure receptacles at its meeting in 
May 2005.  The outcome of those deliberations was presented in document TRANS/WP.15/AC.1/2005/42/Add.1-OCTI/RID/GT-III/2005/42/Add.1.

5.	At the meeting of the ad hoc working group, the CEFIC representative undertook to draw up a document for the Joint Meeting highlighting the differences between the existing requirements of subsection 4.1.4.4 and the new provisions to be taken up under subsection 4.1.3.6.  This was issued as informal document INF.16.

6.	INF.16 also contained a proposal to delete subsection 4.1.4.4, which was not adopted (see the report of the Joint Meeting, TRANS/WP.15/AC.1/100-OCTI/RID/GT-III/2005-B, para. 53).

7.	As this decision was taken by a slight majority, the chair of the Joint Meeting asked that another document be submitted on the subject so as to ensure closer harmonization with the United Nations Model Regulations.

8.	The delegation of Germany said that it was prepared to draw up a proposal for a forthcoming session in order to provide clarification.

9.	All the United Nations Nos. in question are listed in the annex in the order of their packing instructions.

### Proposals

10.	Amendments to packing instruction P401:

Particular requirement PR2, applicable to the use of pressure receptacles for substances other than those of class 2, calls for periodic tests to be carried out on pressure receptacles every five years.  The provisions of subsection 4.1.3.6 extend the period to 10 years.  For corrosive substances, the time between periodic tests should not be extended.  The following new special packing provision, specific to RID/ADR/ADN should therefore be added to the packing instruction for United Nations Nos. 1183, 1242, 1295 and 2988:

“RR xa	For United Nations Nos. 1183, 1242, 1295 and 2988, the pressure receptacles shall be subjected to the tests every five years at a pressure of not less than 0.6 MPa (6 bar) in accordance with subsection 4.1.3.6.”

11.	Amendments to packing instruction P402:

Particular requirement PR1, applicable to the use of pressure receptacles for substances other than those of class 2, calls for a test pressure of not less than 10 bars for pressure receptacles.  Since that is the generally required test pressure for gas receptacles, a reduction to 6 bars does not seem justified.  The following new special packing provision, specific to RID/ADR/ADN, should therefore be added to the packing instruction for United Nations Nos. 1389, 1391, 1411, 1421, 1928, 3129, 3130
and 3148:

“RR xb	For United Nations Nos. 1389, 1391, 1411, 1421, 1928, 3129, 3130 
and 3148, the pressure receptacles shall be subjected to an initial test and to periodic tests at a pressure of not less than 1 MPa (10 bar) in accordance with subsection 4.1.3.6.”

12.	Amendments to packing instruction P402:

Particular requirement PR1, applicable to the use of pressure receptacles for substances other than those of class 2, calls for periodic tests to be carried out on pressure receptacles every five years.  The provisions of subsection 4.1.3.6 extend the period to 10 years.  For corrosive substances, the time between periodic tests should not be extended.  The following new special packing provision, specific to RID/ADR/ADN, should therefore be added to the packing instruction for United Nations No. 3129:

“RR xc	For United Nations No. 3129, the pressure receptacles shall be subjected to the tests every five years at a pressure of not less than 1 MPa (10 bar) in accordance with subsection 4.1.3.6.”

13.	Amendments to packing instruction P601:

Particular requirement PR3, applicable to the use of pressure receptacles for substances other than those of class 2, calls for periodic tests to be carried out on pressure receptacles every five years.  The provisions of subsection 4.1.3.6 extend the period to 10 years.  For corrosive substances, the time between periodic tests should not be extended.  The following new special packing provision, specific to RID/ADR/ADN, should therefore be added to the packing instruction for United Nations No. 1251:

“RR xd	For United Nations No. 1251, the pressure receptacles shall be subjected to the tests every five years at a pressure of not less than 1 MPa (10 bar) in accordance with subsection 4.1.3.6.”

14.	Amendments to packing instruction P601:

Particular requirement PR6, applicable to the use of pressure receptacles for substances other than those of class 2, sets out particular requirements for bromine in respect of the materials to be used for pressure receptacles and their closing devices.  Since the substance in question is highly corrosive, from the technical safety point of view, it is unacceptable to extend the time between periodic tests.  The following new special packing provision, specific to RID/ADR/ADN, should therefore be added to the packing instruction for United Nations No. 1744:

“RR xe	For United Nations No. 1744 containing less than 0.005% water, or between 0.005% and 0.2% water, provided that in the latter case measures are taken to prevent corrosion of the lining of the receptacles, the pressure receptacles shall be subjected to the tests every five years at a pressure of not less than 1 MPa (10 bar) in accordance with subsection 4.1.3.6.  The receptacles shall be made of steel and shall be equipped with a leakproof lining made of lead or of some other material affording equivalent protection and with a hermetic closure; receptacles made of monel alloy or nickel, or with a nickel lining, shall also be permitted.  The closures shall be sited in the upper part of the receptacles so as to avoid permanent contact with the liquid phase.”

15.	Amendments to packing instruction P601:

Particular requirement PR7, applicable to the use of pressure receptacles for substances other than those of class 2, stipulates that precise instructions exist on the packaging for United Nations No. 1614.  The United Nations Recommendations mention only packing instruction P099.  In order to continue applying the current packing requirements, the whole of particular requirement PR7 should be added to the packing instruction as PR xf, a new special packing provision, specific to RID/ADR/ADN.

16.	Amendments to packing instruction P601:

As a consequence of the above amendments, special packing provision RR3 specific to RID/ADR/ADN should be deleted.

17.	As a consequence of the above amendments, the phrase “and in 4.1.4.4” should be deleted from the last sentence of paragraph 4.1.3.6.1, the text in brackets “(see also the Table in 4.1.4.4)” should be deleted from the introductory sentences in packing instructions P400, P401 and P402 and subsection 4.1.4.1 itself should be deleted.

### Justification

Safety implications:	It is no longer necessary to limit the capacity of pressure receptacles used for solid or liquid substances to 450 litres, for example, as experience has shown that larger receptacles can be used.

According to the most recent information, increasing the degree of filling will not entail an added technical safety risk.

The extension of the time between periodic tests corresponds with current practice and is only questionable or unacceptable in the case of corrosive substances.

Reducing the inert gas gauge pressure during carriage from 0.5 bar to less than half (0.2 bar) will run no technical safety risk, as it is possible that the pressure in question will not be maintained during carriage, when the inert gas dissolves in the substance carried.  In this case, it is the elimination of the air in the liquid phase that is important.

Feasibility:	Since the new requirements for the carriage of dangerous solid and liquid substances in pressure receptacles will be introduced in RID/ADR/ADN as of 1 January 2007 and the subsection’s requirements will remain unchanged, adoption of these amendments will ensure better harmonization with the United Nations Model Regulations.

Practical implementation:	The high level of interest shown by industrial concerns in this subject demonstrates that a solution must be found to the problem of carrying substances other than those of class 2 in pressure receptacles.

## Annex

Packing instruction P400 	(On 1 January 2007, the entries highlighted in yellow (or in gray, on a black-and-white printout) will be deleted.  The substances in question must thereafter be carried in accordance with the conditions of United Nations No. 3394.)

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1366 | DIETHYLZINC | 4.2 | SW | I | 4.2+ 4.3 | 320 | LQ0 | P400 PR1 |
| 1370 | DIMETHYLZINC | 4.2 | SW | I | 4.2+ 4.3 | 320 | LQ0 | P400 PR1 |
| 2445 | LITHIUM ALKYLS, LIQUID | 4.2 | SW | I | 4.2+ 4.3 | 274 320 | LQ0 | P400 PR1 |
| 2845 | PYROPHORIC LIQUID, ORGANIC, N.O.S. | 4.2 | S1 | I | 4.2 | 274 | LQ0 | P400 PR1 |
| 2870 | ALUMINIUM BOROHYDRIDE | 4.2 | SW | I | 4.2+ 4.3 |  | LQ0 | P400 PR1 |
| 3051 | ALUMINIUM ALKYLS | 4.2 | SW | I | 4.2+ 4.3 | 274 320 | LQ0 | P400 PR1 |
| 3052 | ALUMINIUM ALKYL HALIDES, LIQUID | 4.2 | SW | I | 4.2+ 4.3 | 274 320 | LQ0 | P400 PR1 |
| 3053 | MAGNESIUM ALKYLS | 4.2 | SW | I | 4.2+ 4.3 | 274 320 | LQ0 | P400 PR1 |
| 3076 | ALUMINIUM ALKYL HYDRIDES | 4.2 | SW | I | 4.2+ 4.3 | 274 320 | LQ0 | P400 PR1 |
| 3194 | PYROPHORIC LIQUID, INORGANIC, N.O.S. | 4.2 | S3 | I | 4.2 | 274 | LQ0 | P400 PR1 |
| 3254 | TRIBUTYLPHOSPHANE | 4.2 | S1 | I | 4.2 |  | LQ0 | P400 PR1 |
| 3394 | ORGANOMETALLIC SUBSTANCE, LIQUID, PYROPHORIC, WATER-REACTIVE | 4.2 | SW | I | 4.2+ 4.3 | 274 | LQ0 | P400 PR1 |

Packing instruction P401

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1183 | ETHYLDICHLOROSILANE | 4.3 | WFC | I | 4.3+3+8 |  | LQ0 | P401 PR2 |
| 1242 | METHYLDICHLOROSILANE | 4.3 | WFC | I | 4.3+3+8 |  | LQ0 | P401 PR2 |
| 1295 | TRICHLORSILANE | 4.3 | WFC | I | 4.3+3+8 |  | LQ0 | P401 PR2 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | 4.3 | WFC | I | 4.3+3+8 | 274 549 | LQ0 | P401 PR2 |

Packing instruction P402

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1389 | ALKALI METAL AMALGAM, LIQUID | 4.3 | W1 | I | 4.3 | 182 274 | LQ0 | P402 PR1 |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION with a flash-point above 60° C | 4.3 | W1 | I | 4.3 | 182 183 274 506 | LQ0 | P402 PR1 |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION with a flash-point not greater than 60° C | 4.3 | W1 | I | 4.3+3 | 182 183 274 506 | LQ0 | P402 PR1 |

Packing instruction P402 (continued)

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1411 | LITHIUM ALUMINIUM HYDRIDE, ETHEREAL | 4.3 | WF1 | I | 4.3+3 |  | LQ0 | P402 PR1 |
| 1421 | ALKALI METAL ALLOY, LIQUID, N.O.S. | 4.3 | W1 | I | 4.3 | 182 274 | LQ0 | P402 PR1 |
| 1928 | METHYL MAGNESIUM BROMIDE IN ETHYL ETHER | 4.3 | WF1 | I | 4.3+3 |  | LQ0 | P402 PR1 |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | WC1 | I | 4.3+8 | 274 | LQ0 | P402 PR1 |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | WC1 | II | 4.3+8 | 274 | LQ10 | P402 IBC01 PR1 |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | WT1 | I | 4.3+ 6.1 | 274 | LQ0 | P402 PR1 |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | WT1 | II | 4.3+ 6.1 | 274 | LQ10 | P402 IBC01 PR1 |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 | W1 | I | 4.3 | 274 | LQ0 | P402 PR1 |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 | W1 | II | 4.3 | 274 | LQ10 | P402 IBC01 PR1 |

Packing instruction P601

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1380 | PENTABORANE | 4.2 | ST3 | I | 4.2+ 6.1 |  | LQ0 | P601 PR1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| 1092 | ACROLEIN, STABILIZED | 6.1 | TF1 | I | 6.1+3 |  | LQ0 | P601 PR3 |
| 1251 | METHYL VINYL KETONE, STABILIZED | 6.1 | TFC | I | 6.1+3+8 |  | LQ0 | P601 PR3 |
| 1259 | NICKEL CARBONYL | 6.1 | TF1 | I | 6.1+3 |  | LQ0 | P601 PR3 |
| 1613 | HYDROCYANIC ACID, AQUEOUS SOLUTION (HYDROGEN CYANIDE, AQUEOUS SOLUTION) with not more than 20% hydrogen cyanide | 6.1 | TF1 | I | 6.1+3 | 48 | LQ0 | P601 PR3 |
| 1994 | IRON PENTACARBONYL | 6.1 | TF1 | I | 6.1+3 |  | LQ0 | P601 PR3 |
| 3294 | HYDROGEN CYANIDE, SOLUTION IN ALCOHOL with not more than 45% hydrogen cyanide | 6.1 | TF1 | I | 6.1+3 | 610 | LQ0 | P601 PR3 |

Packing instruction P601 (continued)

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1185 | ETHYLENEIMINE, STABILIZED | 6.1 | TF1 | I | 6.1+3 |  | LQ0 | P601 PR4 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| 2480 | METHYL ISOCYANATE | 6.1 | TF1 | I | 6.1+3 |  | LQ0 | P601 PR5 |
| 2481 | ETHYL ISOCYANATE | 3 | FT1 | I | 3+6.1 |  | LQ0 | P601 PR5 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| 1744 | BROMINE or BROMINE SOLUTION | 8 | CTI | I | 8+6.1 |  | LQU | P601 PR6 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| 1614 | HYDROGEN CYANIDE, STABILIZED, containing less than 3% water and absorbed in a porous inert material | 6.1 | TF1 | I | 6.1+3 | 603 | LQ0 | P099 P601 PR7 |
| Packing instruction P602 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) |
| 1605 | ETHYLENE DIBROMIDE | 6.1 | T1 | I | 6.1 |  | LQ0 | P602 PR3 |

# Footnotes

*  Circulated by the Central Office for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT-III/2006/30.

GE.06-23486  (E)    300806    010906

# Text boxes

-----