| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/104 14 July 2006 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.40. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 2 TO REGULATION No. 81

(Rear view mirrors (motorcycles/mopeds)

Submitted by the Working Party on General Safety Provisions (GRSG)

Note:	The text reproduced below was adopted by GRSG at its ninetieth session. It is based on document ECE/TRANS/WP.29/GRSG/2006/16, amended as reproduced in para. 52 of the report. It is submitted to WP.29 and to AC.1 for consideration (ECE/TRANS/WP.29/GRSG/69, paras. 47 and 52).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraphs 1. to 1.2., insert a reference to a new footnote 1/, the corresponding footnote 1/ and amend to read:

"1.	SCOPE

This Regulation applies:

1.1.	To rear view mirrors intended to be installed on vehicles of categories L 1/ without 	bodywork partly or wholly enclosing the driver and

1.2.	To the installation of rear view mirrors on vehicles of category L without bodywork partly or wholly enclosing the driver 2/.

__________________

1/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4).

2/	For power-driven vehicles having less than four wheels and fitted with bodywork which partly or wholly encloses the driver the requirements of Regulation No. 46 shall apply."

Paragraph 5.4.1., the reference to footnote 1/ and footnote 1/, renumber as footnote 3/ and  amend to read:

"3/	1 for Germany, 2 for France, 3 for Italy, 4 for the Netherlands, 5 for Sweden, 6 for Belgium, 7 for Hungary, 8 for the Czech Republic, 9 for Spain, 10 for Serbia and Montenegro, 11 for the United Kingdom, 12 for Austria, 13 for Luxembourg, 14 for Switzerland, 15 (vacant), 16 for Norway, 17 for Finland, 18 for Denmark, 19 for Romania, 20 for Poland, 21 for Portugal, 22 for the Russian Federation, 23 for Greece, 24 for Ireland, 25 for Croatia, 26 for Slovenia, 27 for Slovakia, 28 for Belarus, 29 for Estonia, 30 (vacant), 31 for Bosnia and Herzegovina, 32 for Latvia, 33 (vacant), 34 for Bulgaria, 35 (vacant), 36 for Lithuania, 37 for Turkey, 38 (vacant), 39 for Azerbaijan, 40 for The former Yugoslav Republic of Macedonia, 41 (vacant), 42 for the European Community (Approvals are granted by its Member States using their respective ECE symbol), 43 for Japan, 44 (vacant), 45 for Australia, 46 for Ukraine, 47 for South Africa, 48 for New Zealand, 49 for Cyprus, 50 for Malta, 51 for the Republic of Korea, 52 for Malaysia and 53 for Thailand.  Subsequent numbers shall be assigned to other countries in the chronological order in which they ratify or accede to the Agreement Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions, and the numbers thus assigned shall be communicated by the Secretary-General of the United Nations to the Contracting Parties to the Agreement."

Paragraph 15.4.1., the reference to footnote */ and footnote */, renumber as footnote 4/ and  amend to read:

"4/	See footnote 3/ of para. 5.4.1."

- - - - -