| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/141 6 October 2006 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.57. of the provisional agenda

## PROPOSAL FOR SUPPLEMENT 4 TO REGULATION No. 13-H

(Braking)

# Submitted by the Working Party on Brakes and Running Gear (GRRF) *

Note:  The text reproduced below was adopted by GRRF at its sixtieth session (ECE/TRANS/WP.29/GRRF/60, para. 10) and is submitted for consideration to WP.29 and AC.1.  It is based on the text of ECE/TRANS/WP.29/GRRF/2006/29, as amended by paragraph 10 of the report.  The modifications proposed in this document are similar to the amendments to Regulation No. 13 (see ECE/TRANS/WP.29/2006/44).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user.

Documents are also available via the INTERNET:

http://www.unece.org/trans/main/welcwp29.htm

_________

*  The UNECE Transport Division has submitted the present document after the official documentation deadline due to its late adoption by GRRF.

#### Insert new paragraphs 2.21. and 2.22., to read:

"2.21.	"Braking signal": logic signal indicating brake activation as specified in paragraph 5.2.22.

2.22.	"Emergency braking signal": logic signal indicating emergency braking as specified in paragraph 5.2.23."

Paragraph 5.2.22., amend to read:

"5.2.22.	Generation of a braking signal to illuminate stop lamps."

Insert new paragraphs 5.2.23. to 5.2.23.2.(b), to read:

"5.2.23.	When a vehicle is equipped with the means to indicate emergency braking, activation and de-activation of the emergency braking signal shall meet the specifications below:

5.2.23.1.	The signal shall be activated by the application of the service braking system at a deceleration of or above 6 m/s2;

The signal shall be de-activated at the latest when the deceleration has fallen below 2.5 m/s2.

5.2.23.2.	The following conditions may also be used:

(a)	by the application of the service braking system in such a manner that it would produce, in an unladen condition and engine disconnected, under the test conditions of Type-0 as described in Annex 3, a deceleration of or above 6 m/s2;

The signal shall be de-activated at the latest when the deceleration has fallen below 2.5 m/s2.

or

(b)	The signal may be activated when the service braking system is applied at a speed above 50 km/h and the antilock system is fully cycling (as defined in paragraph 2. of Annex 6).

The signal shall be deactivated when the antilock system is no longer fully cycling."

- - - - -