| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/44 27 March 2006 Original: ENGLISH |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth session

Geneva, 20-23 June 2006

Item 4.2.7. of the provisional agenda

## PROPOSAL FOR SUPPLEMENT 2 TO THE 10 SERIES OF AMENDMENTS

## TO REGULATION No. 13

(Braking)

# Submitted by the Working Party on Brakes and Running Gear (GRRF)

Note:  The text reproduced below was adopted by GRRF at its fifty-ninth session (ECE/TRANS/WP.29/GRRF/59, paras. 39 and annex 3) and is submitted for consideration to WP.29 and AC.1.  It is based on the text of ECE/TRANS/WP.29/GRRF/2006/2, as replaced in annex 3 to the report.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Insert new paragraphs 2.32. and 2.33., to read:

"2.32.	Braking signal: logic signal indicating brake activation as specified in paragraph 5.2.1.30.

2.33.	Emergency braking signal: logic signal indicating emergency braking as specified in paragraph 5.2.1.31."

Paragraph 5.2.1.30., amend to read:

"5.2.1.30.	Generation of a braking signal to illuminate stop lamps."

Insert new paragraphs 5.2.1.31. to 5.2.1.31.2.(b), to read:

"5.2.1.31.	When a vehicle is equipped with the means to indicate emergency braking, activation and de-activation of the emergency braking signal shall meet the specifications below:

5.2.1.31.1.	The signal shall be activated by the application of the service braking system as follows:

|  | Shall not be activated below |
| --- | --- |
| M1 and N1 | 6 m/s2 |
| M2, M3, N2 and N3 | 4 m/s2 |

The signal shall be de-activated for all vehicles at the latest when the deceleration has fallen below 2.5 m/s2.

5.2.1.31.2.	The following conditions may also be used:

(a)	The signal may be activated by the application of the service braking system in such a manner that it would produce, in an unladen condition and engine disconnected, under the test conditions of Type-0 as described in annex 4, a deceleration as follows:

|  | Shall not be activated below |
| --- | --- |
| M1 and N1 | 6 m/s2 |
| M2, M3, N2 and N3 | 4 m/s2 |

The signal shall be de-activated for all vehicles at the latest when the deceleration has fallen below 2.5 m/s2.

or,

(b)	The signal may be activated when the service braking system is applied at a speed above 50 km/h and the antilock system is fully cycling (as defined in paragraph 2. of annex 13).

The signal shall be deactivated when the antilock system is no longer fully cycling."

- - - - -