| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/46 27 March 2006 Original: ENGLISH |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth session

Geneva, 20-23 June 2006

Item 4.2.33. of the provisional agenda

## PROPOSAL FOR SUPPLEMENT 4 TO REGULATION No. 106

(Pneumatic tyres for agricultural vehicles)

# Submitted by the Working Party on Brakes and Running Gear (GRRF)

Note:  The text reproduced below was adopted by GRRF at its fifty-ninth session (ECE/TRANS/WP.29/GRRF/59, para. 26) and is submitted for consideration to WP.29 and AC.1.  It is based on the text of document ECE/TRANS/WP.29/GRRF/2005/15/Rev.1, not amended.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Insert a new paragraph 2.15.8., to read:

"2.15.8.	The letters "IF" before the nominal section width in case of "Improved Flexion Tyre".

The letters "VF" before the nominal section width in case of "Very High Flexion Tyre"."

Insert a new paragraph 2.20.1., to read:

"2.20.1.	"Improved Flexion Tyre" or "Very High Flexion Tyre" describe a pneumatic-tyre structure in which the carcass is more resistant than that of the corresponding standard tyre."

Insert a new paragraph 2.30.2., to read:

"2.30.2.	The table "Variation of load capacity with speed" is not applicable to "Improved Flexion" or "Very High Flexion" tyres."

Paragraph 3.1.4.2., amend to read:

"3.1.4.2.	in the case of implement tyre for mixed applications the tyre must be marked with two service descriptions one for "trailer" applications and the other for "traction" applications, each supplemented with the relevant symbol (see paragraphs 2.23. and 2.24. above) as follows:

|  | or |  |
| --- | --- | --- |

"

Insert a new paragraph 3.1.12., to read:

"3.1.12.	The inscription "IF" shall be added in front of the tyre-size designation when the tyre is "Improved Flexion Tyre".

The inscription "VF" shall be added in front of the tyre-size designation when the tyre is "Very High Flexion Tyre".

Annex 3, part A, note (a), amend to read:

"(a)	the size designation, comprising the prefix (if any), the nominal section width, the nominal aspect ratio, the type-of-structure symbol (where applicable) and the nominal rim diameter, must be grouped as shown in the examples:

360/70 R 24, IF 360/70 R 24, VF 360/70 R 24."

Annex 5, table 2 (3 of 3), low section height, between the tyre size designations 7.5L-15 and

17.5L-24, insert a new tyre size "14.9LR-20" to read:

"

| Tyre size designation | Theoretical rim width code (A1) | Nominal section Width (S1) (mm) | Overall Diameter (D) (mm) | Nominal rim Diameter (d) (mm) |
| --- | --- | --- | --- | --- |
|  |  | Radial | Diagonal | Radial | Diagonal |  |
| ........ |  |  |  |  |  |  |
| 14.9LR-20 | 13 | 378 |  | 1100 |  | 508 |
| ........ |  |  |  |  |  |  |

"

Annex 7, part A, insert a new sentence below the table to read:

"The above load/speed variations table does not apply to IF and VF Tyres."

- - - - -