| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/71 27 March 2006 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-thirty-ninth session

Geneva, 20-23 June 2006,

Item 4.2.31. of the provisional agenda

PROPOSAL FOR DRAFT SUPPLEMENT 3 TO THE 01 SERIES OF AMENDMENTS TO REGULATION No. 94

(Frontal collision protection)

Note by the World Forum for Harmonization of Vehicle Regulations (WP.29)

Note:  The document reproduced below was agreed by WP.29 at its one-hundred-and-thirty-eighth session.  It is based on the proposal of ECE/TRANS/WP.29/2006/29, as modified (ECE/TRANS/WP.29/1050, para.48).  It is submitted for consideration to WP.29 and AC.1.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user.

Documents are also available via the INTERNET:

http://www.unece.org/trans/main/welcwp29.htm

Paragraph 1., amend to read:

"1.	SCOPE

This Regulation applies to vehicles of category M1 1/of a total permissible mass not exceeding 2.5 tonnes; other vehicles may be approved at the request of the manufacturer. "

Insert a new paragraph 11.3., to read:

"11.3.	As long as there are no requirements in this Regulation with regard to the protection of the occupants by means of a full frontal impact test, Contracting Parties may continue to apply the requirements already in force for that purpose at the time of acceding to this Regulation."

- - - - -

___________

1/	As defined in annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (TRANS/WP.29/78/Rev.1/Amend.2 as last amended by its Amendment 4).