| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/80 17 July 2006 ENGLISH Original: ENGLISH AND FRENCH |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.9. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 12 TO THE 02 SERIES OF AMENDMENTS

TO REGULATIONS No. 19

(Front fog lamps)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-sixth session.  It is based on TRANS/WP.29/GRE/2005/27/Rev. 1, as amended by para. 32 of the report.  It is submitted to WP.29 and AC.1 for consideration and vote (ECE/TRANS/WP.29/GRE/56, paras. 32 and 33).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user.

Documents are also available via the INTERNET:

http://www.unece.org/trans/main/welcwp29.htm

REGULATION No. 19 – (Fog lamps)

Amend the title, to read:

"UNIFORM PROVISIONS CONCERNING THE APPROVAL OF POWER-DRIVEN VEHICLE FRONT FOG LAMPS"

Paragraph SCOPE, renumber as paragraph 0. and amend to read:

"0.	SCOPE 1/:

This Regulation applies to front fog lamps for vehicles of categories L3, L4, L5, L7, M, N, and T */.

______________

### 1/  Nothing in this Regulation …

*/  As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3) (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)."

### - - - - -