| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/92 9 August 2006 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.41. of the provisional agenda

PROPOSAL FOR SUPPLEMENT 10 TO REGULATION No. 87

(Daytime running lamps)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-sixth session.  It is based on ECE/TRANS/WP.29/GRE/2004/5/Rev. 2, as amended by para. 41 to the report.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRE/56, paras. 41 and 42).

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user.

Documents are also available via the INTERNET:

http://www.unece.org/trans/main/welcwp29.htm

List of contents (ANNEXES), amend to read:

" ….

Annex 6  -  Minimum requirements for sampling by an inspector

Annex 7  -  Minimum angles required for light distribution in space"

Text of the Regulation,

Paragraphs 7.1. to 7.3., amend to read:

"7.1.	The luminous intensity of the light emitted by each lamp shall not be less than 400 cd in the axis of reference.

7.2.	Outside the reference axis and within the angular fields defined in the arrangement diagram in Annex 7 to this Regulation, the intensity of the light emitted by each lamp must:

7.2.1.	In each direction corresponding to the points in the table of standard light distribution reproduced in Annex 3 to this Regulation, be not less than the minimum specified in paragraph 7.1. above, multiplied by the percentage specified in the said table of the direction in question, and

7.2.2.	not exceed 1,200 cd in any direction the lamp is visible.

7.3.	Moreover, throughout the field defined in the diagram in Annex 7, the intensity of the light emitted must not be less than 1.0 cd."

Paragraph 8., amend to read:

"8.	APPARENT SURFACE

The area of the apparent surface in the direction of the axis of reference of the lamp shall be not less than 25 cm² and not more than 200 cm²."

Annex 3, paragraph 5., amend the table of standard light distribution to read:

"

"

Insert a new Annex 7, to read:

"Annex 7

MINIMUM ANGLES REQUIRED FOR LIGHT DISTRIBUTION IN SPACE

In all cases, the minimum vertical angles of light distribution in space are 10° above and 5° below the horizontal for DRL devices included in the Regulation.

Minimum horizontal angles of light distribution in space:

"

- - - - -

# Text boxes

10°

5°

5°

20°

10°

5°

20°

10°

5°

V

V

H

90

90

10

10

10

10

100

70

70

70

70

25

25

20

20

20

20

20

20

20

H