| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRSG/2006/11 9 February 2006 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on General Safety Provisions (GRSG)

(Ninetieth session, 24-28 April 2006,

agenda item 2.2.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 26

(Exterior projections)

Transmitted by the expert from Belgium

Note:	The text reproduced below was prepared by the expert from Belgium in order to clarify the requirements for sheet metal edges.  The proposal is based on a document without an official symbol (informal document No. GRSG-89-28), distributed at the eighty-ninth session of GRSG (TRANS/WP.29/GRSG/68, para. 48).  The modifications to the current text of the Regulation (up to the 03 series of amendments) are marked in bold characters.

A.	PROPOSAL

Paragraph 6.8.1., amend to read:

"6.8.1.	Sheet-metal edges, such as gutter edges and the rails of sliding doors, shall not be permitted unless they are folded back or are fitted with a shield meeting the requirements of this Regulation which are applicable to it.

An unprotected edge shall be considered to be folded back either if it is folded back by approximately 180 º, or if it is folded towards the bodywork in such a manner that it cannot be contacted by a sphere having a diameter of 100 mm.

The requirements of paragraph 5.4. shall not apply to the following sheet metal edges: rear edge of bonnet, front edge of rear luggage boot and wheel arch edge."

B.	JUSTIFICATION

Some sheet-metal edges can be considered as not dangerous due to their location (edges not likely to increase the risk or seriousness of bodily injury).

Through the years, the interpretations have been developed and it has been agreed by different Approval Authorities that such parts as rear edge of bonnet, front edge of rear luggage boot and wheel arch edges are in compliance with the requirements of Regulation No. 26 as last amended, if they comply with the requirements applicable for sheet-metal edges (paragraph 6.8.1.).

The purpose of this proposal is to define these parts and to specify that only the requirements of paragraph 6.8.1. are applicable to these parts.

- - - - -