| Transmitted by the expert from Australia | Informal document No. GRSP-40-02 (40th GRSP, 12-15 December 2006, agenda item B.1.11.) |
| --- | --- |

#### Proposal for draft amendment to Regulation No. 94

(Protection of occupant in the event of a frontal collision)

Note:  	The text presented was transmitted by the expert from Australia in order to clarify head injury requirements in Regulation No. 94.

A.	PROPOSAL

Annex 4: "DETERMINATION OF PERFORMANCE CRITERIA"

Paragraph 1., amend to read:

“1.	HEAD INJURY CRITERIA”

Paragraph 1.2., amend to read:

“1.2.	If there is contact between the head and any vehicle component, a calculation of the value of HPC is made,….”

Paragraph 1.1., to be deleted.

Paragraphs 1.2., 1.2.1., 1.2.2., 1.2.3., 1.2.4. and 1.3., to be renumbered as 1.1., 1.1.1., 1.1.2., 1.1.3., 1.1.4. and 1.2. respectively.

B.	JUSTIFICATION

ECE Regulation No. 94, Paragraph 5.2.1.1. reads

Annex 4 specifies the method for determining performance criteria:

Annex 4, paragraph 1 appears to be ambiguous.

The heading for this paragraph is Head Performance Criterion (HPC), however, subparagraph 1.3. concerns an additional requirement for 3ms resultant head acceleration, which is a different assessment value from HPC.

Subparagraph 1.1. states that “this criterion” is satisfied if there is no contact between the dummy head and any vehicle component.

Is this intended to mean that HPC is satisfied if there is no head contact, but that the 3ms resultant head acceleration must be assessed regardless of head contact?

If GRSP confirms that the intention is that 3ms head acceleration must be assessed regardless of head contact, Australia would propose the above mentioned amendments to the text of Regulation No. 94.

- - - - -

# Text boxes

TRANS/WP.29/GRSP/2004/11

page 8