INF.21

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Eighty-second session

Geneva, 7-10 May 2007

Item 5 of the provisional agenda

##### COMMENTS ON ECE/TRANS/WP.15/2007/4 – INSTRUCTIONS IN WRITING

Transmitted by EIGA (European Industrial Gas Association)

Introduction

EIGA noted some discrepancies in the hazard characteristics of gases.

They are noted by underlining in the original table.

| Additional guidance to vehicle crews on the hazard characteristics of dangerous goods by class and on actions subject to prevailing circumstances |
| --- |
| Danger labels and placards | Hazard characteristics | Additional guidance |
| (1) | (2) | (3) |
| Explosive substances and articles 1 1.5 1.6 | May have a range of properties and effects such as mass detonation; projection of fragments; combustion; formation of bright light, loud noise or smoke. Sensitive to shocks and/or impacts and/or heat. | Take cover but stay away from windows. |
| Explosive substances and articles 1.4 | Slight risk of explosion. | Take cover but stay away from windows. |
| Flammable gases 2.1 | Risk of fire. Risk of explosion. May be under pressure Risk of asphyxiation May cause burns and/or frostbite. Containments may explode when heated. | Take cover. Keep out of low areas. |
| Non-flammable, non-toxic gases 2.2 | Risk of asphyxiation. May be under pressure. May cause frostbite. Containments may explode when heated. | Take cover. Keep out of low areas. |
| Toxic gases 2.3 | Risk of intoxication. May be under pressure. May cause burns and/or frostbite. Containments may explode when heated. | Take cover. Keep out of low areas. |
| Flammable liquids 3 | Risk of fire. Risk of explosion. Containments may explode when heated. | Take cover. Keep out of low areas. Prevent leaking substances from running into the aquatic environment or the sewage system. |

_________