Proposal for an Amendment to  gtr No. 3

(Motorcycle brake systems)

Transmitted by the representative of Canada

The following text refers to document ECE/TRANS/180/Add.3

A. PROPOSAL

Throughout the document, the text "category 3-4" must be replaced with "category 3-5", and the text "category 3-5" must be replaced with the text "category 3-4".

B. JUSTIFICATION.

The above amendment is necessary to reflect the amendment to the "Special Resolution No. 1 concerning common definitions of vehicle categories, masses and dimensions (S.R.1)" (TRANS/WP.29/1045 and ECE/TRANS/WP.29/1045/Amend.1) adopted by the Executive Committee of the 1998 Agreement (AC.3) at its March 2007 session (ECE7TRANS/WP.29/1058, para.105), which is applicable to global technical regulations under the 1998 Agreement.  The proposed amendment is an alignment of the subcategories of category 3 vehicles in S.R.1 to the subcategories of category L vehicles in the "Consolidated Resolution on the Construction of Vehicles (R.E.3)" that is applicable to Regulations annexed to the1958 Agreement.  Specifically, the defining criteria for category 3-4 and 3-5 vehicles in S.R.1 were interchanged such that category 3-4 is now synonymous with category L4 in R.E.3, and category 3-5 is now synonymous with category L5 in R.E.3.

To reflect these changes, the gtr on motorcycle brake systems must be amended such that all references to "category 3-4" must be replaced to read "category 3-5", and similarly, all references to "category 3-5" must be replaced to read "category 3-4".

___________

Note by the Secretary:  In accordance with paragraph 6.4. of the 1998 Agreement, a proposal for amending any global technical regulation established in the Global Registry shall be submitted by a Contracting Party to AC.3 following the procedure of paragraph. 6.3. of the Agreement.

- - - - -