Proposal for amendments to document ECE/TRANS/WP.29/2007/60

The following text is based on document ECE/TRANS/WP.29/2007/60.  New text is inserted in bold.  Deleted text is shown in strikeout.

On page 2, table of content, the square brackets shall be deleted in order to read:

“Annex 3C:	Attestation with regard to paragraph 3.2.9.”

On pages 6 and 7, item 3.2.9, the square brackets shall be deleted in order to read:

“3.2.9.	Components sold as aftermarket equipment and intended for the installation in motor vehicles need no type approval if they are not related to immunity related functions (see paragraph 2.12.).  In this case a declaration must be issued by the manufacturer that the ESA fulfils the requirements of this Regulation and in particular the limits defined in paragraphs 6.5., 6.6., 6.8. and 6.9.

During the transition period, ending on 4 November 2008, the person or legal entity responsible for placing on the market of such a product has to submit all relevant information and/or a sample to a Technical Service which will determine if the equipment is immunity related or not.  The result of the inspection shall be available within three weeks and not require additional testing.  A document according to the example given in Annex 3C shall be issued by the Technical Service within the same period.  In case of doubts and if the Technical Service refuses to issue an attestation according to Annex 3C, the manufacturer has to apply for type approval for his product.”

On page 30, Annex 4, the last sentence in item 1.2 is amended to read:

1.2.	Test method

…

If not otherwise stated in this annex the test shall be performed according to CISPR 12 (amendment 1, fifth edition  2005).

- - - - -