Proposal for the 11 series of amendments to Regulation No. 13

It is based on ECE/TRANS/WP.29/2007/106.

- PROPOSAL

Paragraph 12.4., amend to read:

"12.4.	Mandatory provisions for vehicles equipped with a vehicle stability function

12.4.1.	Requirements for the equipment of vehicles with vehicle stability functions as specified in paragraphs 5.2.1.32. and 5.2.2.23. of this Regulation, as amended by the 11 series of amendments, shall be applied as follows:

| Vehicle category | Application date (as from the date after entry into force of the 11 series of amendments) |
| --- | --- |
|  | Contracting Parties shall grant approvals only if the vehicle type to be approved meets the requirements of this Regulation as amended by the 11 series of amendments. | Contracting Parties applying this Regulation may refuse first national or regional registration of a vehicle which does not meet the requirements of the 11 series of amendments to this Regulation. |
| M2 | 60 months | 84 months |
| M3 (Class III) 3/ | 12 months | 36 months |
| M3 (other than above) 4/ | 24 months | 48 months |
| N2 5/ | 48 months | 72 months |
| N3 (tractors for semi-trailers) 6/ | 12 months | 36 months |
| N3 (other than above) 7/ | 24 months | 48 months |
| O3 8/ | 36 months | 60 months |
| O4 | 24 months | 36 months |

"

- JUSTIFICATION

These paragraphs are editorial correction align with the general guidelines for UNECE regulatory procedures and transitional provisions in UNECE Regulations, TRANS/WP.29/1044 which was approved at WP.29 at its one-hundred-and-thirty-sixth session.

- - - - -