| Transmitted by the expert from GTB | Informal document No. GRE-60-06 (60th GRE, 1 - 3 October 2008, agenda item 3(a)) |
| --- | --- |

21 August 2008

REGULATION No. 37 (Filament lamps)

Proposal for Supplement 33 to the 03 series of amendments

BACKGROUND

At its fifty-ninth session GRE considered two proposals from India regarding new filament light sources (GRE-59-38 and GRE-59-42) and agreed to resume consideration of these proposals at its sixtieth session, pending technical review by the experts from GTB and IEC

(ECE/TRANS/WP.29/GRE/2008/59, par. 6).

The proposals from India have since been distributed with official symbols (ECE/TRANS/WP.29/GRE/2008/27 and ECE/TRANS/WP.29/GRE/2008/28).

GTB POSITION

1)	GENERAL COMMENTS

As a consequence of the decision taken by GRE, GTB initiated a round of comments to the Indian proposals among its experts on Light Sources. After their evaluation GTB has concluded that a preliminary point of view can be presented at this time, but that more time is needed to prepare a consolidated position.

The major comments so far concern the use of existing caps for new light source categories. This may be acceptable if those light sources are only used in motorcycle applications and/or for wedge base light sources.

However, the caps of the proposed light source categories P18/5W and PR18/5W are already specified for light source categories P21/5W reps PR21/5W used in automotive signal lamps in general.  Therefore, the development of additional keys for existing caps is considered necessary.  The proposed caps for WY10W and WY16W do not exist and need to be standardised by IEC.

In the conventional process of introduction of new light sources, a proposal is developed in GTB, and the original author submits proposals for standardisation of new caps and its holders via the respective national committee of IEC.  The process in IEC is subject to strict rules as to procedure and timing and can hardly be changed; it takes nearly 24 months. Usually, GTB arranges the timing of proposals for new light sources to GRE in such a way that they are synchronised with the corresponding proposals to IEC. In this way, entry into force of the amendments to Regulation No. 37 and publication of the related IEC positively voted documents occur around the same moment in time. In this case, it looks like the proposals from India to GRE are ahead of the IEC process.

W10W and WY10W are proposed as wedge base alternative. "Wedge base" is indeed the only discriminating factor since the objective luminous flux is equal to that of H6W respectively HY6W and R10W respectively RY10W, wattage is not lower and dimensions are larger.

2)	PRELIMINARY CONCLUSIONS

- GTB would like to understand from the Indian delegation why existing categories with nearly the same specifications do not fulfil the requirements of the Indian industry.

- GTB need more time to conclude on the WY16W proposal (including cap).

- GTB suggests in general that one cap key is not used for more than one category in order to avoid mis-insertion of light sources into lamps. For wedge base lamps however, this may not be possible.  Therefore, in case of introduction of P18/5W and PR18/5W, new keys are recommended.

- GTB recommends that light source proposals to GRE that require a new IEC cap should be aligned with the IEC timetable. Type approval of new categories should not be granted before the IEC process has come to a stage where the design of the cap is final (RVC or later stages like FDIS or publication of the amendment of the standard).

3)	DETAILED COMMENTS

A. Comparison of major characteristics

B. Comparison per colour

C. List of categories

D. List of sheets

A. COMPARISON OF MAJOR CHARACTERISTICS

|  | Category | Objective Luminous flux (lm) | +/- | Max Objective Wattage (W) | IEC Cap | Max length to reference plane | Total length (Specified by R37) | Max diameter (mm) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| New proposals India | W10W | 125 | 20% | 11 | W2.1x9.5d | 32 | 38,1 | 15,7 | cap also W2.2W, W2.5W, W3W, W5W, WR5W, WY5W, W16W |
|  | WY10W | 75 | 20% | 11 | W3x9.5d | 32 | 38,1 | 15,7 | cap non-existing; also proposed for WY16W |
|  | WY16W | 189 | 20% | 21,35 | W3x9.5d | 32 | 38,1 | 15,7 | cap non-existing; also proposed for WY10W |
|  | P18/5W (major) | 325 | 15% | 23,5 | BAY15d | 45 |  | 26,5 | cap also: P21/5W |
|  | P18/5W (minor) | 35 | 20% | 6,6 |  |  |  |  |  |
|  | PR18/5W (major) | 76 | 20% | 23,5 | BAW15d | 45 |  | 26,5 | cap also: PR21/5W |
|  | PR18/5W (minor) | 8 | 25% | 6,6 |  |  |  |  |  |
| New proposals GTB | H10W | 200 | 12% | 12 | BAU9s | 28 |  | 9,25 | cap in IEC process (CD) |
|  | HY10W | 120 | 17% | 12 | BAUZ9s | 28 |  | 9,25 | cap in IEC process (CD) |
| Existing | H6W | 125 | 12% | 7,35 | BAX9s | 28 |  | 9,25 |  |
|  | HY6W | 75 | 17% | 7,35 | BAZ9s | 28 |  | 9,25 |  |
|  | R10W | 125 | 20% | 11 | BA15s | 30 |  | 19 |  |
|  | RY10W | 75 | 20% | 11 | BAU15s | 30 |  | 19 |  |
|  | W16W | 310 | 20% | 21,35 | W2.1x9.5d | 32 | 38,1 | 15,7 |  |
|  | H21W | 600 | 12% | 26,25 | BAY9s | 33 |  | 9,25 |  |
|  | HY21W | 300 | 17% | 26,25 | BAW9s | 33 |  | 9,25 |  |
|  | P21/5W (major) | 440 | 15% | 26,5 | BAY15d | 45 |  | 26,5 |  |
|  | P21/5W (minor) | 35 | 20% | 6,6 | BAY15d | 45 |  | 26,5 |  |
|  | PR21/5W (major) | 105 | 20% | 26,5 | BAW15d | 45 |  | 26,5 |  |
|  | PR21/5W (minor) | 8 | 25% | 6,6 | BAW15d | 45 |  | 26,5 |  |

12V versions

(Decimal comma used, as specified by ISO.)

B. COMPARISON PER COLOUR

| Colour | Category | Objective Luminous flux (lm) | +/- | Max Objective Wattage (W) | IEC Cap | Max length to reference plane | Total length (Specified by R37) | Max diameter (mm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1. White | H21W | 600 | 12% | 26,25 | BAY9s | 33 |  | 9,25 |
| 1. White | P21/5W (major) | 440 | 15% | 26,5 | BAY15d | 45 |  | 26,5 |
| 1. White | P18/5W (major) | 325 | 15% | 23,5 | BAY15d | 45 |  | 26,5 |
| 1. White | W16W | 310 | 20% | 21,35 | W2.1x9.5d | 32 | 38,1 | 15,7 |
| 1. White | H10W | 200 | 12% | 12 | BAU9s | 28 |  | 9,25 |
| 1. White | H6W | 125 | 12% | 7,35 | BAX9s | 28 |  | 9,25 |
| 1. White | R10W | 125 | 20% | 11 | BA15s | 30 |  | 19 |
| 1. White | W10W | 125 | 20% | 11 | W2.1x9.5d | 32 | 38,1 | 15,7 |
| 1. White | P21/5W (minor) | 35 | 20% | 6,6 | BAY15d | 45 |  | 26,5 |
| 1. White | P18/5W (minor) | 35 | 20% | 6,6 | BAY15d | 45 |  | 26,5 |
| 2. Amber | HY21W | 300 | 17% | 26,25 | BAW9s | 33 |  | 9,25 |
| 2. Amber | WY16W | 189 | 20% | 21,35 | W3x9.5d | 32 | 38,1 | 15,7 |
| 2. Amber | HY10W | 120 | 17% | 12 | BAUZ9s | 28 |  | 9,25 |
| 2. Amber | HY6W | 75 | 17% | 7,35 | BAZ9s | 28 |  | 9,25 |
| 2. Amber | RY10W | 75 | 20% | 11 | BAU15s | 30 |  | 19 |
| 2. Amber | WY10W | 75 | 20% | 11 | W3x9.5d | 32 | 38,1 | 15,7 |
| 3. Red | PR21/5W (major) | 105 | 20% | 26,5 | BAW15d | 45 |  | 26,5 |
| 3. Red | PR18/5W (major) | 76 | 20% | 23,5 | BAW15d | 45 |  | 26,5 |
| 3. Red | PR21/5W (minor) | 8 | 25% | 6,6 | BAW15d | 45 |  | 26,5 |
| 3. Red | PR18/5W (minor) | 8 | 25% | 6,6 | BAW15d | 45 |  | 26,5 |

12V versions

(Decimal comma used, as specified by ISO.)

C. LIST OF CATEGORIES

The proposal from India for insertion of new categories into the list of categories should be corrected and read as follows:

|  | Category |  | Sheet number(s) |  |
| --- | --- | --- | --- | --- |
|  | C5W |  | C5W/1 |  |
|  | H6W |  | H6W/1 |  |
|  | HY6W |  | H6W/1 |  |
|  | HY21W |  | H21W/1 to 2 |  |
|  | P13W |  | P13W/1 to 3 |  |
|  | P18/5W |  | P18/5W/1 to 3 |  |
|  | P19W |  | P19W/1 to 3 |  |
|  | P21W |  | P21W/1 to 2 |  |
|  | P21/4W |  | P21/4W/1 | (P21/5W/2 to 3) |
|  | P21/5W |  | P21/5W/1 to 3 |  |
|  | P24W |  | P24W/1 to 3 |  |
|  | P27W |  | P27W/1 to 2 |  |
|  | P27/7W |  | P27/7W/1 to 3 |  |
|  | PC16W |  | PC16W/1 to 3 |  |
|  | PCR16W |  | PC16W/1 to 3 |  |
|  | PCY16W |  | PC16W/1 to 3 |  |
|  | PR18/5W |  | PR18/5W/1 |  |
|  | PR19W |  | P19W/1 to 3 |  |
|  | PR21W |  | PR21W/1 | (P21W/2) |
|  | PR21/4W |  | PR21/4W/1 | (P21/5W/2 to 3) |
|  | PR21/5W |  | PR21/5W/1 | (P21/5W/2 to 3) |
|  | PR24W |  | P24W/1 to 3 |  |
|  | PR27/7W |  | PR27/7W/1 | (P27/7W/2 to 3) |
|  | PS19W |  | P19W/1 to 3 |  |
|  | PS24W |  | P24W/1 to 3 |  |
|  | PSR19W |  | P19W/1 to 3 |  |
|  | PSR24W |  | P24W/1 to 3 |  |
|  | PSY19W |  | P19W/1 to 3 |  |
|  | PSY24W |  | P24W/1 to 3 |  |
|  | PY19W |  | P19W/1 to 3 |  |
|  | PY21W |  | PY21W/1 | (P21W/2) |
|  | PY24W |  | P24W/1 to 3 |  |
|  | PY27/7W |  | PY27/7W/1 | (P27/7W/2 to 3) |
|  | R5W |  | R5W/1 |  |
|  | R10W |  | R10W/1 |  |
|  | RR5W |  | R5W/1 |  |
|  | RR10W |  | R10W/1 |  |
|  | RY10W |  | R10W/1 |  |
|  | T1.4W |  | T1.4W/1 |  |
|  | T4W |  | T4W/1 |  |
|  | W2.3W |  | W2.3W/1 |  |
|  | W3W |  | W3W/1 |  |
|  | W5W |  | W5W/1 |  |
|  | W10W |  | W10W/1 |  |
|  | W15/5W |  | W15/5W/1 to 3 |  |
|  | W16W |  | W16W/1 |  |
|  | W21W |  | W21W/1 to 2 |  |
|  | W21/5W |  | W21/5W/1 to 3 |  |
|  | WP21W |  | WP21W/1 to 2 |  |
|  | WPY21W |  | WP21W/1 to 2 |  |
|  | WR5W |  | W5W/1 |  |
|  | WR21/5W |  | WR21/5W/1 | (W21/5W/2 to 3) |
|  | WY2.3W |  | WY2.3W/1 |  |
|  | WY5W |  | W5W/1 |  |
|  | WY10W |  | WY10W/1 |  |
|  | WY16W |  | WY16W/1 |  |
|  | WY21W |  | WY21W/1 to 2 |  |

D. LIST OF SHEETS

The proposal from India for insertion of new sheets into the list of sheets should be corrected and read as follows:

|  | Sheet number(s) |  |
| --- | --- | --- |
|  | C5W/1 |  |
|  | C21W/1 to 2 |  |
|  | H1/1 to 3 |  |
|  | H3/1 to 4 |  |
|  | H4/1 to 5 |  |
|  | H7/1 to 4 |  |
|  | H8/1 to 4 |  |
|  | H9/1 to 4 |  |
|  | H10/1 to 3 |  |
|  | H11/1 to 4 |  |
|  | H12/1 to 3 |  |
|  | H13/1 to 4 |  |
|  | H14/1 to 4 |  |
|  | H15/1 to 5 |  |
|  | H6W/1 |  |
|  | H21W/1 to 2 |  |
|  | H27W/1 to 3 |  |
|  | HB3/1 to 4 |  |
|  | HB4/1 to 4 |  |
|  | HIR1/1 to 3 |  |
|  | HIR2/1 to 3 |  |
|  | HS1/1 to 5 |  |
|  | HS2/1 to 3 |  |
|  | HS5/1 to 4 |  |
|  | HS6/1 to 4 |  |
|  | P13W/1 to 3 |  |
|  | P18/5W/1 to 3 |  |
|  | P19W/1 to 3 |  |
|  | P21W/1 to 2 |  |
|  | P21/4W/1 |  |
|  | P21/5W/1 to 3 |  |
|  | P24W/1 to 3 |  |
|  | P27W/1 to 2 |  |
|  | P27/7W/1 to 3 |  |
|  | PC16W/1 to 3 |  |
|  | PR18/5W/1 |  |
|  | PR21W/1 |  |
|  | PR21/4W/1 |  |
|  | PR21/5W/1 |  |
|  | PR27/7W/1 |  |
|  | PY21W/1 |  |
|  | PY27/7W/1 |  |
|  | R2/1 to 3 |  |
|  | R5W/1 |  |
|  | R10W/1 |  |
|  | S1/S2/1 to 2 |  |
|  | S3/1 |  |
|  | T1.4W/1 |  |
|  | T4W/1 |  |
|  | W2.3W/1 |  |
|  | W3W/1 |  |
|  | W5W/1 |  |
|  | W10W/1 |  |
|  | W15/5W/1 to 3 |  |
|  | W16W/1 |  |
|  | W21W/1 to 2 |  |
|  | W21/5W/1 to 3 |  |
|  | WP21W/1 to 2 |  |
|  | WR21/5W/1 |  |
|  | WY2.3W/1 |  |
|  | WY10W/1 |  |
|  | WY16W/1 |  |
|  | WY21W/1 to 2 |  |

- - - - - -