Draft amendments to document ECE/TRANS/WP.29/GRPE/2008/2

The text reproduced below was prepared by the expert from CLEPA to revise document ECE/TRANS/WP.29/GRPE/2008/2 regarding the use of an On-Board Diagnostic (OBD) system, designed for "monofuel plus" systems to also be used as a "bifuel" system, when certain conditions are met.  This revision corrects formatting errors in the original document.

A.	PROPOSAL

Annex 11, paragraph 3.9.4., correct to read:

"3.9.4.	Regarding the status code (as described in paragraph 3.6. of this annex), one of the following two options has to be used if one or more of the diagnostics reporting readiness is fuel type specific:

(a)	the status code is fuel specific, i.e. use of two status codes, one for each fuel type;

(b)	the status code shall indicate fully evaluated control systems for both fuel types (petrol and NG/LPG) when the control systems are fully evaluated for one of the fuel types.

If none of the diagnostics reporting readiness is fuel type specific, then only one the status code has to be supported."

- - - - -