CLEPA Position on:

# Text boxes

Lane Departure Warning System (LDWS)

- Scope: mandatory for all vehicles (M & N)

  - Exemption of special purpose vehicles TBD

- Amendment of R79 	(steering)

- Functional requirements

  - Lane warning mandatory

  - Lane keeping optional

- Speed range

  - Between 60-130 km/h mandatory

  - Outside this range optional

- Detection capabilities: reaction when

  - Maximum 0.3 m outside of the lane marking

- Failure warning

  - Failure warning & non-failure loss of functionality 
indicators mandatory

- Switch-off

  - Driver shall be able to switch off manually

  - Automatic default to ‘ON’ at start-up

Advanced Emergency Braking System (AEBS)

- Scope: mandatory for

  - HDV: 	M2, M3, N2 and N3 with EVSC

  - PC: 	M1 and N1

- Amendment of

  - HDV: 	R13 	(braking)

  - PC: 	R13H 	(braking)

- Functional requirements

  - HDV: 	warning & autonomous braking mandatory

  - PC: 	warning & brake support function mandatory
	autonomous braking optional

- Speed range

  - Between 20-130 km/h mandatory

  - Outside this range optional

- Detection capabilities: reaction to

  - Moving and stopped vehicles mandatory

  - Stationary vehicles, motorcycles and pedestrians 
optional

- Failure warning

  - Failure warning & non-failure loss of functionality 
indicators mandatory

- Switch-off

  - Driver shall not be able to switch off manually

- Override

  - Driver shall always be able to override