PROPOSAL

Paragraph 6.1.3, amend to read:

"6.1.3.	Load Test Three (applicable to doors that open in a vertical direction)

6.1.3.1.	Each primary door latch system on back doors shall not disengage from the fully latched position when a load of 9,000 N is applied in the direction of the axis of the hinge pin. a direction orthogonal to the directions specified in paragraphs 6.1.1.1. and 6.1.2.1., when tested in accordance with paragraph 7.1.1.1.

Paragraph 6.1.5.1.(d), amend to read:

"6.1.5.1.	........

(d) On back doors which open in a vertical direction only, not separate when a vertical load of 9,000 N is applied in the direction of the axis of the hinge pin.

Annex 3,

Paragraph 1., amend to read:

"1.	Purpose.

These tests are …………..direction.  For back doors only which open in a vertical direction, the tests are intended …………………………."

Paragraph 2.3., amend to read:

"2.3.	Load Test Three (Back For Ddoors Only that open in a vertical direction)"

Title for Figure 3-3, amend to read:

"Figure 3-3 - Door Latch – Tensile Testing Fixture for Load Test Three (Back Doors OnlyFor doors that open in a vertical direction)"

Annex 4

Paragraph 2.3.3.5., amend to read:

"2.3.3.5.	Vertical Setup 1. (applicable to doors that open in a vertical direction Only for back doors).   Orient the door……………………."

Paragraph 2.3.3.6., amend to read:

"2.3.3.6.	Vertical Setup 2. (Applicable to doors that open in a vertical direction Only for back doors). Orient the door ………………….."

#### Annex 5

Paragraph 1., amend to read:

"1.	Purpose

These tests are conducted …………., and, for back doors onlydoors that open in a vertical direction, vertical vehicle directions."

Paragraph 2.1.3., amend to read:

"2.1.3.	Vertical Load Test (Backdoors OnlyFor doors that open in the vertical direction)"

Title for Figure 3-3, amend to read:

"Figure 5-2 – Static load test directions for back doors that open in the vertical direction."

Justification:

In line with proposals made for changes in the text of the GTR these proposed changes in text provide consideration in cases where back or side doors open vertically (e.g. gull-wing).