Proposal for draft corrigendum to Revision 2 of Regulation N°44

A.	PROPOSAL

Paragraph 7.1.4.4.1.1., add the footnote:

7. 1. 4. 4. 1. 1. Forward facing child restraints: the head of the manikin shall not pass beyond the planes BA and DA as defined in Figure 1 below.

This shall be judged up to 300 ms or the moment that the manikin has come to a definitive standstill whatever occurs first.

* / For the purpose of the test specified in paragraph 7. 1. 4. 1. 10. 1. 1., this dimension shall be  500  mm.

B.	JUSTIFICATION

During its 33rd session the GRSP accept a document for Revision 1 - Amendment 5

Supplement 6 to the 03 series of amendments - Date of entry into force: 12 August 2004

without reference to the footnote.

This footnote was added during the 32nd session of GRSP. See report TRANS/WP.29/32 page 22.

7.1.4.1.10.2. For ISOFIX child restraint system of other size classes with the anti-rotation device in use."

Paragraph 7.1.4.4.1.1., figure 1, insert a reference to a footnote 5/ to the 550 dimension, and insert the corresponding footnote 5/, to read:

_____________

"5/ For the purpose of the test specified in paragraph 7.1.4.1.10.1.1., this dimension shall be 500 mm."

All technical services are applying the requirement of the footnote on the current tests.