WP.15/AC.2/15/INF.9

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of Experts on the Regulations annexed to the

European Agreement concerning the International Carriage

of Dangerous Goods by Inland Waterways (ADN)

(ADN Safety Committee)

Fifteenth session

Geneva, 24-28 August 2009

Agenda item 7

SPECIAL AUTHORIZATIONS, DEROGATIONS AND EQUIVALENTS

Special authorization requested by Shell and proposed entry for Table C

Submitted by the Government of the Netherlands

3.2.4.1 Model special authorization under section 1.5.2

Special authorization under 1.5.2 of ADN

Under 1.5.2 of ADN, the transport in tank vessels of the substance specified in the annex to this special authorization shall be authorized in the conditions referred to therein. Before transporting the substance, the carrier shall be required to have it added to the list referred to in 1.16.1.2.5 of ADN by a recognized classification society.

This special authorization shall be valid ...........................................................................................

(places and/or routes of validity)

It shall be valid for two years from the date of signature, unless it is repealed at an earlier date.

Issuing State: ................................................

Competent authority: ....................................

ECE/TRANS/WP.15/AC.2/26

page 136

Date: .............................................................

Signature: .....................................................

3.2.4.2 Application form for special authorizations under section 1.5.2

For applications for special authorizations, please answer the following questions and points.*

Data are used for administrative purposes only and are treated confidentially.

Applicant

SHELL CHEMICALS EUROPE B.V.

P.O. Box 8610

3067GJ Rotterdam

The Netherlands

Summary of the application

Authorization for transport in tank vessels of IP Extraction Feed as a substance of

Class 3

Annexes

(with brief description)

Application made:

At:     S.C.E., Rotterdam

Date:  06-08-2009

Signature: J.van Berkel

1. General data on the dangerous substance

1.1 Is it a pure substance , a mixture X, a solution ?

1.2 Technical name Isoprene extraction Feed

1.3 Synonym. : Crude C5 stream , Raw C5 , Crude C5 , Isoprene Concentrate, Crude

Isoprene, Hydrocarbons C5-rich-.

1.4  Trade name.  Isoprene Extraction feed

* For questions not relevant to the subject of the application, write “not applicable”.

ECE/TRANS/WP.15/AC.2/26

1.5 Structure formula and, for mixtures, composition and/or concentration.

Isoprene                   10 – 25%

Dicyclopentadiene     2 -   5%

Cyclopentadiene        5 -  12%

Pentanes (N+Iso)     25  - 35%

1.3 Pentadiene         10 -  20%

Other Hydrocarbons 48 -   3%

1.6 Hazard class and, where applicable classification code, packing group.

Class 3, PG I, classification code F1,

1.7 UN No. 3295

2. Physico-chemical properties

2.1 State during transport:liquid

2.2 Density of liquid at 20 º C 678 kg/M3

2.3 Transport temperature <25 degr. C

2.4 Melting point or range not spplicable.

2.5 Boiling point or range 34 - 60 º C.

2.6 Vapour pressure at 15 º C –53.30 kPa, 30 º C  –16.62 kPa,

40º C    18.06 kPa  50 º C    62.95 kPa

2.7 Cubic expansion coefficient 0,001546 K-1

2.8 Solubility in water at 20 º C

Saturation concentration 0,05 mg/l (negligible)

or

Miscibility with water at 15 º C

Complete Xpartial none

2.9 Colour. Waterwhite to very slightly coloured

2.10 Odour. Unpleasant

2.11 Viscosity <1 mm2/s.

2.12 Flow time (ISO 2431-1996) not Applicable.

2.13 Solvent separation test not applicable .

2.14 pH of the substance or aqueous solution.  7

2.15 Other information. none

ECE/TRANS/WP.15/AC.2/26

3. Technical safety properties

3.1 Auto-ignition temperature in accordance with IEC 60079-4 (corresponds to

DIN 51 794) 350 º C; where applicable, indicate the temperature class in accordance with

EN 50 014: not applicable.

3.2 Flash-point <-20 degr. C (estimated value)

For flash-points up to 175 º C

Closed-cup test methods - non-equilibrium procedure

ABEL method: EN ISO 13736:1997

ABEL-PENSKY method: DIN 51755-1:1974 and DIN 51755-2:1978 or AFNOR

method: M07-019

PENSKY-MARTENS method: EN ISO 2719:2004

LUCHAIRE apparatus: French standard AFNOR T 60-103:1968

TAG method: ASTM D 56-02

Closed-cup test methods - equilibrium procedure

Rapid equilibrium procedure: EN ISO 3679:2004; ASTM D 3278-96:2004

Closed-cup equilibrium procedure: EN ISO 1523:2002; ASTM D 3941-90:2001

For flash-points above 175 º C

In addition to the above-mentioned methods, the following open-cup test method

may be applied:

CLEVELAND method: EN ISO 2592:2002; ASTM D 92-02b

3.3 Explosion limits:

Determination of upper and lower explosion limits in accordance with EN 1839:2004.

3.4 Maximum safe gap in accordance with IEC 60079-1:2003 between 1 and 12

3.5 Is the substance stabilized during transport? If so, provide data on the stabilizer:

Yes, Topanol A087 (specification in product 75 – 150 ppm)

3.6 Decomposition products in the event of combustion on contact with air or under the

influence of an external fire: not applicable

ECE/TRANS/WP.15/AC.2/26

3.7   Is the substance fire intensifying?                                      Yes

3.8   Abrasion (corrosion) not applicable mm/year.

3.9   Does the substance react with water or moist air by releasing flammable or toxic

gases?                                                                                  No

Gases released: none

3.10  Does the substance react dangerously in any other way?  No

3.11  Does the substance react dangerously when reheated?     No

4. Physiological hazards

4.1 LD50 and/or LC50 value. Necrosis value (where applicable, other toxicity criteria in

accordance with 2.2.61.1 of ADN).

CMR properties according to Categories 1A and 1B of chapters 3.5, 3.6 and 3.7 of

GHS

LD50: >2000 mg/kg Rabbit           LC50: >20 mg/l /4 hours Rat

4.2 Does decomposition or reaction produce substances posing physiological hazards?

(Indicate which substances where known)                           No

4.3 Environmental properties (see 2.4.2.1 of ADN)

Acute toxicity:

LC50 96 hr for fish           1  <= 10 mg/l

EC50 48 hr for crustacea   1  <= 10 mg/l

ErC50 72 hr for algae        1  <= 10 mg/l

Chronic toxicity:

NOEC .................................. mg/l                              not applicable

BCF ...................................... mg/l or log Kow ........   not applicable

Easily biodegradable ............ no

5.   Data on hazard potential

5.1 What specific damage is to be expected if the hazard characteristics produce their

effect?

Combustion

Injury

Corrosion

Intoxication in the event of dermal absorption

Intoxication in the event of absorption by inhalation

Mechanical damage

Destruction

Fire

Abrasion (corrosion to metals)

Environmental pollution

6. Data on the transport equipment

6.1 Are particular loading requirements envisaged/necessary (what are they)?

Yes. Tankbarge type C 50 kPa,

7. Transport of dangerous substances in tanks

7.1 With which materials is the substance to be carried compatible?

Stainless steel, Zinc coating, Epoxy coating.

8. Technical safety requirements

8.1 Taking into account the current state of science and technology, what safety measures

are necessary in the light of the hazards posed by the substance or liable to arise in the

course of the transport process as a whole?

Prepurge barge tanks with inert gas (Nitrogen) to <0,5% O2, maintain O2 level; Max

product temperature during transport 25 degr. C.

8.2 Additional safety measures

Use of stationary or mobile techniques to measure flammable gases and flammable

liquid vapours

Use of stationary or mobile techniques (toximeters) to measure concentrations of

toxic substances

Proposed entry for Table C

| Annex |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3a | 3b | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 |
| UN-N0. or substance Identification No. | Name and description | Class | Classification code | Packing groupe | Dangers | Type of tank vessel | Cargo tank design | Cargo tank type | Cargo tank equipment | Opening pressure of the high Velocity vent valve in kPa | Maximum degree of filling in in % | Relative density at 20 ºC | Type of sampling device | Pump room below deck permitted | Temperature Class | Explosion groupe | Ant-explosion protection required | Equipment required | Number of cones/blue lights | Additional requirements/Remarks |
| 3295 | HYDROCARBONS, LIQUID,N.O.S. CONTAINS ISOPRENE AND PENTADIENE (vp at 50 ºC higher than 110 kPa), stabilized | 3 | F1 | I | 3, unst. (N2, CMR) | C | 2 | 2 | 3 | 50 | 95 | 0,678 gr/ml | 1 | YES | T43) | II B4) | yes | PP,EX, A | 1 | 3,27, 29 |