| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/105 23 July 2009 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-ninth session

Geneva, 10-13 November 2009

Item 4.2.28 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 9 to Regulation No. 110

(Specific components for CNG)

Submitted by the Working Party on General Safety Provisions (/

The text reproduced below was adopted by the Working Party on General Safety (GRSG) at its ninety-sixth session.  It is based on ECE/TRANS/WP.29/GRSG/2009/3, not amended.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRSG/75, para. 30.)

Insert a new paragraph 17.9.4., to read:

"17.9.4. 	For vehicles of categories M2, M3, N2 and N3, 1/ the filling unit (receptacle) shall comply with the drawing specifications detailed in Figure 2 of Annex 4F or with the drawing specifications detailed in Figure 1 of Annex 4F".

Annex 4F,

Paragraph 2.1., amend to read:

"2.1.	The filling unit shall comply with the requirements laid down in paragraph 3. and shall have the dimensions of paragraph 4."

Paragraph 2.2., amend to read (including the insertion of a new footnote 2/):

"2.2.	Filling units designed in accordance with ISO 14469-1 first edition 2004-11-01 1/ or ISO 14469-2:2007 2/ and meeting all the requirements therein are deemed to fulfill the requirements of paragraphs 3. and 4. of this annex."

__________

2/	Road vehicles — Compressed natural gas (CNG) refueling connector — Part 2: 20 MPa (200 bar) connector, size 2"

Paragraph 4.1., footnote 2/ should be renumbered as footnote 3/

Insert a new paragraph 4.2., to read:

"4.2.	Figure 2 shows the dimensions of the filling unit for vehicles of categories M2, M3, N2 and N3. 3/"

Insert, after Figure1, a new Figure 2, to read:

"Fig. 2:         20 MPa Filling unit Size 2 (receptacle) for M2, M3, N2 and N3 vehicles

"

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.