| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRRF/2009/33 3 July 2009 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear

Sixty-sixth session

Geneva, 15-17 September 2009

Item 3(f) of the provisional agenda

REGULATIONS Nos. 13 AND 13-H

(Braking)

Electronic Vehicle Stability Control system

Proposal for amendments to Regulation No. 13

Submitted by the expert from the United Kingdom (

The text reproduced below was prepared by the expert from the United Kingdom to clarify that a Vehicle Stability Function may be fitted to category N1 voluntarily.  The modifications to the existing text of the Regulation are marked in bold and strikethrough characters.

A.	PROPOSAL

Annex 1

Insert a new paragraph 5.2.1.33., to read:

"5.2.1.33.	Category N1 vehicles having no more than 3 axles may be equipped with a vehicle stability function. If fitted, it shall include roll-over control and directional control and meet the technical requirements of Annex 21 to this Regulation."

B.	JUSTIFICATION

The recent 11 series of amendments to Regulation No.13 requires on a mandatory basis that certain categories of M2, M3, N2, N3, O3 and O4 vehicles be equipped with a Vehicle Stability Function (VSF). However, although there was an understanding within GRRF that an N1 could be fitted with a VSF voluntarily, it would appear that there is some confusion with the permissive requirement for N1 vehicles which requires clarification.  Therefore, the above proposed minor amendment should address any uncertainty.

- - - - -

# Footnotes

(  In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.