REGULATIONS Nos. 13 AND 13-H

(Braking)

Emergency Stop Signal

Proposal for amendments to Regulation No. 13-H

The text reproduced below was prepared by the expert from the International Organization of Motor Vehicle Manufacturers (OICA) in order to improve the wording of the prescriptions for electric regenerative braking.  It supersedes ECE/TRANS/WP.29/GRRF/2009/2/Rev.1.  The modifications to the existing text of the Regulation are marked in bold characters or as strikethrough.

A.	PROPOSAL

Paragraph 5.2.22.4., amend to read:

"5.2.22.4.	Electric regenerative braking systems as defined in paragraph 2.17., which produce a retarding force upon release of the throttle pedal, accelerator control, shall generate the signal mentioned above according to the following provisions:

| Vehicle decelerations | Signal generation |
| --- | --- |
| ≤ 0.7 m/s² | The signal shall not be generated |
| > 0.7 m/s² and ≤ 1.3 m/s² | The signal may be generated |
| > 1.3 m/s² | The signal shall be generated |

In all cases the signal shall be de-activated at the latest when the deceleration has fallen below 0.7 m/s². 6/

12.X.		As from the official date of entry into force of Supplement XX to the original version of this Regulation, no Contracting Party applying this Regulation shall refuse to grant ECE approval under this Regulation as amended by Supplement XX.

12.X.		Contracting Parties applying this Regulation shall continue to grant approvals to those types of vehicles which comply with the requirements of this Regulation as amended by Supplement XX-1 to the original version of this Regulation during the 48 months period which follows the date of entry into force of Supplement XX.

- - - - -

# Text boxes

Natural engine brake, M1 diesel vehicle, 1-5 gear

-1,4

-1,2

-1

-0,8

-0,6

-0,4

-0,2

0

0

50

100

150

200

250

Vehicle speed (km/h)

Deceleration (m/s2)

1st gear

2nd gear

4th gear

3rd gear