UN/SCEGHS/19/INF.38

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Globally Harmonized 1 July 2010 System of Classification and Labelling of Chemicals Nineteenth session Geneva, 30 June-2 July 2010 Item 2 (a) of the provisional agenda Updating of the third revised edition of the Globally Harmonized System of Classification and Labelling of Chemicals (GHS): Physical hazards

Comments on INF.19: Amendments to Chapter 2.5 (Gases under pressure)

Transmitted by the expert from Germany

# Text boxes

?

Yes

Yes

(High pressure)

Liquefied gas

Warning

Yes

Yes

Is the gas packaged under pressure and partially liquid 
at temperatures above – 50°C?

Yes

Yes

No

Yes

Not classified as a gas under pressure

Is the gas contained in a receptacle at a pressure of 200 kPa (gauge) or more at 20°C, or is the gas liquefied or liquefied and refrigerated?

No

The substance or mixture is a gas

Is the gas dissolved in a liquid solvent under a pressure of 200 kPa (gauge) or more 
at 20°C?

Is the critical temperature between –50 °C and +65 (C?

Compressed gas

Warning

Refrigerated 
liquefied gas

Warning

(Low pressure)

Liquefied gas

Warning

No

Is the gas entirely in gaseous state at –50 (C?

No

Is the gas made partially liquid because of its low temperature?

Is the critical temperature above +65 °C?

No

Dissolved gas

Warning

Yes

Yes

(High pressure)

Liquefied gas

Warning

Yes

Yes

Is the gas packaged under pressure and partially liquid 
at temperatures above – 50°C?

Yes

Yes

No

Yes

Not classified as a gas under pressure

Is the gas contained in a receptacle at a pressure of 200 kPa (gauge) or more at 20°C, or is the gas liquefied or liquefied and refrigerated?

No

The substance or mixture is a gas

Is the gas dissolved in a liquid solvent under a pressure of 200 kPa (gauge) or more 
at 20°C?

Is the critical temperature between –50 °C and +65 (C?

Compressed gas

Warning

Refrigerated 
liquefied gas

Warning

(Low pressure)

Liquefied gas

Warning

No

Is the gas entirely in gaseous state at –50 (C?

No

Is the gas made partially liquid because of its low temperature?

Is the critical temperature above +65 °C?

No

Dissolved gas

Warning