|  | United Nations | ECE/TRANS/WP.29/2010/120 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 4 August 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-second session

Geneva, 9–12 November 2010

Item 4.4.2 of the provisional agenda

1958 Agreement – Consideration of draft amendments
 to existing Regulations proposed by GRSP

Proposal for Supplement 2 to the 07 series of amendments to Regulation No. 14 (safety-belt anchorages)

Submitted by the Working Party on Passive Safety *

The text reproduced below was adopted by the Working Party on Passive Safety (GRSP) at its forty-seventh session. It is based on ECE/TRANS/WP.29/GRSP/2010/9, as amended by paragraph 21. of the report (ECE/TRANS/WP.29/GRSP/47, para. 21). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 5.3.8.3., amend to read:

“5.3.8.3.	Notwithstanding paragraph 5.3.8.1. at least one of the two ISOFIX positions systems shall be installed at the second seat row. This does not apply to vehicles of category M1 with:

(a)	Not more than two passenger doors and

(b)	A rear designated seating position for which interference with transmission and/or suspension components prevents the installation of ISOFIX anchorages according to the requirements of paragraph 5.2.3. and

(c)	Having a Power to mass ratio index (PMR) exceeding 140 according to the definitions within Regulation No. 51, and

(d)	Having an engine developing a maximum power greater than 200 kW. Such a vehicle needs to have only one ISOFIX anchorage system at a front passenger designated seating position [combined with an airbag deactivation device.”

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.