|  | United Nations | ECE/TRANS/WP.29/2010/124 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 4 August 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-second session

Geneva, 9–12 November 2010

Item 4.8.1 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda
to existing Regulations proposed by GRSP

Proposal for Corrigendum 4 to Revision 3 to Regulation No. 12 (Steering mechanism)

Submitted by the Working Party on Passive Safety *

The text reproduced below was adopted by the Working Party on Passive Safety (GRSP) at its forty-seventh session. It is based on ECE/TRANS/WP.29/GRSP/2010/14, as amended by paragraph 17. of the report (ECE/TRANS/WP.29/GRSP/47, para. 17). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Annex 4,

Insert a new paragraph 2.3.1., to read:

“2.3.1.	Following are non mandatory additional guidelines for mechanical properties of the bodyblock

(a)	Rate of loading during stiffness measurement: 250 ±50 mm/min,

(b)	Centre of gravity: 551.2 ±6 mm from top of the bodyblock,

(c)	Moment of inertia about lateral axis through centre of gravity: 2.26 ±0.23 kg x m2.”

Annex 5,

Paragraph 3.2., amend to read:

“3.2.	The head form shall be fitted with two accelerometers capable of measuring values in the impact direction.”

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.