|  | United Nations | ECE/TRANS/WP.29/2010/88 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 9 April 2010 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-first session

Geneva, 22 – 25 June 2010

Item 4.2.15 of the provisional agenda

1958 Agreement – Consideration of draft amendments
to existing Regulation

Proposal for Corrigendum 1 to Supplement 34 to the 03 series of amendments to Regulation No. 37 (Filament Lamps)

Submitted by the Working Party on Lighting and Light-Signalling (GRE)*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-third session. It is based on informal document No. GRE-63-05. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/63).

Annex 1, Sheet H16/1, footnote 5/, correct to read:

“5/	Notes concerning the filament diameter.

(a)	No actual diameter restrictions apply but the objective for future developments is to have d max. = 1.1 mm.

(b)	For the same manufacturer, the design diameter of standard (étalon) filament lamp and filament lamp of normal production shall be the same.”

Sheet H16/3, the table, correct to read:

“…

| Test voltage | Volts | 13.2 | 13.2 |
| --- | --- | --- | --- |
| Objective values | Watts | 26 max. | 26 max. |
|  | Luminous flux | 500+10% / -15 % |  |

…”

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.