| Transmitted by the expert from Japan | Informal document No. GRSG-99-27 (99th GRSG, 19-22 October 2010 agenda item 11) |
| --- | --- |

Proposal for amendment to Regulation No. 125 (Forward field of vision of drivers)

A.	PROPOSAL

Paragraph 2.16., amend to read:

2.16.	"A pillar" means any the foremost and outermost roof support forward of the vertical transverse plane located 68 mm in front of the V points and includes non-transparent items such as windscreen mouldings and door frames, attached or contiguous to such a support.

B.	JUSTIFICATION

Some vehicles look as if they would have two A-pillars in each side.

In this case, the number of A pillar seems to be conflicted with Paragraph 5.1.2.2.

Therefore, the definition of "A pillar" is clarified by aligning with Regulation No. 29.