## Slide 1: Pole Side Impact GTR: Assessment of Safety Need: Initial Data Collection
Robert Hogan
Department of Infrastructure and Transport
PSI-01-07

## Slide 2: Data request
Focus of data request:
  Up to date statistics covering a number of regions/countries – to gauge the magnitude of the problem (older data in GRSP paper)
  Time series – allowing assessment of the impact of positive safety developments, including ESC
  Categories of vehicles – enabling consideration of which vehicles should be covered by a GTR

## Slide 3: Data Issues
Issues
  Number of countries still to provide data
  Data is very patchy in terms of vehicle categories and years covered
  Definitions vary (especially for injury figures and vehicle categories)
In the time available, analysis has focused on fatalities

## Slide 4: Preliminary Analysis - 1
Fatality levels from pole side impacts vary from country to country
  although there may be coding issues
Other side impacts are still a very significant source of fatalities
Rollovers are a very significant source of fatalities
The limited data available suggest M1 fatalities greatly outnumber N1 fatalities, but together the constitute nearly all pole side impact fatalities
  indicating a GTR may sensibly cover both

## Slide 5: Preliminary Analysis - 2
Data from a number of countries suggest pole side impact fatalities have decreased marginally more than the general road toll
  but in countries where they have been a major issue, they remain a major issue
Other side impact fatalities show a greater decrease
Rollover fatalities have increased in several countries

## Slide 6: United States
In 2009, there were 1,371 four-wheeled vehicle occupant fatalities in pole side impacts
4,872 in other side impacts and
8,794 in rollovers
  These figures are 4.1%, 14.4% and 26.0% respectively of the US’ road toll
  5.7%, 20.4% and 36.8% respectively of four-wheeled occupant fatalities
Of these numbers, 1,353, 4,746 and 8,267 were in passenger cars/small trucks
    5.8%, 20.3% and 35.6% of occupant fatalities in these types of vehicles
(pole = pole/tree/shrub/fire hydrant)

## Slide 7: Canada
In 2007, there were 16 M1 and N1 vehicle occupant fatalities in pole side impacts
353 in other side impacts and
273 in rollovers
  These figures were 0.6%, 12.8% and 9.9% respectively of Canada’s road toll

## Slide 8: Australia
In 2006, there were 161 four-wheeled vehicle occupant fatalities in pole side impacts
172 in other side impacts and
317 in rollovers
  These figures were 10.4%, 10.7% and 19.8% respectively of Australia’s road toll, and
  14.7%, 15.7% and 29.0% respectively of occupant fatalities in four-wheeled vehicles
Of these numbers, 149, 157 and 253 were in M1 vehicles
    16.3%, 17.2% and 27.8% of occupant fatalities in M1 vehicles

## Slide 12: Victoria (Australian state)
In 2009, there were 31 four-wheeled vehicle occupant fatalities in pole side impacts
20 in other side impacts and
38 in rollovers
  These figures were 10.7%, 6.8% and 13.1% respectively of Victoria’s road toll, and
  15.8%, 10.2% and 19.4% respectively of occupant fatalities in four-wheeled vehicles
Of these numbers, 25, 17 and 23 were in M1 vehicles
    16.7%, 11.3% and 15.3% of occupant fatalities in M1 vehicles

## Slide 13: New Zealand
In 2009, there were 7 four-wheeled vehicle occupant fatalities in pole side impacts (fairly typical)
41 in other side impacts and
89 in rollovers
  These figures were 1.8%, 10.7% and 23.2% respectively of New Zealand’s road toll
  2.4%, 13.9% and 30.2% respectively of occupant fatalities in four-wheeled vehicles

## Slide 14: Republic of Korea
In 2009, there were 204 four-wheeled vehicle occupant fatalities in pole side impacts
1,024 in other side impacts and
190 in rollovers
  These figures were 3.5%, 17.5% and 3.25% respectively of the ROK’s road toll
  10.3%, 51.8% and 9.6% respectively of occupant fatalities in four-wheeled vehicles
(NB: pole impacts = all impacts with fixed objects)

## Slide 17: Japan
Data is for M1 vehicles
60 reported fatalities from pole side impacts and 254 reported fatalities from other side impacts in the period 2005-07 - 1.3% and 5.4% respectively of fatalities in M1 vehicles in that period
  Fatality figures do not include people not wearing seatbelts – about 50% of the Japanese road toll
  The definition of pole is restricted and does not include trees

## Slide 18: Europe
Awaiting data from all countries
APROSYS (2009) reported approximately 10,000 car occupant fatalities in side impact crashes in Europe annually.
In Germany in 2008, 931 fatalities were due to collisions with trees – 20.8% of the road toll
  In the large majority of cases (810/907), passenger cars responsible
  Germany is to provide fuller statistics, but likely that over half of the collisions were pole side impacts
In the UK in 2009, at least 265 fatalities were due to pole impacts – 11.9% of the road toll

## Slide 19: Vehicle Coverage - 1
In the period 2000-2006 in Australia
  M1 (93.4%) and N1 (6.5%) vehicles accounted for 100% of four-wheeled occupant fatalities in pole side impacts
  M1 (93.3%) and N1 (5.3%) vehicles accounted for 98.6% of four-wheeled occupant fatalities in other side impacts
  M1 (80.6%) and N1 (8.4%) vehicles accounted for 89.0% of four-wheeled occupant fatalities in rollovers
In period 2000-2009 in the US, passenger cars and light trucks accounted for 98.9%, 97.7% and 94.3% respectively of pole side impact, other side impact and rollover occupant fatalities in four-wheeled vehicles

## Slide 20: Vehicle Coverage - 2
Side impacts and rollovers present a similar hazard for N1 vehicles as for M1 vehicles
In the period 2000-2006 in Australia
  12.1% of occupant fatalities in N1 vehicles were in pole side impacts
  13.1% in other side impacts, and
  26.5% in rollovers

## Slide 21: Trends over time
In Australia road fatalities decreased by 11.8% between 2000 and 2006 and four-wheeled vehicle occupant fatalities by 15.2%
  In the same period M1 occupant fatalities decreased in pole side impacts and other side impacts by 18.7% and 35.0% and increased in rollovers by 19.5%
    The M1 category is the most likely to reflect improvements due to ESC
In Victoria road fatalities decreased by 28.7% between 2000 and 2009 and four-wheeled vehicle occupant fatalities by 30.7%
  In the same period M1 occupant fatalities decreased in pole side impacts, other side impacts and rollovers by 40.4%, 59.5% and 39.4% respectively (small numbers)

## Slide 22: Trends over time - 2
In New Zealand road fatalities decreased by 16.8% between 2000 and 2009 and four-wheeled vehicle occupant fatalities by 21.3%
  In the same period all four-wheeled vehicle occupant fatalities decreased in pole side impacts and other side impacts by 22.2% and 43.8% and increased in rollovers by 11.3% (small numbers)
In the US road fatalities decreased by 19.4% between 2000 and 2009 and four-wheeled vehicle occupant fatalities by 27.6%
  In the same period passenger car/light truck occupant fatalities decreased in pole side impacts, other side impacts and rollovers by 16.2%, 37.2% and 17.0% respectively
In Germany, total road fatalities decreased by 40.3% in the period 2000 to 2008, while fatalities with trees decreased by 44.8%

## Slide 23: Next steps
Complete initial data collection by end December
Analyse – serious injuries as well as fatalities
Consider further more detailed data requirements (including age, gender, body region injured)