INF.46

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods 	16 September 2011

Joint Meeting of the RID Committee of Experts and the
Working Party on the Transport of Dangerous Goods

Geneva, 13–23 September 2011

Item 4 of the provisional agenda

Harmonization with the United Nations Recommendations 
on the Transport of Dangerous Goods

Alternative wording for the new sentence in 5.2.1.1

Note from the secretariat

The secretariat proposes the following alternative wording to clarify the new second sentence in 5.2.1.1.

"The UN number and the letters "UN" shall be at least 12 mm high, except for packages of 30 litres capacity or less or of 30 kg maximum net mass and for cylinders of 60 litres water capacity or less, when they shall be at least 6 mm in height and except for packages of 5 litres or 5 kg or less when they shall be of an appropriate size.".

Version with revision marks:

"The UN number and the letters "UN" shall be at least 12 mm high, except for packages of 30 litres capacity or less or of 30 kg maximum net mass and for cylinders of 60 litres water capacity or less, when they shall be at least 6 mm in height and except for packages of 5 litres or 5 kg or less when they shall be of an appropriate size.".

_____________