|  | United Nations | ECE/TRANS/WP.29/2011/133 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 29 July 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

155th session

Geneva, 15–18 November 2011

Item 4.11.6 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda

to existing Regulations submitted by GRE

Proposal for Corrigendum 1 to Revision 1 to Regulation No. 104 (Retro-reflective markings)

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fifth session to introduce editorial correction. It is based on ECE/TRANS/WP.29/GRE/2011/4 not amended (ECE/TRANS/WP.29/GRE/65, para. 31). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Annex 7, paragraph 1, correct to read:

"When illuminated with a CIE Standard illuminant A and measured as recommended by CIE publication No. 54, 1982, the coefficient of retro-reflection R' in candelas per m2 per lux (cd/m2/lux) of the retro-reflective areas in new condition shall be at least as indicated in table 1 for yellow, white and red materials."

Annex 7, table 1, correct to read:

# "Table 1

Minimum values for the Coefficient of Retro-reflection R’ [cd.m-2.lx-1]

| Observation angle α [º] | Entrance Angle β [º] |
| --- | --- |
| α=0.33(20’) | β1 | 0 | 0 | 0 | 0 | 0 |
|  | β2 | 5 | 20 | 30 | 40 | 60 |
| Colour |  |  |  |  |  |  |
| Yellow |  | 300 | -- | 130 | 75 | 10 |
| White |  | 450 | -- | 200 | 95 | 16 |
| Red |  | 120 | 60 | 30 | 10 | -- |

"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208/, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.