|  | United Nations | ECE/TRANS/WP.29/2011/137 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 2 August 2011 Original: English English and Russian only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

One-hundred-and-fifty-fifth session

Geneva, 15-18 November 2011

Item 4.12.4 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda 
to existing Regulations submitted by GRSG

Proposal for Corrigendum 7 to Supplement 2 to Regulation No. 107 (M2 and M3 vehicles)

Submitted by the Working Party on General Safety Provisions *

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its 100th session. It is based on GRSG-100-07, as reproduced in Annex II to the report (ECE/TRANS/WP.29/GRSG/79, para. 12). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

I.	Proposal

Приложение 3,Пункт 7.6.2.7., исправить следующим образом:

"7.6.2.7.	 При наличии аварийных люков они должны размещаться следующим образом: если имеется только один люк, то он должен устанавливаться в средней трети пассажирского салона; если имеется два люка, то они должны быть разнесены, причем расстояние между ближайшими краями отверстий, измеренное по линии, параллельной продольной оси транспортного средства, должно быть не менее 2 м".

Приложение 3,Пункт 7.12.4., исправить следующим образом:

"7.12.4.	Подъем каждой ступеньки в междуэтажной лестнице двухэтажного транспортного средства должен быть закрыт".

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.